Source	Marketwire
Date	10/30/2014
Time	06:39:14 AM

Company	 MIDLANDS MINERALS CORPORATION
Title	Midlands Minerals Announces Further High-Grade Silver Intercepts at Parlozi





    CDNX Symbol: MEX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Midlands Minerals Corporation

TSX VENTURE SYMBOL: MEX

October 30, 2014

Midlands Minerals Announces Further High-Grade Silver Intercepts at Parlozi

Phase 1 Drilling Completed

TORONTO, ONTARIO--(Marketwired - Oct. 30, 2014) - Midlands Minerals Corporation 
("Midlands" or the "Company") (TSX VENTURE:MEX) announces new high-grade silver 
assays from the Plandiste prospect on its Parlozi project in Serbia, and the 
successful completion of the initial commitment to Reservoir Minerals Inc. 
("Reservoir") (TSX VENTURE:RMC) allowing the Company to appraise the next phase 
of exploration work.

Highlights

/T/

--  Drilling at the Plandiste prospect, the first of six untested targets,
intersected seven zones of old underground workings and three additional
unmined, mineralized structures. New drill results over apparent
thicknesses at Plandiste include:
--  178 g/t silver and 1.0% lead over 2.30 metres (216 g/t silver
equivalent)
--  210 g/t silver and 0.9% lead over 1.40 metres (241 g/t silver
equivalent)
--  Drilling successfully validated the intercepts in the historic resource
at the Parlozi prospect.
--  The Company is currently reviewing the exploration work that would be
required to advance the project from the information obtained in the
Phase 1 work program.
--  Midlands currently has $2 million in the treasury.

/T/

Craig Pearman, President and CEO stated: "This drill program has achieved its 
purpose in providing the Company an opportunity to further evaluate the Parlozi 
project in a cost-effective and sound manner, and meeting the minimum spend 
commitment. It has enabled us to take significant steps forward in our 
geological modeling and we continue to see evidence for a large polymetallic 
mineralization system. The Company is currently appraising the implications of 
these Phase 1 drill results on a Phase 2 exploration program and operational 
budget which will be the subject of a future release."

Drill program

Subsequent to the news release of September 3, 2014, two additional core holes 
for 451.7 metres completed the first phase of exploration. Core drilling in 
Phase 1 has therefore totaled 1,714.4 metres in six drill holes and exceeded 
the drill commitment to Reservoir by 214.4 metres. The location and status of 
the Phase 1 drill holes are presented in Table 1 and Figure 1. All reported 
composites are listed in Table 3.

/T/

----------------------------------------------------------------------------
Depth     Azimuth         Dip
Drill Hole ID      (m)   (degrees)   (degrees)   Prospect   Comment
----------------------------------------------------------------------------
14-PA-001        645.0          95         -62   Parlozi    Results released
on Sept 3
----------------------------------------------------------------------------
14-PA-001A       124.8          97         -66   Parlozi    Results released
on Sept 3
----------------------------------------------------------------------------
14-PA-002        233.0         203         -64   Plandiste  Results released
on Sept 3
----------------------------------------------------------------------------
14-PA-003        259.9         201         -65   Plandiste  Results released
on Sept 3
----------------------------------------------------------------------------
14-PA-004        240.0          90         -65   Parlozi    This release
----------------------------------------------------------------------------
14-PA-005        211.7         155         -50   Plandiste  This release
----------------------------------------------------------------------------
Table 1: Holes drilled during Phase 1

/T/

Parlozi prospect

Drill hole 14-PA-004 tested the up-dip extension towards surface of the 
polymetallic mineralization at distance from the Parlozi historic resource. A 
hydrothermal breccia zone of 4.8 metres thickness, and averaging 0.78% lead and 
0.32% zinc, was intersected at a down-hole depth of 67.9 metres close to the 
zone of the ancient surface workings at Parlozi (Table 3). In addition, 
14-PA-004 also intersected a zone of 1.4 g/t gold over 0.7 metres at a 
down-hole depth of 173.7 metres (Table 3). The mineralization in the drill hole 
is interpreted as distal and is not representative of the mineralization in the 
area of the historic resources.

Drill hole 14-PA-001 had previously successfully confirmed the presence of 
multiple high-grade veins combined with wide zones of carbonate replacement 
mineralization in the area of the historic resource (reported in the 
press-release of September 3, 2014) with intercepts over apparent widths of:

/T/

--  291 g/t silver, 2.2% lead and 0.2% zinc over 2.45 metres from 154.0
metres (458 g/t silver equivalent)
--  174 g/t silver, 2.5% lead and 3.8% zinc over 2.95 metres from 301.65
metres (340 g/t silver equivalent)
--  299 g/t silver, 1.1% lead and 0.3% zinc over 5.10 metres from 534.4
metres (373 g/t silver equivalent)

/T/

In 1986, a resource estimate at the Parlozi prospect based on ten of the drill 
holes (totaling 4507.8 metres) is reported in a report by Radulovic titled 
"Geological-economic evaluation of ore bearing structure Parlozi in Babe 
deposit on the level of prospecting exploration" (unpublished report from 
Serbian Ministry of Mines and Energy). The historical resource estimate is 
based on five mineralized horizons along a strike length of approximately 450 
metres and between 200 and 500 metres below surface. This historical resource 
classified as C1 plus C2 resources in accordance with the Yugoslav reporting 
system, is estimated to contain 6.5 million tonnes at an average grade of 4.1% 
lead, 2.1% zinc, 0.3% copper and 130 g/t silver. This historical resource 
estimate was not estimated under the guidance of National Instrument (NI) 
43-101 and does not meet the CIM definition standard. A qualified person as 
defined by NI 43-101 has not undertaken sufficient work to classify these 
figures as mineral resources or mineral reserves, and additional drilling is 
require to do so. Midlands is not treating them as current mineral resources or 
mineral reserves. The historical resource estimate is only considered as 
relevant as a guide to future exploration.

Plandiste prospect

Drill hole 14-PA-005 was added to the drill program following recent structural 
analysis which indicated the possibility that 14-PA-002 and 14-PA-003 may not 
have fully tested the downdip extension of the high-grade mineralization that 
was sampled in an adit (671 g/t silver and 20.8% lead over 6.0 metres) and 
reported in the press release of May 13, 2014.

Drill hole 14-PA-005 successfully intersected ten separate structures, all of 
which are interpreted to be zones of mineralization. Seven of these 
intersections are represented as underground workings, and an additional three 
newly defined mineralized structures were intercepted which returned the 
composite assays listed in Table 2.

/T/

----------------------------------------------------------------------------
From       To Interval    Pb    Zn    Cu     Ag    Au   AgEq
Hole ID            m        m        m     %     %     %    g/t   g/t    g/t
----------------------------------------------------------------------------
14-PA-005     136.60   137.70     1.10  3.51  0.02  0.02   64.8  0.07  162.4
----------------------------------------------------------------------------
14-PA-005(i)  171.20   173.50     2.30  1.03  0.12  0.02  177.8  0.12  216.0
----------------------------------------------------------------------------
14-PA-005     187.00   188.40     1.40  0.91  0.10  0.00  210.0  0.09  241.4
----------------------------------------------------------------------------
Table 2: Drill intercepts at Plandiste (full list of composites in Table 3).

Note: Drill intervals are apparent thicknesses Additional drilling is
required to establish true thicknesses. Silver equivalents are based on the
rounded average of each metal price over the last 5 years (2009-2013),
assuming 100% recovery: Pb $2,100/t; Zn $2,000/t; Cu $7,300/t; Ag $25.0/oz;
Au $1,350/oz.
(i) Mine fill material was intersected in underground workings. It is
interpreted as collapsed material from the top of the workings.

/T/

Drill hole 14-PA-005 therefore drilled through a zone of intense historical 
mining, of significantly greater importance than recorded in any historical 
data. This has provided useful information on the focus of the historical 
mining at Plandiste and makes a significant contribution to the developing 
geological model at the Plandiste prospect. It is anticipated that subsequent 
to, and pursuant on results from a ground geophysical survey, the swarm of 
interpreted mineralized structures intercepted by hole 14-PA-005 at Plandiste 
would need to be drilled in future to obtain clean intercepts away from 
historic mining. Importantly, it appears that the Plandiste intercepts 
represent distal mineralization which provides added encouragement to test 
Plandiste to depth in Phase 2 drilling.

Other targets

Midlands is currently obtaining quotes for an induced polarization (IP) 
geophysical survey to cover the southern prospects of the Parlozi licence 
(Kukac, Maxim, Gomilice and Glavcine exploration targets). This data will be 
merged with the individual Phase 1 geophysical surveys that were already 
completed over the Plandiste and Parlozi prospects. These surveys, in 
combination with structural mapping would precede and facilitate Phase 2 drill 
planning.

Systematic QA/QC protocols are followed on the project including insertion of 
duplicate, blank and standard samples in all sample batches. The samples were 
submitted to SGS laboratory located in Bor, Serbia for preparation and assaying 
for gold using a standard 30 gram fire assay method with atomic absorption 
finish. Sample pulps with 85% of content lower than 75 microns were analyzed at 
SGS laboratory in Bor as well for 49 elements using ICP-MS following digestion 
by 4 acids. Samples with results greater than 100 g/t silver or greater than 1% 
lead, zinc or copper in the ICP-MS results were re-analyzed using 4 acid 
digestion and atomic absorption finish.

Additional information is found on SEDAR (www.sedar.com), in the updated 
Independent Technical Report on the Parlozi property prepared in compliance 
with NI 43-101 filed on April 24, 2014. Dr. Dominique Fournier, EurGeol, a 
"Qualified Person" as defined by National Instrument 43-101, has reviewed and 
approved the technical information and data included in this press release.

About Midlands Minerals Corporation

Midlands has an option agreement with Reservoir Minerals ("Reservoir") (TSX 
VENTURE:RMC) to earn up to a 75% interest in Reservoir's Parlozi 
zinc-lead-silver project in Serbia announced April 24, 2014.

Midlands is a Canadian resource company with common shares that trade on the 
TSX Venture Exchange under the symbol "MEX". The Parlozi Project, the Company's 
flagship, is a 91 square kilometre exploration permit which is conveniently 
located 35 kilometres south of Belgrade, the capital of Serbia. The Parlozi 
permit covers occurrences of historical lead-zinc-silver mining in the 
Kosmaj-Babe area of the Sumadija mining district in central Serbia. The 
mineralization in the permit comprises silver-bearing vein and replacement-type 
lead-zinc sulphides hosted by carbonate sedimentary rocks associated with 
intrusive Tertiary quartz latite dykes and volcanic breccias. This type of 
mineralization has long supported lead-zinc-silver mining operations in the 
region. Additional information on Midlands can be viewed under the Company's 
profile at www.sedar.com or on Midlands' website: www.midlandsminerals.com.

To view Figure 1 please click on the following link: 
http://media3.marketwire.com/docs/MEX1030.pdf

/T/

----------------------------------------------------------------------------
Inter-
From      To    val    Pb    Zn    Cu    Ag    Au Pb+Zn Ag Eq
HoleID            m       m      m     %     %     %   g/t   g/t     %   g/t
----------------------------------------------------------------------------
14-PA-001     63.10   67.70   4.60  1.42  0.05  0.11  10.5  0.94  1.47
including    63.10   63.60   0.50  2.91  0.10  0.12  57.8  5.32  3.01
14-PA-001    154.00  156.45   2.45  2.21  0.19  0.71 291.4  0.73  2.40 457.9
14-PA-001    209.80  210.90   1.10  0.45  0.22  0.23  82.0  0.54  0.66 148.9
14-PA-001    262.30  262.80   0.50  7.35  4.51  0.08  37.0  0.15 11.86
14-PA-001    283.90  295.75  11.85  1.03  2.22  0.02  17.1  0.02  3.25
including   291.10  295.75   4.65  1.77  3.95  0.03  30.1  0.02  5.72
and         292.10  294.65   2.55  2.22  5.64  0.04  42.4  0.03  7.85
14-PA-001    301.65  304.60   2.95  2.52  3.81  0.03 173.9  0.05  6.33 340.3
including   301.65  302.60   0.95  6.10  9.53  0.05 506.0  0.14 15.63 914.8
14-PA-001    377.70  384.10   6.40  1.66  1.81  0.01  19.9  0.17  3.47
including   377.70  378.50   0.80  5.23  1.05  0.02  43.0  0.15  6.28
and         381.40  384.10   2.70  2.38  3.97  0.02  33.6  0.14  6.35
14-PA-001    419.00  420.70   1.70  2.76  2.66  0.04  40.2  0.11  5.42
14-PA-001    434.00  438.70   4.70  2.42  2.26  0.02  33.9  0.12  4.68
including   434.70  435.55   0.85  6.43  6.40  0.03  77.0  0.22 12.83
14-PA-001    504.00  510.50   6.50  1.16  1.13  0.07  61.8  0.09  2.29 131.9
including   509.75  510.50   0.75  0.98  0.18  0.21 170.0  0.07  1.16 222.7
14-PA-001    516.55  517.35   0.80  1.84  2.55  0.23 120.0  0.06  4.39 256.0
14-PA-001    534.40  539.50   5.10  1.15  0.26  0.11 298.9  0.51  1.41 372.9
including   537.00  539.50   2.50  2.00  0.50  0.08 567.2  0.96  2.51 691.4
14-PA-001    609.00  615.50   6.50  1.71  1.43  0.35 102.8  0.09  3.14 219.6
------------
14-PA-001A    60.20   71.60  11.40  1.09  0.05  0.34  40.7  0.40  1.14
including    61.40   64.60   3.20  1.24  0.04  0.17  18.9  1.10  1.28
and          61.40   63.00   1.60  1.75  0.06  0.31  31.0  2.12  1.81
and          65.50   66.40   0.90  1.77  0.03  0.36 197.0  0.15  1.80
14-PA-001A    73.60   75.20   1.60  2.01  0.07  0.03  35.2  0.51  2.08
14-PA-001A    90.20   93.40   3.20  1.93  0.19  0.05  15.7  0.15  2.12
----------------------------------------------------------------------------14-P
A-002     93.10   95.40   2.30  2.46  0.15  0.01  25.5  0.07  2.61
------------
14-PA-003    136.90  139.00   2.10  4.25  0.07  0.02 355.3  0.18  4.32 480.1
----------------------------------------------------------------
including   137.90  139.00   1.10  5.30  0.09  0.04 623.0  0.24  5.39 779.9
------------
14-PA-004(1)  67.90    72.7   4.80  0.78  0.32  0.03  3.47  0.12  1.10
----------------------------------------------------------------
14-PA-004    173.70  174.40   0.70  0.23  0.23  0.00   0.7  1.40  0.46
------------
14-PA-005    136.60  137.70   1.10  3.51  0.02  0.02  64.8  0.07  3.53 162.4
----------------------------------------------------------------
14-PA-005(2) 171.20  173.50   2.30  1.03  0.12  0.02 177.8  0.12  1.15 216.0
14-PA-005    187.00  188.40   1.40  0.91  0.10  0.00 210.0  0.09  1.01 241.4
----------------------------------------------------------------------------
Table 3: Comprehensive table of composites of significant Phase 1 drill
intercepts at the Parlozi and Plandiste prospects.

The composite is calculated as a silver equivalent based on the rounded
average of each metal price over the last 5 years (2009-2013): Pb $2,100/t;
Zn $2,000/t; Cu $7,300/t; Ag $25.0/oz; Au $1,350/oz. Only composites greater
than 150 g/t AgEq m (silver equivalent in g/t multiplied by metres of
intercepts) are listed. Drill intervals are apparent thicknesses.
(1) Intercept below the 150 g/t AgEq m cut-off
(2) Mine fill material was intersected in underground workings. It is
interpreted as collapsed material from the top of the workings.

/T/

On behalf of the Board of Directors of Midlands Minerals Corporation,

Craig Pearman, President and CEO

This news release includes certain forward-looking statements or information. 
All statements other than statements of historical fact included in this 
release, including, without limitation, statements regarding the completion of 
the Transaction, the receipt of regulatory approvals, the Company's future 
plans, objectives or expectations of the Company are forward-looking statements 
that involve various risks and uncertainties. There can be no assurance that 
such statements will prove to be accurate and actual results and future events 
could differ materially from those anticipated in such statements. Important 
factors that could cause actual results to differ materially from the Company's 
plans or expectations include risks relating to the fluctuating gold prices, 
possibility of equipment breakdowns and delays, exploration cost overruns, 
availability of capital and financing, general economic, market or business 
conditions, regulatory changes, timeliness of government or regulatory 
approvals and other risks detailed herein and from time to time in the filings 
made by the Company with securities regulators. The Company expressly disclaims 
any intention or obligation to update or revise any forward-looking statements 
whether as a result of new information, future events or otherwise except as 
otherwise required by applicable securities legislation. Neither the TSX 
Venture Exchange, its Regulation Services Provider (as that term is defined in 
the policies of the TSX Venture Exchange, nor the OTCQX accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Midlands Minerals Corporation
Craig Pearman
President and CEO
+1 604 366 2229
cpearman@midlandsminerals.com

or

Midlands Minerals Corporation
Nick Tintor
Chairman
+1 416 987 0855
ntintor@rgmi.ca

or

Midlands Minerals Corporation
Nancy Curry
Corporate Communications
+1 604 220 2971
ncurry@midlandsminerals.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=505028352