Source	MARKET NEWS
Date	10/30/2014
Time	07:09:26 AM

Company	 Midlands Minerals Corporation
Title	Midlands 
Minerals Announces Further High grade S





    CDNX Symbol: MEX











Press Release	




[200/News Release]MEXVMIDLANDS MINERALS CORPOCT 30 2014  07:07 AMMidlands 
Minerals Announces Further High grade Silver --->@NEWS RELEASE
MIDLANDS MINERALS CORP ("MEX-V;MDLXF-0")
RESERVOIR MINERALS INC. ("RMC-V")
- Midlands Minerals Announces Further High-grade Silver
- Intercepts At Parlozi

Midlands Minerals Corporation ("Midlands" or the "Company")
announces new high-grade silver assays from the Plandiste prospect on
its Parlozi project in Serbia, and the successful completion of the
initial commitment to Reservoir Minerals Inc. ("Reservoir") allowing
the Company to appraise the next phase of exploration work.

Highlights



--  Drilling at the Plandiste prospect, the first of six untested targets,
intersected seven zones of old underground workings and three
additional
unmined, mineralized structures. New drill results over apparent
thicknesses at Plandiste include:
--  178 g/t silver and 1.0% lead over 2.30 metres (216 g/t silver
equivalent)
--  210 g/t silver and 0.9% lead over 1.40 metres (241 g/t silver
equivalent) --  Drilling successfully validated the intercepts
in the historic resource
at the Parlozi prospect. --  The Company is currently reviewing the
exploration work that would be
required to advance the project from the information obtained in
the
Phase 1 work program. --  Midlands currently has $2 million in the
treasury.

Craig Pearman, President and CEO stated: "This drill program has
achieved its purpose in providing the Company an opportunity to further
evaluate the Parlozi project in a cost-effective and sound manner, and
meeting the minimum spend commitment. It has enabled us to take
significant steps forward in our geological modeling and we continue to
see evidence for a large polymetallic mineralization system. The
Company is currently appraising the implications of these Phase 1 drill
results on a Phase 2 exploration program and operational budget which
will be the subject of a future release."

Drill program

Subsequent to the news release of September 3, 2014, two
additional core holes for 451.7 metres completed the first phase of
exploration. Core drilling in Phase 1 has therefore totaled 1,714.4
metres in six drill holes and exceeded the drill commitment to
Reservoir by 214.4 metres. The location and status of the Phase 1 drill
holes are presented in Table 1 and Figure 1. All reported composites
are listed in Table 3.

//st

---------------------------------------------------------------------------
-
Depth     Azimuth         Dip
Drill Hole ID      (m)   (degrees)   (degrees)   Prospect   Comment
---------------------------------------------------------------------------
-
14-PA-001        645.0          95         -62   Parlozi    Results released
on Sept 3
---------------------------------------------------------------------------
-
14-PA-001A       124.8          97         -66   Parlozi    Results released
on Sept 3
---------------------------------------------------------------------------
-
14-PA-002        233.0         203         -64   Plandiste  Results released
on Sept 3
---------------------------------------------------------------------------
-
14-PA-003        259.9         201         -65   Plandiste  Results released
on Sept 3
---------------------------------------------------------------------------
-
14-PA-004        240.0          90         -65   Parlozi    This release
---------------------------------------------------------------------------
-
14-PA-005        211.7         155         -50   Plandiste  This release
---------------------------------------------------------------------------
-

Table 1: Holes drilled during Phase 1

//et

Parlozi prospect

Drill hole 14-PA-004 tested the up-dip extension towards surface
of the polymetallic mineralization at distance from the Parlozi
historic resource. A hydrothermal breccia zone of 4.8 metres thickness,
and averaging 0.78% lead and 0.32% zinc, was intersected at a down-hole
depth of 67.9 metres close to the zone of the ancient surface workings
at Parlozi (Table 3). In addition, 14-PA-004 also intersected a zone of
1.4 g/t gold over 0.7 metres at a down-hole depth of 173.7 metres
(Table 3). The mineralization in the drill hole is interpreted as
distal and is not representative of the mineralization in the area of
the historic resources.

Drill hole 14-PA-001 had previously successfully confirmed the
presence of multiple high-grade veins combined with wide zones of
carbonate replacement mineralization in the area of the historic
resource (reported in the press-release of September 3, 2014) with
intercepts over apparent widths of:



--  291 g/t silver, 2.2% lead and 0.2% zinc over 2.45 metres from 154.0
metres (458 g/t silver equivalent) --  174 g/t silver, 2.5% lead
and 3.8% zinc over 2.95 metres from 301.65
metres (340 g/t silver equivalent) --  299 g/t silver, 1.1% lead
and 0.3% zinc over 5.10 metres from 534.4
metres (373 g/t silver equivalent)

In 1986, a resource estimate at the Parlozi prospect based on ten
of the drill holes (totaling 4507.8 metres) is reported in a report by
Radulovic titled "Geological-economic evaluation of ore bearing
structure Parlozi in Babe deposit on the level of prospecting
exploration" (unpublished report from Serbian Ministry of Mines and
Energy). The historical resource estimate is based on five mineralized
horizons along a strike length of approximately 450 metres and between
200 and 500 metres below surface. This historical resource classified
as C1 plus C2 resources in accordance with the Yugoslav reporting
system, is estimated to contain 6.5 million tonnes at an average grade
of 4.1% lead, 2.1% zinc, 0.3% copper and 130 g/t silver. This
historical resource estimate was not estimated under the guidance of
National Instrument (NI) 43-101 and does not meet the CIM definition
standard. A qualified person as defined by NI 43-101 has not undertaken
sufficient work to classify these figures as mineral resources or
mineral reserves, and additional drilling is require to do so. Midlands
is not treating them as current mineral resources or mineral reserves.
The historical resource estimate is only considered as relevant as a
guide to future exploration.

Plandiste prospect

Drill hole 14-PA-005 was added to the drill program following
recent structural analysis which indicated the possibility that
14-PA-002 and 14-PA-003 may not have fully tested the downdip extension
of the high-grade mineralization that was sampled in an adit (671 g/t
silver and 20.8% lead over 6.0 metres) and reported in the press
release of May 13, 2014.

Drill hole 14-PA-005 successfully intersected ten separate
structures, all of which are interpreted to be zones of mineralization.
Seven of these intersections are represented as underground workings,
and an additional three newly defined mineralized structures were
intercepted which returned the composite assays listed in Table 2.

//st

---------------------------------------------------------------------------
-
From       To Interval    Pb    Zn    Cu     Ag    Au   AgEq
Hole ID            m        m        m     %     %     %    g/t   g/t    g/t
---------------------------------------------------------------------------
-
14-PA-005     136.60   137.70     1.10  3.51  0.02  0.02   64.8  0.07  162.4
---------------------------------------------------------------------------
-
14-PA-005(i)  171.20   173.50     2.30  1.03  0.12  0.02  177.8  0.12  216.0
---------------------------------------------------------------------------
-
14-PA-005     187.00   188.40     1.40  0.91  0.10  0.00  210.0  0.09  241.4
---------------------------------------------------------------------------
-




Table 2: Drill intercepts at Plandiste (full list of composites in Table
3).

Note: Drill intervals are apparent thicknesses Additional drilling is
required to establish true thicknesses. Silver equivalents are based on the
rounded average of each metal price over the last 5 years (2009-2013),
assuming 100% recovery: Pb $2,100/t; Zn $2,000/t; Cu $7,300/t; Ag $25.0/oz;
Au $1,350/oz.
* Mine fill material was intersected in underground workings. It is
interpreted as collapsed material from the top of the workings.

//et

Drill hole 14-PA-005 therefore drilled through a zone of intense
historical mining, of significantly greater importance than recorded in
any historical data. This has provided useful information on the focus
of the historical mining at Plandiste and makes a significant
contribution to the developing geological model at the Plandiste
prospect. It is anticipated that subsequent to, and pursuant on results
from a ground geophysical survey, the swarm of interpreted mineralized
structures intercepted by hole 14-PA-005 at Plandiste would need to be
drilled in future to obtain clean intercepts away from historic mining.
Importantly, it appears that the Plandiste intercepts represent distal
mineralization which provides added encouragement to test Plandiste to
depth in Phase 2 drilling.

Other targets

Midlands is currently obtaining quotes for an induced polarization
(IP) geophysical survey to cover the southern prospects of the Parlozi
licence (Kukac, Maxim, Gomilice and Glavcine exploration targets). This
data will be merged with the individual Phase 1 geophysical surveys
that were already completed over the Plandiste and Parlozi prospects.
These surveys, in combination with structural mapping would precede and
facilitate Phase 2 drill planning.

Systematic QA/QC protocols are followed on the project including
insertion of duplicate, blank and standard samples in all sample
batches. The samples were submitted to SGS laboratory located in Bor,
Serbia for preparation and assaying for gold using a standard 30 gram
fire assay method with atomic absorption finish. Sample pulps with 85%
of content lower than 75 microns were analyzed at SGS laboratory in Bor
as well for 49 elements using ICP-MS following digestion by 4 acids.
Samples with results greater than 100 g/t silver or greater than 1%
lead, zinc or copper in the ICP-MS results were re-analyzed using 4
acid digestion and atomic absorption finish.

Additional information is found on SEDAR (www.sedar.com), in the
updated Independent Technical Report on the Parlozi property prepared
in compliance with NI 43-101 filed on April 24, 2014. Dr. Dominique
Fournier, EurGeol, a "Qualified Person" as defined by National
Instrument 43-101, has reviewed and approved the technical information
and data included in this press release.

About Midlands Minerals Corporation

Midlands has an option agreement with Reservoir Minerals
("Reservoir") (TSX VENTURE:RMC) to earn up to a 75% interest in
Reservoir's Parlozi zinc-lead-silver project in Serbia announced April
24, 2014.

Midlands is a Canadian resource company with common shares that
trade on the TSX Venture Exchange under the symbol "MEX". The Parlozi
Project, the Company's flagship, is a 91 square kilometre exploration
permit which is conveniently located 35 kilometres south of Belgrade,
the capital of Serbia. The Parlozi permit covers occurrences of
historical lead-zinc-silver mining in the Kosmaj-Babe area of the
Sumadija mining district in central Serbia. The mineralization in the
permit comprises silver-bearing vein and replacement-type lead-zinc
sulphides hosted by carbonate sedimentary rocks associated with
intrusive Tertiary quartz latite dykes and volcanic breccias. This type
of mineralization has long supported lead-zinc-silver mining operations
in the region. Additional information on Midlands can be viewed under
the Company's profile at www.sedar.com or on Midlands' website:
www.midlandsminerals.com.

To view Figure 1 please click on the following link:
http://media3.marketwire.com/docs/MEX1030.pdf

//st

---------------------------------------------------------------------------
-
Inter-
From      To    val    Pb    Zn    Cu    Ag    Au Pb+Zn Ag Eq
HoleID            m       m      m     %     %     %   g/t   g/t     %   g/t
---------------------------------------------------------------------------
-
14-PA-001     63.10   67.70   4.60  1.42  0.05  0.11  10.5  0.94  1.47
including    63.10   63.60   0.50  2.91  0.10  0.12  57.8  5.32  3.01
14-PA-001    154.00  156.45   2.45  2.21  0.19  0.71 291.4  0.73  2.40 457.9
14-PA-001    209.80  210.90   1.10  0.45  0.22  0.23  82.0  0.54  0.66 148.9
14-PA-001    262.30  262.80   0.50  7.35  4.51  0.08  37.0  0.15 11.86
14-PA-001    283.90  295.75  11.85  1.03  2.22  0.02  17.1  0.02  3.25
including   291.10  295.75   4.65  1.77  3.95  0.03  30.1  0.02  5.72
and         292.10  294.65   2.55  2.22  5.64  0.04  42.4  0.03  7.85
14-PA-001    301.65  304.60   2.95  2.52  3.81  0.03 173.9  0.05  6.33 340.3
including   301.65  302.60   0.95  6.10  9.53  0.05 506.0  0.14 15.63 914.8
14-PA-001    377.70  384.10   6.40  1.66  1.81  0.01  19.9  0.17  3.47
including   377.70  378.50   0.80  5.23  1.05  0.02  43.0  0.15  6.28
and         381.40  384.10   2.70  2.38  3.97  0.02  33.6  0.14  6.35
14-PA-001    419.00  420.70   1.70  2.76  2.66  0.04  40.2  0.11  5.42
14-PA-001    434.00  438.70   4.70  2.42  2.26  0.02  33.9  0.12  4.68
including   434.70  435.55   0.85  6.43  6.40  0.03  77.0  0.22 12.83
14-PA-001    504.00  510.50   6.50  1.16  1.13  0.07  61.8  0.09  2.29 131.9
including   509.75  510.50   0.75  0.98  0.18  0.21 170.0  0.07  1.16 222.7
14-PA-001    516.55  517.35   0.80  1.84  2.55  0.23 120.0  0.06  4.39 256.0
14-PA-001    534.40  539.50   5.10  1.15  0.26  0.11 298.9  0.51  1.41 372.9
including   537.00  539.50   2.50  2.00  0.50  0.08 567.2  0.96  2.51 691.4
14-PA-001    609.00  615.50   6.50  1.71  1.43  0.35 102.8  0.09  3.14 219.6

------------
14-PA-001A    60.20   71.60  11.40  1.09  0.05  0.34  40.7  0.40  1.14
including    61.40   64.60   3.20  1.24  0.04  0.17  18.9  1.10  1.28
and          61.40   63.00   1.60  1.75  0.06  0.31  31.0  2.12  1.81
and          65.50   66.40   0.90  1.77  0.03  0.36 197.0  0.15  1.80
14-PA-001A    73.60   75.20   1.60  2.01  0.07  0.03  35.2  0.51  2.08
14-PA-001A    90.20   93.40   3.20  1.93  0.19  0.05  15.7  0.15  2.12
---------------------------------------------------------------------------
-
14-PA-002     93.10   95.40   2.30  2.46  0.15  0.01  25.5  0.07  2.61

------------
14-PA-003    136.90  139.00   2.10  4.25  0.07  0.02 355.3  0.18  4.32 480.1
----------------------------------------------------------------
including   137.90  139.00   1.10  5.30  0.09  0.04 623.0  0.24  5.39 779.9

------------14-PA-004(1)  67.90    72.7   4.80  0.78  0.32  0.03  3.47  0.12  
1.10
----------------------------------------------------------------
14-PA-004    173.70  174.40   0.70  0.23  0.23  0.00   0.7  1.40  0.46

------------
14-PA-005    136.60  137.70   1.10  3.51  0.02  0.02  64.8  0.07  3.53 162.4
----------------------------------------------------------------
14-PA-005(2) 171.20  173.50   2.30  1.03  0.12  0.02 177.8  0.12  1.15 216.0
14-PA-005    187.00  188.40   1.40  0.91  0.10  0.00 210.0  0.09  1.01 241.4
---------------------------------------------------------------------------
-

Table 3: Comprehensive table of composites of significant Phase 1 drill
intercepts at the Parlozi & Plandiste prospects.

The composite is calculated as a silver equivalent based on the rounded
average of each metal price over the last 5 years (2009-2013): Pb $2,100/t;
Zn $2,000/t; Cu $7,300/t; Ag $25.0/oz; Au $1,350/oz. Only composites
greater than 150 g/t AgEq*m (silver equivalent in g/t multiplied by metres
of intercepts) are listed. Drill intervals are apparent thicknesses.
(1) Intercept below the 150 g/t AgEq*m cut-off
(2) Mine fill material was intersected in underground workings. It is
interpreted as collapsed material from the top of the workings.

//et

On behalf of the Board of Directors of Midlands Minerals
Corporation,

Craig Pearman, President and CEO

This news release includes certain forward-looking statements or
information. All statements other than statements of historical fact
included in this release, including, without limitation, statements
regarding the completion of the Transaction, the receipt of regulatory
approvals, the Company's future plans, objectives or expectations of
the Company are forward-looking statements that involve various risks
and uncertainties. There can be no assurance that such statements will
prove to be accurate and actual results and future events could differ
materially from those anticipated in such statements. Important factors
that could cause actual results to differ materially from the Company's
plans or expectations include risks relating to the fluctuating gold
prices, possibility of equipment breakdowns and delays, exploration
cost overruns, availability of capital and financing, general economic,
market or business conditions, regulatory changes, timeliness of
government or regulatory approvals and other risks detailed herein and
from time to time in the filings made by the Company with securities
regulators. The Company expressly disclaims any intention or obligation
to update or revise any forward-looking statements whether as a result
of new information, future events or otherwise except as otherwise
required by applicable securities legislation. Neither the TSX Venture
Exchange, its Regulation Services Provider (as that term is defined in
the policies of the TSX Venture Exchange, nor the OTCQX accepts
responsibility for the adequacy or accuracy of this release.

ENQUIRIES:
Midlands Minerals Corporation
Craig Pearman
President and CEO
+1 604 366 2229
cpearman@midlandsminerals.com

Midlands Minerals Corporation
Nick Tintor
Chairman
+1 416 987 0855
ntintor@rgmi.ca

Midlands Minerals Corporation
Nancy Curry
Corporate Communications
+1 604 220 2971
ncurry@midlandsminerals.com
TSX Venture closing price for MEX-V
Date: 2014/10/28
Closing Price: 0.01

TEL:  (604) 366 2229       Midlands Minerals Corporation
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1430200014TS11430201296-07070920141030