Source	MARKET NEWS
Date	10/30/2014
Time	08:01:31 AM

Company	 Midlands Minerals Corporation
Title	High 
grade Silver Mineralization At The Parlozi





    CDNX Symbol: MEX











Press Release	





RESERVOIR MINERALS INC ("RMC-V;RVRLF-0")
MIDLANDS MINERALS CORPORATION ("MEX-V")
- High-grade Silver Mineralization At The Parlozi Project, And
- Midlands Fulfil Initial Expenditure And Drilling Commitment

Reservoir Minerals Inc. ("RMC" or the "Company") is pleased to
report results of recent drilling at the Parlozi silver-lead-zinc
Project in central Serbia with partner Midlands Minerals Corporation
("Midlands"). The most encouraging intercepts include 177.8 grams per
tonne (g/t) silver and 1.0% lead over 2.30 metres from 171.20 to 173.50
metres, and 210.0 g/t silver and 0.9% lead over 1.40 metres from 187.0
to 188.40 metres in drill hole 14-PA-005 at the Plandiste prospect.
Midlands have now completed the expenditure and drilling requirements
stipulated in the Option Agreement.

Simon Ingram, President and CEO commented: "We are pleased that
Midlands have completed their initial drilling and expenditure
commitment within the agreed time, and that the results continue to
confirm the presence of high-grade silver mineralisation in two
prospect areas. The Company now looks forward to Midlands continuing
exploration of these and other prospects in the Parlozi permit."

The Parlozi Project

The 91 square kilometre Parlozi exploration permit covers multiple
occurrences of historic silver-lead-zinc mining in the Kosmaj-Babe area
of the Sumadija mining district in central Serbia. Midlands has entered
into an option agreement ("Parlozi Option Agreement" with Reservoir to
earn up to a 75% interest in the Parlozi project (Company News Release
April 7th, 2014). The Parlozi Option Agreement provides that Midlands
can earn an initial 51% interest in the Project by spending C$4.5
million on exploration over four years. Midlands has completed the
initial minimum expenditure of C$500,000 and 1,500 meters of drilling
before September 30, 2014, Midlands remaining expenditure commitment is
C$1,500,000 by January 15, 2016 and C$2,500,000 by January 15, 2018.
Thereafter, Midlands can earn an additional 14% interest over two years
by obtaining a mining exploitation permit from the Serbian Government
and a further 10% (for a total of 75%) by completing a bankable
feasibility study within two years of obtaining a mining exploitation
permit.

The Company's exploration has been focused on the Parlozi
(Kosmaj-Babe) and Plandiste prospects. Maps and further information on
the Project are provided on the Company website
(www.reservoirminerals.com).

Table 1: Drill holes reported from Parlozi Exploration Permit.
Maps showing the location of all drill holes are provided on the
Company website (www.reservoirminerals.com).

//st
-----------------------------------------------------------------------
-----
Azimuth   Declination
Drill Hole ID  (degrees) (degrees)    Depth (m)  Prospect
---------------------------------------------------------------------------
-
Reported in News
14-PA-001       95         -62        645.0     Parlozi  Release September
3, 2014
------------------------------------------------
14-PA-001A      97         -66        124.8
----------------------------------------------------------
14-PA-002      203         -64        233.0    Plandiste
------------------------------------------------
14-PA-003      201         -65        259.9
---------------------------------------------------------------------------
-
Reported in this
14-PA-004      090         -65        240.0     Parlozi    News Release
----------------------------------------------------------
14-PA-005      155         -50        211.7    Plandiste
---------------------------------------------------------------------------
-
TOTAL                  1,714.4
---------------------------------------------------------------------------
-
//et

Parlozi Prospect

Drill hole 14-PA-004 was designed to intersect the up-dip
extensions towards the surface from the intercepts reported previously
and the historic resource. The hole intersected weakly mineralized
hydrothermal breccias at a down-hole depth of 67.9 metres. These
breccias may be distal to the known mineralisation at depth.

The Parlozi (also known as Kosmaj-Babe) deposit is described in the
Mining Districts of Serbia, District Database (Ministry of Mining and
Energy, 2002) with a historical resource of 6.5 Mt @ 4.1% Pb, 2.1% Zn,
0.3% Cu and 130 g/t Ag. The historical resources were calculated
according to the Yugoslav resource criteria (similar to the Soviet
classification) from 11 drill holes along a 700 metre strike length.
These historical resources are not compliant with National Instrument
43-101 guidelines and should not be relied on, but the Company
considers that they are relevant to the assessment of the Parlozi
Project.

Plandiste Prospect

The Plandiste prospect is located in the south of the Parlozi
permit perimeter, and approximately 1.4 kilometres west of the Parlozi
prospect. Earlier underground sampling by the Company identified
high-grade silver-lead-zinc mineralization (see Company News Release,
May 13, 2014). Drill hole 14-PA-005 was designed to test the down-dip
extension of the high-grade mineralization that was sampled in an adit
(671 g/t silver and 20.8% lead over 6.0 metres). Drill hole 14-PA-005
successfully intersected ten discrete mineralized structures and
collapsed underground workings, including three newly defined
mineralized structures that yielded the results in Table 2.

Table 2: Significant drill intercepts drill hole 14-PA-005,
Plandiste prospect.

//st

-----------------------------------------------------------------------
-----
From     To    Interval    Pb      Zn      Cu      Ag      Au
Hole ID     m       m        m        %       %       %      g/t     g/t
---------------------------------------------------------------------------
-
14-PA-005 136.60  137.70    1.10     3.51    0.02    0.02    64.8    0.07
171.20  173.50    2.30     1.03    0.12    0.02    177.8   0.12
187.00  188.40    1.40     0.91    0.10    0.00    210.0   0.09
---------------------------------------------------------------------------
-

Note: Drill intervals are apparent thicknesses. Additional drilling is
required to establish the orientation & true thicknesses of the
mineralization, but they will generally be less.

//et

Sample Analysis and Quality Control:

Drill hole orientations were surveyed at approximately 50 metre
intervals. The samples were collected in accordance with the Company
protocols that are compatible with accepted industry procedures and
best practice. Samples through the reported intervals were up to 2
metres in length.

The samples were submitted to SGS laboratory located in Bor,
Serbia, for preparation. Sample pulps with 85% of content lower than 75
microns were analyzed at SGS laboratory in Bor for 49 elements
including silver, lead, zinc and copper by ICP-MS after a 4-acid
digestion. Samples with ICP-MS results greater than 100 g/t silver or
greater than 1% lead, zinc or copper, were re-analyzed using 4-acid
digestion and atomic absorption finish. All samples were assayed for
gold using a standard 30 gram fire assay method with atomic absorption
finish.

The Company follows industry standard quality assurance and
quality control procedures for sampling. The QA/QC programme includes
the insertion of blanks, duplicates and certified standards into the
sample stream.

Qualified Person:

Dr. Duncan Large, Chartered Engineer (UK) and Eur. Geol., a
Qualified Person under National Instrument 43-101 Standards of
Disclosure for Mineral Projects of the Canadian Securities
Administrators and a consultant to the Company, has approved the
technical disclosure in this release and verified the data disclosed.

About the Company:

Reservoir Minerals Inc. is an international mineral exploration
and development company run by an experienced technical and management
team, with a portfolio of precious and base metal exploration
properties in Europe and Africa. The Company operates an exploration
partnership business model to leverage its expertise through to
discovery.

This news release includes certain "forward-looking statements"
under applicable Canadian securities legislation. Such forward-looking
statements or information, including but not limited to those with
respect to exploration results, involve known and unknown risks,
uncertainties, and other factors which may cause the actual results,
performance or achievements of Reservoir Minerals Inc. to be materially
different from any future results, performance or achievements
expressed or implied by such forward-looking statements or information.
Such factors include, among others, the actual prices of commodities,
the factual results of current exploration, development and mining
activities, changes in project parameters as plans continue to be
evaluated, as well as those factors disclosed in documents filed from
time to time with the securities regulators in the applicable Provinces
of British Columbia and Alberta.

Neither the TSX Venture Exchange nor the Investment Industry
Regulatory Organization of Canada accepts responsibility for the
adequacy or accuracy of this release.

TSX Venture closing price for MEX-V
Date: 2014/10/28
Closing Price: 0.01

TEL:  +1.416.703.0010  Reservoir Minerals Inc.
Chris MacIntyre, VP Corporate Development
E-mail: chris@reservoirminerals.com
Internet: www.reservoirminerals.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1430200020TS11430201493-07584120141030