Source	MARKET NEWS
Date	10/30/2014
Time	09:57:47 AM

Company	 Northern Abitibi Mining Corp.
Title	The 2014 Exploration Program Has Been Completed





    CDNX Symbol: NAI











Press Release	





The 2014 Exploration Program Has Been Completed At NorthernAbitibi's Ches 
Property, British Columbia --->@NEWS RELEASE
NORTHERN ABITIBI MINING CORP ("NAI-V;NOMNF-0")
- The 2014 Exploration Program Has Been Completed At Northern
- Abitibi's Ches Property, British Columbia

Northern Abitibi Mining Corp. ("Northern Abitibi or the Company")
is pleased to announce that the planned 2014 exploration program has
been completed at the Company's Ches property in Central British
Columbia.

The 9 day exploration program included the mechanical excavation
of 7 trenches which were subsequently washed, mapped, and chip sampled.
During the program a total of 274 surface rock samples were collected
and sent to Activation Laboratories in Kamloops for assay, with results
expected in 4 to 6 weeks.

Trenching and surface mapping have successfully traced alteration
and variable sulfide mineralization over an area at least 1.5
kilometres long by 0.5 kilometres wide. Several new exposures
containing variable amounts of
chalcopyrite-molybdenite-sphalerite-scheelite have been uncovered and
then sampled to determine if they have potential for economic grades.

Geologic mapping and field data is presently being compiled and
interpreted and will be presented along with assay results as they
become available.

The Ches Property

The road accessible Ches Property is located 80 kilometres south
of Burns Lake on the south side of Ootsa Lake. Mineralization consists
of pyrrhotite-chalcopyrite-scheelite replacement (skarn) style
mineralization in calcareous sedimentary rocks and quartz
chalcopyrite-molybdenite-scheelite stockwork veining in fine grained
siltstones. Historic Assessment Reports state average grades from
surface sampling of 0.52% copper and 4.7 g/t silver over a zone 350
metres wide, and copper in soil geochemical anomalies up to 350 metres
wide and 800 to 1500 metres long, and open along strike. Subsequent
surface grab sampling reported in a 2009 Technical Report by Scarlet
Resources Ltd. returned values up to 1% copper, 16 g/t silver, and 0.3%
tungsten from the replacement-skarn style mineralization, and values up
to 0.45% copper, 0.02% molybdenum, 7 g/t silver, and 0.1% tungsten from
the stockwork zone. These mineralized zones have never been trenched or
drill tested. The sampling results above are considered historic in
nature, they have not been confirmed by Northern Abitibi, and should
not be relied upon.

Dr. Shane Ebert, P. Geo. is the Qualified Person responsible for
the preparation of this news release.

Shane Ebert, President/Director

The TSX Venture Exchange has neither approved nor disapproved of
the contents of this press release.

Except for the historical and present factual information
contained herein, the matters set forth in this news release, including
words such as "expects", "projects", "plans", "anticipates" and similar
expressions, are forward-looking information that represents management
of Northern Abitibi's internal projections, expectations or beliefs
concerning, among other things, future operating results and various
components thereof or the economic performance of Northern Abitibi. The
projections, estimates and beliefs contained in such forward-looking
statements necessarily involve known and unknown risks and
uncertainties, which may cause Northern Abitibi's actual performance
and financial results in future periods to differ materially from any
projections of future performance or results expressed or implied by
such forward-looking statements. These risks and uncertainties include,
among other things, those described in Northern Abitibi's filings with
the Canadian securities authorities. Accordingly, holders of Northern
Abitibi shares and potential investors are cautioned that events or
circumstances could cause results to differ materially from those
predicted. Northern Abitibi disclaims any responsibility to update
these forward-looking statements.
































TEL:  1.250.964.2699  Shane Ebert

Northern Abitibi Mining Corp.
TSX Venture closing price for NAI-V
Date: 2014/10/16
Closing Price: 0.01

TEL:  1.403.233.2636  Jean Pierre Jutras
Internet: www.naminco.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1430200029TS11430201906-09554720141030