Source	MARKET NEWS
Date	10/01/2015
Time	11:03:56 AM

Company	 Lomiko Metals Inc.
Title	Drill 15.30 M 
Of 10.54% And 117.75 M Of 4.05% Fl





    CDNX Symbol: LMR











Press Release	





CANADA STRATEGIC METALS INC ("CJC-V")
LOMIKO METALS INC ("LMR-V")
- Drill 15.30 M Of 10.54% And 117.75 M Of 4.05% Flake Graphite
- In The Graphene-battery Zones At La Loutre

Canada Strategic Metals Inc. ("Canada Strategic Metals" or "the
Company") and Lomiko Metals Inc. are very pleased to announce the
results for seven (7) in-fill holes in the newly-named Graphene-Battery
zones where high grade samples were discovered and reported July 29,
2015. Three zones known as Graphene, Battery and Refractory have been
identified to date. So far, a total of 19 holes have been reported for
the drilling campaign, holes 1-11 in the Refractory zone were reported
September 24, 2015.

The La Loutre property consists of contiguous claim blocks
totalling approximately 2 867.29 hectares (28,67 km2) situated
approximately 53 km east of Imerys Carbon and Graphite, formerly known
as the Timcal Graphite Mine, North America's only operating graphite
mine, and 117 km northwest of Montreal.

A map of hole localisation and results is available on the web
site of the Company at: www.csmetals.ca.
Highlighted Refractory Zone Results Reported September 24, 2015
(Holes 1-11)*

//st
Drill                                 Mineralization
Hole #  Easting Northing  Azimuth     Dip From To  Length    Gp
(UTM)    (UTM)(degrees)(degrees) (m)(m)   along     %
the core
LL-15-01 499261  5097902      60  -50   5.90  11.35  5.45 11.65
LL-15-02 499207  5097991                4.35   9.60  5.25 14.76
Including:               4.35   8.60  4.25 17.69
LL-15-04 499177  5098217      60  -50   4.75  12.50  7.75  7.25
LL-15-09 499388  5098121      67  -50 116.25 207.00 90.75  9.00
Including:             136.50 199.30 62.80 11.88
//et

* Length along the core. The Company doesn't have enough
information to estimates the true width of the mineralized zone
intersected in the drill holes.

Table of mineralized graphene-battery zone intersections (holes
12-19)*

//st
Drill                                 Mineralization
Hole #  Easting Northing  Azimuth     Dip From To  Length    Gp
(UTM)    (UTM)(degrees)(degrees) (m)(m)   along     %
the core
LL-15-12 499186  5097387     64  -50   3.00  51.00  48.00  2.49 (1)
LL-15-13 499086  5097346     62  -50  57.70 145.65  87.95  2.50 (2)
160.00 165.60   5.60  1.52
LL-15-14 499049  5097304     60  -50  75.40 193.15 117.75  4.05 (3)
195.15 196.30   1.15  5.83
201.15 207.15   6.00  1.46
243.40 247.90   4.50  2.55
LL-15-15 499154  5097301     60  -50   2.20 130.25 128.05  3.47 (4)
Including:                             2.20  19.80  17.60  4.87
Including:                            28.70  38.75  10.05  9.97
LL-15-16 499194  5097337     64  -50   3.70 100.30  96.60  3.74 (5)
Including:                             3.70  19.00  15.30 10.54 (6)
LL-15-17 499178  5097212     55  -50   2.80 110.50 107.70  2.87 (7)
Including:                             2.80  17.00  14.20  4.62 (8)
Including:                           105.15 110.50   5.35 11.36
LL-15-18 499222  5097237     63  -50   1.80  15.00  13.20  2.07
15.00  18.00   3.00 Lost core
18.00  75.00  57.00  2.08
LL-15-19 499092  5097162     62  -50  84.00 179.00  95.00  3.70 (9)
Including:                            85.25  95.00   9.75  9.42
Including:                           175.00 179.00   4.00 16.86
//et

* Core length; the Company estimates the true width of the
mineralized zone at 70 to 95% of the core length.

//st
(1)                                        no sample 48.35-48.70
(2)                         no sample 62.75-63.05, 140.90-141.60
(3)                                        no sample 76.90-77.10
(4)                                        no sample 40.80-41.15;
(5)                             no sample 8.40-8.75; 99.10-99.65
(6)                                          no sample 8.40-8.75
(7)                   no sample 6.35-7.20; 10.45-10.95; 13-14.20
(8)                   no sample 6.35-7.20; 10.45-10.95; 13-14.20
(9)                                      no sample 172.40-172.65
//et

The 2015 drilling program is managed by Consul-Teck Exploration of
Val-d'Or, Quebec, who designed the drilling campaign, supervised the
program and logged and sampled the core.

Consul-Teck Exploration implemented QA/QC procedures to ensure
best practices in sampling and analysis of the core samples. The drill
core was logged and then split, with one half sent for assay and the
other retained in the core box as a witness sample. Duplicates and
blanks were inserted regularly into the sample stream.

The samples in secure tagged bags were delivered directly to the
analytical facility for analysis. In this case, the analytical facility
was the ALS minerals in Val-d'Or, Quebec. The samples are weighed and
identified prior to sample preparation. The samples are crushed to 70%
minus 2 mm, then separated and pulverized to 85% passing 75um. All
samples are analyzed for Carbon Graphite using C-IR18.

Jean-Sebastien Lavallee (OGQ #773), Geologist, is a shareholder of
both companies, President and Chief Executive Officer of the Canada
Strategic and a Qualified Person under NI 43-101, has reviewed and
approved the technical content of this release.

About Canada Strategic Metals

Canada Strategic Metals is an emerging company focused on the
exploration and development of a number of projects covering over
20,000 hectares in Quebec. With broad management experience in green
technology and junior resource exploration and development, Canada
Strategic Metals is well positioned to aggressively advance this
promising property portfolio for its shareholders.

For more information on the Company, please visit www.csmetals.ca.


Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for LMR-V
Date: 2015/09/30
Closing Price: 0.03

TEL: 819-354-5146  Jean-Sebastien Lavallee, P. Geo
President and Chief Executive Officer
Canada Strategic Metals Inc.
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1527300047TS11527302068-11015220151001