Source	MARKET NEWS
Date	10/15/2015
Time	12:13:19 PM

Company	 Kivalliq Energy Corporation
Title	Generates 
High Priority Basement Targets At Hatc





    CDNX Symbol: KIV











Press Release	





KIVALLIQ ENERGY CORP ("KIV-V")
- Generates High Priority Basement Targets At Hatchet Lake

Kivalliq Energy Corporation ("Kivalliq") announced the results from
the summer exploration program at Kivalliq's 100% owned Hatchet Lake
Property in the Athabasca Region of Saskatchewan.

"Results from Kivalliq's first exploration program at the Hatchet
Lake property have confirmed and enhanced basement hosted uranium
targets identified by previous operators Hathor and Rio Tinto. Further
work to advance the project in 2016 is warranted." stated Jeff Ward,
Kivalliq's President. "Based on Hatchet Lake's strategic location near
all of Canada's uranium mining and milling infrastructure, a discovery
here would have significant development advantages."

The 13,711 hectare (33,881 acre) Hatchet Lake Property is situated
on the Mudjatik-Wollaston Transition Zone, 39 kilometres along trend
from Rio Tinto's Roughrider deposit and within 29 kilometres of Cameco
Corporation's Eagle Point uranium mine. The 2015 program budgeted at
$500,000 was designed to verify airborne geophysical signatures and
confirm uranium anomalism in priority target areas.

Highlights of the 2015 program include:

//st
908 soil and 1322 vegetation (biogeochemical) samples verified historic
results and identified priority target areas at Upper Manson and SW
Scrimes, both having soil and vegetation geochemical uranium anomalies;
140 line kilometres of ground magnetic and VLF EM geophysical surveying
resolved multiple conductive trends and geology at Upper Manson and on the
Scrimes Peninsula;
Grab samples at SW Scrimes returned values up to 2.43%
U(sub)3(/sub)O(sub)8(/sub) from pegmatite boulders and 0.68%
U(sub)3(/sub)O(sub)8(/sub) from a new pegmatitic occurrence in outcrop;
Comprehensive processing and analysis of all available datasets by Condor
Consulting Inc. (Condor) generated a new "Geointerp" for the Property with
17 prioritized target zones, four of which are considered high-priority and
correspond to Kivalliq's key target areas.

//et

Two high-priority zones, Upper Manson and SW Scrimes, have emerged
based on work to date. The Upper Manson and SW Scrimes targets occur
within northeast trending pelitic and psammopelitic gneiss host rocks
and are highlighted by uranium anomalism noted in historic samples from
boulders, lake sediments, soils and vegetation. Work by Kivalliq in
2015 was able to confirm anomalous uranium geochemistry in all six
areas sampled (soil and vegetation), as well as upgrade the geological
and structural model for Hatchet mineralization through Condor's
independent analysis. For maps showing results from the 2015 Hatchet
Lake Exploration Program that includes relevant historic data, please
visit: http://kivalliqenergy.com/uranium/hatchet_lake/maps

Soil Geochemical Sampling

A total of 826 Enzyme Leach (EL) soil samples were collected and
sent for ICP-MS geochemical analysis. Background was the 96th
percentile at 2.70 parts per billion (ppb) U and was determined by the
mean plus one standard deviation (Table 1). Anomalous values were
identified in all six grids sampled in 2015. In addition, 82
conventional soil samples were collected at Upper Manson to calibrate
the 2015 EL soil results to earlier soil values reported by Hathor
Exploration Ltd (Hathor).

Vegetation (Biogeochemical) Sampling

A total of 1322 black spruce twig vegetation (biogeochemical)
samples were collected and sent for Ashed Vegetation 59 element ICP-MS
bio-geochemical analysis. Background was calculated at 1.36 parts per
million (ppm U), the 87thA percentile using the mean plus one standard
deviation (Table 1). Anomalous values were identified in all six grids
sampled in 2015.

Results from the 2015 program confirmed the efficacy of black
spruce sampling as a reliable geochemical method. When used in
conjunction with geophysical surveys and soil geochemistry, vegetation
sampling is proving to be an effective tool to advance targets.

Table 1: Hatchet 2015 Geochemical Sampling Program - Comparative
Percentile Values for Uranium

//st
2015A Enzyme Leach Soil
Geochemical ResultsA
Comparative Percentile
Values forA Uranium            A                 2015A Vegetation
(Biogeochemical) ResultsA
Comparative Percentile
Values for Uranium
Percentile               A U (ppb)A              PercentileA U (ppm)
99%                      A     8.2A                     99%A    2.32
98%                      A     5.7A                     95%A    1.77
96%                      A     2.7A                     87%A    1.36
Min                      A     0.1A                     MinA    0.17
Max                      A     337A                     MaxA    4.39
Mean                     A       1A                    MeanA    0.86

//et

Prospecting

The 2015 prospecting program included the collection of 24 grab
samples from outcrop and boulders primarily in the Upper Manson and SW
Scrimes areas. Samples were mainly collected from pegmatites and
leucogranites which represent the majority of exposed radioactive rocks
in the Property area. Of significance, the SW Scrimes area returned
values of 2.43% U(sub)3(/sub)O(sub)8 (/sub)and 1.39%
U(sub)3(/sub)O(sub)8 (/sub)respectively from boulder float at a known
occurrence on the north side of Scrimes Lake. A sample from a new
radioactive pegmatite outcrop discovered on the south side of Scrimes
Lake assayed 0.68% U(sub)3(/sub)O(sub)8(/sub). Anomalous grab samples
at Upper Manson confirmed the extent, location and setting of historic
uranium occurrences.

Ground Geophysical Surveying

Ground magnetic and VLF-EM surveys were carried out on four grids
at Hatchet Lake. Approximately 140 line kilometres of ground geophysics
focussed on geochemically anomalous areas and priority airborne
versatile time domain EM (VTEM) conductors. Grid lines were spaced 50
and 100 metres apart, with readings taken at 12.5 metre intervals. The
survey grids are dominated by northeast trending magnetic features with
prominent north trending faulting. The VLF-EM surveys were able to
resolve tightly spaced, multiple, shallow conductive trends in both the
Upper Manson and Scrimes Peninsula grids, areas where the airborne VTEM
suggested broader, singular conductive responses.

Condor Consulting Inc. Geophysical Interpretation

As part of the 2015 program, Condor Consulting Inc. conducted
comprehensive processing and analysis of two airborne surveys flown
over the Property in 2007 (airborne VTEM by Geotech and high resolution
airborne magnetics by Goldak). Multiple other data sets compiled by
Kivalliq that include radiometric, soil, vegetation and boulder
sampling data (2006 and 2012) were incorporated in the interpretation.
Condor's work resulted in a detailed "GeoInterp" which will be used for
future geological and structural interpretation. In addition, Condor
independently identified 17 target zones, four of which are considered
high-priority and correspond to Kivalliq's key target areas.

QA/QC

Jeff Ward, P.Geo., President of Kivalliq and a Qualified Person for
Kivalliq, has reviewed and approved the publicly available scientific
and technical information by previous exploration groups contained in
this release. Previous exploration results by Hathor and Rio Tinto
referred to herein are historical in nature and have not been verified
by Kivalliq. However, Kivalliq believes these results are relevant
since programs were carried out by knowledgeable explorers in
accordance with acceptable industry practices at the time.

Rock and conventional soil samples from the Hatchet Lake Property
were sent to the Saskatchewan Research Council ("SRC") for analysis.
The SRC facility operates in accordance with ISO/IEC 17025:2005
(CAN-P-4E), General Requirements for the Competence of Mineral Testing
and Calibration laboratories and is accredited by the Standards Council
of Canada. Rock samples are first analyzed by SRC's ICP-OES
multi-element Uranium exploration ICP1 method. ICP results U ) 1,000
ppm are analyzed using SRC's ISO/IEC 17025:2005-accredited
U(sub)3(/sub)O(sub)8(/sub) Assay method. Conventional soil samples
undergo standard geochemical analysis using ICP-MS. Laboratory quality
control (QC) includes a repeat analysis on every 20th sample. All QA/QC
results for both rocks and conventional soil samples were within
expectations.

Enzyme leach (EL) soil samples and vegetation (biogeochemical)
samples were sent to Activation Laboratories Ltd. (Actlabs). The
Actlabs facility is accredited to international quality standards
through the International Organization for
Standardization/International Electrotechnical Commission (ISO/IEC)
17025 (ISO/IEC 17025 includes ISO 9001 and ISO 9002 specifications)
with CAN-P-1578 (Forensics), CAN-P-1579 (Mineral Analysis) and
CAN-P-1585 (Environmental) for specific registered tests by the SCC.
For EL soil sample analysis, a 0.75 gram sample of B soil horizon is
leached in an enzyme matrix for one hour, where it reacts with
amorphous MnO2 dissolving it. Metals complex with the acid present and
solutions are analyzed and reported in ppb with a detection limit of )
0.1 ppb U. Vegetation samples were processed using the "ashed
vegetation" 59 element ICP/MS biogeochemical analysis method, reported
in ppm, with a detection limit of 0.001 ppm U. QA/QC includes field
standards, blanks and duplicates, and those inserted by the Actlabs.
All QA/QC results were within expectations.

Ground magnetic and VLF-EM surveying was conducted by SJ Geophysics
Ltd using GEM GSM-19 magnetometer units. The VLF-EM survey
instrumentation was on board the GEM magnetometers and collected data
from transmission stations at Jim Creek (Seattle), Washington
transmitting at 24.8 kHz and Cutler, Maine transmitting at 24.0 kHz.
QA/QC was provided SJ Geophysics Ltd and by in3D Geophysics Ltd.

Condor Consulting Inc. are recognized experts in the field of
airborne electromagnetics and were retained to perform a detailed
interpretation on aeromagnetic surveys flown in 2007 over the Hatchet
Lake Property by Hathor Exploration Ltd.

About Kivalliq Energy Corporation

Kivalliq Energy Corporation (TSX VENTURE: KIV) is a Vancouver-based
company with a portfolio of high-quality uranium exploration projects
in Canada. Kivalliq holds Canada's highest-grade uranium resource
outside of Saskatchewan. The Company's flagship project, the 105,280
hectare Angilak Property in Nunavut Territory, hosts the Lac 50 Trend
with a NI 43-101 Inferred Resource of 2,831,000 tonnes grading 0.69%
U3O8, totaling 43.3 million pounds U3O8. Kivalliq's comprehensive
exploration programs continue to advance the Lac 50 Trend and
demonstrate the "District Scale" potential of the Angilak Property. For
disclosure related to the inferred resource for the Lac 50 Trend
uranium deposits, please refer to Kivalliq's news release of March 1,
2013.

In Saskatchewan, Kivalliq holds a 100% interest in the 13,711
hectare Hatchet Lake Property adjacent to the north-eastern margin of
the highly prolific uranium-producing Athabasca Basin. Compilation of
results from previous exploration by Hathor Exploration Limited and Rio
Tinto have identified multiple, priority unconformity-related basement
targets at Hatchet Lake and guided the exploration reported herein.

Kivalliq also holds a 100% interest in the 200,677 hectare Genesis
Property located northeast of Saskatchewan's Athabasca Basin, with
Roughrider Exploration Limited funding the current exploration program
pursuant to an option to acquire up to an 85% interest in the property.
This highly prospective project is located along the Wollaston-Mudjatik
trend and extends 90 kilometres northeast from Wollaston Lake to the
Manitoba border.

Kivalliq's team of northern exploration specialists has forged
strong relationships with sophisticated resource sector investors and
Angilak Property partner Nunavut Tunngavik Inc. (NTI). Kivalliq was the
first company to sign a comprehensive agreement to explore for uranium
on Inuit Owned Lands in Nunavut Territory, Canada and is committed to
building shareholder value while adhering to high levels of
environmental and safety standards and proactive local community
engagement.

On behalf of the Board of Directors

"Jim Paterson"

James R. Paterson, CEO

Kivalliq Energy Corporation

Kivalliq Energy Corporation is a member of the Aurora Mineral
Resource Group of companies. For more information please visit
www.auroraresource.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Certain disclosures in this release constitute forward-looking
statements that are subject to numerous risks, uncertainties and other
factors relating to Kivalliq's operations as a mineral exploration
company that may cause future results to differ materially from those
expressed or implied in such forward-looking statements, including
risks as to the completion of the plans and projects. Readers are
cautioned not to place undue reliance on forward-looking statements.
Other than as required by applicable securities legislation, Kivalliq
expressly disclaims any intention or obligation to update or revise any
forward-looking statements whether as a result of new information,
future events, or otherwise.

Kivalliq Energy Corporation
www.kivalliqenergy.com
Investor Relations
1.888.331.2269
604.646.4527
info@kivalliqenergy.com
______________________________________
_______________________________________________
TSX Venture closing price for KIV-V
Date: 2015/10/14
Closing Price: 0.08
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1528700024TS11528701955-12115320151015