Source	MARKET NEWS
Date	10/20/2015
Time	07:33:04 AM

Company	 Westhaven Ventures Inc.
Title	Commences Drilling on its Shovelnose Gold Proper





    CDNX Symbol: WHN











Press Release	





Commences Drilling on its Shovelnose Gold Property --->@NEWS RELEASE
WESTHAVEN VENTURES INC ("WHN-V")
- Commences Drilling on its Shovelnose Gold Property

Westhaven Ventures Inc. is pleased to announce drilling has begun
on its 18,412 hectare Shovelnose gold property, located within the
prospective Spences Bridge Gold Belt (SBGB), approximately 30 km south
of Merritt, British Columbia.

The drill program will consist of approximately 1,500 metres of
diamond drilling with the goal to further expand and outline the extent
of the newly recognized epithermal gold system present on the property.
Drilling to date has expanded a highly anomalous silicified zone or cap
where a sub horizontal near surface zone grading 0.54 g/t Au and 4.77
g/t Ag over 50.4 metres, which includes 13.7 metres grading 0.91 g/t Au
and 6.65 g/t Ag, was intersected.

Drill hole SN15-01, which is currently in progress, has
intersected approximately 42.5 metres (25.6- 68.1m) of highly
silicified tuff with vuggy, locally variably pyritic, quartz veining.
From 68.1 metres to 148 metres, there has been a succession of
heterolithic tuffs and rhyolite flows and no silicification has been
observed.

Ground Geophysics

Approximately 14 line kilometres of combined geophysical surveys
including Induced Polarization (IP), ground magnetics, and VLF-EM were
recently completed on the Line 6, MIK and Tower zones along with the
intervening ground where drilling has traced a broad zone of near
surface, lower grade gold-silver mineralization. The survey outlined
several targets which will be drill tested, including high
chargeability anomalies which can be indicative of sulphides associated
with auriferous quartz veins and high resistivity anomalies which may
be due to quartz veining and associated gold-bearing silicification.

Shovelnose Gold Property Overview

To date, 24 drill holes (2 were abandoned in overburden) have been
diamond drilled for a cumulative total of 3,089 metres, in three
separate target areas. Gold and silver mineralization, associated with
quartz veining and silicification, has been encountered in all 24
holes. In addition, there is evidence of a significant mineralized
alteration system within the property where float samples grading 119
g/t Au (Gold) and 273 g/t Ag (Silver), veins in trenching grading 66
g/t Au and wide low grade alteration zones typical of epithermal gold
deposits have been discovered.

Please refer to the Shovelnose Project page on our website for
further information and drill hole locations.
www.westhavenventures.com/projects/shovelnose_gold_property/

On behalf of the Board of Directors
WESTHAVEN VENTURES INC.
"Gareth Thomas"
Gareth Thomas, Director

About Westhaven Ventures Inc.

Westhaven Ventures Inc. is a Canadian based exploration company
focused on the acquisition and exploration of prospective resource
properties. Westhaven is focused on advancing its Shovelnose gold,
Prospect Valley gold, Ben and Ben South nickel projects in British
Columbia. Westhaven trades on the TSX Venture Exchange under the ticker
symbol WHN. For further information, please call 604- 681-5558 or visit
Westhaven's website at www.westhavenventures.com

Qualified Person Statement

L. John Peters, P.Geo., who is a Qualified Person within the
context of National Instrument 43-101 has read and takes responsibility
for this release.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.
______________________________________
_______________________________________________
TSX Venture closing price for WHN-V
Date: 2015/10/09
Closing Price: 0.07
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1529200024TS11529201396-07304920151020