Source	Marketwire
Date	10/26/2015
Time	05:03:08 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Additional Results from 2015 Expansion Drilling on 
the NW Brodie Trend, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

October 26, 2015

Scorpio Gold Reports Additional Results from 2015 Expansion Drilling on the NW 
Brodie Trend, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 26, 2015) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports 
additional results from the 2015 expansion drilling program on the NW Brodie 
trend at its70% owned Mineral Ridge project, located in Nevada.

Exploration drilling along the NW Brodie trend in 2015 continues to outline a 
semi-continuous mineralized corridor up to 300 meters wide that extends over a 
500 meter strike length between the Brodie and Bluelite deposits. This area 
lies well outside of currently defined resources and modelled pit outlines. The 
Company's management believes that results to date are promising and may 
potentially allow for building a new resource in this area.

Highlights from this latest phase of the 2015 drilling program on the NW Brodie 
trend include:

/T/

--  MR151623: 3.81 grams per tonne ("g/t") gold over 3.05 meters
--  MR151634: 1.11 g/t gold over 4.57 meters
--  MR151635: 1.04 g/t gold over 7.62 meters
--  MR151636: 1.23 g/t gold over 9.14 meters
--  MR151637: 1.16 g/t gold over 3.05 meters
--  MR151661: 4.07 g/t gold over 18.29 meters
--  MR151752: 4.87 g/t gold over 4.57 meters
--  MR151754: 2.54 g/t gold over 6.10 meters
--  MR151756: 3.98 g/t gold over 6.10 meters

/T/

A drill hole location map is available at: DH Plan

Table 1. NW Brodie Trend - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole            Azm   Dip  From   To Width   From     To  Width   Gold  Gold
No.           (deg) (deg)  (ft) (ft)  (ft)    (m)    (m)    (m)  (OPT) (g/t)
----------------------------------------------------------------------------
MR151623          0   -90   150  155     5  45.72  47.24   1.52  0.177  6.07
----------------------------------------------------------------------------
170  180    10  51.82  54.86   3.05  0.111  3.81
----------------------------------------------------------------------------
195  200     5  59.44  60.96   1.52  0.016  0.55
----------------------------------------------------------------------------
MR151624          0   -90    40   45     5  12.19  13.72   1.52  0.051  1.75
----------------------------------------------------------------------------
MR151625          0   -90               No Significant Results
----------------------------------------------------------------------------
MR151631          0   -90   120  125     5  36.58  38.10   1.52  0.117  4.01
----------------------------------------------------------------------------
175  185    10  53.34  56.39   3.05  0.015  0.50
----------------------------------------------------------------------------
245  250     5  74.68  76.20   1.52  0.016  0.55
----------------------------------------------------------------------------
280  290    10  85.34  88.39   3.05  0.023  0.77
----------------------------------------------------------------------------
315  325    10  96.01  99.06   3.05  0.015  0.51
----------------------------------------------------------------------------
MR151632          0   -90    75   80     5  22.86  24.38   1.52  0.023  0.79
----------------------------------------------------------------------------
185  200    15  56.39  60.96   4.57  0.017  0.58
----------------------------------------------------------------------------
MR151633          0   -90     0    5     5   0.00   1.52   1.52  0.030  1.03
----------------------------------------------------------------------------
110  120    10  33.53  36.58   3.05  0.023  0.79
----------------------------------------------------------------------------
135  140     5  41.15  42.67   1.52  0.019  0.65
----------------------------------------------------------------------------
MR151634          0   -90   210  225    15  64.01  68.58   4.57  0.032  1.11
----------------------------------------------------------------------------
245  255    10  74.68  77.72   3.05  0.040  1.35
----------------------------------------------------------------------------
330  350    20 100.58 106.68   6.10  0.024  0.83
----------------------------------------------------------------------------
360  370    10 109.73 112.78   3.05  0.020  0.69
----------------------------------------------------------------------------
MR151635          0   -90   210  230    20  64.01  70.10   6.10  0.014  0.46
----------------------------------------------------------------------------
285  310    25  86.87  94.49   7.62  0.030  1.04
----------------------------------------------------------------------------
330  360    30 100.58 109.73   9.14  0.022  0.75
----------------------------------------------------------------------------
380  385     5 115.82 117.35   1.52  0.021  0.72
----------------------------------------------------------------------------
400  405     5 121.92 123.44   1.52  0.038  1.30
----------------------------------------------------------------------------
430  435     5 131.06 132.59   1.52  0.023  0.79
----------------------------------------------------------------------------
MR151636          0   -90   200  205     5  60.96  62.48   1.52  0.048  1.65
----------------------------------------------------------------------------
245  250     5  74.68  76.20   1.52  0.178  6.10
----------------------------------------------------------------------------
285  320    35  86.87  97.54  10.67  0.017  0.59
----------------------------------------------------------------------------
345  375    30 105.16 114.30   9.14  0.036  1.23
----------------------------------------------------------------------------
440  445     5 134.11 135.64   1.52  0.098  3.36
----------------------------------------------------------------------------
MR151637          0   -90   155  180    25  47.24  54.86   7.62  0.018  0.63
----------------------------------------------------------------------------
265  275    10  80.77  83.82   3.05  0.034  1.16
----------------------------------------------------------------------------
310  315     5  94.49  96.01   1.52  0.025  0.87
----------------------------------------------------------------------------
355  360     5 108.20 109.73   1.52  0.026  0.89
----------------------------------------------------------------------------
370  375     5 112.78 114.30   1.52  0.035  1.19
----------------------------------------------------------------------------
MR151639          0   -90   225  230     5  68.58  70.10   1.52  0.059  2.02
----------------------------------------------------------------------------
365  370     5 111.25 112.78   1.52  0.016  0.55
----------------------------------------------------------------------------
MR151640          0   -90   140  145     5  42.67  44.20   1.52  0.019  0.65
----------------------------------------------------------------------------
230  250    20  70.10  76.20   6.10  0.023  0.77
----------------------------------------------------------------------------
MR151661          0   -90    85   90     5  25.91  27.43   1.52  0.059  2.02
----------------------------------------------------------------------------
155  160     5  47.24  48.77   1.52  0.051  1.75
----------------------------------------------------------------------------
170  175     5  51.82  53.34   1.52  0.015  0.51
----------------------------------------------------------------------------
215  220     5  65.53  67.06   1.52  0.169  5.79
----------------------------------------------------------------------------
230  245    15  70.10  74.68   4.57  0.040  1.38
----------------------------------------------------------------------------
270  275     5  82.30  83.82   1.52  0.027  0.93
----------------------------------------------------------------------------
305  365    60  92.96 111.25  18.29  0.119  4.07
----------------------------------------------------------------------------
460  465     5 140.21 141.73   1.52  0.016  0.55
----------------------------------------------------------------------------
550  555     5 167.64 169.16   1.52  0.017  0.58
----------------------------------------------------------------------------
590  600    10 179.83 182.88   3.05  0.034  1.15
----------------------------------------------------------------------------
780  790    10 237.74 240.79   3.05  0.016  0.55
----------------------------------------------------------------------------
MR151662          0   -90     0    5     5   0.00   1.52   1.52  0.121  4.15
----------------------------------------------------------------------------
MR151663          0   -90   175  180     5  53.34  54.86   1.52  0.045  1.54
----------------------------------------------------------------------------
MR151664          0   -90   225  230     5  68.58  70.10   1.52  0.067  2.30
----------------------------------------------------------------------------
245  250     5  74.68  76.20   1.52  0.108  3.70
----------------------------------------------------------------------------
MR151665          0   -90   230  235     5  70.10  71.63   1.52  0.020  0.69
----------------------------------------------------------------------------
MR151667          0   -90   170  175     5  51.82  53.34   1.52  0.018  0.62
----------------------------------------------------------------------------
MR151668          0   -90               No Significant Results
----------------------------------------------------------------------------
MR151669          0   -90   190  195     5  57.91  59.44   1.52  0.022  0.75
----------------------------------------------------------------------------
230  235     5  70.10  71.63   1.52  0.017  0.58
----------------------------------------------------------------------------
MR151748          0   -90   125  130     5  38.10  39.62   1.52  0.012  0.41
----------------------------------------------------------------------------
MR151749          0   -90   115  120     5  35.05  36.58   1.52  0.015  0.51
----------------------------------------------------------------------------
MR151750          0   -90   115  120     5  35.05  36.58   1.52  0.015  0.51
----------------------------------------------------------------------------
MR151751          0   -90     0   15    15   0.00   4.57   4.57  0.031  1.07
----------------------------------------------------------------------------
MR151752          0   -90    15   30    15   4.57   9.14   4.57  0.142  4.87
----------------------------------------------------------------------------
incl                         15   20     5   4.57   6.10   1.52  0.331 11.35
----------------------------------------------------------------------------
125  135    10  38.10  41.15   3.05  0.031  1.05
----------------------------------------------------------------------------
MR151753          0   -90     0   15    15   0.00   4.57   4.57  0.037  1.27
----------------------------------------------------------------------------
MR151754          0   -90     5   25    20   1.52   7.62   6.10  0.074  2.54
----------------------------------------------------------------------------
MR151755          0   -90     0    5     5   0.00   1.52   1.52  0.012  0.41
----------------------------------------------------------------------------
MR151756          0   -90    30   50    20   9.14  15.24   6.10  0.116  3.98
----------------------------------------------------------------------------
incl                         35   40     5  10.67  12.19   1.52  0.361 12.38
----------------------------------------------------------------------------
145  150     5  44.20  45.72   1.52  0.033  1.13
----------------------------------------------------------------------------
MR151757          0   -90    45   50     5  13.72  15.24   1.52  0.201  6.89
----------------------------------------------------------------------------
MR151758          0   -90               No Significant Results
----------------------------------------------------------------------------
MR151759          0   -90   145  150     5  44.20  45.72   1.52  0.011  0.38
----------------------------------------------------------------------------
MR151760          0   -90               No Significant Results
----------------------------------------------------------------------------
MR151761          0   -90   135  140     5  41.15  42.67   1.52  0.071  2.43
----------------------------------------------------------------------------
150  155     5  45.72  47.24   1.52  0.043  1.47
----------------------------------------------------------------------------
MR151762          0   -90   170  175     5  51.82  53.34   1.52  0.014  0.48
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project available at: MR QAQC.

About Scorpio Gold
Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Elevon, LLC (30%). Mineral Ridge is a conventional open pit mining and heap 
leach operation. The Mineral Ridge property is host to multiple gold-bearing 
structures, veins and lenses at exploration, development and production stages. 
Scorpio Gold also holds a 100% interest in the advanced exploration-stage 
Goldwedge property in Manhattan, Nevada, with a fully permitted underground 
mine and 400 ton per day mill facility. The Goldwedge mill facility has been 
placed on a care and maintenance basis and can be restarted immediately when 
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a Qualified Person 
as defined by National Instrument 43-101 and has reviewed and approved the 
content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley,

President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including the potential addition of new mineral 
resources along the NW Brodie trend. Such forward-looking statements involve 
known and unknown risks, uncertainties and other factors that could cause 
actual events or results to differ materially from estimated or anticipated 
events or results implied or expressed in such forward-looking statements, 
including risks involved in mineral exploration and development programs and 
those risk factors outlined in the Company's Management Discussion and Analysis 
as filed on SEDAR. Any forward-looking statement speaks only as of the date on 
which it is made and, except as may be required by applicable securities laws, 
the Company disclaims any intent or obligation to update any forward-looking 
statement, whether as a result of new information, future events or results or 
otherwise. Forward-looking statements are not guarantees of future performance 
and accordingly undue reliance should not be put on such statements due to the 
inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Torrey Hills Capital
Jim Macdonald
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=546405335