Source	MARKET NEWS
Date	10/29/2015
Time	11:20:18 AM

Company	 Happy Creek Minerals Ltd.
Title	Drills 
5 Metres of 1.0% W03 at Nightcrawler, Fox





    CDNX Symbol: HPY











Press Release	





HAPPY CREEK MINERALS LTD ("HPY-V;HPYCF-0")
- Drills 5 Metres of 1.0% W03 at Nightcrawler, Fox Tungsten
- Property

Happy Creek Minerals Ltd. (the "Company) is pleased to
announce preliminary drill results and an update from its 100% owned,
150 square kilometre Fox tungsten property located in the south central
Cariboo, British Columbia.

Between September 5th and October 3rd, eight NQ-size diamond core
drill holes totaling approximately 1,500 metres has explored a portion
of the eastern end of the road-accessible Nightcrawler tungsten skarn
zone. Preliminary results from the first two holes have been received
and are presented here.

Drill hole F15-02 returned 5 metres of 1.0% W03 (tungsten
trioxide), starting from 138 metres down-hole. The intercept is
approximately 113 metres below and 25 metres to the east of the Creek
prospect where outcrop and subcrop samples have yielded from 1.2% up to
6.0% W03 in grab samples over a distance of 90 metres (refer to press
release dated September 17, 2015). The Creek prospect remains undefined
and open in extent, and is interpreted to represent one of at least
three other mineralized layers that occur further south and at higher
elevation above and behind the drill site.

Drill hole F12-01 was collared on the western side of the Creek
prospect and drilled at -55 degrees to the north. However, at this
location the favorable skarn stratigraphic unit has been replaced by
granite where the mineralized zone was expected to occur.

Additional drill results are pending.

During 2015, the Company also completed geological and soil
geochemical surveys, rock sampling, ultra violet lamp prospecting at
the North zone, a property-wide low-level airborne magnetic and
radiometric geophysical survey, and collected a 500 kg metallurgical
sample from the Ridley Creek (RC) prospect. A MSc. Geology thesis was
also initiated at the University of British Columbia.

David Blann, P.Eng., President of Happy Creek states: "The Fox
property has delivered another outstanding result from a
road-accessible area that adds to the resource potential already
identified at three zones on Deception Mountain, 4.5 km to the north.
F15-02 returned 5 metres of 1.0% tungsten trioxide that is the best
intercept to date from the Nightcrawler area and all the work completed
this year marks another positive step forward for the project. Over the
next few months we intend to prepare an initial NI43-101 resource
estimate on a portion of the project and to conduct engineering studies
and permitting activities. The Fox is a large scale, quality new
tungsten discovery globally and we look forward to advancing this
project further next year."
About the Fox property

The Fox property hosts a tungsten and molybdenum mineral system
that is 10 km by 3 km in dimension. Although most of the property is
under-explored, it has returned among the highest grade tungsten drill
intervals globally in a newly discovered near-surface setting. Drill
results from Deception Mountain are from three zones over a distance of
two kilometres. Results include 33 selected intervals averaging 2.5%
W03 over 2.92 metres, and overall, 49 of 60 holes average 8.2 metres of
0.70% W03 within 26 metres of surface. Highlights of drilling in two
zones include intervals such as 26 metres of 1.2% W03 and 14.8 metres
of 4.0% W03, respectively. The Nightcrawler zone is an area 1.5 km by
500 metres in dimension where widely spaced drilling has returned
positive results in multiple layers. Results include 2.0 metres of
0.74% W03, 5.0 metres of 0.33% W03 and 5.0 metres of 1.0% W03. All
zones are open in extent.

Complete details of the Company's drill results and maps can be
found on the website at www.happycreekminerals.com, or within news
releases filed on SEDAR.

On behalf of the Board of Directors,

"David E Blann"

____________________
_______________________________________________
TSX Venture closing price for HPY-V
Date: 2015/10/27
Closing Price: 0.11
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1530100037TS11530101941-11184620151029