Source	MARKET NEWS
Date	10/24/2016
Time	05:31:30 AM

Company	 Bellhaven Copper & Gold Inc.
Title	Updated NI 43 101 Mineral Resource for La Mina P





    CDNX Symbol: BHV











Press Release




[200/News Release]BHVVBELLHAVEN COPPER & GOLD INCOCT 24 2016  05:27 AM
Updated NI 43 101 Mineral Resource for La Mina Project, Colombia --->@NEWS 
RELEASE
BELLHAVEN COPPER & GOLD INC ("BHV-V;BHVCF-0")
- Updated NI 43-101 Mineral Resource for La Mina Project, Colombia

Bellhaven Copper & Gold Inc. ("Bellhaven" or the "Company") is
pleased to announce the results of an updated National Instrument
43-101 mineral resource estimate for its 100%-controlled La Mina
gold-(copper) project ("La Mina" or "the Project"), Colombia. The
Mineral Resource incorporates only La Cantera and Middle Zone prospects
and does not include the highly prospective La Garrucha prospect
located approximately 800 m to the east. Highlights pertaining to the
updated mineral resource estimate include:

//st

1.01 Moz gold equivalent contained in Indicated Mineral Resources
and 0.43 Moz gold equivalent contained in Inferred Mineral Resources at
base-case 0.25 g/t gold cut-off grade.
1.23 Moz gold-equivalent contained in Indicated Mineral Resources
and 0.53 Moz gold equivalent in Inferred Mineral Resources at breakeven
0.10 g/t gold cut-off grade (See Tables 1 and 2 for details on tonnages,
grades, and contained metals at various cut-off grades).
Approximately 70% of the Mineral Resources are now classified as
Indicated Mineral Resources whereas previously all of the Mineral Resources
were defined as Inferred Mineral Resources.
The Mineral Resources are now in-pit constrained mineral resources
("in-pit resources"). Previously the Mineral Resources were in-situ mineral
resources ("in-situ resources").

//et

Dr. Paul Zweng, Bellhaven's CEO and Chairman, commented as
follows:

"We are very pleased with the revised mineral resource estimate
for the La Mina Project which incorporates additional drill holes as
well as updated metal prices, metallurgical recoveries, and mining/cost
factors. The revised Mineral Resources are defined as in-pit resources
whereas in the past all were delimited as in-situ resources--the new
Mineral Resources are thus more conservative.  The conversion of ~70%
of the Mineral Resources to Indicated Mineral Resources is a huge
value-add for Bellhaven's shareholders.  These two improvements greatly
upgrade the quality of the Mineral Resource, thereby de-risking the
Project."

"The aeromagnetic anomaly over the nearby La Garrucha prospect is
substantially larger than those over either La Cantera or Middle Zone
prospects.  Drill holes collared at La Garrucha have yielded multiple
100-m-plus intercepts of 1.0 g/t gold (or better) grades (see press
releases of June 5 and 27, July 10, and September 10, 2013).  Next year
we intend to drill the requisite number of holes at La Garrucha so as
to provide the basis for calculating a mineral resource estimate for
this prospect."

La Mina Revised Mineral Resource Estimate

Metal Mining Consultants Inc. ("MMC") of Highlands Ranch, Colorado
prepared the mineral resource estimate in accordance with the
definitions in Canadian National Instrument 43-101 ("NI 43-101").  The
updated Mineral Resource incorporates 14 new drill holes collared at
the Middle Zone prospect (with two holes extending into La Cantera
prospect) undertaken by Bellhaven between May and December 2012 (see
news releases dated September 6, 2012 and December 27, 2012). The
resource estimate does not include an additional eleven holes drilled
at other prospects in the concession, including La Garrucha, after the
announcement of the initial mineral resource estimate.

The new mineral resource estimate was calculated using a
Whittle-Pit algorithm.  The input parameters used to calculate the
in-pit resources are as follows: median consensus long-term projected
metal prices (as of July, 2016) of US$1275/oz gold, US$17.75/oz silver,
and US$2.75/lb copper, G&A of US$0.98 per tonne, open-pit mining costs
of US$1.72 per tonne, processing costs of US$5.83 per tonne,
metallurgical recoveries of 93% for gold and 90% for copper, and an
average pit-slope of 50 degrees.

Table 1 presents the Mineral Resources calculated at a series of
gold cut-off grades.  The breakeven cut-off is 0.10 g/t gold, meeting
the standard for "reasonable prospects for eventual economic
extraction".  The base-case cut-off grade of 0.25 g/t gold highlighted
in Table 1 is currently our best estimate for mineral resources within
a future PEA mine plan and will be modified, if necessary, once the
revised PEA is completed.

//st
Table 1. Mineral Resources for La Mina Project (La Cantera and Middle
Zone only), Colombia.

Cut-off Metric   Grades                  Contained Metal
Grade   Tonnes
(g/t    ('000)
Au)              Au    Ag    Cu    AuEq  Au       Ag        Cu          AuEq
(g/t) (g/t)  (%)   (g/t) (oz)     (oz)      (lbs, '000) (oz)
Indicated Mineral Resources
0.10    49,495   0.49  1.39  0.18  0.78  785,731 2,205,058 193,397 1,233,559
0.20    33,060   0.66  1.66  0.22  1.01  701,485 1,765,284 163,235 1,078,136
0.25    28,170   0.74  1.77  0.24  1.12  666,761 1,606,962 150,242 1,013,185
0.30    24,676   0.81  1.86  0.26  1.21  639,282 1,479,395 139,719   961,231
0.40    19,374   0.93  2.05  0.28  1.38  579,166 1,279,923 121,344   858,706
0.50    16,288   1.02  2.21  0.31  1.50  534,159 1,157,354 109,935   787,387
Inferred Mineral Resources
0.10    21,854   0.44  1.43  0.19  0.75  311,141 1,001,704  93,464   526,674
0.20    14,533   0.59  1.63  0.25  0.98  274,743   763,659  79,272   456,352
0.25    12,394   0.65  1.75  0.27  1.07  259,626   696,520  73,294   427,408
0.30    10,883   0.71  1.84  0.29  1.16  249,627   642,890  68,473   406,264
0.40    8,312    0.82  2.00  0.31  1.32  220,021   533,276  57,632   351,749
0.50    6,734    0.91  2.14  0.33  1.43  197,025   463,073  49,257   309,713
//et

//st
Table 1 footnotes:
1. Mineral resources are not mineral reserves & do not have demonstrated
economic viability.  There is no certainty that all or any part of the
mineral resources will be converted into mineral reserves.
2. Gold-equivalent grades were calculated using the following formula:
AuEq = Au (g/t) + [Cu(%)} x {%Recoverable Cu / %Recoverable Au} x {Cu
Price/Au Price} x 22.0462 x 31.1035] + [Ag (g/t) x {Ag Price/Au Price}].
Metal prices used were the median consensus long-term prices as of Jul,
2016 for gold (US$1,275/oz), silver (US$17.75), & copper (US$2.75).  Metal
prices are not constant & are subject to change.  Metal recoveries of 93%
Au & 90% Cu are estimates based on metallurgical results announced in
Bellhaven's news release dated Sep 21, 2016.
3. All quantities are rounded to the appropriate number of significant
figures; consequently sums may not add up due to rounding.
//et

The Mineral Resource for La Mina incorporates the La Cantera and
Middle Zone porphyry deposits.  These two deposits occur within 400 m
of each other. At average grades of 1.12 g/t gold equivalent (Indicated
Resources) and 1.07 g/t gold equivalent (Inferred Resources), La Mina
is one of the richest porphyry projects in the Americas.

Table 2.  Total Indicated & Inferred Mineral Resources for La
Mina Project (Cut-off Grade: 0.25 g/t Au)

//st
Deposit   Metric    Grades                  Contained Metal
Tonnes
('000)  Au    Ag    Cu    AuEq  Au       Ag        Cu        AuEq
(g/t) (g/t) (%)   (g/t) (oz)     (oz)      (lbs,     (oz)
'000)



Indicated Mineral Resources
La Cantera 17,984   0.87  2.06  0.32  1.37 503,021 1,191,062 125,344 789,953
Middle
Zone      10,186   0.50  1.27  0.11  0.68 163,740   415,899  24,898 223,232
Total
Indicated 28,170   0.74  1.77 0.24 1.12 666,761 1,606,962 150,242 1,013,185
Inferred Mineral Resources
La Cantera 10,806   0.69  1.83  0.29  1.15 239,715   635,766  70,256 400,099
Middle
Zone       1,588   0.39  1.19  0.09  0.53  19,911    60,754   3,038  27,309
Total
Inferred  12,394   0.65  1.75  0.27  1.07  259,626  696,520  73,294 427,408
//et



//st
Table 2 footnotes:  See footnotes appearing immediately below Table 1.

//et

Mineral resources do not have demonstrated economic viability.
Future in-fill drilling as well as Preliminary Economic Assessment,
Pre-Feasibility and Feasibility Studies will determine the percentage
of the Inferred Resources, if any, which can be placed into the
mineable category.  Bellhaven is not aware of any environmental,
permitting, legal, title, taxation, socio-political, marketing or other
issues which may materially impact this estimate of mineral resources.

Geologic Model and Modeling Parameters

The updated mineral resource calculation reflects additional
drilling that was completed subsequent to the August 2012 Technical
Report. The revised resource estimation is based on 88 drill holes and
14,284 meters of drilling with a total of and 14,284 two-meter-length
composites.  Geologic volumes were used to constrain the estimation.
The grade estimation strategy was determined to remain unchanged from
previous resource estimates. Mineralization was estimated using the
Inverse Distance Squared ("ID2") estimation technique. Hard boundaries
were also set such that only composites matching the respective
lithology could be used as part of the estimation. Sample intervals
were only used if they were greater than or equal to 1.5 meters in
length. With the exception of block and sample restrictions, the search
parameters were the same for each geologic domain.

Metallurgical testing of material from La Mina has given greater
confidence in the classification of its Mineral Resources.
Approximately 70% of the updated Mineral Resources are classified as
Indicated. Indicated Mineral Resources were defined as blocks that are
within 35 meters of a drill hole and where a minimum of two drill holes
were used to determine the estimated grade.  A grade-capping strategy
was employed to limit the impact of high-grade outlier samples.  Silver
was capped at 25.5 ppm, gold was capped at 4.2 ppm, and copper was
capped at 3000 ppm. Density measurements for the Mineral Resource were
determined by 636 individual measurements of drill-core samples.

The scientific and technical information in this news release was
prepared under the supervision of Mr. Thomas J. Drown, P.Geo.  Mr.
Drown has more than 25 years relevant experience and is a British
Colombia Professional Geoscientist.  He has been a senior project
geologist with the Company at the La Mina Project and serves as the
qualified person as defined by National Instrument 43-101.

Mr. Scott Wilson, Principal for Metal Mining Consultants, Inc.,
and a Qualified Person as defined by NI 43-101, has reviewed and
approved the process and economic information contained in this
release.

Mr. Gregory Chlumsky, Principal for InterPro, and a Qualified
Person as defined by NI 43-101, has reviewed and approved the process
and economic information contained in this release.

About Bellhaven

Bellhaven Copper & Gold Inc. is a Canadian-listed (TSX-V: BHV)
exploration company exploring for gold and copper in Colombia.  The
Company's goal is to be a leader in gold and copper development in
Colombia.  Bellhaven focuses on discovery, acquisition and development
of high-quality resources in a safe and responsible manner for the
benefit of all of its stakeholders. The Company's flagship project is
the La Mina gold-(copper) porphyry deposit in the Middle Cauca belt of
Colombia. The Company is currently seeking to develop and to grow these
resources through mine development and through ongoing exploration on
the La Mina concession. For more information regarding Bellhaven,
please visit our website at www.bellhavencg.com.

On behalf of the board of directors,

Dr. Paul L. Zweng

BELLHAVEN COPPER & GOLD INC.

Statements in this press release include, other than purely
historical information, certain "forward-looking information" and
"forward-looking statements" (collectively "forward-looking
statements") within the meaning of applicable Canadian and United
States securities legislation including the United States Private
Securities Litigation Reform Act of 1995. All statements, other than
statements of historical fact, included herein, without limitation,
statements relating to the future operating or financial performance of
Bellhaven, planned expenditures and the anticipated activity at La Mina
Project, are forward-looking statements. Forward-looking statements are
frequently, but not always, identified by words such as "expects",
"anticipates", "believes", "intends", "estimates", "potential",
"possible", and similar expressions, or statements that events,
conditions, or results "will", "may", "could", or "should" occur or be
achieved. These forward-looking statements may include statements
regarding perceived merit of properties; exploration plans and budgets;
mineral reserves and resource estimates; work programs; capital
expenditures; timelines; strategic plans; market prices for precious
and base metals; or other statements that are not statements of fact.
Forward-looking statements involve various risks and uncertainties.
There can be no assurance that such statements will prove to be
accurate, and actual results and future events could differ materially
from those anticipated in such statements. Important factors that could
cause actual results to differ materially from Bellhaven's expectations
include the uncertainties involving the need for additional financing
to explore and develop properties and availability of financing in the
debt and capital markets; uncertainties involved in the interpretation
of drilling results and geological tests and the estimation of reserves
and resources; the need for cooperation of government agencies and
native groups in the development and operation of properties; the need
to obtain permits and governmental approvals; risks of construction and
mining projects such as accidents, equipment breakdowns, bad weather,
non-compliance with environmental and permit requirements,
unanticipated variation in geological structures, metal grades or
recovery rates; unexpected cost increases, which could include
significant increases in estimated capital and operating costs;
fluctuations in metal prices and currency exchange rates; and other
risks and uncertainties disclosed in Bellhaven's Annual Report for the
year ended April 30, 2016 filed with Canadian securities regulatory
authorities and in other Bellhaven reports and documents filed with
applicable securities regulatory authorities from time to time.
Bellhaven's forward-looking statements reflect the beliefs, opinions,
and projections on the date the statements are made. Bellhaven assumes
no obligation to update the forward-looking statements or beliefs,
opinions, projections, or other factors, should they change, except as
required by law.
Mineral resources are not mineral reserves and do not have
demonstrated economic viability.  There is no certainty that all or any
part of the mineral resources will be converted into mineral reserves.
Gold-equivalent grades were calculated using the following formula:
AuEq = Au (g/t) + [Cu(%)} x {%Recoverable Cu / %Recoverable Au} x {Cu
Price/Au Price} x 22.0462 x 31.1035] + [Ag (g/t) x {Ag Price/Au
Price}].  Metal prices used were the median consensus long-term prices
as of July 2016 for gold (US$1,275/oz), silver (US$17.75), and copper
(US$2.75).  Metal prices are not constant and are subject to change.
Metal recoveries of 93% Au and 90% Cu are estimates based on
metallurgical results announced in Bellhaven's news release dated
September 21, 2016.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

SOURCE Bellhaven Copper & Gold Inc.
























































TSX Venture closing price for BHV-V
Date: 2016/10/20
Closing Price: 0.53

TEL: (808) 377-1947
E-mail: pzweng@gmail.com

Internet: http://www.bellhavencg.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1629700008TS11629700682-05275120161024