Source	MARKET NEWS
Date	10/25/2016
Time	07:21:07 AM

Company	 Vulcan Minerals Inc.
Title	Commences 
Colchester Copper Gold Field Program i





    CDNX Symbol: VUL











Press Release





VULCAN MINERALS INC ("VUL-V")
- Commences Colchester Copper-Gold Field Program in Newfoundland

Vulcan Minerals Inc. ("the Company" - "Vulcan") announces that it
has commenced field operations at the Colchester copper-gold property
in north-central Newfoundland. A grid totalling approximately 25 line
kilometers is currently being cut to facilitate a high resolution
Induced Polarization (IP) geophysical survey and geological mapping.
A thorough compilation of historic data of the project has been
undertaken including the digitization of all relevant geological data
and drilling records. These data include 22,000 metres of drilling over
110 holes (1963-2005), various soil sampling surveys and 15 geophysical
surveys of varying vintages and quality including a 2005 high
resolution airborne magnetic and VTEM survey. Selected data have been
incorporated into 3D modelling software where the analysis indicates
that the known mineralized zones remain open in all directions. As
well, several encouraging zones on the property identified by trenching
or scout drilling remain undelineated, providing the potential for
discoveries outside the main Colchester and McNeilly zones. The
upcoming geophysical survey will focus on the underexplored Old English
area in an attempt to calibrate and test the IP technology as a drill
target and geologic mapping tool in an area with both copper and gold
potential. For example, drillhole H-83 intersected 65.7 m of 0.52% Cu
including 17.1 m of 1.0% Cu in a continuously sampled sulfide bearing
chlorite-quartz shear zone. Hole CC-03-09 intersected 4.2 grams/tonne
gold over 2.9 m. A drilling program is planned to test encouraging IP
anomalies identified in the current program, preferably before yearend.
Based on the variety of mineralization identified from historic
information and observed in the field, the Company believes the
property will require systematic evaluation utilizing state of the art
geophysical technology to direct the drilling strategy.
The following tables highlight some of the historic drill
intersections retrieved from records at the Department of Natural
Resources, Government of Newfoundland and Labrador. These composited
intervals represent length-weighted averages and usually occur within
wider mineralized sections grading below 1% copper (Table 1). The
intervals are drilled thicknesses in holes generally inclined at 50-60
degrees into steeply dipping zones and are thus believed to represent
near but not true thicknesses. Gold analyses were generally not carried
out on the historic holes except for the 2003-2005 program
(representing only 20 of the 110 holes on the property); highlights for
drilling samples from that program exceeding 1 gram gold per tonne are
presented in Table 2.

//st
Table 1. Select composited historical Colchester copper drilling results
Hole-ID    Zone         From (m)  To (m)    Length   Composited Cu (%)
(m)
436-11     McNeilly     86.28     90.83      4.55     4.55 m @ 3.82%
436-16     Colchester  142.30     157.60     15.30     15.30 m @ 1.02%
436-16     Colchester  167.94     178.13     10.19     10.19 m @ 1.07%
436-21     Colchester   23.96     38.10     14.14     14.14 m @ 1.95%
436-21     Colchester   53.04     71.63     18.59     18.59 m @ 1.61%
436-21     Colchester   53.04     73.10     20.06     20.06 m @ 1.51%
436-30     Colchester   59.74     69.98     10.24     10.24 m @ 2.20%
436-31     Colchester  175.26     189.07     13.81     13.81 m @ 1.07%
436-35     Colchester   76.20     90.37     14.17     14.17 m @ 1.06%
436-37     Colchester   46.02     57.21     11.19     11.19 m @ 1.33%
436-38     Colchester  183.28     193.55     10.27     10.27 m @ 1.16%
436-39     Colchester  178.61     192.27     13.66     13.66 m @ 1.01%
436-41     Colchester  128.96     155.45     26.49     26.49 m @ 1.43%
436-6      Colchester  106.68     131.06     24.38     24.38 m @ 1.21%
436-8      Colchester  119.09     131.98     12.89     12.89 m @ 1.32%
CC-03-02   Colchester   74.20     90.00     15.80     15.80 m @ 2.19%
CC-03-11   McNeilly     72.85     84.00     11.15     11.15 m @ 1.68%
CC-04-18   Colchester   34.30     46.90     12.60     12.60 m @ 1.15%
CC-04-19   Colchester  208.80     221.40     12.60     12.60 m @ 1.04%
H-45       Colchester  233.17     248.20     15.03     15.03 m @ 1.06%
H-48       Colchester  322.78     346.01     23.31     23.31 m @ 1.24%
H-49       Colchester  187.45     203.61     16.16     16.16 m @ 1.68%
H-50       Colchester  270.51     281.94     11.43     11.43 m @ 1.32%
H-51       Colchester   70.10     82.60     12.50     12.50 m @ 2.49%
H-51       Colchester  160.02     192.63     32.61     32.61 m @ 1.04%
H-52       Colchester  146.91     172.21     25.30     25.30 m @ 1.02%
H-61       McNeilly     69.34     82.30     12.96     12.96 m @ 1.97%
H-69       Colchester  192.02     202.69     10.67     10.67 m @ 1.27%
H-78       Old English  96.62     132.59     35.97     35.97 m @ 1.03%
H-83       Old English 118.02     137.16     17.14     17.14 m @ 1.01%




Table 2. Select composited historical Colchester gold drilling results )
1.0 g/t Au.
Hole-ID      Zone        From (m)     To (m)    Length   Composited Au
(g/t)
(m)
CC-03-02     Colchester     76.20     80.05     3.85     3.85 m @ 5.86 g/t
CC-03-03     Colchester     30.85     33.40     2.55     2.55 m @ 9.79 g/t
CC-03-03     Colchester     61.55     62.65     1.10     1.10 m @ 1.63 g/t
CC-03-04     Colchester     28.65     30.57     1.92     1.92 m @ 3.33 g/t
CC-03-07     Old English     29.56     31.54     1.98     1.98 m @ 1.28 g/t
CC-03-07     Old English     41.76     42.40     0.64     0.64 m @ 3.23 g/t
CC-03-07     Old English     47.85     49.07     1.22     1.22 m @ 2.03 g/t
CC-03-07     Old English     54.28     55.00     0.72     0.72 m @ 1.04 g/t
CC-03-08     Old English     42.00     43.00     1.00     1.00 m @ 1.53 g/t
CC-03-08     Old English     71.07     71.50     0.43     0.43 m @ 1.56 g/t
CC-03-08     Old English     72.48     73.03     0.55     0.55 m @ 2.06 g/t
CC-03-09     Old English     93.50     94.00     0.50     0.50 m @ 1.30 g/t
CC-03-09     Old English     97.60     100.50     2.90     2.90 m @ 4.18
g/t
CC-03-11     McNeilly        56.00     57.00     1.00     1.00 m @ 1.07 g/t
CC-03-11     McNeilly        80.00     81.00     1.00     1.00 m @ 1.54 g/t
CC-04-14     Colchester      32.35     33.95     1.60     1.60 m @ 1.65 g/t
CC-04-16     Colchester     183.50     185.10     1.60     1.60 m @ 1.17
g/t
CC-04-17     Colchester     18.60     19.30     0.70     0.70 m @ 1.07 g/t
//et

The Colchester property is owned 100% by Vulcan with no underlying
royalties and consists of over 2,500 hectares covering four past
producing historic copper mines and is accessible by paved road
approximately 25 kilometres off the Trans Canada Highway. The area is
serviced by an airport at Deer Lake 110 kilometres to the southwest.
Please refer to our webpage www.vulcanminerals.ca for location and
geology maps.
Patrick J. Laracy, P. Geo, President, and Patrick Collins, P. Geo,
are qualified persons responsible for the contents of this news release
as defined in National Instrument 43-101.
Vulcan is establishing itself as a leading explorer in
Newfoundland and Labrador focussed on project generation, value
addition and partnering. Vulcan has projects available for option and a
competent team to operate all exploration activities. Contact us for
opportunity in mineral exploration and development.
The TSX Venture Exchange has not reviewed and does not accept
responsibility for the adequacy or accuracy of this release. This
release may contain certain forward-looking statements. Actual events
or results may differ from the Company's expectations. Certain risk
factors beyond the Company's control may affect the actual results
achieved. Accordingly, readers are advised not to place undue reliance
on forward-looking information. Except by law, the Company undertakes
no obligation to publicly update or revise forward-looking information.

TSX Venture closing price for VUL-V
Date: 2016/10/21
Closing Price: 0.04

TEL: (709) 754-3186    Patrick J. Laracy, President
E-mail:   info@vulcanminerals.ca
Internet: www.vulcanminerals.ca
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1629800024TS11629801230-07174020161025