Source	Marketwire
Date	10/12/2016
Time	05:01:39 AM

Company	 INDEPENDENCE GOLD CORP.
Title	Independence Gold Intersects 7.73 g/t Gold Across 6.1 m, Boulevard 
Project, Yukon





    CDNX Symbol: IGO











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Independence Gold Corp.

TSX VENTURE SYMBOL: IGO

October 12, 2016

Independence Gold Intersects 7.73 g/t Gold Across 6.1 m, Boulevard Project, 
Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 12, 2016) - Independence Gold 
Corp. (TSX VENTURE:IGO) ("Independence" or "the Company") is pleased to 
announce new gold discoveries on its 100% owned Boulevard Project, contiguous 
to Goldcorp Inc.'s Coffee Gold Deposit in the White Gold District, Yukon. The 
best intercepts include 7.73 grams per tonne (g/t) gold ("Au") across 6.1 
metres ("m") and 1.19 g/t Au over 22.9 m at the Sunset Zone, 4.36 g/t Au across 
6.1 m within the Sunrise Zone, and 4.28 g/t Au over 4.6 m at the Denali Zone.

Sunrise - Sunset Area

A total of 1,401 m of reverse circulation ("RC") drilling was completed in 15 
drill holes within the Sunrise-Sunset area, located 8.5 kilometres ("km") 
southwest of the Coffee deposit. Drilling evaluated multi-element soil 
anomalies within the 2.3 km long Sunset trend and focused on testing new, 
potentially sub-parallel mineralized zones at Sunrise. Significant intercepts 
are presented in the table below. A table of all 2016 drill results and a map 
showing the drill hole locations is posted on the Company's website.

/T/

----------------------------------------------------------------------------
Length
Drill hole    Zone           From (m)       To (m)       (m)(i)     Au (g/t)
----------------------------------------------------------------------------
BV16-47       Sunset              4.6         27.4         22.9         1.19
----------------------------------------------------------------------------
Incl.       Sunset              4.6          7.6          3.1         4.33
----------------------------------------------------------------------------
BV16-51       Sunrise            65.5         67.1          1.5         1.39
----------------------------------------------------------------------------
BV16-53       Sunrise            16.8         22.9          6.1         4.36
----------------------------------------------------------------------------
Incl.       Sunrise            18.3         21.3          3.1         8.27
----------------------------------------------------------------------------
BV16-53       Sunrise            50.3         59.4          9.2         0.36
----------------------------------------------------------------------------
BV16-54       Sunset             24.4         64.0         39.6         1.58
----------------------------------------------------------------------------
Incl.       Sunset             24.4         30.5          6.1         7.73
----------------------------------------------------------------------------
BV16-56       Sunset             18.3         22.9          4.6         3.05
----------------------------------------------------------------------------
Incl.       Sunset             19.8         21.3          1.5         7.98
----------------------------------------------------------------------------
(i)True thickness estimated to be 60-70% of drill intercepts

/T/

Drill hole BV16-54 tested a robust multi-element soil anomaly at the southeast 
end of the Sunset trend and returned 7.73 g/t Au over 6.1 m which occurs within 
a broad zone that returned 1.58 g/t Au over 39.6 m. This mineralization is 
hosted within quartzite and is cross cut by massive quartz veins. The drill 
hole was oxidized to a down hole depth of 45 m and ended in mineralization. Six 
drill holes were completed at the western extent of the Sunset Zone; BV16-47 
intersected 1.19 g/t Au over 22.9 m including 4.33 g/t Au over 3.1 m. Drill 
hole BV16-56 returned 3.05 g/t Au over 4.6 m including a higher grade core 
which grades 7.98 g/t Au over 1.5 m. Further to the southeast at the Sunrise 
Zone, BV16-53 intersected 4.36 g/t Au over 6.1 m including 8.27 g/t Au over 3.1 
m. This defines a new parallel, north-trending structure, situated 75 m 
southeast of drill hole BV15-31 which returned 7.23 g/t Au over 12.2 m (news 
release August 24, 2015). Mineralization in BV16-53 occurs in a strongly 
oxidized zone within quartzite and is associated with an increase in quartz 
veining.

One of the primary objectives of this years' Sunrise-Sunset drill program was 
to evaluate the relationship between cross cutting quartz veins and gold 
mineralization. Based on the available core and RC drill data, the two primary 
controls on mineralization are the presence of massive quartz veins, comprising 
up to 80% of the rock and a resistive quartzite host rock. Pyrite +/- 
arsenopyrite and stibnite are irregularly developed within mineralized zones 
and oxidation levels are variable but proved more extensive in the 2016 
mineralized intercepts. All drill holes were oriented to the east to 
effectively cross-cut the southwest striking, steeply northwest dipping quartz 
veins.

Denali Zone

A total of 1,545 m of RC drilling was completed in 15 drill holes at the Denali 
Zone, situated 14.5 km to the west of the Coffee deposit, along an interpreted 
extension of the Coffee Creek fault system. The primary focus for this drilling 
program was to test along strike and down dip of YCS15-03 which returned 4.25 
g/t Au over 6.1 m (news release August 24, 2015). Significant drill hole 
results are provided in the table below:

/T/

----------------------------------------------------------------------------
Drill hole             From (m)         To (m)  Length (m)(i)       Au (g/t)
----------------------------------------------------------------------------
YCS16-06                   19.8           25.9            6.1           0.98
----------------------------------------------------------------------------
YCS16-06                  115.8          120.4            4.6           2.33
----------------------------------------------------------------------------
Incl.                   115.8          117.4            1.5           6.35
----------------------------------------------------------------------------
YCS16-07                   68.6           70.1            1.5           1.78
----------------------------------------------------------------------------
YCS16-08                   99.1          103.6            4.6           4.28
----------------------------------------------------------------------------
YCS16-10                   18.3           19.8            1.5           1.20
----------------------------------------------------------------------------
YCS16-11                   24.4           29.0            4.6           0.95
----------------------------------------------------------------------------
YCS16-12                    7.6           10.7            3.1           1.94
----------------------------------------------------------------------------
YCS16-16                   39.6           59.4           19.8           0.47
----------------------------------------------------------------------------
Incl.                    57.9           59.4            1.5           2.27
----------------------------------------------------------------------------
(i)True thickness estimated to be 60-70% of drill intercepts

/T/

YCS16-08 was drilled approximately 50 m down dip to the northeast from the 2015 
discovery hole and returned 4.28 g/t Au over 4.6 m. YCS16-07 was also drilled 
down dip and intersected 1.78 g/t Au over 1.5 m. The mineralized zone appears 
to plunge moderately to the north-northeast, is variably hosted in quartzite 
and quartz biotite schist, and is typically associated with an increase in fine 
grained pyrite. YCS16-16 intercepted a broad zone of mineralization at the 
northwestern end of the Denali Zone, returning 0.47 g/t Au over 19.8 m with 
oxidation to a down hole depth of 53 m. YCS16-12, at the eastern end of the 
trend returned 1.94 g/t Au over 3.1 m.

The Company plans to complete a desktop study to determine the nature of gold 
mineralization at Boulevard as well as prepare for a follow-up drill program on 
the Sunrise-Sunset and Denali Zones in 2017.

The Company is pleased to report that a Rotary Air Blast drilling program was 
completed on the Rosebute property, located 29 km north of Kinross' Golden 
Saddle Deposit. Drilling included 12 holes for a total of 923.5 m. All drilling 
was focused on the Hudbay Zone and the Company will provide a summary of 
results in the coming weeks.

All samples were submitted to SGS Minerals Services in Burnaby, BC for sample 
preparation by crushing to 75% less than 2 millimetres, creation of a 250 g 
split, and then pulverizing to 85% passing 75 microns. Sample pulps are 
submitted for gold analysis with a 30 g fire assay and AAS finish (code 
GE-FAA313). Samples are also submitted for a 52 element analysis using an aqua 
regia digest and ICP-AES and ICP-MS analysis (GE-ICM14B). Control samples 
(accredited gold standards and blanks) were inserted into the sample sequence 
on a regular basis monitor precision of results.

David Gale, P.Geo., the Company's Qualified Person as defined by National 
Instrument 43-101 for the White Gold District, has reviewed the technical 
information in this news release and has approved the disclosure herein.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed mineral 
exploration company listed on the TSX Venture Exchange, with a portfolio of 
projects in the Yukon and the 3Ts Project in British Columbia. The Company's 
holdings range from early stage grassroots exploration to advanced-stage 
resource expansion. For additional information, please visit the Company's 
website www.ingold.ca.

INDEPENDENCE GOLD CORP.

Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release contains forward-looking statements and forward-looking 
information (collectively, "forward-looking statements") within the meaning of 
applicable Canadian securities legislation. All statements, other than 
statements of historical fact, included herein are forward-looking statements. 
Although the Company believes that such statements are reasonable, it can give 
no assurance that such expectations will prove to be correct. The Company 
cautions investors that any forward-looking statements by the Company are not 
guarantees of future results or performance, and that actual results may differ 
materially from those in forward-looking statements as a result of various 
factors. All of the Company's public disclosure filings may be accessed via 
www.sedar.com. Readers are urged to review these materials, including the 
technical reports filed with respect to the Company's mineral properties.

- 30 -

CONTACT INFO:

Independence Gold Corp.
Corporate Development
604-687-3959
info@ingold.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=578848037