Source	MARKET NEWS
Date	10/27/2016
Time	06:08:04 AM

Company	 Independence Gold Corp.
Title	Intersects Gold Mineralization, Rosebute Propert





    CDNX Symbol: IGO











Press Release





Intersects Gold Mineralization, Rosebute Property, Yukon --->@NEWS RELEASE
INDEPENDENCE GOLD CORP ("IGO-V")
- Intersects Gold Mineralization, Rosebute Property, Yukon

Independence Gold Corp. ("Independence" or "the Company") is
pleased to announce that it has intersected multiple broad zones of
gold mineralization at the Hudbay Zone on the Rosebute property under
option from Taku Gold Corporation. Intercepts include 0.50 grams per
tonne ("g/t") gold ("Au") over 36.6 metres ("m"), 0.31 g/t Au over 38.1
m and 0.15 g/t Au over 91.4 m.

The Rosebute property contains two significant gold geochemical
anomalies, the Norwest Zone and Hudbay Zones. The 2016 drill program
used a Rotary Air Blast ("RAB") drill to complete 12 holes (923.5 m) at
the Hudbay Zone. Drill results from this initial evaluation of the
Hudbay Zone are presented in the table below. A summary of all 2016
drill results and a map showing the drill hole locations can be found
on the Company's website (http://www.ingold.ca).

//st
Drill hole     From (m)   To (m)   Length (m)*   Au (g/t)
RO16-06             3.1     16.8          13.7       0.29
RO16-06            22.9     32.0           9.1       0.22
RO16-08             0.0     12.2          12.2       0.32
RO16-09             9.1    100.6          91.4       0.15
Incl.              53.3     56.4           3.1       1.67
RO16-10             6.1    100.6          94.5       0.12
RO16-10            62.5     71.6           9.2       0.29
RO16-15            12.2     48.8          36.6       0.50
Incl.              25.9     27.4           1.5       1.68
& Incl.            45.7     47.2           1.5       2.50
RO16-16            10.7     48.8          38.1       0.31
Incl.              39.6     41.2           1.5       1.26
//et

*True thickness estimated to be 70-90% of drill intercepts

The Hudbay Zone is identified by a 1.3 km long
gold-silver-tungsten-molybdenum (Au-Ag-W-Mo) soil-geochemical anomaly
that is open to the north and west. Hudbay was previously tested by
mechanical trenching which yielded results of 1.5 g/t Au over 20 m, 6.2
g/t Au over 5 m and 0.35 g/t Au over 81 m as noted in Taku's news
release on September 12, 2012.

Drill holes RO16-15 and RO16-16, located in the northern portion
of the Hudbay anomaly returned the most encouraging results. RO16-15
intersected 0.50 g/t Au over 36.6 m, including 2.50 g/t Au over 1.5 m.
RO16-16 intersected 0.31 g/t Au over 38.1 m, including 1.26 g/t Au over
1.5 m. Both intercepts are hosted within a quartz biotite schist and
are spatially associated with increased concentrations of massive
quartz veins. Sulphides are rare and typically absent within the
mineralized zones. These two drill holes occur on the northeast margin
of a structurally bounded, magnetic anomaly that measures 450 m x 450
m. Coincident with this geophysical target is the Au-Ag-W-Mo soil
anomaly that is open to the west in an area that has not been
geochemically sampled or geophysically surveyed. The Company plans to
fully define the western extent of this Zone by collecting grid-style
soil samples and expanding upon the existing geophysical dataset in
2017 with the intent to define drill targets.

The remaining drill holes focused on the southern half of the
Hudbay Zone and variably intersected broad zones of gold mineralization
such as RO16-09 which returned 0.15 g/t Au over 91.4 m, including 1.67
g/t Au over 3.1 metres.

The first drill program at the Hudbay Zone focused on the
gold-rich portion of the soil geochemical anomaly and is encouraging as
it identifies a positive correlation between an increase in quartz
veining and gold mineralization.

The Hudbay Zone is underlain primarily by metasedimentary rocks,
situated on the western margin of a north-trending potassium feldspar
rich orthogneiss unit. Mineralization appears to have a stronger
association with the metasedimentary package which is comprised of
quartz biotite schist and quartzite, with minor orthogneiss. Both rock
types are cross cut by shallowly south-dipping quartz veins that are
aligned within a shallowly south-dipping, pervasive foliation.

The Rosebute Property is located approximately 58 km south of
Dawson City, Yukon and approximately 29 km north of the Golden Saddle
Deposit owned by Kinross Gold Corporation. The Property is contiguous
to the west of the Company's Henderson project, and is situated in
close proximity to the northern access road proposed by Goldcorp that
will provide access to the multi-million ounce Coffee gold deposit.

All samples were submitted to SGS Minerals Services in Burnaby, BC
for sample preparation by crushing to 75% less than 2 millimetres,
creation of a 250 g split, and then pulverizing to 85% passing 75
microns. Sample pulps are submitted for gold analysis with a 30 g fire
assay and AAS finish (code GE-FAA313). Samples are also submitted for a
52 element analysis using an aqua regia digest and ICP-AES and ICP-MS
analysis (GE-ICM14B). Control samples (accredited gold standards and
blanks) were inserted into the sample sequence on a regular basis
monitor precision of results.

David Gale, P.Geo., the Company's Qualified Person as defined by
National Instrument 43-101 for the White Gold District, has reviewed
the technical information in this news release and has approved the
disclosure herein.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed
mineral exploration company listed on the TSX Venture Exchange, with a
portfolio of projects in the Yukon and the 3Ts Project in British
Columbia. The Company's holdings range from early stage grassroots
exploration to advanced-stage resource expansion. For additional
information, please visit the Company's website www.ingold.ca.

INDEPENDENCE GOLD CORP.
Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking statements and
forward-looking information (collectively, "forward-looking
statements") within the meaning of applicable Canadian securities
legislation. All statements, other than statements of historical fact,
included herein are forward-looking statements. Although the Company
believes that such statements are reasonable, it can give no assurance
that such expectations will prove to be correct. The Company cautions
investors that any forward-looking statements by the Company are not
guarantees of future results or performance, and that actual results
may differ materially from those in forward-looking statements as a
result of various factors. All of the Company's public disclosure
&#64257;lings may be accessed via www.sedar.com. Readers are urged to
review these materials, including the technical reports filed with
respect to the Company's mineral properties.

TSX Venture closing price for IGO-V
Date: 2016/10/26
Closing Price: 0.17

TEL:  604-687-3959  Independence Gold Corp.
EMAIL:  info@ingold.ca
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1630000005TS11630000903-06061320161027