Source	Marketwire
Date	10/27/2016
Time	05:02:25 AM

Company	 INDEPENDENCE GOLD CORP.
Title	Independence Gold Intersects Gold Mineralization, Rosebute Property, Yukon





    CDNX Symbol: IGO











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Independence Gold Corp.

TSX VENTURE SYMBOL: IGO

October 27, 2016

Independence Gold Intersects Gold Mineralization, Rosebute Property, Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 27, 2016) - Independence Gold 
Corp. (TSX VENTURE:IGO) ("Independence" or "the Company") is pleased to 
announce that it has intersected multiple broad zones of gold mineralization at 
the Hudbay Zone on the Rosebute property under option from Taku Gold 
Corporation. Intercepts include 0.50 grams per tonne ("g/t") gold ("Au") over 
36.6 metres ("m"), 0.31 g/t Au over 38.1 m and 0.15 g/t Au over 91.4 m.

The Rosebute property contains two significant gold geochemical anomalies, the 
Norwest Zone and Hudbay Zones. The 2016 drill program used a Rotary Air Blast 
("RAB") drill to complete 12 holes (923.5 m) at the Hudbay Zone. Drill results 
from this initial evaluation of the Hudbay Zone are presented in the table 
below. A summary of all 2016 drill results and a map showing the drill hole 
locations can be found on the Company's website (http://www.ingold.ca).

/T/


----------------------------------------------------------------------------
Drill hole       From (m)        To (m)      Length (m)(i)    Au (g/t)
----------------------------------------------------------------------------
RO16-06           3.1           16.8           13.7           0.29
----------------------------------------------------------------------------
RO16-06          22.9           32.0            9.1           0.22
----------------------------------------------------------------------------
RO16-08           0.0           12.2           12.2           0.32
----------------------------------------------------------------------------
RO16-09           9.1           100.6          91.4           0.15
----------------------------------------------------------------------------
Incl.      53.3           56.4            3.1           1.67
----------------------------------------------------------------------------
RO16-10           6.1           100.6          94.5           0.12
----------------------------------------------------------------------------
RO16-10          62.5           71.6            9.2           0.29
----------------------------------------------------------------------------
RO16-15          12.2           48.8           36.6           0.50
----------------------------------------------------------------------------
Incl.      25.9           27.4            1.5           1.68
----------------------------------------------------------------------------
and Incl.         45.7           47.2            1.5           2.50
----------------------------------------------------------------------------
RO16-16          10.7           48.8           38.1           0.31
----------------------------------------------------------------------------
Incl.      39.6           41.2            1.5           1.26
----------------------------------------------------------------------------
(i)True thickness estimated to be 70-90% of drill intercepts

/T/

The Hudbay Zone is identified by a 1.3 km long gold-silver-tungsten-molybdenum 
(Au-Ag-W-Mo) soil-geochemical anomaly that is open to the north and west. 
Hudbay was previously tested by mechanical trenching which yielded results of 
1.5 g/t Au over 20 m, 6.2 g/t Au over 5 m and 0.35 g/t Au over 81 m as noted in 
Taku's news release on September 12, 2012.

Drill holes RO16-15 and RO16-16, located in the northern portion of the Hudbay 
anomaly returned the most encouraging results. RO16-15 intersected 0.50 g/t Au 
over 36.6 m, including 2.50 g/t Au over 1.5 m. RO16-16 intersected 0.31 g/t Au 
over 38.1 m, including 1.26 g/t Au over 1.5 m. Both intercepts are hosted 
within a quartz biotite schist and are spatially associated with increased 
concentrations of massive quartz veins. Sulphides are rare and typically absent 
within the mineralized zones. These two drill holes occur on the northeast 
margin of a structurally bounded, magnetic anomaly that measures 450 m x 450 m. 
Coincident with this geophysical target is the Au-Ag-W-Mo soil anomaly that is 
open to the west in an area that has not been geochemically sampled or 
geophysically surveyed. The Company plans to fully define the western extent of 
this Zone by collecting grid-style soil samples and expanding upon the existing 
geophysical dataset in 2017 with the intent to define drill targets.

The remaining drill holes focused on the southern half of the Hudbay Zone and 
variably intersected broad zones of gold mineralization such as RO16-09 which 
returned 0.15 g/t Au over 91.4 m, including 1.67 g/t Au over 3.1 metres.

The first drill program at the Hudbay Zone focused on the gold-rich portion of 
the soil geochemical anomaly and is encouraging as it identifies a positive 
correlation between an increase in quartz veining and gold mineralization.

The Hudbay Zone is underlain primarily by metasedimentary rocks, situated on 
the western margin of a north-trending potassium feldspar rich orthogneiss 
unit. Mineralization appears to have a stronger association with the 
metasedimentary package which is comprised of quartz biotite schist and 
quartzite, with minor orthogneiss. Both rock types are cross cut by shallowly 
south-dipping quartz veins that are aligned within a shallowly south-dipping, 
pervasive foliation.

The Rosebute Property is located approximately 58 km south of Dawson City, 
Yukon and approximately 29 km north of the Golden Saddle Deposit owned by 
Kinross Gold Corporation. The Property is contiguous to the west of the 
Company's Henderson project, and is situated in close proximity to the northern 
access road proposed by Goldcorp that will provide access to the multi-million 
ounce Coffee gold deposit.

All samples were submitted to SGS Minerals Services in Burnaby, BC for sample 
preparation by crushing to 75% less than 2 millimetres, creation of a 250 g 
split, and then pulverizing to 85% passing 75 microns. Sample pulps are 
submitted for gold analysis with a 30 g fire assay and AAS finish (code 
GE-FAA313). Samples are also submitted for a 52 element analysis using an aqua 
regia digest and ICP-AES and ICP-MS analysis (GE-ICM14B). Control samples 
(accredited gold standards and blanks) were inserted into the sample sequence 
on a regular basis monitor precision of results.

David Gale, P.Geo., the Company's Qualified Person as defined by National 
Instrument 43-101 for the White Gold District, has reviewed the technical 
information in this news release and has approved the disclosure herein.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed mineral 
exploration company listed on the TSX Venture Exchange, with a portfolio of 
projects in the Yukon and the 3Ts Project in British Columbia. The Company's 
holdings range from early stage grassroots exploration to advanced-stage 
resource expansion. For additional information, please visit the Company's 
website www.ingold.ca.

INDEPENDENCE GOLD CORP.

Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release contains forward-looking statements and forward-looking 
information (collectively, "forward-looking statements") within the meaning of 
applicable Canadian securities legislation. All statements, other than 
statements of historical fact, included herein are forward-looking statements. 
Although the Company believes that such statements are reasonable, it can give 
no assurance that such expectations will prove to be correct. The Company 
cautions investors that any forward-looking statements by the Company are not 
guarantees of future results or performance, and that actual results may differ 
materially from those in forward-looking statements as a result of various 
factors. All of the Company's public disclosure filings may be accessed via 
www.sedar.com. Readers are urged to review these materials, including the 
technical reports filed with respect to the Company's mineral properties.

- 30 -

CONTACT INFO:

Independence Gold Corp.
Investor Relations
604-687-3959
info@ingold.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=580132744