Source	MARKET NEWS
Date	10/18/2017
Time	05:19:32 AM

Company	 Dios Exploration Inc.
Title	Dios Au33 
Project: CLN Gold Showing Yielded Up T





    CDNX Symbol: DOS











Press Release





DIOS EXPLORATION INC ("DOS-V")
- Dios Au33 Project: CLN Gold Showing Yielded Up To 12.55 G/t Au

DIOS EXPLORATION(TSX VENTURE:DOS) reports the CLN (Chain Lake
North) gold showingreturned gold assays in grams/ton up to 12.55; 6.64;
4.66; 4.45; 2.01; 1.98 g/t Au along a 75 meter strikein the lower part
of a cliff along the eastwest mineralized altered structure (eight
samples out of nine taken assaying over 0.5 g/t Au).

Mineralization is typically a 5 to 15 m wide foliated altered zone
(alternating cm biotite-rich/quartz-pyrite-magnetite with potassic
feldspar bands) in tonalites. Pyrite contents of foliated zone vary
from 1 to 10%, averaging 2-5% with some local magnetite (nil-2%).

Previous CLN sampling on the upper south part of this 10 m high
cliff yielded values of 2.23; 2.56; 5.15 and 12.65 g/t Au. The CLN zone
is quite similar to the Heberto gold zone about 2 km south (4.8 g/t
gold over 8.65 m and 3.7 g/t gold over 13 m true widths), but striking
differently with a steeper attitude. The CLN zone is bordered to the
north by hematized magnetic tonalite along a regional eastwest (Chain
Lake) structure. The low magnetic Chain Lake structure is characterized
by strong gold in soil anomalies (B horizon): 13 to 300 ppb gold
including several values of 40 to 59 and 93, 102, 176, 300 ppb gold.

Samples were collected and assayed at ALS Val d'Or under
supervision of Harold Desbiens, M.Sc. Geo 43-101 QP. DIOS Au33 property
is located in James Bay, Quebec, 55 km south of large Eleonore gold
deposit and 15 km west of Clearwater gold deposit.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for DOS-V
Date: 2017/10/17
Closing Price: 0.08

TEL:  (514) 923-9123  Marie-Jose Girard, 43-101 QP, President & CEO
DIOS Exploration Inc.
EMAIL:  mjgirard@diosexplo.com
INTERNET:  www.diosexplo.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1729000002TS11729000732-05160020171018