Source	Marketwire
Date	10/18/2017
Time	05:01:01 AM

Company	 RADISSON MINING RESOURCES INC.
Title	Radisson extends the Vintage Zone to 325 m along strike with an intercept 
of 9.7 g/t gold over 2.9 m at the O'Brien project





    CDNX Symbol: RDS











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Radisson Mining Resources Inc.

TSX VENTURE SYMBOL: RDS
OTC PINK SYMBOL: RMRDF

October 18, 2017

Radisson extends the Vintage Zone to 325 m along strike with an intercept of 
9.7 g/t gold over 2.9 m at the O'Brien project


ROUYN-NORANDA, QUEBEC--(Marketwired - Oct. 18, 2017) - Radisson Mining 
Resources Inc. (TSX VENTURE:RDS)(OTC:RMRDF) ("Radisson" or the "Company") is 
pleased to announce that hole OB-17-48 has successfully extended the Vintage 
zone by additional 125 m along strike at the O'Brien gold project. The project 
is located along the Cadillac Break halfway between Rouyn-Noranda and Val-d'Or 
in Quebec, Canada. The Vintage zone is parallel to, and to the north of bulk of 
current resources at the O'Brien project. The zone is located only 85 meters 
north of the Cadillac Break in a context that is similar to producing and 
historical mines in the Cadillac mining camp. The structure has been traced by 
drilling on over 325 meters strike length from East to West, vertical height of 
up to 360 meters and remains open in all directions.

Press release highlights:

/T/

--  Hole OB-17-48 extended the Vintage Zone by over 125 meters along strike
with intercept of 9.7 g/t Au over 2.9 m at 208 meters below surface.
Assays are pending for the final portion of Hole OB-17-48. (See figure
1)

--  The Vintage Zone has been traced over a strike length of 325 meters and
vertical height of up 360 meters.

--  Additional drill results are expected from Hole OB-17-49 completed in
vertical extension of Hole OB-17-42, which returned 13.7 g/t Au over 1.5
meters. (See October 3rd, 2017 Press release)

/T/

Mario Bouchard, President and CEO commented: "Current exploration results 
continue to increase the overall dimension of the Vintage Zone. The Zone as now 
been traced on over 325 meters and remains open in all directions. Due to its 
high grade potential and proximity to current resources, the Vintage Zone has 
the potential to be an important part of O'Brien's exploration and development 
plan. As we await final results from the drill program completed this summer on 
the Vintage Zone, we are currently planning a drill program in order to test 
lateral and at depth extension of this zone."

Table 1 Drilling results summary

/T/

----------------------------------------------------------------------------
Drill hole      From      To  Length     Grade (g/t)        Interpreted zone
----------------------------------------------------------------------------
(m)     (m)     (m)              Au
----------------------------------------------------------------------------
OB-17-46        86.0    88.5     2.5             4.4         Piche Volcanics
----------------------------------------------------------------------------
Including       88.0    88.5     0.5            15.9   Piche Volcanics (i)VG
----------------------------------------------------------------------------
OB-17-48       208.6   211.5     2.9             9.7          Cadillac wacke
----------------------------------------------------------------------------
OB-17-48       260.0   260.5     0.5         PENDING    Cadillac wacke (i)VG
----------------------------------------------------------------------------
(i)VG; Denotes presence of visible gold
Note; Results are presented as down hole width; true width are estimated
between 55 to 70% of down hole thickness.

/T/

Vintage zone exploration program

As the company is waiting for final results from the drill program completed on 
the Vintage Zone, review of current results and historical exploration programs 
from the Vintage Zone is progressing in order to define a second phase 
exploration program.

The Vintage zone is a parallel zone of the O'Brien project located 
approximately 85 meters north of the Cadillac Break in the Cadillac Group of 
meta-sediments comprising sequence of polymictic conglomerate, banded iron 
formation (BIF) and grauwacke. In comparison, current resources of 36E and 
Kewagama zones are located in the Piche Group, south of the Cadillac Break. The 
Vintage zone saw small historical exploration programs, which were never 
followed upon. In 2017, the company established several high-priority 
exploration drill targets through historical data compilation in this area of 
the O'Brien gold project. The first six drill holes that tested these targets 
were completed over a strike length of 325 meters. The new info added to the 
few available historical information helps to demonstrate the continuity and 
the favourable geometry of the Vintage zone. All intercepts remain open in all 
direction.

2017 drill program completed at 20,000 meters, 10,500 meters in assays pending

Furthermore, the company announces that it has completed the drill program 
planned in 2017 to approximate total of 20,000 meters. The drill program was 
completed with two main objectives. An approximate total of 15,000 meters was 
completed for resource expansion from surface to a depth of 500 meters. As a 
second objective, the approximate 5,000 meters exploration drill program 
completed, focused on high-priority exploration targets defined outside the 
main sector of current resources of the O'Brien gold project, including the 
Vintage Zone.

There are currently 20 drill holes in assays pending for a total an approximate 
total of 10,500 meters.

All drill cores in this campaign are NQ in size. Assays were completed on sawn 
half-cores, with the second half kept for future reference. The samples were 
analyzed using standard fire assay procedures with Atomic Absorption (AA) 
finish at Swastika Laboratories Ltd, in Swastika, Ontario. Samples yielding a 
grade higher than 5 g/t were analyzed a second time by fire assay with 
gravimetric finish at the same laboratory. Samples containing visible gold were 
analyzed with metallic sieve procedure. Standard reference materials and blank 
samples were inserted prior to shipment for quality assurance and quality 
control (QA/QC) program.

Qualified Person

Tony Brisson, P. Geo, independent consultant, acts as a Qualified Person as 
defined in National Instrument 43-101 and has reviewed and approved the 
technical information in this press release.

About Radisson Mining Resources Inc.

Radisson is a Quebec-based mineral exploration company. The O'Brien project, 
cut by the regional Cadillac Break, is Radisson's flagship asset. The project 
hosts the former O'Brien Mine, considered to have been the Abitibi Greenstone 
Belt's highest-grade gold producer during its production (1,197,147 metric tons 
at 15.25 g/t Au for 587,121 ounces of gold from 1926 to 1957; InnovExplo, April 
2015).

For more information on Radisson, visit our website at www.radissonmining.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements: This press release may contain certain 
forward-looking information. All statements included herein, including the 
scheduled Closing date, but other than statements of historical fact, is 
forward-looking information and such information involves various risks and 
uncertainties. There can be no assurance that such information will prove to be 
accurate, and actual results and future events could differ materially from 
those anticipated in such information. A description of assumptions used to 
develop such forward-looking information and a description of risk factors that 
may cause actual results to differ materially from forward looking information 
can be found in Radisson's disclosure documents on the SEDAR website at 
www.sedar.com.

- 30 -

CONTACT INFO:

Hubert Parent-Bouchard
Corporate Development
819-763-9969
hpbouchard@radissonmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=599647741


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Radisson Mining Resources Inc.

TSX VENTURE SYMBOL: RDS
OTC PINK SYMBOL: RMRDF

October 18, 2017

Radisson extends the Vintage Zone to 325 m along strike with an intercept of 
9.7 g/t gold over 2.9 m at the O'Brien project


ROUYN-NORANDA, QUEBEC--(Marketwired - Oct. 18, 2017) - Radisson Mining 
Resources Inc. (TSX VENTURE:RDS)(OTC:RMRDF) ("Radisson" or the "Company") is 
pleased to announce that hole OB-17-48 has successfully extended the Vintage 
zone by additional 125 m along strike at the O'Brien gold project. The project 
is located along the Cadillac Break halfway between Rouyn-Noranda and Val-d'Or 
in Quebec, Canada. The Vintage zone is parallel to, and to the north of bulk of 
current resources at the O'Brien project. The zone is located only 85 meters 
north of the Cadillac Break in a context that is similar to producing and 
historical mines in the Cadillac mining camp. The structure has been traced by 
drilling on over 325 meters strike length from East to West, vertical height of 
up to 360 meters and remains open in all directions.

Press release highlights:

/T/

--  Hole OB-17-48 extended the Vintage Zone by over 125 meters along strike
with intercept of 9.7 g/t Au over 2.9 m at 208 meters below surface.
Assays are pending for the final portion of Hole OB-17-48. (See figure
1)

--  The Vintage Zone has been traced over a strike length of 325 meters and
vertical height of up 360 meters.

--  Additional drill results are expected from Hole OB-17-49 completed in
vertical extension of Hole OB-17-42, which returned 13.7 g/t Au over 1.5
meters. (See October 3rd, 2017 Press release)

/T/

Mario Bouchard, President and CEO commented: "Current exploration results 
continue to increase the overall dimension of the Vintage Zone. The Zone as now 
been traced on over 325 meters and remains open in all directions. Due to its 
high grade potential and proximity to current resources, the Vintage Zone has 
the potential to be an important part of O'Brien's exploration and development 
plan. As we await final results from the drill program completed this summer on 
the Vintage Zone, we are currently planning a drill program in order to test 
lateral and at depth extension of this zone."

Table 1 Drilling results summary

/T/

----------------------------------------------------------------------------
Drill hole      From      To  Length     Grade (g/t)        Interpreted zone
----------------------------------------------------------------------------
(m)     (m)     (m)              Au
----------------------------------------------------------------------------
OB-17-46        86.0    88.5     2.5             4.4         Piche Volcanics
----------------------------------------------------------------------------
Including       88.0    88.5     0.5            15.9   Piche Volcanics (i)VG
----------------------------------------------------------------------------
OB-17-48       208.6   211.5     2.9             9.7          Cadillac wacke
----------------------------------------------------------------------------
OB-17-48       260.0   260.5     0.5         PENDING    Cadillac wacke (i)VG
----------------------------------------------------------------------------
(i)VG; Denotes presence of visible gold
Note; Results are presented as down hole width; true width are estimated
between 55 to 70% of down hole thickness.

/T/

Vintage zone exploration program

As the company is waiting for final results from the drill program completed on 
the Vintage Zone, review of current results and historical exploration programs 
from the Vintage Zone is progressing in order to define a second phase 
exploration program.

The Vintage zone is a parallel zone of the O'Brien project located 
approximately 85 meters north of the Cadillac Break in the Cadillac Group of 
meta-sediments comprising sequence of polymictic conglomerate, banded iron 
formation (BIF) and grauwacke. In comparison, current resources of 36E and 
Kewagama zones are located in the Piche Group, south of the Cadillac Break. The 
Vintage zone saw small historical exploration programs, which were never 
followed upon. In 2017, the company established several high-priority 
exploration drill targets through historical data compilation in this area of 
the O'Brien gold project. The first six drill holes that tested these targets 
were completed over a strike length of 325 meters. The new info added to the 
few available historical information helps to demonstrate the continuity and 
the favourable geometry of the Vintage zone. All intercepts remain open in all 
direction.

2017 drill program completed at 20,000 meters, 10,500 meters in assays pending

Furthermore, the company announces that it has completed the drill program 
planned in 2017 to approximate total of 20,000 meters. The drill program was 
completed with two main objectives. An approximate total of 15,000 meters was 
completed for resource expansion from surface to a depth of 500 meters. As a 
second objective, the approximate 5,000 meters exploration drill program 
completed, focused on high-priority exploration targets defined outside the 
main sector of current resources of the O'Brien gold project, including the 
Vintage Zone.

There are currently 20 drill holes in assays pending for a total an approximate 
total of 10,500 meters.

All drill cores in this campaign are NQ in size. Assays were completed on sawn 
half-cores, with the second half kept for future reference. The samples were 
analyzed using standard fire assay procedures with Atomic Absorption (AA) 
finish at Swastika Laboratories Ltd, in Swastika, Ontario. Samples yielding a 
grade higher than 5 g/t were analyzed a second time by fire assay with 
gravimetric finish at the same laboratory. Samples containing visible gold were 
analyzed with metallic sieve procedure. Standard reference materials and blank 
samples were inserted prior to shipment for quality assurance and quality 
control (QA/QC) program.

Qualified Person

Tony Brisson, P. Geo, independent consultant, acts as a Qualified Person as 
defined in National Instrument 43-101 and has reviewed and approved the 
technical information in this press release.

About Radisson Mining Resources Inc.

Radisson is a Quebec-based mineral exploration company. The O'Brien project, 
cut by the regional Cadillac Break, is Radisson's flagship asset. The project 
hosts the former O'Brien Mine, considered to have been the Abitibi Greenstone 
Belt's highest-grade gold producer during its production (1,197,147 metric tons 
at 15.25 g/t Au for 587,121 ounces of gold from 1926 to 1957; InnovExplo, April 
2015).

For more information on Radisson, visit our website at www.radissonmining.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements: This press release may contain certain 
forward-looking information. All statements included herein, including the 
scheduled Closing date, but other than statements of historical fact, is 
forward-looking information and such information involves various risks and 
uncertainties. There can be no assurance that such information will prove to be 
accurate, and actual results and future events could differ materially from 
those anticipated in such information. A description of assumptions used to 
develop such forward-looking information and a description of risk factors that 
may cause actual results to differ materially from forward looking information 
can be found in Radisson's disclosure documents on the SEDAR website at 
www.sedar.com.

- 30 -

CONTACT INFO:

Hubert Parent-Bouchard
Corporate Development
819-763-9969
hpbouchard@radissonmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=599647741