Source	MARKET NEWS
Date	10/18/2017
Time	05:19:33 AM

Company	 Radisson Mining Resources Inc.
Title	Extends The Vintage Zone To 325 M Along Strike W





    CDNX Symbol: RDS











Press Release





Extends The Vintage Zone To 325 M Along Strike With An Intercept Of9.7 G/T 
Gold Over 2.9 M At The O'brien Project --->@NEWS RELEASE
RADISSON MINING RESOURCES INC ("RDS-V")
- Extends The Vintage Zone To 325 M Along Strike With An
- Intercept Of 9.7 G/T Gold Over 2.9 M At The O'brien Project

Radisson Mining Resources Inc. ("Radisson" or the "Company") is
pleased to announce that hole OB-17-48 has successfully extended the
Vintage zone by additional 125 m along strike at the O'Brien gold
project. The project is located along the Cadillac Break halfway
between Rouyn-Noranda and Val-d'Or in Quebec, Canada. The Vintage zone
is parallel to, and to the north of bulk of current resources at the
O'Brien project. The zone is located only 85 meters north of the
Cadillac Break in a context that is similar to producing and historical
mines in the Cadillac mining camp. The structure has been traced by
drilling on over 325 meters strike length from East to West, vertical
height of up to 360 meters and remains open in all directions.

Press release highlights:

//st

* Hole OB-17-48 extended the Vintage Zone by over 125 meters along strike
with intercept of 9.7 g/t Au over 2.9 m at 208 meters below surface.
Assays are pending for the final portion of Hole OB-17-48. (See figure 1)

//et

//st

* The Vintage Zone has been traced over a strike length of 325 meters and
vertical height of up 360 meters.

//et

//st

* Additional drill results are expected from Hole OB-17-49 completed in
vertical extension of Hole OB-17-42, which returned 13.7 g/t Au over 1.5
meters. (See October 3rd, 2017 Press release)

//et

Mario Bouchard, President and CEO commented: "Current exploration
results continue to increase the overall dimension of the Vintage Zone.
The Zone as now been traced on over 325 meters and remains open in all
directions. Due to its high grade potential and proximity to current
resources, the Vintage Zone has the potential to be an important part
of O'Brien's exploration and development plan. As we await final
results from the drill program completed this summer on the Vintage
Zone, we are currently planning a drill program in order to test
lateral and at depth extension of this zone."

Table 1 Drilling results summary

//st

Drill hole   From    To      Length   Grade (g/t)   Interpreted zone

(m)     (m)     (m)      Au

OB-17-46     86.0    88.5    2.5      4.4           Piche Volcanics

Including    88.0    88.5    0.5      15.9          Piche Volcanics *VG

OB-17-48     208.6   211.5   2.9      9.7           Cadillac wacke

OB-17-48     260.0   260.5   0.5      PENDING       Cadillac wacke *VG

//et

//st

*VG; Denotes presence of visible gold

Note; Results are presented as down hole width; true width are estimated
between 55 to 70% of down hole thickness.

//et

Vintage zone exploration program

As the company is waiting for final results from the drill program
completed on the Vintage Zone, review of current results and historical
exploration programs from the Vintage Zone is progressing in order to
define a second phase exploration program.

The Vintage zone is a parallel zone of the O'Brien project located
approximately 85 meters north of the Cadillac Break in the Cadillac
Group of meta-sediments comprising sequence of polymictic conglomerate,
banded iron formation (BIF) and grauwacke. In comparison, current
resources of 36E and Kewagama zones are located in the Piche Group,
south of the Cadillac Break. The Vintage zone saw small historical
exploration programs, which were never followed upon. In 2017, the
company established several high-priority exploration drill targets
through historical data compilation in this area of the O'Brien gold
project. The first six drill holes that tested these targets were
completed over a strike length of 325 meters. The new info added to the
few available historical information helps to demonstrate the
continuity and the favourable geometry of the Vintage zone. All
intercepts remain open in all direction.

2017 drill program completed at 20,000 meters, 10,500 meters in
assays pending

Furthermore, the company announces that it has completed the drill
program planned in 2017 to approximate total of 20,000 meters. The
drill program was completed with two main objectives. An approximate
total of 15,000 meters was completed for resource expansion from
surface to a depth of 500 meters. As a second objective, the
approximate 5,000 meters exploration drill program completed, focused
on high-priority exploration targets defined outside the main sector of
current resources of the O'Brien gold project, including the Vintage
Zone.

There are currently 20 drill holes in assays pending for a total
an approximate total of 10,500 meters.

All drill cores in this campaign are NQ in size. Assays were
completed on sawn half-cores, with the second half kept for future
reference. The samples were analyzed using standard fire assay
procedures with Atomic Absorption (AA) finish at Swastika Laboratories
Ltd, in Swastika, Ontario. Samples yielding a grade higher than 5 g/t
were analyzed a second time by fire assay with gravimetric finish at
the same laboratory. Samples containing visible gold were analyzed with
metallic sieve procedure. Standard reference materials and blank
samples were inserted prior to shipment for quality assurance and
quality control (QA/QC) program.

Qualified Person

Tony Brisson, P. Geo, independent consultant, acts as a Qualified
Person as defined in National Instrument 43-101 and has reviewed and
approved the technical information in this press release.

About Radisson Mining Resources Inc.

Radisson is a Quebec-based mineral exploration company. The
O'Brien project, cut by the regional Cadillac Break, is Radisson's
flagship asset. The project hosts the former O'Brien Mine, considered
to have been the Abitibi Greenstone Belt's highest-grade gold producer
during its production (1,197,147 metric tons at 15.25 g/t Au for
587,121 ounces of gold from 1926 to 1957; InnovExplo, April 2015).

For more information on Radisson, visit our website at
www.radissonmining.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-Looking Statements: This press release may contain certain
forward-looking information. All statements included herein, including
the scheduled Closing date, but other than statements of historical
fact, is forward-looking information and such information involves
various risks and uncertainties. There can be no assurance that such
information will prove to be accurate, and actual results and future
events could differ materially from those anticipated in such
information. A description of assumptions used to develop such
forward-looking information and a description of risk factors that may
cause actual results to differ materially from forward looking
information can be found in Radisson's disclosure documents on the
SEDAR website at www.sedar.com.

TSX Venture closing price for RDS-V
Date: 2017/10/17
Closing Price: 0.15

TEL:  819-763-9969  Hubert Parent-Bouchard, Corporate Development
EMAIL:  hpbouchard@radissonmining.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1729000005TS11729000740-05160220171018