Source	MARKET NEWS
Date	10/03/2017
Time	05:52:02 AM

Company	 Algold Resources Ltd.
Title	Extends 
High Grade Salma Vein to 3 km Strike





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDF-0")
- Extends High Grade Salma Vein to 3 km Strike

ALGOLD RESOURCES LTD. ("Algold" or the "Corporation") today
announced assay results, including high grade values of 100 g/t Au and
89 g/t Au, from rock chip panel (1m(2)) sampling carried out on the new
Salma vein at the Corporation's Tijirit project in Mauritania. Assay
results from the samples, which were gathered during recent systematic
50 meters spaced pitting and trenching exploration activities, extend
the known gold mineralized structure to 3 kilometers on strike.

Highlights
* 100 g/t Au - In-pit (10 meters below the surface), 1 m(2) panel sample
* 100 g/t Au - In-pit (7 meters below the surface), 1 m(2) panel sample
* 88.9 g/t Au - In-pit (9.5 meters below the surface), 1 m(2) panel sample
* 25 samples grading higher than 10 g/t Au - 1 m(2) panel samples
* 75 samples grading higher than 1.0 g/t Au - 1 m(2) panel samples
* Average grade of 10.0 g/t Au (104 rock chip samples)
* Average grade of 13.3 g/t Au for samples grading )1 g/t Au (75 rock chip
samples)
Trenching and Pitting Program

Assay results grading up to 100 g/t Au and 88.9 g/t Au were
recorded from a series of pits dug over a 3 kilometers strike (Figure 1
(https://www.globenewswire.com/Tracker?data=r9WvnZe8SuoB5BN4If8mBSknTWsaI6u
S3QoEYl2iAS1H6AQT4m1iT6EVkkLxe-mbKEHDohDeX70QbDKL44uziTituZtVfz92bUmzLMoCR5
K8wYUpeUR8MELtKfTLySAcuG5SUb9dPPNENY1_jQefjw==)). The Salma vein
represents the newest high-grade discovery at Tijirit, located only
five kilometers from the Eleonore and the Lily veins. The Salma vein
has now been traced over a three-kilometer-long mineralized gold
structure situated on the prospective granite-greenstone contact zone.
Results from the Salma vein were not included in Algold's most recent
NI 43-101 technical report.
The results from the rock-chip-sampling program continue to
demonstrate the significant potential for the identification of
additional high-grade gold zones throughout the more than
25-kilometer-long Eleonore corridor. The 104 rock chip samples, which
were gathered over an area of 1x1 meters, taken at the base of a series
of 1-to-10-meter-deep pits, were collected during detailed mapping
traverses. Importantly, of the 104 samples, 25 samples assayed graded
higher than 10 g/t Au with 75 grading over 1.0 g/t Au.

The pitting and trenching sampling was carried out during the
month of August 2017, concurrently to Algold's Phase III drilling
program, which also concluded during the month. Algold expects to
receive additional results from its Phase III drilling program assays
in the coming weeks, approximately 5,000 of which are still pending.

Granite Contact Zone
The eastern boundary of this contact is located 3.6 kilometers
east of Eleonore and extends to the north for approximately nine
kilometers. Auriferous quartz veins have been identified over much of
this contact, located within a potential "pressure shadow" setting. All
of these results are sited outside the area of the mineral resources
currently defined on the property (reference: Algold's press release
dated June 15, 2017).

"These results highlight the compelling potential of the new Salma
vein to rapidly add substantial high-grade resources at the Tijirit
Project," said Algold CEO, Francois Auclair. "We continue to focus on
building and expanding upon the existing and new mineralized zones,
which are all within very close proximity."

Detailed geological descriptions of all mineralized zones can be
found on Algold's website (www.algold.com) and on SEDAR (www.sedar.com)
in the report entitled "Algold 43-101 Technical Report: Tijirit Maiden
Mineral Resources Estimates for the Tijirit Gold Project in
Mauritania".

Quality Assurance / Quality Control (QA/QC)
Analytical work for drill core and chips, geochemical samples and
rock chip samples is being carried out at the independent SGS
Laboratories Ltd. in Bamako, Mali. The 50 g fire assay with ASS finish
analytical services are accredited by SANAS and are carried out with a
quality assurance protocol in line with ISO 17025:2005. Samples are
stored at the Corporation's field camps and put into sealed bags until
delivered by a geologist on behalf of Algold to the laboratory in
Bamako, Mali, where samples are prepared and analyzed. Samples are
logged in the tracking system, weighed, dried and finely crushed to
better than 70%, passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A
split of up to 1,000 g is taken and pulverized to better than 85%,
passing a 75-micron (Tyler 200 mesh) screen, and a 50-gram split is
analyzed by fire assay with an AA finish.

This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andr Ciesielski, DSc., PGeo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by
NI43-101Standards of Disclosure for Mineral Projects. Andre Ciesielski
has further approved the scientific and technical disclosure in the
news release.

ABOUT ALGOLD
Algold Resources Ltd. is focused on the exploration and
development of gold deposits in West Africa. The board of directors and
management team are seasoned resource industry professionals with
extensive experience in the exploration and development of world-class
gold projects in Africa. Neither TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in policies of
the TSX Venture Exchange) accepts responsibility for the adequacy or
accuracy of this release.



Algold Resources Ltd.
1320, boul. Graham, Suite 132, Mont-Royal, Qubec, H3P 3C8, www.algold.com

Franois Auclair M.Sc., PGeo
President & Chief Executive Officer
f.auclair@algold.com
+1 (514) 889 5089

Alex Ball
Executive VP, Finance and Corporate Development
a.ball@algold.com
+1 (647) 919 2227



//st

Table 1 - Gold Assay Results (Reference: Figure 1)

Sample East-  North-  Au    Descrip- Comments      Strike (RHR) Dip
ID     ing    ing     (g/t) tion
UTm    UTM
A10118 487283 2257314 100.0 Qtz vein 11 meter pit  176
A10180 487513 2258923 100.0 Qtz vein 7.2 meter pit 170
A10176 487543 2258771  88.9 Qtz vein 9.5 meter pit 115           52
A10183 487307 2258309  53.9 Qtz vein 5 meter pit   180           44
A10184 487288 2258355  52.7 Qtz vein 4 meter pit   170           60
A10188 487284 2258403  39.2 Qtz vein 5 meter pit   164
A10123 487282 2257373  33.4 Qtz vein 8 meter pit   184
A10114 487274 2257258  31.8 Qtz vein 8.5 meter pit 190           50
A10101 486924 2256066  31.5 Qtz vein 7.3 meter pit 170           50
A10156 487406 2258112  29.2 Qtz vein 7.7 meter pit 182           42
A10103 486968 2256449  25.8 Qtz vein 7 meter pit   176
A10097 486911 2255830  23.0 Qtz vein 5 meter pit   170
A10119 487283 2257314  23.0 Qtz vein 11 meter pit  176
A10162 487409 2258219  23.0 Qtz vein 5 meter pit   165
A10126 487280 2257407  20.5 Qtz vein 10 meter pit  185
A10181 487307 2258309  19.9 Qtz vein 5 meter pit   180           44
A10186 487288 2258355  16.0 Qtz vein 4 meter pit   170           60
A10135 487355 2257600  15.1 Qtz vein 8.5 meter pit 182
A10130 487300 2257466  14.7 Qtz vein 7.5 meter pit 180
A10154 487406 2258112  14.1 Qtz vein 7.7 meter pit 182           42
A10165 487414 2258278  13.8 Qtz vein 7 meter pit   192           40
A10182 487307 2258309  13.6 Qtz vein 5 meter pit   180           44
A10134 487355 2257600  13.4 Qtz vein 8.5 meter pit 182
A10143 487361 2257827  11.4 Qtz vein 10 meter pit  185
A10159 487413 2258170  11.4 Qtz vein 5.3 meter pit 180           50
A10153 487406 2258112  9.69 Qtz vein 7.7 meter pit 182           42
A10115 487274 2257258  8.89 Qtz vein 8.5 meter pit 190           50
A10102 486927 2256061   8.6 Qtz vein 7.3 meter pit 170           50
A10116 487274 2257258  8.49 Qtz vein 8,5 meter pit 190           50
A10096 486911 2255830  7.83 Qtz vein 5 meter pit   170
A10124 487282 2257373  7.09 Qtz vein 8 meter pit   184
A10167 487414 2258278  6.85 Qtz vein 7 meter pit   192           40
A10125 487280 2257407  6.55 Qtz vein 10 meter pit  185
A10127 487280 2257407   5.9 Qtz vein 10 meter pit  185
A10094 486915 2255757   5.4 Qtz vein 6 meter pit   178
A10150 487391 2258016  5.36 Qtz vein 3 meter pit   166           52
A10099 486922 2255857   5.3 Qtz vein 3 meter pit   176           70




Sample East-  North-  Au    Descrip- Comments      Strike (RHR) Dip
ID     ing    ing     (g/t) tion
UTm    UTM
A10169 487425 2258381 5.09  Qtz vein 5.5 meter pit 162
A10108 487526 2257083 4.79  Qtz vein 8 meter pit   188           52
A10121 487282 2257373 4.78  Qtz vein 8 meter pit   184
A10155 487406 2258112 4.6   Qtz vein 7.7 meter pit 182           42
A10142 487361 2257827 4.59  Qtz vein 10 meter pit  185
A10193 487266 2258459 4.59  Qtz vein 3.2 meter pit 120           58
A10187 487288 2258355 4.38  Qtz vein 4 meter pit   170           60
A10192 487266 2258459 4.09  Qtz vein 3.2 meter pit 120           58
A10113 487274 2257258 4.07  Qtz vein 8.5 meter pit 190           50
A10122 487282 2257373 3.83  Qtz vein 8 meter pit   184
A10110 487526 2257083 3.82  Qtz vein 8 meter pit   188           52
A10107 487504 2256905 3.29  Qtz vein 7 meter pit   176
A10174 487440 2258441 3.17  Qtz vein 7.5 meter pit 220
A10095 486911 2255830 3.08  Qtz vein 5 meter pit   170
A10149 487393 2258019 3.04  Qtz vein 3 meter pit   166           52
A10160 487413 2258170 3.03  Qtz vein 5.3 meter pit 180           50
A10166 487414 2258278 2.85  Qtz vein 7 meter pit   192           40
A10104 487504 2256905 2.83  Qtz vein 7 meter pit   176
A10120 487283 2257314 2.78  Qtz vein 11 meter pit  176
A10141 487361 2257827 2.76  Qtz vein 10 meter pit  185
A10131 487331 2257509 2.64  Qtz vein 1 meter pit   185           40
A10191 487284 2258403 2.49  Qtz vein 5 meter pit   164
A10117 487283 2257314 2.24  Qtz vein 11 meter pit  176
A10146 487399 2257968 2.22  Qtz vein 6 meter pit   160           70
A10144 487361 2257827 2.11  Qtz vein 10 meter pit  185
A10145 487399 2257968 1.9   Qtz vein 6 meter pit   160           70
A10164 487409 2258219 1.83  Qtz vein 5 meter pit   165
A10190 487284 2258403 1.83  Qtz vein 5 meter pit   164
A10128 487280 2257407 1.58  Qtz vein 10 meter pit  185
A10189 487284 2258403 1.55  Qtz vein 5 meter pit   164
A10129 487300 2257466 1.53  Qtz vein 7.5 meter pit 180
A10140 487347 2257713 1.5   Qtz vein 2.4 meter pit 190           52
A10147 487399 2257968 1.33  Qtz vein 6 meter pit   160           70
A10112 487273 2257234 1.23  Qtz vein 5 meters pit  182           44
A10105 487504 2256905 1.22  Qtz vein 7 meter pit   176
A10158 487413 2258170 1.2   Qtz vein 5.3 meter pit 180           50
A10152 487401 2258064 1.08  Qtz vein 4.7 meter pit 196           60
A10179 487543 2258771 1.06  Qtz vein 9.5 meter pit 115           52
//et
______________________________________
_______________________________________________
TSX Venture closing price for ALG-V
Date: 2017/10/02
Closing Price: 0.18
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1727500015TS11727500917-05490320171003