Source	CANADA NEWSWIRE
Date	10/06/2017
Time	07:26:47 AM

Company	 Zonte Metals Inc.
Title	Zonte Announces Discovery at the Two Four Target and Results from Late
Summer Field Exploration Program at the McConnells Jest Project, Yukon
Territory.





    CDNX Symbol: ZON











Press Release




" BC-Zonte-TwoFourTarget   10-06 1689
News release via Canada NewsWire, Halifax 902-422-1411 -ME-

Attention Business Editors:
^Zonte Announces Discovery at the Two Four Target and Results from Late
Summer Field Exploration Program at the McConnells Jest Project, Yukon
Territory.@

TSXV - ZON
HALIFAX, Oct. 6, 2017 /CNW/ - Zonte Metals Inc. (TSXV: ZON) (the
"Company" or "Zonte") is pleased to announce the Phase 1 drill results as well
as highlights from the late summer 2017 field exploration program at its
McConnells Jest Project located in the Yukon Territory. Highlights include:
<<

--  Drilling on the Two Four Target which returned:
o 32.02m of 0.49 g/t Au in MJ-04 from 45.80m, with 20.44 m of 0.72 g/t Au from
61.37m;
o 29.60m of 0.53 g/t Au in MJ-04 from 112.90m, with 20.28m of 0.69 g/t Au from
122.22m;
--  Discovery of high-grade mineralization at the Tea Zone Target where a
quartz-arsenopyrite vein returned 129 g/t Au; and
--  Discovery of the new J Zone Target where sampling of arsenopyrite veins
returned values up to 5.35 g/t Au.
>>
Phase 1 Drilling
A total of 1027 metres was drilled in five holes on three targets over a
small area of the pluton with the majority of the approximately 3,371 hectare
property remaining untested. Two holes were drilled on each of the Hill and
Two Four Targets with a single hole completed at the Pink Mountain Target.
Highlights from the drill program confirmed mineralization at the Two Four
Target as summarized in the table below. Both drill holes were drilled from
the same drill pad; MJ-03 was drilled at an azimuth of 335 degrees with a 65
degree dip and MJ-04 was drilled at an azimuth of 285 degrees with a 45 degree
dip. Results from MJ-03 returned anomalous gold values hosted in
quartz-arsenopyrite (+/- pyrite) veins over 100m of the drill core. Drill hole
MJ-04, drilled from the same pad, was drilled to a depth of 148.13m towards
the mapped edge of the pluton and past any known surface mineralization to
test a soil covered area. The drill hole stayed in the pluton over its length
and intersected upper and lower mineralized zones. A 20.45m interval in the
upper mineralized zone returned 0.72 g/t Au, within a 62.43m mineralized
interval. The lower zone, at the bottom of the drill hole, from 112.90 to
142.50m returned 0.53 g/t Au, including a 20.28m interval with 0.69 g/t Au.
This lower zone showed an increase in veining and had a higher proportion of
pyrite to arsenopyrite compared to the upper mineralized zone.

Drill
Hole           From (m)        To (m)        Interval (m)        Gold (g/t)
-----           -------         -----         -----------         ----------

MJ-03                     10.71         19.04                8.33            
0.20
-----                     -----         -----                ----            
----

107.49        214.27              106.78            0.18
------        ------              ------            ----

including          107.49        189.30               81.81            0.20
---------          ------        ------               -----            ----


MJ-04                     19.39         81.82               62.43            
0.27
-----                     -----         -----               -----            
----

including           45.80         81.82               32.02            0.49
---------           -----         -----               -----            ----

including           61.37         81.82               20.45            0.72
---------           -----         -----               -----            ----

112.90        142.50               29.60            0.53
------        ------               -----            ----

122.22        142.50               20.28            0.69
------        ------               -----            ----

134.49        142.50                8.01            1.13
------        ------                ----            ----

Note: depths and thicknesses listed in the table and throughout the press
release are core depths and the true thickness is not known at this time.
The surface projection of the mineralization intersected in the bottom
portion of MJ-04 may extend the target to the west under soil cover. The drill
holes at the Two Four were collared on the southern portion of the zone and
much of the target remains to be tested. Further exploration and drilling is
required to follow-up on these results. A map showing the drill hole locations
is found on the company's webpage www.zontemetals.com.
Drill core from the Pink Mountain Target was different in character to
the Two Four Target with reduced veining and more intense fracturing. Results
showed spotty anomalous gold values in several intervals. The single drill
hole was at the western end of the target which covers an area approximately
300m by 300m and further work is warranted on this target. Results from the
Hill Target were generally low.
Late Summer 2017 Field Exploration
Field exploration was primarily focused on the Pink Mountain, Hill and
Two Four Target areas for the majority of the summer. A one-day field trip was
completed to the Tea Zone where high-grade mineralization was discovered and
limited exploration was carried out to the north of Pink Mountain where the J
Zone was discovered.
At the Tea Zone target, on the north-western side of the pluton, outcrop
exposure was limited to a narrow valley where a number of veins were
identified at the southern end. One high-grade sample was collected from a
quartz-arsenopyrite vein which ranged from 5 to 10cm in width and assayed 129
g/t Au. Two other veins returned 0.92 g/t and 2.72 g/t Au in this area. Soil
geochemistry exhibits a multi-element anomaly which extends from the sampled
veins to the west for 390m and having at least 200m dimension in a north-south
orientation. No exploration was completed in this area with the multi-element
soil anomaly. Note the rock samples are grab samples, which are not
necessarily representative of mineralization hosted on the property.
The J Zone, formerly known as the Seven-Four target, was discovered this
summer after following up on a historic rock sample. This target lies about
1.3km north of Pink Mountain and is located within an area of the pluton with
dense fracturing. The zone is characterized by fracture hosted narrow
arsenopyrite veins. Sampling of the arsenopyrite veins returned values from
anomalous to 5.35 g/t Au. The mineralization which is exposed in a cliff face
appears to sit in a SW-NE structure that is 150m wide and over 500m long.
Additional soil sampling and more detailed rock sampling is required to
delineate this target. A number of other samples returned gold values in the
area between the J Zone and Pink Mountain targets, however, outcrop exposure
was poor and this larger area warrants detailed exploration. Note the rock
samples noted in the late summer exploration results are grab samples, which
are not necessarily representative of mineralization hosted on the property.
Much of the success in identifying targets was a result of following up
on historic soil and rock sampling. A number of other targets from that
historic data set were identified and remain to be field checked. One of the
largest and strongest is the 400m by 500m Big Quartz target where
multi-element soil geochemistry, including Au, As, Bi, Sb and W, illustrate a
large target on the western side of the pluton.
A map of the McConnel Jest Property, illustrating the multiple targets
identified to date, can be obtained on the Company's website at
www.zontemetals.com.
Terry Christopher, President and CEO of Zonte comments "During a short
field program, the Company was able to identity and drill three targets. The
Phase 1 drill results confirm the presence of an Intrusion Related Gold System
with the discovery at the Two Four Target. This discovery along with the
identification of a high-grade 129 g/t Au vein at the Tea Zone and the
discovery of gold mineralization at the J Zone confirms a widespread gold
system at the McConnells Jest Project. The successes to date have occurred
with limited exploration and the majority of the pluton remains to be
explored."
Qualified Person
Andy Randell, P.Geo. is the qualified person as defined by NI 43-101 and
is responsible for the preparation of the Technical Report and the technical
disclosures in this press release.
Rock and Protocol and Drill Sampling Protocol
See the June 9, 2017 news release for details on the surface rock
sampling protocol. All 2017 drill core samples were carried out in a careful
and diligent manner using scientifically established sampling practices
designed and tested to ensure that the results are representative and
reliable. All drill core was logged and prepared for shipment on site and
shipped to ALS in Whitehorse using a third-party contractor, under Zonte
personnel supervision. QA/QC included the systematic insertion of certified
standards, blanks and field duplicates. Samples were described, photographed,
tagged and sealed prior to being aggregated into rice bags and submitted for
analysis by ALS Global and analyzed for the ME-ICP41a package (34 element
ICP-AES) and AU-AA24 for gold (a 50 gram Fire Assay Au finish). ALS Global is
an independent, reputable and accredited full-service commercial laboratory
accredited to ISO/IEC 17025:2005. ALS Global also provides its own internal
QA/QC protocol of blanks, duplicates and standards in each work order, which
is supplied to the Zonte with the rock sample analysis.
About Zonte
Zonte Metals Inc. is a junior explorer focused on gold and copper. The
Company has signed an Option Agreement to acquire 100% of the McConnells Jest
project, in the Tintina Gold Belt, located in the Yukon Territory, which is
composed of 172 claims totaling approximately 3371 hectares, and holds the
drill ready Wings Point Gold Project located in Newfoundland and Labrador. In
addition, the Company and a Colombian partner have an application over open
areas sitting on top of the Gramalote Deposit in Colombia, which is held by
AngloGold Ashanti (NYSE: AU) and B2Gold (TSX: BTO, NYSE: BTG). The title
issuance is being contested by the state governing the application and the
Company has started legal action to protect its rights.
Forward-Looking Information
This news release contains forward-looking statements which include
statements regarding the Corporation's future plans, as well as statements
regarding financial and business prospects and the Corporation's future plans,
objectives or economic performance and financial outlooks. The Corporation
believes that the expectations reflected in this news release are reasonable
but actual results may be affected by a variety of variables and may be
materially different from the results or events predicted in the
forward-looking statements. Readers are therefore cautioned not to place undue
reliance on these forward-looking statements.
In evaluating forward-looking statements readers should consider the risk
factors which could cause actual results or events to differ materially from
those indicated by such forward-looking statements. These forward-looking
statements are made as of the date hereof, and unless otherwise required by
applicable securities laws, the Corporation does not intend nor does it
undertake any obligation to update or revise any forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy of accuracy of this release.

SOURCE Zonte Metals Inc.



View original content:
http://www.newswire.ca/en/releases/archive/October2017/06/c6022.html

-0-                           10/06/2017
/For further information: Terry Christopher, CEO and President,
902-405-3520, info(at)zontemetals.com, www.zontemetals.com/
/Web Site: www.zontemetals.com /
(ZON.)

CO:  Zonte Metals Inc.
ST:  Yukon
IN:  MNG PRM MIN
SU:

-30-