Source	MARKET NEWS
Date	10/10/2017
Time	10:28:48 AM

Company	 Sego Resources Inc.
Title	Diamond 
Drilling Program on Princeton Copper gol





    CDNX Symbol: SGZ











Press Release





SEGO RESOURCES INC ("SGZ-V")
- Diamond Drilling Program on Princeton Copper-gold Porphyry to Start
- October 17, 2017

Sego Resources Inc. ("Sego" or "the Company") will start a diamond
drill program on the Cuba Zone of its Miner Mountain Copper-Gold
Porphyry Project near Princeton, BC on October 17, 2017.

The drilling is planned with an initial two diamond drill holes
totalling 600 metres, with a goal of extending diamond drill holes 21
and 28 both laterally and at depth (see drill hole assays from this
area below).  Sego's geologists use handheld XRF devices to gain
real-time estimates of mineralization in the freshly-returned drill
core.  Based on the XRF results, Sego will extend the depths of any
holes that continue to show mineralization down-hole.  Further diamond
drilling will be planned based on the information gained.

The previous drill holes in this area were announced March 12,
2012 and are as follows:

"The assay results from west to east:

//st

* DDH 21 from 10.06m to 110.45m, 100.39m of 0.946% Cu, 0.55 g/t Au, 3.473
g/t Ag Including from 10.06 to 45.11m, 35.05m of 2.457% Cu, 1.35 g/t Au,
8.896 g/t Ag;

//et

(Twin of PDH 9 from 12 to 64 m, 1.264% Cu, 1.061 g/t Au, 3.79 g/t
Ag)

//st

* DDH 23 from 43.5m to 74.98m, 31.48m of 0.172% Cu, 0.228 g/t Au, 0.619 g/t
Ag Including from 62.79m to 74.98m, 12.19m of 0.3 % Cu, 0.469 g/t Au,
0.951 g/t Ag;

//et

(Twin of PDH 02 from 60 to 70 m, 0.355% Cu, 0.446 g/t Au, 1.2 g/t
Ag)

//st

* DDH 24 from 11.58 to 139.6m, 128.02m of 0.344% Cu, 0.296 g/t Au, 0.975
g/t Ag Including from 42.06m to 84.73m, 42.67m of 0.737% Cu, 0.751 g/t
Au, 1.57g/t Ag;

//et

(Twin of PDH 77 from 38 to 93m, 54m of 0.342% Cu with 0.473 g/t Au)

//st

* DDH 25 from 11.28m to 17.37m, 5.99m of 1.372% Cu, 0.677 g/t Au;

//et

(Twin of PDH 94 from 18 to 100m, 82m of 1.006% Cu, 0.576 g/t Au,
1.69 g/t Ag)

//st

* DDH 26 from 17.37m to 29.57m, 12.2m of 1.163% Cu, 0.759 g/t Au;

//et

(Twin of PDH 94 from 18 to 100m, 82m of 1.006% Cu, 0.576 g/t Au,
1.69 g/t Ag)

//st

* DDH 27 from 8.23 to 96.62m, 88.39m of 0.222% Cu, 0.192 g/t Au, 0.428 g/t
Ag Including from 60.05 to 78.33m, 18.28m of 0.546% Cu, 0.339 g/t Au,
0.733 g/t Ag;
* DDH 28 from 7.62 to 77.12m, 69.5m of 0.257% Cu, 0.193 g/t Au, 0.644 g/t
Ag Including from 38.1 to 62.48, 24.38m of 0.451% Cu, 0.32 g/t Au, 0.9
g/t Ag.

//et

Final two intervals of DDH 28 from 199.64m to 205.74m are 3m of
4233 ppm Cu, 117.9 ppb Au, and 3m of 5890 ppm Cu with 259 ppb Au,
respectively.

Geology

Core logging has indicated the presence of a large package of
highly altered Nicola group volcanics (flows and tuffs) to a depth of
300 metres. Alteration varies in intensity from whole rock replacement
to lightly altered rock with preserved textures. Alteration styles
identified in hand specimen, included potassic, albitic, and
propylitic, which have also been identified in thin section from
previous drilling. Overprinting all is gypsum-albite-calcite-pyrite in
a late stage event which crosscuts all other alteration/mineralization.


Mineralization ranges from chalcopyrite-bornite pyrite to
chalcopyrite-pyrite, to pyrite only.  At the highest grades,
chalcopyrite and bornite occur in fine grained net-textured to massive
disseminations throughout the rock, at lower grades they preferentially
replace the mafic minerals in volcanics. Notably the highest grade
material is closer to surface in most drill holes. Pyrite is ubiquitous
outside the highest grade material, occurring with chalcopyrite in
veins, as fracture fillings as replacements of mafic minerals or as
fine grained disseminations. In the gypsum-calcite-albite phase
described above the amount of pyrite can be over 10% in select
intervals.

The drilling indicates that mineralization remains open in all
directions.  Further work will look to expand the near surface
mineralization, and to explore below the current level of drilling
where alteration/geophysics suggests a large target remains to be
tested."

The Miner Mountain Project is an extensive alkalic copper-gold
porphyry system near Princeton, BC.  The ease of access and limited
snowfall has made winter drilling possible in previous drill campaigns
conducted by Sego.  Sego has a 5 year area-based permit and an
excellent working relationship with the local community and First
Nations.

This News Release was reviewed and approved by V.A. Preto Ph.D.,
P. Eng. and Selina Tribe, Ph.D., P.Geo. Qualified Persons under NI 43
-101.

Sego is 100% owner of the Miner Mountain Project, an alkalic
copper-gold porphyry exploration project near Princeton, British
Columbia. The property is 2,056.54 hectares in size and located 15
kilometres north of the Copper Mountain Mine operated by Copper
Mountain Mining Corporation and Mitsubishi Materials Corporation.  Sego
has a Memorandum of Understanding with the Upper Similkameen Indian
Band, on whose Traditional Territory the Miner Mountain Project is
situated.

For further information please contact:

J. Paul Stevenson, CEO (604) 682-2933 or toll free 1-866-683-2933


Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. No regulatory authority has approved or disapproved the
information contained in this news release.

This release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other
than statement of historical facts that address future production,
reserve potential, exploration drilling, exploitation activities and
events or developments that the Company expects re forward-looking
statements. Although the Company believes the expectations expressed in
such forward-looking statements are based on reasonable assumptions,
statements are not guarantees of future performance and actual results
or developments may differ materially from the forward-looking
statements. Factors that could cause actual results to differ
materially from those in forward-looking statements include market
prices, exploitation and exploration successes, continued availability
of capital and financing, general economic, market or business
conditions. Investors are cautioned that any such statements are not
guarantees of future performance and those actual results or
developments may differ materially from those projected in the
forward-looking statements.

TSX Venture closing price for SGZ-V
Date: 2017/10/06
Closing Price: 0.05

TEL: 604-682-2933    SEGO RESOURCES INC
FAX: 604-687-0586
E-mail: officemanager@segoresources.com
Website: http://www.segoresources.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1728200041TS11728202157-10272720171010