Source	Marketwire
Date	10/13/2017
Time	07:02:55 AM

Company	 SATORI RESOURCES INC.
Title	Satori Intersects 3.03 g/t Au over 4.5 metres at Tartan Lake





    CDNX Symbol: BUD











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Satori Resources Inc.

TSX VENTURE SYMBOL: BUD

October 13, 2017

Satori Intersects 3.03 g/t Au over 4.5 metres at Tartan Lake


TORONTO, ONTARIO--(Marketwired - Oct. 13, 2017) -

THIS NEWS RELEASE IS NOT INTENDED FOR DISSEMINATION IN THE UNITED STATES OR 
DISTRIBUTION TO U.S. NEWSWIRE SERVICES

Satori Resources Inc. (TSX VENTURE:BUD) ("Satori" or the "Company") is pleased 
to announce the results of a 2,045 metre drill program at the Company's 100% 
owned Tartan Lake Gold Mine Project ("Tartan Lake" or the "Project") located in 
Flin Flon, Manitoba.

Commencing on June 12, 2017, the Company undertook a limited drill program 
focusing on the South Zone. Upon completion of the program a total of 2,045 
metres were drilled in 6 diamond drill holes. The results of the program both 
confirmed and provided a basis for further exploration of the South Zone 
portion of the resource model, developed in November of 2016, which is found in 
the NI 43-101 compliant resource estimate in the "Tartan Lake Project Technical 
Report" authored by Mining Plus Canada Consulting, April, 2017. This most 
recent drilling intersected gold mineralization both along strike and down dip 
beyond the existing resource limits.

Interim CEO Bruce Reid Stated: "These drilling results at Tartan increase the 
zone of mineralization and provide the basis for a more focused drill program 
on the South Zone."

Table 1 below indicates the significant results in grams of gold per tonne (g/t 
Au) by hole for this program:

/T/

----------------------------------------------------------------------------
Intersection
----------------------------------------------------------------------------
From        To   Length(i)        Au  Avg. Grade    Length
Hole #             (m)       (m)         (m)     (g/t)    (g/t Au)       (m)
----------------------------------------------------------------------------
TL17-07            212       213           1      3.55        3.55      1.00
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-07            221       222           1      2.59
------------------------------------------------------
TL17-07            222       223           1      0.03
------------------------------------------------------
TL17-07            223       224           1      0.25
------------------------------------------------------        2.34      6.00
TL17-07            224       225           1      2.54
------------------------------------------------------
TL17-07            225       226           1      6.72
------------------------------------------------------
TL17-07            226       227           1       1.9
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-07            267       268           1      0.62
----------------------------------------------------------------------------
TL17-07            268       269           1      4.41        2.07      3.00
----------------------------------------------------------------------------
TL17-07            269       270           1      1.17
----------------------------------------------------------------------------
TL17-07            282       283           1      3.09
------------------------------------------------------
TL17-07            283       284           1      0.87
------------------------------------------------------
TL17-07            284       285           1      4.76
------------------------------------------------------
TL17-07            285     286.6         1.6      2.67
------------------------------------------------------
TL17-07          286.6       288         1.4      0.01        2.16      9.00
------------------------------------------------------
TL17-07            288       289           1      0.15
------------------------------------------------------
TL17-07            289       290           1     4.315
------------------------------------------------------
TL17-07            290       291           1     1.985
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-08            205       206           1      3.77
------------------------------------------------------        2.85      2.00
TL17-08            206       207           1      1.92
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-08            216       217           1     11.03
------------------------------------------------------
TL17-08            217       218           1     0.045
------------------------------------------------------
TL17-08            218       219           1      0.65
------------------------------------------------------
TL17-08            219    219.72        0.72      1.71
------------------------------------------------------        2.55      8.00
TL17-08         219.72       221        1.28      0.95
------------------------------------------------------
TL17-08            221       222           1     0.025
------------------------------------------------------
TL17-08            222       223           1      0.03
------------------------------------------------------
TL17-08            223       224           1     6.175
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-08            238       239           1     3.635
------------------------------------------------------
TL17-08            239       240           1       1.7
------------------------------------------------------        2.15      4.00
TL17-08            240       241           1      2.07
------------------------------------------------------
TL17-08            241       242           1      1.19
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-08            299       300           1     3.875        3.88      1.00
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-08            308       309           1      1.41        1.41      1.00
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-09          49.01     50.03        1.02      1.36        1.36      1.02
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-09          221.1    222.53        1.43      1.17
------------------------------------------------------        1.87      2.21
TL17-09         222.53    223.31        0.78      3.16
----------------------------------------------------------------------------
TL17-10            108       109           1      1.14
------------------------------------------------------
TL17-10            109       110           1      0.39
------------------------------------------------------        1.39      4.00
TL17-10            110       111           1      1.66
------------------------------------------------------
TL17-10            111       112           1      2.38
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL17-11            224    225.58        1.58      3.91
------------------------------------------------------
TL17-11         225.58    226.38         0.8      1.71
------------------------------------------------------        3.03      4.45
TL17-11         226.38    227.54        1.16      4.54
------------------------------------------------------
TL17-11         227.54    228.45        0.91      0.76
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
TL11-12                          No significant results
----------------------------------------------------------------------------
(i) The lengths indicated are core length samples and do not represent true
width values.

/T/

Technical Information

The surface exploration drilling was conducted by Black Hawk Drilling of 
Smithers, British Columbia, and carried out under the supervision of Peter 
Karelse P.Geo., registered in the Province of Ontario, a Geological Consultant, 
who is a qualified person as defined by NI 43- 101. Mr. Karelse has more than 
30 years of experience in gold exploration and development. All technical 
information in this press release has been reviewed and approved by Mr. 
Karelse. Samples were transported directly in secure containers from the Satori 
site in Flin Flon, Manitoba, to the TSL Laboratories ("TSL") in Saskatoon, 
Saskatchewan. TSL, which is an accredited ISO/IEC 17025 lab, assayed the 
samples using standard fire assay methods with a gravimetric finish. Certified 
standards are placed in the sample stream at a rate of one standard per 20 
samples. Certified blanks are placed in the sample stream at a rate of one 
blank every 40 samples.

ABOUT SATORI RESOURCES INC.

Satori is a Toronto-based mineral exploration and development company whose 
primary property is the Tartan Lake Gold Mine Project (100% interest), located 
in the prolific Flin Flon mining district, in Manitoba, Canada. The Tartan Lake 
Gold Mine had historical high-grade production of 48,000 ounces of gold between 
1987 and 1989. The Project hosts a largely intact 450 tonne per day gold 
concentrator and related infrastructure, along with a decline ramp providing 
access to developed gold mineralization within the Main and South Zones to a 
vertical depth of 320 metres.

For further information, please visit www.satoriresources.ca.

Neither TSX Venture Exchange Inc. nor its Regulation Services Provider (as that 
term is defined in policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

CAUTION REGARDING FORWARD-LOOKING INFORMATION

This news release of Satori contains statements that constitute 
"forward-looking statements." Such forward-looking statements involve known and 
unknown risks, uncertainties and other factors that may cause Satori's actual 
results, performance or achievements, or developments in the industry to differ 
materially from the anticipated results, performance or achievements expressed 
or implied by such forward-looking statements.

- 30 -

CONTACT INFO:

Bruce Reid
Chief Executive Officer
info@satoriresources.ca
www.satoriresources.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=599541467