Source	MARKET NEWS
Date	10/16/2017
Time	06:56:20 AM

Company	 Rye Patch Gold Corp.
Title	Outlines 
Program to Expand Oxide Resources and E





    CDNX Symbol: RPM











Press Release





RYE PATCH GOLD CORP ("RPM-V;RPMGF-0")
- Outlines Program to Expand Oxide Resources and Explore
- Sulfide Potential at Florida Canyon and Lincoln Hill

Rye Patch Gold Corp. (the "Company" or "Rye Patch") outlines a
three-year program to expand oxide resource and delineate sulfide
potential along the Oreana trend in west-central Nevada. The program is
designed to increase measured and indicated oxide resources at Florida
Canyon and Lincoln Hill and quantify and deliver a sulfide resource
beneath the Florida Canyon oxide deposit. A Phase 1 10,000 metre
expansion drilling campaign at the Florida Canyon mine is planned which
seeks to increase the oxide resource and to test and confirm the grade,
character and extent of the sulfide mineralization beneath the oxide
ore body.
The initial drill program will consist of 1,200 metres of core and
8,800 metres of reverse circulation drilling. Drillhole depths will
range between 150 to 300 metres for the sulfide program and 60 to 180
metres for the oxide program. The estimated cost of the phase-1
campaign is US$1 million, and the program commenced in early October.

At the end of the three-year program, Rye Patch anticipates
delivering significant additional oxide resources at Florida Canyon and
Lincoln Hill, and a sulfide resource beneath the Florida Canyon oxide
deposit. A portion of the sulfide body above the water table may also
lend itself to an accelerated mine and processing option for the
Company.

William Howald, the Company's President and CEO noted, "Over the
history of the Florida Canyon mine, a total of 3.5-million ounces of
gold from oxide material has been placed on the historic leach pad and
the Company is currently mining a 1.12-million ounces of measured and
indicated oxide gold resource. Based on our exploration model,
Management believes the sulfide resource beneath Florida Canyon has a
similar number of ounces of gold but at a much higher grade. If our
exploration model is correct, the combined oxide and sulfide
mineralization could make Florida Canyon a world-class deposit in
Nevada."

Sulfide Program

The core program will focus on the sulfide deposit beneath the
Florida Canyon oxide resource. The objective of the drill program is to
establish the overall size, extent and thickness of the sulfide body
and collect material for additional metallurgical testing.

In 1996, Pegasus Gold completed an internal report titled "Sulfide
Project Pre-feasibility Study" dated July 18, 1996 on the sulfide
mineralization at Florida Canyon. A total of 262 drillholes (241 RC and
21 core) touched or penetrated the sulfide body and yielded an average
grade of 2.36 g/t gold in the sulfide with gold values as high as 100
g/t Au (2.93 opt Au) in a northeast oriented structural zone. Pegasus
completed a resource estimate within a Whittle pit design at US$400
gold price, and a series of metallurgical tests including floatation,
pressure oxidation, roasting, and bio-oxidation. The metallurgical test
work showed an overall recovery of 90% with flotation with 94% of the
gold reporting to a sulfide concentrate. Additional metallurgical test
work will be done by Rye Patch on material from the drill program. A
Qualified Person has not done sufficient work to classify this
historical information as a current mineral resource or mineral reserve
and the Company is not treating this historical information as a
current mineral resource or mineral reserve.

The core program will also test the distribution of the sulfide
body and validate the current geologic model and high-grade ore
controls. Core holes will be located to test the down dip extension of
sulfides between the Radio Tower and Central pits; the down dip
extension west of the Main pit; and potential structural zone east of
the Radio Tower and Central pit areas.
An additional 2,700 metres of reverse circulation drilling will
target the down dip potential and structural controls on the sulfide
zone to help validate the geologic model. The RC program will fill in
gaps between historic sulfide drilling programs to see if the
mineralization connects between areas which, if positive, could have a
dramatic impact on the potential size of the sulfide mineralization.

Oxide Program

The objective of the oxide program is to expand and upgrade the
current oxide resource and step out along structural zones. A total of
5,500 metres of drilling is planned with drillhole depths ranging
between 60 and 180 metres. The program will include upgrading inferred
material within the designed pits to measured and indicated adjacent to
the Radio Tower and Central pit areas. A major portion of the program
will be step-out drilling along low- and high&#8209;angle structural
trends.

The primary drill target is the contact between Grass Valley
siltstone and Natchez Pass limestone. The contact is a low-angle fault
(thrust fault) which controls mineralization in Radio Tower and Central
pits. The zone is significant within the mine and may represent a
regional exploration target. Drilling will target jasperioid alteration
and hydrothermal breccias within the thrust fault zone.

Mr. William Howald, AIPG Certified Professional Geologist #11041,
Rye Patch Gold's CEO and President with a BSc. in Geological
Engineering, is a Qualified Person as defined under National Instrument
43-101. He has reviewed and approved the contents of this news release.


About Rye Patch Gold Corp. Rye Patch Gold Corp. is a Nevada
focused, Tier 1, precious metal mining company engaged in the mining,
development and exploration of a 180 square kilometre land package
along the prospective Oreana trend in west central Nevada. Leveraging
its strong financial position and cash to acquire the Florida Canyon
Gold mining operation, Rye Patch now controls a trend&#8209;scale
platform with mining operations, resource projects and significant
exploration potential. The combination of mining and a growth profile
along a major Nevada gold trend positions Rye Patch to become an
emerging North American mid-tier precious metal producer. For more
information, please visit our website at www.ryepatchgold.com.

On behalf of the Board of Directors

'William Howald'

William C. (Bill) Howald, CEO & President

Forward-Looking Statements

This news release contains forward-looking statements relating to
future plans and objectives of the Company, future production and
deliveries of gold, proposed operations of the Company including mine
development, funding requirements, future events and conditions and
other statements that are not historical facts, all of which are
subject to various risks and uncertainties. The Company's actual
results, programs and financial position could differ materially from
those anticipated in such forward-looking statements as a result of
numerous factors, some of which may be beyond the Company's control.
These factors include, but are not limited to: future deliveries of
gold pursuant to the forward gold price contract facility, the
achievement of mine redevelopment plans and production results; the
availability of funds; the financial position of Rye Patch; the timing
and content of work programs; the results of exploration activities and
development of mineral properties; the interpretation of drilling
results and other geological data; the reliability of calculation of
mineral resources; the reliability of calculation of precious metal
recoveries; the receipt and security of mineral property titles;
project cost overruns or unanticipated costs and expenses; fluctuations
in metal prices; currency fluctuations; and general market and industry
conditions.

Forward-looking statements are based on the expectations, opinions
and assumptions of the Company's management on the date the statements
are made including, but not limited to, the continued operation of the
Company's mining operations, no material adverse change in the market
price of commodities, and mining operations and production to be
completed in accordance with management's expectations. The assumptions
used in the preparation of such statements, although considered
reasonable at the time of preparation, may prove to be imprecise and,
as such, undue reliance should not be placed on forward-looking
statements. As a result, the Company cannot guarantee that the
drawdowns under the Credit Facility and the Florida Canyon mine
redevelopment will be completed on the terms and within the time
disclosed herein or at all.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Rye Patch Gold Corp, info@ryepatchgold.com, Tel.: (604) 638-1588,
Fax: (604) 638-1589
______________________________
_______________________________________________
TSX Venture closing price for RPM-V
Date: 2017/10/13
Closing Price: 0.21
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1728800025TS11728801359-06555120171016