Source	MARKET NEWS
Date	10/17/2017
Time	05:16:27 AM

Company	 Kesselrun Resources Ltd.
Title	Channel 
Sample Results Of 7.7 G/T Au, 23.9 G/T A





    CDNX Symbol: KES











Press Release





KESSELRUN RESOURCES LTD ("KES-V")
- Channel Sample Results Of 7.7 G/T Au, 23.9 G/T Ag Over 3.1
- metres

Kesselrun Resources Ltd. ("Kesselrun") is pleased to provide the
following update on its 100% owned Huronian Gold Project:

Ongoing surface exploration at Huronian continues to yield
encouraging results. Surface channel sampling results received include
7.7 g/t gold, 23.9 g/t silver over a composite sample length of 3.1
metres on the Fisher zone and 1.1 g/t gold, 8.0 g/t silver over a
composite sample length of 8.2 metres on the McKellar zone. The Fisher
zone is a previously identified zone of gold and silver mineralization
located on one of numerous splays from the main Huronian Shear Zone.
The McKellar zone is the southwest strike extension of the historically
mined Huronian zone.

As previously released (see KES NR September 26 and October 11,
2017), a new location of the Huronian Shear Zone and associated splays
has been interpreted by Kesselrun's team. Kesselrun believes that the
area holds the potential to host a significant gold resource and its
exploration efforts are being executed to test that theory.

Michael Thompson, P.Geo., President and CEO commented, "The
channel sampling of known zones on Huronian is being done to give the
team a better understanding of the relationship between alteration,
structure and gold mineralization, thus enabling us to better explore
for extensions to these zones and entirely new zones. These encouraging
results confirm the gold potential of the area".

Table 1: Summary of Significant Channel Sample Results - Huronian
Project (1)

//st

Channel ID     Zone      Weighted Grade      Weighted Grade     Length (m)
Au (g/t)            Ag (g/t)

FC14       Fisher           7.7                23.9             3.1

FC22       Fisher           1.5                 5.7             5.8

FC20       Fisher           1.1                 7.5             3.5

FC4        Fisher           1.2                 2.9             3.4

FC3        Fisher           1.3                 4.2             1.6

FC21       Fisher           0.5                 1.7             5.7

M12       McKellar          1.1                 8.0             8.2

M35       McKellar          1.0                 1.2             6.0

M13       McKellar          0.9                 9.0             9.0

M17       McKellar          1.0                 7.0             3.7

M10       McKellar          0.8                 8.5             5.1

M7       McKellar          0.9                 7.1             4.1

M23       McKellar          0.8                 3.8             3.4
M1       McKellar          1.0                 8.0             2.4

//et

(1) Contiguous sampling lengths are dictated by the exposure of
rock available to sample and not necessarily the width of the zone.
Channel samples are cut as close to perpendicular to the strike of
mineralization as possible but are not representative of true width of
the zone.

Kesselrun holds 4.7M First Mining Finance shares with a current
value of over $3M as of market close yesterday which management
believes gives the company sufficient means to implement its corporate
strategy going forward.

The Huronian Gold Project consists of 154 unpatented mining claims
and four patented mining claims for a total land package of 5,200
hectares. The project is situated in the highly prolific Shebandowan
Greenstone Belt located in the Abitibi-Wawa Subprovince approximately
100 km west of Thunder Bay, Ontario along major transportation and
power routes.

The project hosts numerous significant gold zones including the
past producing Huronian Mine that produced 29,629 ounces gold and
170,463 ounces silver from 143,724 tons from 1932-1936 (Ontario
Ministry of Northern Development and Mines Production Records). The
project also covers the southwest strike extension of Wesdome Gold
Mine's Moss Lake Gold Deposit. The Moss Lake Gold Deposit hosts an NI
43-101 compliant resource estimate of 40 million tonnes at a grade of
1.1 g/t (1,377,300 oz Au) Indicated and an additional 50 million tonnes
at a grade of 1.1 g/t (1,751,600 oz Au) Inferred (Moss Lake Gold Mines
NR February 20, 2013) as well as an NI 43-101 compliant Preliminary
Economic Assessment (Moss Lake Gold Mines NR July 29, 2013).

Michael Thompson, P. Geo., President and CEO of Kesselrun, is the
Qualified Person responsible for the project as defined by National
Instrument 43-101 and has approved the technical information in this
news release.

QA/QC

Kesselrun has implemented a quality control program for the trench
sampling and planned drill program to ensure best practice in sampling
and analysis. The planning, execution and monitoring of Kesselrun's
quality control programs are under the supervision of Michael Thompson,
P. Geo. Kesselrun maintains strict quality assurance/quality control
protocols including the systematic insertion of certified standard
reference and blank materials into each sample batch. Analyses in this
release were performed by Activation Laboratories Ltd. (Actlabs) of
Thunder Bay, Ontario with ISO 17025 accreditation. Samples are
transported in security sealed bags to Accurassay and all samples were
analyzed using industry-standard techniques. Gold and silver was
analyzed by a standard 50 gram fire assay with an AAS and a gravimetric
finish on samples greater than 5 g/t.

About Kesselrun Resources Ltd.

Kesselrun Resources is a Thunder Bay, Ontario-based mineral
exploration company focused on growth through property acquisitions and
discoveries. Kesselrun's management team possesses strong geological
and exploration expertise with particular experience in Northwest
Ontario. For more information about Kesselrun Resources, please visit
www.kesselrunresources.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

For additional information please contact:

Kesselrun Resources Ltd.

Michael Thompson, P. Geo., President & CEO
807.285.3323
michaelt@kesselrunresources.com

Corporate Communications
1.866.416.7941
information@kesselrunresources.com

Forward Looking Statements - Certain information set forth in this
news release may contain forward-looking statements that involve
substantial known and unknown risks and uncertainties. These
forward-looking statements are subject to numerous risks and
uncertainties, certain of which are beyond the control of Kesselrun,
including, but not limited to the impact of general economic
conditions, industry conditions, volatility of commodity prices,
dependence upon regulatory approvals, the execution of definitive
documentation, the availability of financing and exploration risk.
Readers are cautioned that the assumptions used in the preparation of
such information, although considered reasonable at the time of
preparation, may prove to be imprecise and, as such, undue reliance
should not be placed on forward-looking statements.

TSX Venture closing price for KES-V
Date: 2017/10/16
Closing Price: 0.16

TEL:  807-285-3323  KESSELRUN RESOURCES LTD
FAX:  807-345-1875
EMAIL:  james@sequoiapartners.ca
WEBSITE:  http://www.kesselrunresources.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1728900009TS11728900764-05145520171017