Source	Marketwire
Date	10/17/2017
Time	05:30:36 AM

Company	 MIDLAND EXPLORATION INC.
Title	Midland Discovers Very High-Grade Gold Showings on Willbob With a Selected 
Grab Sample Yielding Up to 419 g/t Au





    CDNX Symbol: MD











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Midland Exploration Inc.

TSX VENTURE SYMBOL: MD

October 17, 2017

Midland Discovers Very High-Grade Gold Showings on Willbob With a Selected Grab 
Sample Yielding Up to 419 g/t Au


MONTREAL, QUEBEC--(Marketwired - Oct. 17, 2017) - Midland Exploration Inc. 
("Midland") (TSX VENTURE:MD) is pleased to announce the most recent results of 
its reconnaissance campaign on the Willbob project (wholly owned by Midland), 
located about 70 km west of Kuujjuaq and close to the Kan project (Osisko 
Mining / Barrick Gold), with the discovery of two new very high-grade gold 
showings in the northern part of the project.

The new "SP" showing is located about 600 meters east of the Golden Tooth 
showing (up to 3.1 g/t Au / 1.7 meters in drillhole in 2016). Grab samples of 
mineralized quartz veins, found within a 120 meters x 50 meters area, yielded 
three very high gold values: 419 g/t Au, 38.3 g/t Au and 21.7 g/t Au. Anomalous 
gold values were also found in the wallrock of the veins, which sometimes 
contains quartz veinlets: 2.04 g/t Au, 0.454 g/t Au, 0.256 g/t Au, 0.176 g/t 
Au, 0.17 g/t Au. Mineralization in the area consists in a series of 
quartz-ankerite tension-type veins, up to 10 cm thick, containing clusters of 
pyrite-galena+/-sphalerite, crosscutting a strongly chloritized and ankeritized 
quartz diorite with disseminated pyrite. Overall, nine (9) grab samples out of 
15 collected from the area returned more than 0.1 g/t Au (note that grab 
samples are selective by nature and values reported may not be representative 
of mineralized zones). A table of results for all samples from the "SP" area 
that yielded more than 0.1 g/t Au can be found at the end of this press release.

The new "Serpent" showing is located about 4.5 kilometers south of the Golden 
Tooth showing, in a poorly explored area where no gold mineralization was known 
before. The mineralization of the Serpent showing is found within a 50-cm thick 
shear zone injected with quartz-calcite-chlorite+/-pyrite veins, crosscutting a 
gabbro. A grab sample from this zone returned 15.35 g/t Au, and three (3) other 
samples also yielded anomalous values: 0.487 g/t Au, 0.448 g/t Au, 0.254 g/t 
Au. Overall, four (4) grab samples out of 6 samples collected from the shear 
zone returned more than 0.1 g/t Au.

These results continue to demonstrate the strong potential of the Willbob 
project for very high-grade orogenic gold mineralization, including in areas 
that were previously unexplored. Additional results from the 2017 prospection 
and drilling campaign will be published in the coming weeks.

Figures showing the location of the new discoveries as well as photos of 
mineralized samples can be viewed using the following link : 
http://media3.marketwire.com/docs/FiguresCommuniqueWillbobSeptembre2017.pdf

Results from grab samples(i) greater than 0.1 g/t Au, "SP" Showing

/T/

----------------------------------------------------------------------------
Sample       UTM_E        UTM_N          Au-AA23 g/t       Au-GRA21 g/t
----------------------------------------------------------------------------
S408613     469962       6422598     greater than 10          419
----------------------------------------------------------------------------
S408610     469963       6422631     greater than 10         38.3
----------------------------------------------------------------------------
S408588     469938       6422628     greater than 10         21.7
----------------------------------------------------------------------------
S408612     469963       6422597            2.04
----------------------------------------------------------------------------
S408587     469972       6422655            0.754
----------------------------------------------------------------------------
S408615     469966       6422537            0.454
----------------------------------------------------------------------------
S408593     469978       6422480            0.256
----------------------------------------------------------------------------
S408590     469929       6422569            0.176
----------------------------------------------------------------------------
S408586     469970       6422654            0.17
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Ag ppm             Pb ppm             Pb pct       Zn ppm     Zn pct
----------------------------------------------------------------------------
42.4       greater than 10000       2.06        10000       1.29
----------------------------------------------------------------------------
18.5       greater than 10000       1.83          21
----------------------------------------------------------------------------
40.5       greater than 10000       4.12          40
----------------------------------------------------------------------------
0.8                432                            589
----------------------------------------------------------------------------
3.7               2780                             12
----------------------------------------------------------------------------
-0.5                43                              66
----------------------------------------------------------------------------
-0.5                12                              30
----------------------------------------------------------------------------
-0.5                76                              53
----------------------------------------------------------------------------
-0.5                 6                              39
----------------------------------------------------------------------------

/T/

(i)note that grab samples are selective by nature and values reported may not 
be representative of mineralized zones. Also note that true thicknesses 
reported in drillholes from this press release cannot be determined with 
available information.

Quality control

Rock samples on the project are assayed by standard 30 gram fire-assaying with 
AA (Au-AA23) or gravimetric finish (Au-GRA21) at ALS Minerals laboratories in 
Val d'Or, Quebec or Sudbury, Ontario. All samples are also analysed for 
multi-elements, using four-acid ICP-AES method. Exploration program design and 
interpretation of results is performed by qualified persons employing a Quality 
Assurance/Quality Control program consistent with industry best practices, 
including the use of standards and blanks with every 20 samples.

About Midland

Midland targets the excellent mineral potential of Quebec to make the discovery 
of new world-class deposits of gold, platinum group elements, base metals and 
rare earth elements. Midland is proud to count on reputable partners such as 
Altius Resources Inc., Agnico Eagle Mines Limited, Teck Resources Limited, 
IAMGOLD Corporation, Osisko Mining Inc., SOQUEM INC., Japan Oil Gas and Metals 
National Corporation, Niobay Metals Inc. and Abcourt Mines Inc. Midland prefers 
to work in partnership and intends to quickly conclude additional agreements in 
regard to newly acquired properties. Management is currently reviewing other 
opportunities and projects to build up the Company portfolio and generate 
shareholder value.

This press release has been prepared by Sylvain Trepanier, P.Geo., VP 
Exploration for James Bay and Northern Quebec at Midland, a "qualified person" 
as defined by NI 43-101. For further information, please consult Midland's 
website: www.midlandexploration.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This press release may contain forward-looking statements that are subject to 
known and unknown risks and uncertainties that could cause actual results to 
vary materially from targeted results. Such risks and uncertainties include 
those described in Midland's periodic reports including the annual report or in 
the filings made by Midland from time to time with securities regulatory 
authorities.

- 30 -

CONTACT INFO:

Gino Roger, President and Chief Executive Officer
450 420-5977
Fax: 450 420-5978
info@midlandexploration.com
www.explorationmidland.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=599569224