Source	MARKET NEWS
Date	10/17/2017
Time	08:05:55 AM

Company	 Stelmine Canada Ltd.
Title	16 New 
Potential Mineralized Zones Up To 24.8 G/





    CDNX Symbol: STH











Press Release





STELMINE CANADA LTD ("STH-V;STLZF-0")
- 16 New Potential Mineralized Zones Up To 24.8 G/t Au In Courcy

Stelmine Canada Ltd. ((( Stelmine ))) is pleased to provide a
summary and highlights of the exploration work accomplished on its
Courcy flagship property during the summer 2017 campaign. The
exploration work allowed the unearthing of 16 new mineralized zones
through overburden stripping generating values up to 24.8 g/t Au from
grab samples. Over 398 m of channel sampling was carried out on 2,000
m2  of rocks stripped of overburden. Analytical results, most of them
from channel samples, are pending.

The property is located in the eastern segment of the Opinaca
sub-province near the Quebec/Labrador border, 100 km west of the city
of Fermont, Quebec. From June 10 to October 4, 2017, our field crew
reinterpreted the geology of the eastern half of the property while
extending the known gold-bearing zones and unearthing new prospective
zones by extensive overburden stripping and rock sampling (Figure 1,
all figures are on our website).

The exploration was carried out by a team of geologists,
technicians and specialists from a base camp built upon the shore of
Lake Couteau. Highlights of the summer campaign are given below :

//st

* Discovery of new potential Au-rich zones;
* More than 16 new mineralized (pyrrhotite-pyrite-chalcopyrite-rich)
zones totalizing ) 2,000m2 were stripped of the overburden, mapped and
sampled (grab and channel samples);
* A total of 751 rock samples, including 433 channel samples having a
total length of 398 m were collected from outcrops, ancient and new
stripped zones. Theses samples were sent for Au and other metal analysis to
the ALS Chemex Laboratories in Val d'Or;
* Geological mapping of the eastern part of the property by our
geologists (35% of the original total property area) allowed the
reinterpretation of the geological and structural framework.

//et

Stelmine also reinterpreted previous airborne and ground-based
geophysical surveys (i.e. Mag, VTEM, TDEM, Max-Min). Rock samples were
sent to IOS Services Geoscientifiques for thin section examination and
rock samples were forwarded to ALS Chemex for whole rock and trace
element analyses.

Analytical Results

Up until now, a total of 473 Au analyses, most of them from grab
samples, were received form the laboratory. A total of 28 analyses
revealed Au concentrations ) 0.30 g/t, several with values ) 1.0 g/t,
including concentrations of 2.84, 4.21, 8.39 and 24.8 g/t Au
respectively. These samples come principally from two main areas
situated west and south of the Courcy camp (Figures 2 and 3).

In the Southern Zone, pyrrhotite-garnet rich BIFs, commonly
containing fuchsite, surrounding quartz arenite/sandstone beds and
altered shear zones/mylonites accompanied by ultramafic sills provide
Au-rich samples along a 1.2 km ENE-WSW-oriented, highly magnetic and
conductive structure(Figure 2). 11 grab samples yielded values ranging
from 0.36 to 24.8 g/t Au. Combining these results with the previous
data obtained by SOQUEM (2004-2006) along the same structure, brings
the total of grab samples having Au values ) 0.3 g/t to 30; yielding an
average concentration of 2.75 g/t Au.

The Western Zone, located west of lake Couteau, reveals
pyrrhotite-rich gold-bearing samples collected from thick BIF beds
(5-10 m) and surrounding pyrrhotite-injected garnet-bearing
meta-greywackes and quartz-veins from an area of 2.5 km2 (Figure 3).
The bulk of the analytical results is yet to be received. Other
gold-bearing grab samples produced Au values from 0.31 to 8.38 g/t Au
averaging 1.49 g/t. 21 Grab samples taken by SOQUEM form the same
BIF-rich area gave an average concentration of 1.93 g/t Au, bringing
the cumulative SOQUEM/Stelmine average to 1.79 g/t Au. A 772 m DDH
campaign distributed in eight holes was also conducted in the Northern
Zone by SOQUEM in 2006. Best results yielded: 0.4 g/t Au @15 m (Hole
no. 2); 0.94 g/t Au @ 10.50 m (Hole no. 4) and 4.27 g/t Au @ 42 m
(including 12.15 g/t Au @ 13.5 m; Hole no. 8).

Geological Mapping

Systematic geological mapping indicates a new lithological and
structural interpretation of the Courcy property. The geological and
structural framework suggests the extension of the metasedimentary
Opinaca sub-province into the Courcy regioninstead of the Opatica.
Numerous (meta-) sedimentary units such as greywackes, mudstones,
quartz arenites, quartzites and polygenic/ monogenic conglomerates are
interbedded with pyrrhotite and garnet-rich Banded Iron Formations
(BIFs) and subordinate volcanic rocks. Numerous ENE-WSW-oriented
shear/mylonite/ and deformation zones were identified in the Southern
Zone near the metasedimentary/tonalite rock contact. A large
NE-SW-oriented synform forms the principal structure.

Geophysics

New geophysics maps drawn through the re-processing and
interpretation of the past data filed by SOQUEM show a clear
distinction in apparent resistivity, whereas the Soulard Formation
containing the Au-mineralized BIFs is characterized by very low
apparent resistivity relative to the Courcy Formation and plutonic
rocks. This testifies of the sedimentary mature of the Soulard
Formation. 2D first derivative and 3D inversion magnetic contour maps
show strong positive anomalies for magnetic-rich ultramafic sills/dykes
and moderate to weak anomalies for pyrrhotite-rich BIFs (Figures 4 and
5). However, the latter show strong conductivities and the calculated
Tau (dB/dt) values from the VTEM survey display relatively high
thickness of sulphide-bearing rocks,mostly associated to BIFs, not only
west of Lake Couteau, but to the less investigated northeast and
southwest regions, opening new possibilities for exploration (Figure
6).

QA/QC Protocol

Stelmine implemented a strict QA/QC protocol in processing all
rock samples collected from the Courcy property. The protocol included
the insertion and monitoring of appropriate reference materials, in
this case high concentration (MA-C2) and low concentration (GTS-2A)
certified gold standards, blanks and duplicates, to validate the
accuracy and precision of the assay results. All rock samples collected
were put in sturdy plastic bags, tagged and sealed in the field under
the supervision of professional geologists. The sample bags were then
put in rice pouches and kept securely in a field tent before being sent
by floatplane to the city of Wabush. Transport to the ALS laboratory in
Val d'Or from Wabush was made by truck from reliable transport
companies. Gold was analyzed by fire assay method (Au-AA25 package) and
other elements including Ag, Cu, Zn, Pb, As and S were determined by
ICP-AES after powder sample dissolution in Aqua-Regia (package
ME-ICP41).

The technical contents of this release were approved by Michel
Boily, PhD, geo; a Qualified Person (QP) as defined by National
Instrument 43-101.

Follow us on www.Stelmine.com and on our Facebook page (Stelmine
Canada) where we uploaded pictures of the Courcy camp and of our crew
at work.

About Stelmine

Stelmine is a junior mining exploration company and its activities
are located in the Province of Quebec. Stelmine holds 754 claims
spanning 383 km2 on the eastern part of the Opinaca metasedimentary
basin, which contains zones with a high potential for gold deposit
discovery in geological contexts similar to the one leading to
discovery of the Eleonore Mine. Its capital stock consists of
21,926,452 issued and outstanding shares for a current market
capitalization of $6.6 million.

Forward-looking statements

Certain statements made herein may constitute forward-looking
statements. These statements relate to future events or the future
economic performance of Stelmine and carry known and unknown risks,
uncertainties and other factors that may appreciably affect their
results, economic performance or accomplishments when considered in
light of the content or implications or statements made by Stelmine.
Actual events or results could be significantly different. Accordingly,
investors should not place undue reliance on forward-looking
statements.

Neither the TSX Venture Exchange nor its regulation services
provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Contact Information:

Isabelle Proulx
President and CEO
581-998-1222
info@stelmine.com
www.Stelmine.com

Christian Guilbaud
Business Development
514-813-7862
______________________________
_______________________________________________
TSX Venture closing price for STH-V
Date: 2017/10/16
Closing Price: 0.29
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1728900037TS11728901747-08025020171017