Source	MARKET NEWS
Date	10/23/2017
Time	05:36:00 AM

Company	 Strikepoint Gold Inc.
Title	Intersects 
15.24m Of 1.05 Gram Per Ton Gold And





    CDNX Symbol: SKP











Press Release





STRIKEPOINT GOLD INC ("SKP-V")
- Intersects 15.24m Of 1.05 Gram Per Ton Gold And 32.0m Of 0.14%
- Copper At The Pluto Project, Yukon Territory

StrikePoint Gold Inc. is pleased to provide drill results and an
exploration update from activities on its Pluto property, Yukon
Territory.

Highlights

//st

* 15.24m at 1.05g/t gold from a Charon Zone drill hole 17-CRN-02 at
Charon
Zone.
* 32.0m at 0.14% copper in hole 17-CRN-07.
* In hole 17-CRN-01, intersected 6.10m at 0.74g/t gold with 1.67% copper.
* Drilling in 6km southwest of Charon in the Hydra Zone returned 10.67m
at
0.4g/t gold with similar geological setting to Charon.
* Mineralization is hosted in limestone layers which are altered by skarn
and marble.
* Host limestone beds exist as multiple layers in the sediment package
and
extend for at least 6km by 3km area.

//et

StrikePoint Gold was active on the project between July 8th and
September 5th, 2017. Extensive mapping of the northeastern portion of
the property was completed, and a total of 117 grab samples were
collected from the area. Twelve RAB drill holes were completed by
GroundTruth Exploration during that time, with eight on the Charon
target and four on the Hydra target, to a total of 1,294m.

Surface results from 2017 were released by StrikePoint in August,
and highlighted assays of 48.4g/t and 36.3g/t gold from within the
Charon Zone, along with copper up to 1.23% (news release dated August
22, 2017).

Shawn Khunkhun (CEO, StrikePoint) comments "The discovery through
drilling of copper and gold mineralization occurring at Pluto is an
exciting development. Despite a lack of outcrop the technical team lead
by our VP Ex, Andy Randell were able to take a significant step on
Pluto, taking the property from a high grade soil anomaly, proving the
mineralizing is present below the surface."

Pluto Property

The Pluto Property is in the Kluane region of the Yukon Territory,
and covers an area of 21km x 22km, and is 100km southwest of the town
of Carmacks. The ground is mainly rolling hills with deep river
valleys, but outcrop exposure is limited. The aim of the 2017 program
was to follow up on the soil anomalies identified in 2012 by Ryan Gold
Corp., and to provide a subsurface context to the geology through RAB
drilling.

Five main target areas have been identified on the property to
date: Charon, Styx, Nyx, Hydra and Cerberus. The first four appear to
have mineralization associated with the interplay between a series of
limestone beds and volcanic dykes, while Cerberus appears to be more
vein hosted gold and silver in nature.

Charon Target

The Charon Target is an area approximately 2.5km by 2km in the
northeastern corner of Pluto. In 2012, soil samples from this site
returned grades up to 15.05g/t gold along a 1km 'band'. Field work
associated these grades with a fairly flat-lying limestone unit within
the schist, that have become mineralized to skarns / marbles where it
was intruded by small scale volcanic (rhyolite / dacite) dykes.

The aim of the 2017 program in this area was primarily to gather
subsurface data through drilling to better understand the geology and
to confirm mineralization at depth. Targeting of the drill holes was
based largely on results from a ground geophysical survey (IP) that
showed bands of low and high resistivity that related to limestone and
schist respectively when traced to surface. Collars were spaced along a
spur from the main ridge on spots where the drill could sit without
interference from talus.

Drill results were as follows:

//st

* 17-CRN-01
* 6.10m @ 0.74g/t Au and 1.67% Cu (4.57m to 10.67m)

//et

17-CRN-02

//st

* 15.24m @ 1.05g/t Au (21.34m to 36.58m), including 3.05m @ 3.81g/t Au
(22.68m to 25.91m)

//et

17-CRN-03

//st

* 3.05m @ 0.12% Cu (76.2m to 79.25m)
* 1.53m @ 0.27% Cu (92.96m to 94.49m)

//et

17-CRN-04

//st

* No significant results

//et

17-CRN-05

//st

* No significant results

//et

17-CRN-06

//st

* 3.05m @ 3.28g/t Au (3.05m to 6.10m)

//et

17-CRN-07

//st

* 32.0m @ 0.14% Cu (from 56.39m to 88.39m)

//et

17-CRN-08

//st

* 7.62m @ 0.24% Cu (from 83.82m to 91.44m)

//et

These results have conclusively proven that the mineralization is
present at depth and is not just from gossanous surficial material. The
copper and gold are associated with sulphide-minerals in the limestone
units, sometimes with significant silver from trace to 35g/t in samples
from the Charon drill holes. Drill holes 17-CRN-01 through to 17-CRN-06
are from one spur line, while 17-CRN-07 and 17-CRN-08 represent a step
out 600m to the east. Further studies are currently underway to
understand the relationships in the ore mineralogy.

Hydra Target

Hydra lies 6km to the southwest of Charon, and represents another
soil anomaly that was related to limestone bands. The decision was made
to drill four holes at Hydra to compare with the geology and
mineralization at Charon.

Hole 17-HYD-02 returned 10.67m at 0.4g/t gold from a limestone
unit, which had a similar mineralogy and setting to the Charon holes.
Although a lower grade, this does seem to infer that the two systems
are related. The limestone units were mapped in several locations
between Charon and Hydra, covering an area of 6km by 2km. Note that the
other three holes at Hydra returned no significant results.

These drill results are compelling as they were not specifically
targeted due to poor surface outcrop, but rather they prove that
mineralization is occurring at depth and is widespread. Data from this
program can now be reviewed and the targeting refined for future
exploration work.

Other Targets

The Styx and Nyx target zones are equivalent in size to Charon,
and bridge the area between that and Hydra. Styx runs along a river
valley, and in several places the limestone beds can be seen
outcropping. It is also apparent that an extensive arm of intrusive
rhyolite pervades into this area. Soil samples taken during the 2012
sampling program shows a concentration of Cu-Au anomalies along the
contact with the intrusive rock.

Nyx lies to the south of the same rhyolitic arm, but also seems to
be coincident with a dioritic intrusive.

Cerberus lies 2.5km east of Charon, and mineralization relates to
quartz veins along the edge of granodioritic intrusive material rather
than the skarns we see elsewhere on the property. Sampling in this area
produced samples ranging from trace to 2.06g/t gold and from trace to
333g/t silver (please refer to August 22, 2017 press release for full
details).

Results from other properties in the Yukon portfolio are pending
and will be released in due course.

QA/QC

The Company maintains a rigorous QA/QC program with respect to the
preparation, shipping, analysis and checking of all samples and data
from the properties. Quality control for field sampling and drill
samples at the Company's projects covers the complete chain of custody
of samples, including sample handling procedures and analytical-related
work, plus the insertion of standard and blank materials. The QA/QC
program also includes data verification procedures. ALS Laboratories in
Vancouver, Canada (ISO 17025:2005 accreditation) assayed all grab
samples from the current field program using fire assay and ICP Mass
Spectroscopy methods. Drill samples were processed by Bureau Veritas
Labs in Vancouver, Canada (ISO9001:2008 accreditation).

The technical information contained in this news release has been
approved by Andy Randell, P. Geo., Vice President, Exploration of
StrikePoint Gold. Mr. Randell is a qualified person as defined in NI
43-101.

For further information, please review the Corporate Presentation
on the StrikePoint Gold Inc. website for a more detailed, comprehensive
review of the 2017 exploration program:
http://www.strikepointgold.com/images/Yukon-Properties-Presentation.pdf.


ON BEHALF OF THE BOARD of STRIKEPOINT GOLD INC.
Shawn Khunkhun, CEO and Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for SKP-V
Date: 2017/10/19
Closing Price: 0.16

TEL:  604-602-1440  Shawn Khunkhun
StrikePoint Gold Inc.
FAX:  604-685-5777
EMAIL:  sk@strikepointgold.com
INTERNET:  www.strikepointgold.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1729500020TS11729500961-05353420171023