Source	MARKET NEWS
Date	10/30/2017
Time	07:22:45 AM

Company	 iMetal Resources Inc.
Title	Exploration Results from its Zone 1 Gold Target,





    CDNX Symbol: IMR











Press Release





Exploration Results from its Zone 1 Gold Target, Gowganda WestProperty, 
Gowganda, Ontario, --->@NEWS RELEASE
IMETAL RESOURCES INC. ("IMR-V")
- Exploration Results from its Zone 1 Gold Target, Gowganda West
- Property, Gowganda, Ontario,

iMetal Resources Inc. ("iMetal" or the "Company") is pleased to
provide an exploration update for its Gowganda West property. The
property is located ~17km west-southwest from the town of Gowganda,
Ontario, which is ~90km southwest of the city of Kirkland Lake. The
Kirkland Lake district is part of the Destor-Porcupine gold camp, one
of the most prolific gold mining districts in North America, with past
production exceeding 70-million ounces of gold. Mining and exploration
have been going on in this district since gold was first discovered
near Timmins in 1907.
The Gowganda West property has recently been increased in size
over the past several months through staking and acquisition to ~105
km2. Subsequent prospecting, rock sampling and assays have resulted in
the identification of four previously unknown gold, silver, copper, and
cobalt mineralized zones. This news release summarizes results to date
at the Zone 1 gold target. News releases from the additional targets
will be released as results become available.
Zone-1 Gold Target
The Zone 1 gold target is located ~300m from the south boundary of
Tahoe Resources Inc.'s claim block that hosts its JUBY gold deposit and
is similar in geological setting, mineralization and alteration. Tahoe
has reported that the JUBY gold deposit has Indicated resources of 1.09
million ounces of gold (26.6 million tonnes at 1.28 g/t Au) and
Inferred resources of 2.91 million ounces of gold (96.2 million tonnes
at 0.94 g/t Au).
Geological Setting
The property is underlain by Archean Timiskaming arenite,
silstone, wacke, argjilite and conglomerate with minor amount of jasper
clasts. Intrusive rocks include Matachewan diabase dykes and a series
of quartz-feldspar dykes. Proterozoic rocks comprise conglomerate,
sandstone, siltstone and argjillite of the Gowganda Formation of the
Huronian Cobalt Group.
Gold Mineralization
The Zone 1 Gold Target is located on claim 4373092, 500 m south of
the Juby Deposit, between Tyrrell and Leonard Townships at UTM
coordinates E0502704, N5270314.  The mineralized zone was exposed by
overburden stripping and is dominated by a 6-10 m wide shear zone
hosted in vertically-dipping and north striking arkose and siltstone.
The sedimentary rocks are altered by pervasive hematite, sericite,
pyrite with localized limonitic gossans. Gold-bearing
quartz-carbonate-sulphide veins vary in width between 2-5 cm and 20-30
cm and are localized both within and crosscutting the shear. Visually,
the gold mineralization occurs in the moderately to intensely altered
sedimentary rocks, is very fine grained and not visible in hand sample.
Gold assays range from 0.10 g/t to 1.90 g/t.
Continuation of Zone 1
Ongoing stripping of outcrop by iMetal prospectors has revealed a
possible northern extension of the Zone 1 gold target.
The extension occurs approximately 140 metres north of the Zone 1
Gold target in a similar geological setting and alteration of host
rocks with gold assays in representative rock chip samples varying
between 0.11 g/t to 6.47 g/t (Table 1).
//st
Sample    UTM East    UTM North    Au g/t

70914    502704    5270379    3.38
70916    502711    5270406    0.43
70918    502701    5270409    0.17
70920    502704    5270377    0.52
70921    502698    5270448    3.07
70926    502699    5270389    2.45
70927    502714    5270381    1.28
70928    502704    5270460    0.21
70929    502711    5270388    0.98
70931    502708    5270386    0.34
70932    502709    5270391    0.73
70933    502712    5270388    0.11
70935    502712    5270389    0.23
70945    502677    5270399    6.47
70946    502686    5270398    0.18
70948    502679    5270413    1.13
//et

Table 1. Summary of assays from the continuation of the Zone 1 Gold Target.
Assays by Swastika Laboratories (Ontario). UTM datum is NAD83 Zone 17.

Comparison with the Juby Gold Deposit
The lithology of the Zone 1 Gold Target is similar with the
lithologies, alteration and mineralization at the main zone of the Juby
gold deposit.  The mineralization at Juby occurs predominantly along
the Tyrrell Structural Zone, which strikes at 105 to 115degree and has
near vertical to vertical dips. It attains widths of between 25 and 100
m and hosts bleached Timiskaming argillite and conglomerate. The
sedimentary rocks are cut by abundant up to 2 m wide feldspar
porphyritic dykes and by variable quartz, carbonate and
quartz-carbonate veins, typically less than 5 cm across. Alteration
consists of weak to intense ankerite-albite-silica-sericite. Feldspar
porphyritic dykes are altered, mineralized and cut by veins and are
mainly proximal to the Juby Main Zone.
Ongoing Exploration
iMetal Resources is currently exploring its Gowganda West property
with a prospecting and rock program including channel sampling, outcrop
stripping and mapping. The aim is to provide a greater understanding of
the Zone 1 Gold Target, expand the zone by ongoing channel sampling,
geophysical surveys and test the extent of gold mineralization in three
dimensions by diamond drilling.
The technical content of this news release has been reviewed and
approved by Mark Fedikow, Ph.D. P.Geo., a qualified person as defined
under Ni 43-101.
This Press Release was prepared by iMetal Resources Inc. Neither
the TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the Policies of the TSX Venture Exchange) has
reviewed nor accepts responsibility for the adequacy or accuracy of
this release.
We Seek Safe Harbor

ON BEHALF OF THE BOARD OF DIRECTORS,

Brian Fagan

President & CEO, iMetal Resources Inc.

StocksAndSpeculations@gmail.com
Tel. (360) 224-7141
______________________________________
_______________________________________________
TSX Venture closing price for IMR-V
Date: 2017/10/27
Closing Price: 0.06
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1730200054TS11730201510-07211720171030