Source	CANADA NEWSWIRE
Date	10/31/2017
Time	06:31:48 AM

Company	 Engold Mines Ltd.
Title	EnGold Provides Lac La Hache Exploration Program Update





    CDNX Symbol: EGM











Press Release




" BC-EnGoldLacLaHache   10-31 0999
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^EnGold Provides Lac La Hache Exploration Program Update@

Aurizon Gold Resource Calculation Pending
VANCOUVER, Oct. 31, 2017 /CNW/ - David H. Brett, President & CEO, EnGold
Mines Ltd., (TSX-V: EGM, "EnGold" or the "Company") reports that EnGold
exploration work at the Company's 100% owned Lac La Hache Property in the
Cariboo Region of BC includes completion of 12 drill holes comprising 4,350
metres and the near completion of a resource calculation for the Aurizon Gold
Zone.
Drilling in the Company's current phase has targeted three separate
priority areas prospective for high grade skarn-style copper, gold, silver
mineralization found at the Company's 2017 discovery and the Spout Deposit.
Drill hole G17-29 at the discovery area successfully extended the mineralized
zone an additional 71m to the southwest, intersecting 21m (true width) of
skarn-style mineralized horizon for which assays are pending. Of the 12 holes,
5 were step outs at the discovery area, 2 targeted the "G2" gravity anomaly
located 1.8km south east of the discovery, 2 targeted "G9" gravity/magnetic
anomaly west of the Spout Deposit, and three short holes were drilled in the
Berkey porphyry area. Maps showing the location of the drill holes and
anomalies can be found on the Company's website www.engold.ca
Results of four additional holes (G17-24, 26, 27, 34) at the discovery
area confirm ground geophysical responses, indicating the zone does not extend
to the west or immediate south of Hole G17-23, or west of Hole G17-15. New
modeling of the ground gravity data indicates a strong anomaly located
northeast of the current drilling. Additional ground gravity surveying is
required and is planned within the next two weeks to better define and
constrain this very encouraging anomaly.
Plans for the remainder of the drill program include testing of the new
extended northeastern anomaly at discovery area, and drilling of untested,
down-dip areas of the Spout North high-grade copper deposit. Previous drilling
of the vertically dipping Spout North skarn structure focused primarily on
near surface (to 60 metres) mineralization in support of a bulk tonnage, open
pit resource model, whereas EnGold envisages a potential high-grade
underground model for the Spout Deposit.
Historical drilling at Spout North has produced some impressive results.
DDH SL92-01, which was drilled down the dip of the North Zone structure,
intersected 64 m (core length, not true width) grading 1.2 % Cu, before
exiting into the footwall rocks. Subsequent drilling was better angled to cut
through the vertical North zone, predominantly at shallow depths: SL10-18 cut
8 m from 35 - 43 m downhole (5.7 m true width), grading 5.4 % Cu, 0.9 gpt Au,
19.4 gpt Ag, 40 % Fe. Deeper intersections, below 100 m vertically are rare:
SL11-72 intersected 8 m from 372.1 - 380.1m downhole (more than 300 m
vertically below surface, >2 m true width) grading 1.73 % Cu, 0.43 gpt Au, 4.6
gpt Ag, 47.5 % Fe. The zone remains open to depth and on strike to the
northwest.
The Aurizon Gold resource estimate is being prepared by independent
geologist Garth Kirkham, P. Geo., of Kirkham Geosystems Ltd, who is a
"qualified person" within the meaning of National Instrument 43-101.
Disclosure of the estimate is expected before the end of November 2017.
EnGold has paused the drill program for two weeks to allow for rotation
of the Company's geological and technical staff. The program will recommence
approximately November 15th and continue into mid December 2017.
"To date only about 40% of the expected Fall 2017 drilling has been
completed, with initial testing at 2 of several new gravity anomalies in
addition to the discovery area, said VP of Exploration Rob Shives, P.Geo. "We
are evaluating those results while extending the discovery area through
additional gravity surveying and drilling in large step-outs. We encouraged by
the emerging extension of a relatively larger, stronger, anomaly to the
northeast of discovery and look forward to drill testing there, following a
brief break."
"EnGold's objective is to building tonnes to include in a possible
high-grade, low-cost underground copper-gold-silver mining operation," said
EnGold President & CEO David Brett. "We envisage the high gold/copper/silver
Aurizon material in the south and the copper/gold/silver skarn material from
the northern part of the property contributing tonnes to our overall economic
model."
The two holes drilled at the G2 anomaly did not encounter the anticipated
skarn mineralization and the strong gravity data remains unexplained. Hole
G2-17-28, drilled to 562 m downhole (487 vertical) intersected a grey,
fine-grained intrusion, with a 78 m (downhole) interval of volcanics
containing some magnetite and chalcopyrite veinlets. Within the volcanics, a
6m interval graded 0.45 % Cu, including 1 m grading 1.11 % Cu. At G9, an area
also described by the Company as "Spout West," SW17-31 encountered
unmineralized massive augite-phyric flows with densities above 3.0 (to 3.2)
which may in part explain the very large and strong gravity anomaly in that
area. Hole SW17-35, drilled from the same collar as SW17-31at 45-degree angle
to a depth of 554.43m, encountered narrow (1-2m) zones of moderate
magnetite-copper mineralization.
About EnGold
EnGold (www.engold.ca) is focused on exploring its 100% owned mineral
property located near the town of Lac La Hache in BC's prolific Cariboo mining
region. EnGold's corporate philosophy rests on three interdependent pillars:
Environment, Engagement and Gold. Through sound environmental stewardship,
commitment to transparent engagement with local communities, the Company is
dedicated to driving exceptional shareholder and stakeholder value by
discovering and developing mineral resources.
Rob Shives P.Geo., VP Exploration and a Qualified Person as defined under
National Instrument 43-101, has reviewed and approved the technical content of
this release.
Engold Mines Ltd.Per/David Brett, MBAPresident & CEO
This news release may contain "forward?looking statements". Readers are
cautioned that any such statements are not guarantees of future performance
and that actual development or results may vary materially from those in these
"forward looking statements."Neither the TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in the policies of the
TSX Venture Exchange) accepts responsibility for the adequacy or accuracy of
this release.
SOURCE Engold Mines Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/October2017/31/c5868.html

-0-                           10/31/2017
/For further information: David Brett, 604-682-2421 or david(at)engold.ca/
(GWRRF EGM.)

CO:  Engold Mines Ltd.
ST:  British Columbia
IN:  MIN MNG PRM
SU:

-30-