Source	Marketwire
Date	10/31/2017
Time	06:00:44 AM

Company	 KENADYR MINING (HOLDINGS) CORP.
Title	Kenadyr Mining Announces assay results from the  first 9 drill holes at 
The East Zone





    CDNX Symbol: KEN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kenadyr Mining (Holdings) Corp.

TSX VENTURE SYMBOL: KEN
OTCQB SYMBOL: KNDYF
FRANKFURT SYMBOL: KM0

October 31, 2017

Kenadyr Mining Announces assay results from the  first 9 drill holes at The 
East Zone

Defines first drill section typical of the adjoining TBL Orebody

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 31, 2017) - Kenadyr Mining 
(Holdings) Corp. (TSX VENTURE:KEN)(OTCQB:KNDYF)(FRANKFURT:KM0) (the 
"Corporation" or "Kenadyr") is pleased to announce the first 9 drill holes at 
The East Zone.

East Zone Drilling

Drilling At Kenadyr's East Zone directly adjacent to Zijin's TBL Mine: 
http://media3.marketwire.com/docs/1104117_1.jpg

The Corporation has completed drilling to define the extent of mineralization 
on the section approximately 100 meters from the boundary to Zijin Mining Group 
Co Ltd.'s ("Zijin") Taldy Bulak Levoberejnyi ("TBL") Mine, and directly on 
strike from the last mine section of the TBL Orebody. Although the TBL Mine is 
highly variable in shape and grade from section to section, the section defined 
on Kenadyr's Borubai License is typical of the sections within the TBL Orebody.

South Zone

As well, previously announced Hole SZ-1-17 (40m @ 6.17 g/t Au and 5m @ 5.8 g/t 
Au) intersected what appears to be the extension of the TBL Orebody to the 
South, an area of gold mineralization (partially defined by extensive (over 
98,200 meters on the Borubai Licenses) historic Soviet drilling). The 
mineralized zones extending in both directions onto the Borubai License (South 
Zone and East Zone) are open along strike, and well mineralized at the current 
extent of drilling.

Ongoing Program

Kenadyr is continuing with the drill program on the East Zone, initially 
stepping out drill fans on 50 meter sections, to test for the strike extension 
of the mineralization defined in these initial 9 drill holes.

The mineralized zone (East Zone) on Kenadyr's Borubai License is rising in 
elevation (as compared to the TBL orebody) and the Corporation intends to 
evaluate the East Zone as a potential open pit mining target.

Surrounding TBL Mine operated by Zijin: 
http://media3.marketwire.com/docs/1104117_2.jpg

A table of significant drill intersections from the initial 9 drill holes are 
tabled below:

/T/

----------------------------------------------------------------------------
Hole Number                          From        To       Interval    g/t Au
----------------------------------------------------------------------------
EZ-1                                  151       201      50 meters      8.15
----------------------------------------------------------------------------
including                             161       179      18 meters      12.8
----------------------------------------------------------------------------
EZ-2                                  110       116       6 meters      1.13
----------------------------------------------------------------------------
EZ-2                                  132       136       4 meters      1.17
----------------------------------------------------------------------------
EZ-2                                  141       151      10 meters      1.03
----------------------------------------------------------------------------
EZ-2                                  194       200       6 meters      1.18
----------------------------------------------------------------------------
EZ-2                                  208       231      23 meters      2.19
----------------------------------------------------------------------------
including                             213       229      16 meters      2.93
----------------------------------------------------------------------------
including                             215       224       9 meters      3.55
----------------------------------------------------------------------------
EZ-3                                  190       250      60 meters      1.01
----------------------------------------------------------------------------
including                             199       222      23 meters      1.23
----------------------------------------------------------------------------
including                             199       202       3 meters      2.59
----------------------------------------------------------------------------
EZ-3                                  315       316        1 meter      2.27
----------------------------------------------------------------------------
EZ-4                                  180       209      29 meters      1.44
----------------------------------------------------------------------------
including                             188       194       6 meters      2.01
----------------------------------------------------------------------------
EZ-4                                  237       239       2 meters      1.45
----------------------------------------------------------------------------
EZ-5                                  152       162      10 meters      1.02
----------------------------------------------------------------------------
includung                             156       160       4 meters      1.53
----------------------------------------------------------------------------
EZ-5                                  174       212      38 meters         1
----------------------------------------------------------------------------
EZ-6                                  178       197      21 meters      1.67
----------------------------------------------------------------------------
including                             182       191       9 meters      2.52
----------------------------------------------------------------------------
EZ-6                                  208       234      26 meters       1.2
----------------------------------------------------------------------------
including                             214       215        1 meter      2.04
----------------------------------------------------------------------------
including                             226       227        1 meter      2.64
----------------------------------------------------------------------------
229       233       4 meters       2.2
----------------------------------------------------------------------------
EZ-6                                  256       260       4 meters      1.56
----------------------------------------------------------------------------
EZ-7                                  190       202      12 meters       2.4
----------------------------------------------------------------------------
EZ-7                                  207       208        1 meter      2.48
----------------------------------------------------------------------------
EZ-7                                  216       227      11 meters      1.21
----------------------------------------------------------------------------
including                             217       219       2 meters       3.4
----------------------------------------------------------------------------
EZ-8                                  146       208      62 meters       2.2
----------------------------------------------------------------------------
including                             160       174      14 meters      3.15
----------------------------------------------------------------------------
including                             166       168       2 meters      5.67
----------------------------------------------------------------------------
including                             172       173        1 meter      5.42
----------------------------------------------------------------------------
including                             186       204      18 meters      3.79
----------------------------------------------------------------------------
including                             193       198       5 meters     10.41
----------------------------------------------------------------------------
EZ-8                                  212       222      10 meters      1.66
----------------------------------------------------------------------------
EZ-9                                  187       198      11 meters      2.56
----------------------------------------------------------------------------
including                             187       195       8 meters      3.19
----------------------------------------------------------------------------
including                             190       193       3 meters       6.2
----------------------------------------------------------------------------

/T/

The Corporation is confident that these intersections are approximate 'true 
widths'.

Kenadyr Drill Plan: http://media3.marketwire.com/docs/1104117_3.jpg and 
http://media3.marketwire.com/docs/1104117_4.jpg

Typical TBL Mine Sections with Kenadyr Drill Section to Scale: 
http://media3.marketwire.com/docs/1104117_5.jpg and 
http://media3.marketwire.com/docs/1104117_6.jpg

TBL Mine Sections with Kenadyr EZ-1 Section for Comparison (to scale): 
http://media3.marketwire.com/docs/1104117_7.jpg and 
http://media3.marketwire.com/docs/1104117_8.jpg

http://media3.marketwire.com/docs/1104117_9.jpg

South Zone drill section for SZ-1-17 - 40m @ 6.17 g/t Au and 5m @ 5.8 g/t Au: 
http://media3.marketwire.com/docs/1104117_10.jpg

http://media3.marketwire.com/docs/1104117_11.jpg

Kenadyr's Borubai project comprises a 100-per-cent-owned exploration license 
covering a contiguous 164-square-kilometre land package that encircles the 
Zijin/Kygysaltyn newly constructed and operational TBL mine, in northern Kyrgyz 
Republic.

Zijin, the majority owner of the TBL mine, is one of China's largest gold 
producers, second- largest copper and zinc producer, as well as a major 
producer of tungsten and iron ore (source: Zijin website). According to a news 
release published by Zijin. on Aug. 15, 2011, the national resources table of 
Kyrgyz Republic stated that the TBL field contains (C1 plus C2) 8,906,100 
tonnes of gold ore (the average grade is 7.23 grams per tonne). The TBL mine is 
designed to produce 125,000 ounces of gold per annum. The TBL mine deposit is 
directly adjacent to Kenadyr's initial drill targets, the South Zone and East 
Zone, which were previously drilled by the Soviets, with drilling on the 
Borubai License exceeding 98,000 meters.

Readers are cautioned that the historical resource and reserve estimates 
relating to the TBL mine do not extend to the Borubai project. Kenadyr has not 
independently verified the information with respect to the TBL mine provided in 
this news release and it is not necessarily indicative of the mineralization on 
the Borubai project. Kenadyr is not aware of the resource and reserve 
categories, or the key assumptions, parameters and methods used to prepare the 
estimates on Zijin's TBL mine. The historical estimates on the TBL mine are not 
current mineral resources or mineral reserves as defined in National Instrument 
43-101. Kenadyr considers the historical estimates on the TBL mine disclosed in 
this news release to be relevant to investors for the purpose of understanding 
Kenadyr's current drill program and exploration strategy.

Kenadyr's Borubai project, which surrounds the TBL mine, has been the subject 
of extensive historic exploration including drilling (98,200 metres in 184 
diamond drill holes), trenching (13,800 cumulative metres), bulldozer cuts 
(33,400 cumulative metres), geologic mapping at 1:25,000 and 1:50,000 scales, 
ridge, spur and grid soil geochemistry for multi-elements (14,200 samples), 
rock geochemical sampling (2,320 samples), pan concentrate sampling (790 
samples), 100 metres of adits, and 184 metres of underground raises. 
Additionally, the entire area has been subject to airborne magnetic, 
radiometric and gravity surveys, as well as ground-based resistivity and 
induced polarization surveys. Additional high grade gold targets exist 
throughout the Borubai license. The entire license has been subject to 
extensive geochemical and geophysical surveys, with follow up trenching and 
drilling on only a few of the identified anomalies.

Additional information in respect of the Corporation's business and the Borubai 
project is available in the Corporation's Annual Information Form dated April 
28, 2017, available under the Corporation's profile on SEDAR.

Kenadyr has an expert team of mine developers with considerable local and 
regulatory knowledge, led by Chief Executive Officer Dr. Alex Becker, who has 
operated successfully in the country for much of the past 20 years. The board 
and management team includes; R. Stuart (Tookie) Angus (Chairman), Alexander 
Becker (Chief Executive Officer), Bryan Slusarchuk (President), Douglas J. 
Kirwin (Director), Brian Lueck (Director) and Kevin Ma (Chief Financial 
Officer). Mark Eaton will act as an adviser to the Corporation.

Brian Lueck, P. Geo, a director of Kenadyr and a qualified person as defined by 
National Instrument 43-101, has reviewed and approved the technical information 
in this news release.

Appointment of Mr. Michael Velletta to Board

In additional news, Mr. Velleta has been appointed to the board of directors of 
Kenadyr. Mr. Veletta was one of the original directors of Kenadyr, as a private 
company, and will re-join the board effective November 1, 2017.

On behalf of Kenadyr Mining (Holdings) Corp.

Dr. Alexander Becker Chief Executive Officer and Director

For more information, visit www.kenadyr.com.

Neither the TSX Venture Exchange nor its regulation services provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Cautionary Note Regarding Forward-Looking Statements

This news release contains forward-looking statements relating to the future 
operations of the Corporation and other statements that are not historical 
facts. Forward-looking statements are often identified by terms such as "will", 
"may", "should", "anticipate", "expects" and similar expressions. All 
statements other than statements of historical fact, included in this release, 
including, without limitation, statements regarding the future plans and 
objectives of the

Corporation are forward-looking statements that involve risks and 
uncertainties. There can be no assurance that such statements will prove to be 
accurate and actual results and future events could differ materially from 
those anticipated in such statements. Important factors that could cause actual 
results to differ materially from the Corporation's expectations include the 
success for failure of the Corporation's proposed exploration activities on the 
Borubai Project or its resource potential relative to the TBL Mine and other 
risks detailed from time to time in the filings made by the Corporation with 
securities regulations.
The reader is cautioned that assumptions used in the preparation of any 
forward-looking information may prove to be incorrect. Events or circumstances 
may cause actual results to differ materially from those predicted, as a result 
of numerous known and unknown risks, uncertainties, and other factors, many of 
which are beyond the control of the Corporation. The reader is cautioned not to 
place undue reliance on any forward-looking information. Such information, 
although considered reasonable by management at the time of preparation, may 
prove to be incorrect and actual results may differ materially from those 
anticipated. Forward-looking statements contained in this news release are 
expressly qualified by this cautionary statement. The forward-looking 
statements contained in this news release are made as of the date of this news 
release and the Corporation will update or revise publicly any of the included 
forward- looking statements as expressly required by Canadian securities law.

- 30 -

CONTACT INFO:

Kenadyr Mining (Holdings) Corp.
Kevin Ma
CFO
(604) 687-7130
info@kenadyr.com
www.kenadyr.com

INDUSTRY: Financial Services - Venture Capital
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=599958015