Source	CANADA NEWSWIRE
Date	11/26/2019
Time	06:04:47 AM

Company	 Colonial Coal International Corp.
Title	Colonial Coal Announces Results of a Preliminary Economic Assessment for
an Open Pit Only Mine at its Huguenot Project





    CDNX Symbol: CAD











Press Release




" BC-Colonial-Open-Pit   11-26 1599
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.425493:
^Colonial Coal Announces Results of a Preliminary Economic Assessment for
an Open Pit Only Mine at its Huguenot Project@

VANCOUVER, Nov. 26, 2019 /CNW/ - Colonial Coal International Corp.
(TSX-V: CAD) (the "Company" or "Colonial Coal"). David Austin, Colonial Coal's
President and CEO, is pleased to announce the results of a recent Preliminary
Economic Assessment (the "PEA") for a stand-alone open pit option at the
Company's 100% owned Huguenot coking coal property (the "Huguenot Project")
located approximately 85 kilometres southeast of Tumbler Ridge in northeast
British Columbia.
This PEA for the stand-alone open pit mine on the Huguenot Project is
preliminary in nature and there is no certainty that the forecast results
stated in the PEA will be realized. In addition, the PEA includes inferred
mineral resources that are considered too speculative geologically to have the
economic considerations applied to them that would enable them to be
categorized as mineral reserves, and there is no certainly that the
preliminary economic assessment will be realized. Furthermore, mineral
resources that are not mineral reserves do not have demonstrated economic
viability.
The PEA report, prepared by Stantec Consulting Services Inc. ("Stantec")
in accordance with CSA National Instrument 43-101 ("NI 43-101") standards,
will be completed and filed on SEDAR (the System for Electronic Document
Analysis and Retrieval) within 45 days. The results of the PEA show that the
Huguenot Project continues to demonstrate positive economics, has viable
development options and is worthy of advancement.
The current PEA report builds upon an original PEA report prepared in
2013 by Norwest Corporation that was updated in 2018 by Norwest, now Stantec,
using then current scoping level cost estimates and economic analyses. The
mining studies previously reported (September 24, 2013 and July 10, 2018 and
by way of corresponding 43-101 Technical Report filings) were based upon
exploiting the coking coal resources by a combination of open pit and
underground mining methods. During the 2018 update, Stantec recognized an
opportunity to significantly expand the open pit to higher stripping ratios,
with correspondingly higher recoverable tonnages of surface mineable coal,
thereby creating the opportunity to examine a surface stand-alone mining
option in a new PEA.
This PEA does not include any further evaluation of the underground
resources nor any potentially mineable coal associated with these resources.
For the current study, Stantec used previously reported surface mineable
resources to develop a revised conceptual mine plan to exploit the coal
resources utilizing a stand-alone open pit, in contrast to the previous
approach of a combined open pit and underground mine. Stantec completed a more
detailed analysis of the open pit design and equipment selection than was
carried out previously, that yielded larger mineable open pit tonnage, longer
mine life and a lower cost mining operation. In addition, alternative means of
product coal transportation were considered which resulted in a revised plan
to transport coal by conventional haul trucks from the mine to the existing
rail line south of Tumbler Ridge, as opposed to the previous concept of direct
rail transport from the mine. The trucking concept has the advantage of lower
capital costs, lower risk and a shorter construction schedule than the rail
option.
Highlights of the revised PEA report are summarized below. All costs are
in US dollars but, where Canadian dollar equivalents are provided, they have
been converted using an exchange rate of US$1.00 equals CAD$1.316.
A summary of the financial analyses is presented in the following tables;
the results show the after tax (including royalty) net present values (NPVs)
at various discount rates and internal rates of return (IRRs) for a range of
coal prices. For the benchmark coal price, Stantec has used US$174 per tonne.
They note that, while a discount may be applied to the benchmark price for
Huguenot product coal, they consider the potential discount to be within the
range of values presented in the tables below.
The capital expenditures are based on two scenarios. The first scenario
assumes that all major mining equipment is purchased outright in the year in
which it is required for the mining operation. This includes replacements as
they are required over the life of the mine. The second scenario assumes that
the major mining equipment will be leased in the year in which it is required
for the mining operation and that replacements will also be leased when the
equipment needs to be replaced.

<<

--  Based on the purchased equipment scenario the financial analysis
suggests that the coal price required to achieve a zero NPV at discount
rates of 5%, 7.5% and 10%, respectively, is about US$113, US$120 and
US$125 per tonne. A coal price of US$137 per tonne is required for an
IRR of 15%.

--  Based on the leased equipment option the financial analysis suggests
that the coal price required to achieve a zero NPV at discount rates of
5%, 7.5% and 10%, respectively, is about US$114, US$119 and US$125 per
tonne. A coal price of US$137 per tonne is required for an IRR of 15%.

--  Measured and Indicated surface mineable coal resources total 132.0
million tonnes, with an additional Inferred resource of 0.5 million
tonnes. Not included in the current PEA are in-situ underground mineable
resources totaling 145.7 million tonnes (Measured and Indicated) and
118.7 million tonnes classified as Inferred.

--  The current PEA economic analysis is based on a conceptual open pit mine
plan targeting 99 million run-of-mine ("ROM") tonnes of resource at an
overall stripping ratio of 10.5:1 (bank cubic metres (bcm):ROM tonnes),
yielding 72 million tonnes of product coal over a mine life of 27 years.
The previous PEA identified a smaller open pit with ROM tonnage of 56
million tonnes at a stripping ratio of 8.6:1, that yielded 39 million
tonnes of product coal over 13 years.

--  Projected clean coal production from open pit mining operations ranges
from 0.7 million tonnes per annum ("Mt/a") to 3.0 Mt/a, averaging
approximately 2.7 Mt/a.

--  Potential coal production is identified as hard coking coal similar to
coking coal currently exported from northeast British Columbia.

--  The stand-alone open pit cash operating costs for the purchased
equipment scenario are estimated at US$55.08 per tonne of product coal
at the mine gate. The cash operating costs for the leased equipment
scenario are estimated at US$61.47 per tonne.

--  Estimated direct operating plus offsite costs for the purchased
equipment scenario (i.e., FOB cost), total US$91.90 per clean tonne
(excluding production taxes and royalties). The FOB cost for the leased
equipment scenario is estimated at US$98.29 per clean tonne (excluding
production taxes and royalties)

--  Pre-production capital cost for the proposed mine in the purchased
equipment scenario is estimated at US$510 million, with additional
sustaining capital of US$215 million over the life-of-mine (LOM).
Pre-production capital cost in the leased equipment scenario is
estimated at US$303 million, with additional sustaining capital of US$42
million over the LOM.

--  The Huguenot Project's proposed payback of initial capital is estimated
within four years from start-up of operations for both scenarios.
<>>
This press release has been reviewed and the scientific and technical
disclosure disclosed herein approved by Derek Loveday, P.Geo., of Stantec, a
Professional Geologist and a Qualified Person as defined in NI 43-101.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
About Colonial Coal International Corp.
Colonial Coal is a publicly traded coal corporation in British Columbia
that focuses primarily on coking coal projects. The northeast Coal Block of
British Columbia, within which our Corporation's projects are located, hosts a
number of proven deposits and has been the subject of M&A activities by
Anglo-American and others. Additional information can be found on the
Company's website www.ccoal.ca or by viewing the Company's filings at
www.sedar.com.
Forward-Looking Information
Information set forth in this news release may involve forward-looking
statements. Forward-looking statements are statements that relate to future,
not past, events. In this context, forward-looking statements often address a
company's expected future business and financial performance, and often
contain words such as "anticipate", "believe", "plan", "estimate", "expect",
and "intend", statements that an action or event "may", "might", "could",
"should", or "will" be taken or occur, or other similar expressions. By their
nature, forward-looking statements involve known and unknown risks,
uncertainties and other factors which may cause our actual results,
performance or achievements, or other future events, to be materially
different from any future results, performance or achievements expressed or
implied by such forward-looking statements. Such factors include, among
others, the following risks: risks associated with marketing and sale of
securities; the need for additional financing; reliance on key personnel; the
potential for conflicts of interest among certain officers or directors with
certain other projects; and the volatility of common share price and volume.
Forward-looking statements are made based on management's beliefs, estimates
and opinions on the date that statements are made and except as required by
law, the Company undertakes no obligation to update forward-looking statements
if these beliefs, estimates and opinions or other circumstances should change.
Investors are cautioned against attributing undue certainty to forward-looking
statements.
THE FORWARD-LOOKING INFORMATION CONTAINED IN THIS NEWS RELEASE REPRESENTS
THE EXPECTATIONS OF THE COMPANY AS OF THE DATE OF THIS NEWS RELEASE AND,
ACCORDINGLY, IS SUBJECT TO CHANGE AFTER SUCH DATE. READERS SHOULD NOT PLACE
UNDUE IMPORTANCE ON FORWARD-LOOKING INFORMATION AND SHOULD NOT RELY UPON THIS
INFORMATION AS OF ANY OTHER DATE. WHILE THE COMPANY MAY ELECT TO, IT DOES NOT
UNDERTAKE TO UPDATE THIS INFORMATION AT ANY PARTICULAR TIME EXCEPT AS REQUIRED
IN ACCORDANCE WITH APPLICABLE SECURITIES LEGISLATION.
SOURCE Colonial Coal International Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/November2019/26/c8342.html

-0-                           11/26/2019
/For further information: Colonial Coal International Corp., Shane
Austin, 604.568.4962, saustin(at)ccoal.ca, www.ccoal.ca/
/Web Site: www.ccoal.ca /
(CAD.)

CO:  Colonial Coal International Corp.
ST:  British Columbia
IN:  MNG MIN
SU:

-30-