Source	CANADA NEWSWIRE
Date	01/18/2021
Time	04:02:39 AM

Company	 Canada Nickel Company Inc.
Title	Amended and Restated NI 43-101 Technical Report on the Mineral Resource
Estimates Crawford Nickel-Cobalt Sulphide Project: Main Zone (Update) and
East Zone (Initial) Deposits





    CDNX Symbol: CNC











Press Release




" BC-CanadaNickel-NI43-101   01-18 2149
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.518348:
^Amended and Restated NI 43-101 Technical Report on the Mineral Resource
Estimates Crawford Nickel-Cobalt Sulphide Project: Main Zone (Update) and
East Zone (Initial) Deposits@

TORONTO, Jan. 18, 2021 /CNW/ - Canada Nickel Company Inc. (TSXV: CNC)
("Canada Nickel" or the "Company") is pleased to announce the filing on SEDAR
of an amended and restated independent National Instrument 43-101 - Standards
of Disclosure for Mineral Projects ("NI 43-101") entitled: "Independent
Technical Report and Mineral Resource Estimates Crawford Nickel-Cobalt
Sulphide Project: Main Zone (Update) and East Zone (Initial) Deposits"
prepared by Scott Jobin-Bevans (Ph.D., PMP, P.Geo.), John Siriunas (M.A.Sc.,
P.Eng.) and David Penswick (P.Eng.) (the "Amended Technical Report").
The Amended Technical Report can be found under the Company's profile at
www.sedar.com. The Amended Technical Report has been filed further to a review
by staff of the Ontario Securities Commission (the "OSC"). The OSC review is
now complete.
The Amended Technical Report includes a conceptual pit envelope
constraint in order to demonstrate reasonable prospects for eventual economic
extraction and updated mineral resource tables. Prior mineral resource
estimates, as previously disclosed in the December 4, 2020 Technical Report,
were not constrained by conceptual pit envelopes. The addition of a pit
constraint resulted in no change to the Measured & Indicated resource in the
Higher Grade Core of the Main Zone, a 1.5 kt reduction in contained nickel in
the overall Measured and Indicated resource to 1,690 kt, and a 335 kt
reduction in contained nickel from the original Inferred resource to 1,183 kt.
90% of the overall reduction in Inferred resources occurred at depths below
300 metres.
In addition, the gram per tonne (g/t) assay values for Palladium (Pd),
Platinum (Pt), and Palladium + Platinum (Pd + Pt) included in Table 10-2 of
the Amended Technical Report have been corrected for holes CR19-05 to CR19-13.
Disclosure of explorations targets for the Main Zone Pd + Pt reef, two
East Zone Pd + Pt reefs and the East Zone nickel domains was also revised to
comply with subsection 2.3(2) of NI 43-101.
Table 1 - Amended Total Mineral Resource Estimate for the Crawford
Nickel-Cobalt Sulphide Project, Ontario


Mineral Resource Estimate

Contained

---

DOMAIN

CLASS  TONNES (Mt)      Ni (%)                      Co (%)     Fe (%)       S 
(%)       Pd (g/t)        Pt (g/t)                     Ni (kt)          Co 
(kt)        Fe (Mt)        Pd (koz)      Pt (koz)

---

MAIN
HIGHER
Measured            151.7         0.32                         0.013         
6.25        0.20           0.029           0.012                         
482.2           19.9            9.5           141            57
GRADE
ZONE

---

Indicated                     128.6         0.30        
0.013                          6.37         0.16       0.027           
0.013                  391.8                   16.5            8.2            
111            52

---

Mea+Ind                      280.2         0.31        
0.013                          6.31         0.18       0.028           
0.012                  873.9                   36.4           17.7            
252           108

---

Inferred                      109.9         0.29        
0.013                          6.66         0.09       0.026           
0.013                  315.0                   14.0            7.3             
93            47

---

MAIN LOWER
Measured             62.5         0.22                         0.013         
6.83        0.05                                                       
135.1            8.2            4.3
GRADE ZONE

---

Indicated                     263.2         0.21        
0.013                          6.90         
0.04                                            557.0                   
34.6           18.2

---

Mea+Ind                      325.6         0.21        
0.013                          6.89         
0.04                                            692.1                   
42.9           22.4

---

Inferred                      210.2         0.21        
0.013                          6.87         
0.06                                            444.9                   
27.1           14.4

---

EAST ZONE
Measured             25.8         0.26                         0.012         
6.02        0.04                                                        
67.4            3.2            1.6

---

Indicated                      21.8         0.26        
0.013                          6.20         
0.04                                             56.2                    
2.7            1.3

---

Mea+Ind                       47.5         0.26        
0.013                          6.11         
0.04                                            123.6                    
6.0            2.9

---

Inferred                      176.7         0.24        
0.013                          6.63         
0.04                                            423.5                   
22.6           11.7

---

TOTAL
Mea+Ind              653         0.26                         0.013         
6.58        0.10           0.028           0.012                       
1,689.6           85.2           43.0           252           108

---

Inferred                        497         0.24        
0.013                          6.74         0.06       0.026           
0.013                1,183.3                   63.8           33.5             
93            47

---




1.         The independent Qualified Person for
the Mineral Resource Estimate, as
defined by NI 43-101, is Dr. Scott
Jobin-Bevans (P.Geo., APGO (number sign)0183),
of Caracle Creek International
Consulting Inc. and Atticus Chile
S.A.  The effective date of the
Mineral Resource Estimate is December
11, 2020.





2.         These Mineral Resources are not Mineral
Reserves as they do not have
demonstrated economic viability. The
quantity and grade of reported
Inferred Resources in this Mineral
Resource Estimate are uncertain in
nature and there has been insufficient
exploration to define these Inferred
Resources as Indicated or Measured,
however it is reasonably expected that
the majority of Inferred Mineral
Resources could be upgraded to
Indicated Mineral Resources with
continued exploration.





3.         A cut-off grade of 0.15% Ni was used
for the low-grade domains (Main and
East zones) and cut-off grades of
0.25% Ni (Main Zone) and 0.21% Ni
(East Zone) were used for the high-
grade domains. Cut-offs were
determined on the basis of core assay
geostatistics and drill core
lithologies for the deposit, and by
comparison to analogous deposit
types.  Given the current stage of
the Project, the mineral resources
contained within the Main and East
zone deposits have not been
constrained by open pit optimization.
The Company is planning to complete
open pit optimization and present
pit-constrained mineral resources as
part of its Preliminary Economic
Assessment ("PEA") scheduled to be
completed by the end of the first
quarter, 2021.





4.         Geological and block models for the
Mineral Resource Estimate used data
from a total of 62 surface drill holes
(51 in the Main Zone and 11 in the
East Zone), completed by Spruce Ridge
Resources (4 holes in 2018) and Noble
Mineral Exploration and Canada Nickel
Company (58 holes in 2019-2020). The
drill database was validated prior to
resource estimation and QA/QC checks
were made using industry-standard
control charts for blanks, core
duplicates and commercial certified
reference material inserted into assay
batches by CNC and by comparison of
umpire assays performed at a second
laboratory.





5.         Estimates in Table 1 have been rounded
to two significant figures.





6.         The mineral resource estimates have
also been revised in the Amended
Technical Report to include a
conceptual pit envelope constraint
that was developed using the
optimization parameters included in
the Amended Technical Report. Metal
prices used (US$) were $7.75/lb
nickel, $15/lb cobalt, $90/tonne
magnetite $1,600/oz Pd, and $800/oz
Pt. Different pit slopes were used
for each layer (in degrees): 9.5 in
clay, 21.8 in gravel and 45 in rock.
Exchange rate utilized was US$/C$ of
$0.75. Mining costs utilized
different values for overburden
(clay, gravel), selective mining and
bulk mining ranging from C$1.75 to
C$3.15/t mined. Processing costs and
G&A for 100ktpd operation were
C$6.18/t. Based on the range of grade
and ratio of sulphur to nickel at
Crawford, recovery could be expected
to range from 10% -60%. It has also
been assumed that 30 - 40% of total
iron would be recovered to a saleable
magnetite concentrate.





7.         The Mineral Resource Estimate was
prepared following the CIM Estimation
of Mineral Resources & Mineral
Reserves Best Practice Guidelines
(November 29, 2019).






MAIN ZONE:




8.         The geological model as applied to the
Mineral Resource Estimate for the Main
Zone comprises three mineralized
domains hosted by variably
serpentinized ultramafic rocks: a
relatively high-grade core (largely
dunite) and two northern and southern
lower grade envelopes (combination of
dunite and peridotite). Individual
wireframes were created for each
domain.





9.         The block model was prepared using
Micromine 2020. A 12 m x 12 m x 9 m
block model was created and samples
were composited at 4.5 m intervals.
Grade estimation from drill hole data
was carried out for Ni, Co, Fe, S, Pd
and Pt using the Ordinary Kriging
interpolation method.





10.        Grade estimation was validated by
comparison of input and output
statistics (nearest neighbour and
inverse distance cubed), swath plot
analysis, and by visual inspection of
the assay data, block model, and
grade shells in cross-sections.





11.        Density estimation was carried out for
the mineralized domains using the
Ordinary Kriging interpolation
method, on the basis of 3,270
specific gravity measurements
collected during the core logging
process, using the same block model
parameters of the grade estimation.
As a reference, the average estimated
density value within the high-grade
is 2.64 g/cm3 (t/m3), while low-
grade domains of the resource model
yielded averages of 2.63 g/cm3 (t/
m3) in the north and 2.71 g/cm3 (t/
m3) in the south.






EAST ZONE:




12.        The geological model as applied to the
Mineral Resource Estimate for the
East Zone comprises three mineralized
domains hosted by variably
serpentinized ultramafic rocks: a
relatively high-grade core (largely
dunite) and two northern and southern
lower grade envelopes (largely
peridotite). Individual wireframes
were created for each domain.





13.        The block model was prepared using
Micromine 2020. A 20 m x 20 m x 15 m
block model was created and samples
were composited at 3 m intervals.
Grade estimation from drill hole data
was carried out for Ni, Co, Fe and S
using the Inverse Distance Squaredmethod.





14.        Grade estimation was validated by
comparison of input and output
statistics (nearest neighbour), swath
plot analysis, and by visual
inspection of the assay data, block
model, and grade shells in cross-
sections.





15.        An average bulk density value for each
mineralized domain was calculated on
the basis of 244 specific gravity
measurements collected during the
core logging process. Blocks within
the high-grade were assigned a
single bulk density value of 2.62 g/
cm3 (t/m3), while low-grade domains
of the resource model were assigned
single bulk density values of 2.66 g/
cm3 (t/m3) in the north and 2.72 g/
cm3 (t/m3) in the south.
Assays, Quality Assurance/Quality Control and Drilling and Assay
Procedures
William E. MacRae, MSc, P.Geo., a Qualified Person as defined by NI
43-101, is responsible for the on-going drilling and sampling program,
including quality assurance (QA) and quality control (QC). The core is
collected from the drill in sealed core trays and transported to the core
logging facility. The core is marked and sampled at 1.5 metre lengths and cut
with a diamond blade saw. Samples are bagged with QA/QC samples inserted in
batches of 35 samples per lot. Samples are transported in secure bags directly
from the Canada Nickel core shack to Actlabs Timmins, an ISO/IEC 17025
accredited lab. Analysis for precious metals (gold, platinum and palladium)
are completed by Fire Assay while analysis for nickel, cobalt, sulphur and 17
other elements are performed using a peroxide fusion and ICP-OES analysis.
Certified standards and blanks are inserted at a rate of one QA/QC sample per
32 core samples making a batch of 35 samples that are submitted for analysis.
Qualified Person and Data Verification
Dr. Scott Jobin-Bevans (P.Geo., APGO (number sign)0183), independent of the 
Company
and a Qualified Person as defined by NI 43-101, has reviewed and approved the
scientific and technical content of this news release, and is responsible for
the Mineral Resource Estimate. The Quality Control-Quality Assurance review
was conducted by independent engineer Mr. John Siriunas (P.Eng., APEO
(number sign)42706010), a Qualified Person as defined by NI 43-101.
About Canada Nickel Company
Canada Nickel Company Inc. is advancing the next generation of
nickel-cobalt sulphide projects to deliver nickel and cobalt required to feed
the high growth electric vehicle and stainless steel markets. Canada Nickel
Company has applied in multiple jurisdictions to trademark the terms NetZero
NickelTM, NetZero CobaltTM, NetZero IronTM and is pursuing the development of
processes to allow the production of net zero carbon nickel, cobalt, and iron
products. Canada Nickel provides investors with leverage to nickel and cobalt
in low political risk jurisdictions. Canada Nickel is currently anchored by
its 100% owned flagship Crawford Nickel-Cobalt Sulphide Project in the heart
of the prolific Timmins-Cochrane mining camp.
Cautionary Statement Concerning Forward-Looking Statements
This press release contains certain information that may constitute
"forward-looking information" under applicable Canadian securities
legislation. Forward looking information includes, but is not limited to,
drill results relating to the Crawford Nickel-Cobalt Sulphide Project, the
potential of the Crawford Nickel-Cobalt Sulphide Project, timing of economic
studies and resource estimates, strategic plans, including future exploration
and development results, and corporate and technical objectives.
Forward-looking information is necessarily based upon a number of assumptions
that, while considered reasonable, are subject to known and unknown risks,
uncertainties, and other factors which may cause the actual results and future
events to differ materially from those expressed or implied by such
forward-looking information. Factors that could affect the outcome include,
among others: future prices and the supply of metals, the future demand for
metals, the results of drilling, inability to raise the money necessary to
incur the expenditures required to retain and advance the property,
environmental liabilities (known and unknown), general business, economic,
competitive, political and social uncertainties, results of exploration
programs, risks of the mining industry, delays in obtaining governmental
approvals, failure to obtain

" BC-CanadaNickel-NI43-101   01-18 2149
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.518348:
^Amended and Restated NI 43-101 Technical Report on the Mineral Resource
Estimates Crawford Nickel-Cobalt Sulphide Project: Main Zone (Update) and
East Zone (Initial) Deposits@

TORONTO, Jan. 18, 2021 /CNW/ - Canada Nickel Company Inc. (TSXV: CNC)
("Canada Nickel" or the "Company") is pleased to announce the filing on SEDAR
of an amended and restated independent National Instrument 43-101 - Standards
of Disclosure for Mineral Projects ("NI 43-101") entitled: "Independent
Technical Report and Mineral Resource Estimates Crawford Nickel-Cobalt
Sulphide Project: Main Zone (Update) and East Zone (Initial) Deposits"
prepared by Scott Jobin-Bevans (Ph.D., PMP, P.Geo.), John Siriunas (M.A.Sc.,
P.Eng.) and David Penswick (P.Eng.) (the "Amended Technical Report").
The Amended Technical Report can be found under the Company's profile at
www.sedar.com. The Amended Technical Report has been filed further to a review
by staff of the Ontario Securities Commission (the "OSC"). The OSC review is
now complete.
The Amended Technical Report includes a conceptual pit envelope
constraint in order to demonstrate reasonable prospects for eventual economic
extraction and updated mineral resource tables. Prior mineral resource
estimates, as previously disclosed in the December 4, 2020 Technical Report,
were not constrained by conceptual pit envelopes. The addition of a pit
constraint resulted in no change to the Measured & Indicated resource in the
Higher Grade Core of the Main Zone, a 1.5 kt reduction in contained nickel in
the overall Measured and Indicated resource to 1,690 kt, and a 335 kt
reduction in contained nickel from the original Inferred resource to 1,183 kt.
90% of the overall reduction in Inferred resources occurred at depths below
300 metres.
In addition, the gram per tonne (g/t) assay values for Palladium (Pd),
Platinum (Pt), and Palladium + Platinum (Pd + Pt) included in Table 10-2 of
the Amended Technical Report have been corrected for holes CR19-05 to CR19-13.
Disclosure of explorations targets for the Main Zone Pd + Pt reef, two
East Zone Pd + Pt reefs and the East Zone nickel domains was also revised to
comply with subsection 2.3(2) of NI 43-101.
Table 1 - Amended Total Mineral Resource Estimate for the Crawford
Nickel-Cobalt Sulphide Project, Ontario


Mineral Resource Estimate

Contained

---

DOMAIN

CLASS  TONNES (Mt)      Ni (%)                      Co (%)     Fe (%)       S 
(%)       Pd (g/t)        Pt (g/t)                     Ni (kt)          Co 
(kt)        Fe (Mt)        Pd (koz)      Pt (koz)

---

MAIN
HIGHER
Measured            151.7         0.32                         0.013         
6.25        0.20           0.029           0.012                         
482.2           19.9            9.5           141            57
GRADE
ZONE

---

Indicated                     128.6         0.30        
0.013                          6.37         0.16       0.027           
0.013                  391.8                   16.5            8.2            
111            52

---

Mea+Ind                      280.2         0.31        
0.013                          6.31         0.18       0.028           
0.012                  873.9                   36.4           17.7            
252           108

---

Inferred                      109.9         0.29        
0.013                          6.66         0.09       0.026           
0.013                  315.0                   14.0            7.3             
93            47

---

MAIN LOWER
Measured             62.5         0.22                         0.013         
6.83        0.05                                                       
135.1            8.2            4.3
GRADE ZONE

---

Indicated                     263.2         0.21        
0.013                          6.90         
0.04                                            557.0                   
34.6           18.2

---

Mea+Ind                      325.6         0.21        
0.013                          6.89         
0.04                                            692.1                   
42.9           22.4

---

Inferred                      210.2         0.21        
0.013                          6.87         
0.06                                            444.9                   
27.1           14.4

---

EAST ZONE
Measured             25.8         0.26                         0.012         
6.02        0.04                                                        
67.4            3.2            1.6

---

Indicated                      21.8         0.26        
0.013                          6.20         
0.04                                             56.2                    
2.7            1.3

---

Mea+Ind                       47.5         0.26        
0.013                          6.11         
0.04                                            123.6                    
6.0            2.9

---

Inferred                      176.7         0.24        
0.013                          6.63         
0.04                                            423.5                   
22.6           11.7

---

TOTAL
Mea+Ind              653         0.26                         0.013         
6.58        0.10           0.028           0.012                       
1,689.6           85.2           43.0           252           108

---

Inferred                        497         0.24        
0.013                          6.74         0.06       0.026           
0.013                1,183.3                   63.8           33.5             
93            47

---




1.         The independent Qualified Person for
the Mineral Resource Estimate, as
defined by NI 43-101, is Dr. Scott
Jobin-Bevans (P.Geo., APGO (number sign)0183),
of Caracle Creek International
Consulting Inc. and Atticus Chile
S.A.  The effective date of the
Mineral Resource Estimate is December
11, 2020.





2.         These Mineral Resources are not Mineral
Reserves as they do not have
demonstrated economic viability. The
quantity and grade of reported
Inferred Resources in this Mineral
Resource Estimate are uncertain in
nature and there has been insufficient
exploration to define these Inferred
Resources as Indicated or Measured,
however it is reasonably expected that
the majority of Inferred Mineral
Resources could be upgraded to
Indicated Mineral Resources with
continued exploration.





3.         A cut-off grade of 0.15% Ni was used
for the low-grade domains (Main and
East zones) and cut-off grades of
0.25% Ni (Main Zone) and 0.21% Ni
(East Zone) were used for the high-
grade domains. Cut-offs were
determined on the basis of core assay
geostatistics and drill core
lithologies for the deposit, and by
comparison to analogous deposit
types.  Given the current stage of
the Project, the mineral resources
contained within the Main and East
zone deposits have not been
constrained by open pit optimization.
The Company is planning to complete
open pit optimization and present
pit-constrained mineral resources as
part of its Preliminary Economic
Assessment ("PEA") scheduled to be
completed by the end of the first
quarter, 2021.





4.         Geological and block models for the
Mineral Resource Estimate used data
from a total of 62 surface drill holes
(51 in the Main Zone and 11 in the
East Zone), completed by Spruce Ridge
Resources (4 holes in 2018) and Noble
Mineral Exploration and Canada Nickel
Company (58 holes in 2019-2020). The
drill database was validated prior to
resource estimation and QA/QC checks
were made using industry-standard
control charts for blanks, core
duplicates and commercial certified
reference material inserted into assay
batches by CNC and by comparison of
umpire assays performed at a second
laboratory.





5.         Estimates in Table 1 have been rounded
to two significant figures.





6.         The mineral resource estimates have
also been revised in the Amended
Technical Report to include a
conceptual pit envelope constraint
that was developed using the
optimization parameters included in
the Amended Technical Report. Metal
prices used (US$) were $7.75/lb
nickel, $15/lb cobalt, $90/tonne
magnetite $1,600/oz Pd, and $800/oz
Pt. Different pit slopes were used
for each layer (in degrees): 9.5 in
clay, 21.8 in gravel and 45 in rock.
Exchange rate utilized was US$/C$ of
$0.75. Mining costs utilized
different values for overburden
(clay, gravel), selective mining and
bulk mining ranging from C$1.75 to
C$3.15/t mined. Processing costs and
G&A for 100ktpd operation were
C$6.18/t. Based on the range of grade
and ratio of sulphur to nickel at
Crawford, recovery could be expected
to range from 10% -60%. It has also
been assumed that 30 - 40% of total
iron would be recovered to a saleable
magnetite concentrate.





7.         The Mineral Resource Estimate was
prepared following the CIM Estimation
of Mineral Resources & Mineral
Reserves Best Practice Guidelines
(November 29, 2019).






MAIN ZONE:




8.         The geological model as applied to the
Mineral Resource Estimate for the Main
Zone comprises three mineralized
domains hosted by variably
serpentinized ultramafic rocks: a
relatively high-grade core (largely
dunite) and two northern and southern
lower grade envelopes (combination of
dunite and peridotite). Individual
wireframes were created for each
domain.





9.         The block model was prepared using
Micromine 2020. A 12 m x 12 m x 9 m
block model was created and samples
were composited at 4.5 m intervals.
Grade estimation from drill hole data
was carried out for Ni, Co, Fe, S, Pd
and Pt using the Ordinary Kriging
interpolation method.





10.        Grade estimation was validated by
comparison of input and output
statistics (nearest neighbour and
inverse distance cubed), swath plot
analysis, and by visual inspection of
the assay data, block model, and
grade shells in cross-sections.





11.        Density estimation was carried out for
the mineralized domains using the
Ordinary Kriging interpolation
method, on the basis of 3,270
specific gravity measurements
collected during the core logging
process, using the same block model
parameters of the grade estimation.
As a reference, the average estimated
density value within the high-grade
is 2.64 g/cm3 (t/m3), while low-
grade domains of the resource model
yielded averages of 2.63 g/cm3 (t/
m3) in the north and 2.71 g/cm3 (t/
m3) in the south.






EAST ZONE:




12.        The geological model as applied to the
Mineral Resource Estimate for the
East Zone comprises three mineralized
domains hosted by variably
serpentinized ultramafic rocks: a
relatively high-grade core (largely
dunite) and two northern and southern
lower grade envelopes (largely
peridotite). Individual wireframes
were created for each domain.





13.        The block model was prepared using
Micromine 2020. A 20 m x 20 m x 15 m
block model was created and samples
were composited at 3 m intervals.
Grade estimation from drill hole data
was carried out for Ni, Co, Fe and S
using the Inverse Distance Squaredmethod.





14.        Grade estimation was validated by
comparison of input and output
statistics (nearest neighbour), swath
plot analysis, and by visual
inspection of the assay data, block
model, and grade shells in cross-
sections.





15.        An average bulk density value for each
mineralized domain was calculated on
the basis of 244 specific gravity
measurements collected during the
core logging process. Blocks within
the high-grade were assigned a
single bulk density value of 2.62 g/
cm3 (t/m3), while low-grade domains
of the resource model were assigned
single bulk density values of 2.66 g/
cm3 (t/m3) in the north and 2.72 g/
cm3 (t/m3) in the south.
Assays, Quality Assurance/Quality Control and Drilling and Assay
Procedures
William E. MacRae, MSc, P.Geo., a Qualified Person as defined by NI
43-101, is responsible for the on-going drilling and sampling program,
including quality assurance (QA) and quality control (QC). The core is
collected from the drill in sealed core trays and transported to the core
logging facility. The core is marked and sampled at 1.5 metre lengths and cut
with a diamond blade saw. Samples are bagged with QA/QC samples inserted in
batches of 35 samples per lot. Samples are transported in secure bags directly
from the Canada Nickel core shack to Actlabs Timmins, an ISO/IEC 17025
accredited lab. Analysis for precious metals (gold, platinum and palladium)
are completed by Fire Assay while analysis for nickel, cobalt, sulphur and 17
other elements are performed using a peroxide fusion and ICP-OES analysis.
Certified standards and blanks are inserted at a rate of one QA/QC sample per
32 core samples making a batch of 35 samples that are submitted for analysis.
Qualified Person and Data Verification
Dr. Scott Jobin-Bevans (P.Geo., APGO (number sign)0183), independent of the 
Company
and a Qualified Person as defined by NI 43-101, has reviewed and approved the
scientific and technical content of this news release, and is responsible for
the Mineral Resource Estimate. The Quality Control-Quality Assurance review
was conducted by independent engineer Mr. John Siriunas (P.Eng., APEO
(number sign)42706010), a Qualified Person as defined by NI 43-101.
About Canada Nickel Company
Canada Nickel Company Inc. is advancing the next generation of
nickel-cobalt sulphide projects to deliver nickel and cobalt required to feed
the high growth electric vehicle and stainless steel markets. Canada Nickel
Company has applied in multiple jurisdictions to trademark the terms NetZero
NickelTM, NetZero CobaltTM, NetZero IronTM and is pursuing the development of
processes to allow the production of net zero carbon nickel, cobalt, and iron
products. Canada Nickel provides investors with leverage to nickel and cobalt
in low political risk jurisdictions. Canada Nickel is currently anchored by
its 100% owned flagship Crawford Nickel-Cobalt Sulphide Project in the heart
of the prolific Timmins-Cochrane mining camp.
Cautionary Statement Concerning Forward-Looking Statements
This press release contains certain information that may constitute
"forward-looking information" under applicable Canadian securities
legislation. Forward looking information includes, but is not limited to,
drill results relating to the Crawford Nickel-Cobalt Sulphide Project, the
potential of the Crawford Nickel-Cobalt Sulphide Project, timing of economic
studies and resource estimates, strategic plans, including future exploration
and development results, and corporate and technical objectives.
Forward-looking information is necessarily based upon a number of assumptions
that, while considered reasonable, are subject to known and unknown risks,
uncertainties, and other factors which may cause the actual results and future
events to differ materially from those expressed or implied by such
forward-looking information. Factors that could affect the outcome include,
among others: future prices and the supply of metals, the future demand for
metals, the results of drilling, inability to raise the money necessary to
incur the expenditures required to retain and advance the property,
environmental liabilities (known and unknown), general business, economic,
competitive, political and social uncertainties, results of exploration
programs, risks of the mining industry, delays in obtaining governmental
approvals, failure to obtain regulatory or shareholder approvals, and the
impact of COVID-19 related disruptions in relation to the Company's business
operations including upon its employees, suppliers, facilities and other
stakeholders. There can be no assurance that such information will prove to be
accurate, as actual results and future events could differ materially from
those anticipated in such information. Accordingly, readers should not place
undue reliance on forward-looking information. All forward-looking information
contained in this press release is given as of the date hereof and is based
upon the opinions and estimates of management and information available to
management as at the date hereof. Canada Nickel disclaims any intention or
obligation to update or revise any forward-looking information, whether as a
result of new information, future events or otherwise, except as required by
law.
View original
content:http://www.prnewswire.com/news-releases/amended-and-restated-ni-43-101
-technical-report-on-the-mineral-resource-estimates-crawford-nickel-cobalt-sul
phide-project-main-zone-update-and-east-zone-initial-deposits-301209828.html
SOURCE Canada Nickel Company Inc.



View original content:
http://www.newswire.ca/en/releases/archive/January2021/18/c9416.html

-0-                           01/18/2021
/For further information: Mark Selby, Chair and CEO, Phone: 647-256-1954,
Email: info(at)canadanickel.com/
/Web Site: https://canadanickel.com/ /
(CNIKF CNC.)

CO:  Canada Nickel Company Inc.
ST:  Ontario
IN:  MNG OTC
SU:

-30-