Source	CANADA NEWSWIRE
Date	01/19/2021
Time	04:03:45 AM

Company	 Azimut Exploration Inc.
Title	Azimut defines excellent gold targets near the Patwon Discovery on the
Elmer Property, James Bay region, Quebec





    CDNX Symbol: AZM











Press Release




" BC-Azimut-gold-Patwon   01-19 1135
News release via CNW Telbec, Montreal 514-878-2520 -ME-

Attention co.128380:
^Azimut defines excellent gold targets near the Patwon Discovery on the
Elmer Property, James Bay region, Quebec@

Up to 880 gold grains in till samples from nine gold-bearing clusters
LONGUEUIL, QC, Jan. 19, 2021 /CNW Telbec/ - Azimut Exploration Inc.
("Azimut" or the "Company") (TSXV: AZM) is pleased to report the preliminary
results of a high-density till sampling survey conducted over the Patwon gold
discovery and its vicinity on the Company's 100% owned Elmer Property (the
"Property") in the James Bay region of Quebec (see Figures 1 to 5). These
results further support the excellent potential for additional discoveries on
the Property, along strike or subparallel to the Patwon Zone.
Till sampling is a classical exploration method to detect specific
minerals (e.g., gold grains) in glacial sediments that may indicate nearby
mineralization. When glaciers erode mineral deposits in bedrock, they produce
a wide range of mineralized fragment sizes (from boulders to fine particles)
that are transported over variable distances. In the case of gold, grain
morphology typically reflects the distance travelled: pristine-shaped grains
suggest the sample may be close to the source of mineralization, rounded
grains signal a distal source.
Salient Facts and Outlook
<<

--  Nine (9) distinct gold-bearing clusters identified in till, mostly
dominated by pristine gold grains. Gold counts reaching up to 881 gold
grains per sample occur within a high-priority exploration corridor
measuring 8 kilometres long by 3 kilometres wide (see Figure 3).

--  Six (6) of these clusters correlate spatially with high-grade gold
prospects, including one directly over the Patwon discovery. The latter
appears to be the direct footprint of this significant mineralized zone
in glacial sediments.

--  Using the Patwon footprint as a reference, the other significant
gold-bearing clusters suggest the presence of multiple mineralized zones
within the priority corridor. The till results will soon be integrated
with other data (induced polarization, prospecting, structural
interpretation) to define drilling targets.

--  A new 15,000-metre diamond drilling program will resume later this month
on the Property with two objectives: 1) Expand the Patwon discovery
along strike and at depth; and 2) Test new targets on strike or
subparallel to Patwon, within the largely underexplored priority
corridor.
<>>
Survey Data and Results
<<

--  A total of 192 till samples were collected and processed by Inlandsis
Consultants in 2020, including 12 samples as a test-survey to
characterize the Patwon footprint and 180 samples within the 8-kilometre
by 3-kilometre priority corridor surrounding Patwon.

--  Sample size ranged from 3 to 15 kilograms due to the poor availability
of till. In some cases, the samples contained a significant amount of
organic material. The grain count per sample was normalized to an
average of 5 kilograms of sieved mineral fraction passing 3 mm. After
extraction of fines by decantation, the dense fraction was extracted by
hand panning and gold grains were counted and described using a
binocular microscope. Quantitative laboratory analysis for gold and a
suite of other elements will be performed on the dense fraction using
INAA and on the fine fraction using ICP-MS. Gold grain counting from
till samples is an indirect exploration technique that, by itself, is
not indicative of gold discoveries in bedrock.

--  Swamps limited the sampling program in certain parts of the corridor.
Several gold-bearing clusters remain open along strike due to these
sampling constraints.

--  A total of 98 samples returned gold grains: 22 with very pristine
grains, 31 pristine, 25 sub-pristine, 17 sub-rounded and 3 rounded. Gold
grain counts have been normalized to 5 kilograms of sieved material.

--  80% of the samples contained very pristine to sub-pristine gold grains
suggesting short transportation distances from mineralized bedrock
(probably less than 200 metres).

--  Detailed results by cluster (see Figure 3)
<>>
Cluster Number of gold-bearing
Highest gold count         Dominant gold grain morphology
till samples                                                  in the cluster
Other information

(normalized to 5-kg sample)

---

(number sign)1                         8                             881
Pristine                           No known gold prospect
nearby. Limited drilling
(one hole outside the
target).



---

(number sign)2                        15                              33      
Mostly pristine to sub-            No known gold prospect
pristine                           nearby. Undrilled sector.



---

(number sign)3                         7                              28      
Mostly pristine, or sub-           Gold prospect on strike (up
rounded                            to 12.6 g/t Au in grabs).
Limited drilling.



---

(number sign)4                         5                              14
Pristine                           Gold prospect (up to 6.7 g/t
Au in grabs); shear zone.


Undrilled area.



---

(number sign)5                         6                              31
Mostly pristine                    Gold prospect nearby (up to
8.6 g/t Au); shear zone.


Undrilled area.



---

(number sign)6                         9                              10      
Mostly pristine to sub-            Gold prospect (up to 77.8 g/
pristine                           t Au and 167 g/t Ag in
grabs); shear zone. Limited
drilling.



---

(number sign)7                         2                              80      
Pristine and sub-pristine          No known gold prospect
nearby. Undrilled area.



---

(number sign)8                         3                               2      
Pristine and sub-rounded           Gold prospect on strike (up
to 6.3 g/t Au in grabs).
Limited drilling.



---

(number sign)9                        22       24 (sampled over Patwon)
Mostly pristine                               Patwon gold zone.


169 (distal)



---
The cluster over the Patwon discovery and its immediate vicinity (cluster
(number sign)9 on Figure 3) is considered to be the direct footprint of the 
mineralized
zone in surficial sediments. Two samples close to the mineralized zone yielded
24 and 41 pristine gold grains. The best sample in the cluster, collected
about 300 metres NW of Patwon, returned 169 sub-pristine grains.
The Patwon discovery
Patwon is shaping up as a significant gold discovery with a high
probability of growth along strike and at depth (see press release of November
30, 2020). Drilling to date has confirmed the mineralized zone extends over a
strike length of 500 metres, a depth of 250 metres and a true width of up to
80 metres.
The Elmer Property
The Elmer Property comprises 515 claims covering 271.3 km2 over a
35-kilometre strike length. The Property is 285 kilometres north of Matagami,
60 kilometres east of the village of Eastmain, and 5 kilometres west of the
paved James Bay Road, a major all-season highway. The region benefits from
quality infrastructure, including significant road access, a hydroelectric
power grid and airports. Azimut staked the Property based on the results of
the Company's predictive modelling for gold in the James Bay region using its
proprietary AZtechMineTM expert system.
This press release was prepared by Dr. Jean-Marc Lulin, P.Geo., acting as
Azimut's qualified person under National Instrument 43-101. This press release
has also been revised by Dr. Rémi Charbonneau, Senior Consulting Quaternary
Geologist for Inlandsis Consultants.
About Azimut
Azimut is a mineral exploration company whose core business is centred on
target generation and partnership development. The Company uses a pioneering
approach to big data analytics (the proprietary AZtechMineTM expert system)
enhanced by extensive exploration know-how. Azimut maintains rigorous
financial discipline and has 69.1 million shares outstanding. Azimut's
competitive edge against exploration risk is founded on systematic
regional-scale data analysis and multiple concurrently active projects.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Azimut Exploration Inc.



View original content:
http://www.newswire.ca/en/releases/archive/January2021/19/c1408.html

-0-                           01/19/2021
/For further information: Contact and Information: Jean-Marc Lulin,
President and CEO, Tel.: (450) 646-3015 - Fax: (450) 646-3045,
info(at)azimut-exploration.com, www.azimut-exploration.com/
/Web Site: www.azimut-exploration.com /
(AZM.)

CO:  Azimut Exploration Inc.
ST:  Quebec
IN:  MNG
SU:

-30-