Source	CANADA NEWSWIRE
Date	01/19/2021
Time	04:33:34 AM

Company	 Neo Lithium Corp.
Title	Neo Lithium Improves Quality of Battery Grade Lithium Carbonate to
99.797% Purity at its Pilot Plant





    CDNX Symbol: NLC











Press Release




" BC-NeoLithiumPilotPlant   01-19 1255
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.265177:
^Neo Lithium Improves Quality of Battery Grade Lithium Carbonate to
99.797% Purity at its Pilot Plant@

<<

--  Significantly improved purity of Battery Grade Lithium Carbonate to
99.797% from 99.599%
--  Quality and purity are already meeting worldwide premium specifications
and very close to CATL's high standards of product quality
<>>
TORONTO, Jan. 19, 2021 /CNW/ - Neo Lithium Corp. ("Neo Lithium" or the
"Company") (TSXV: NLC) (OTCQX: NTTHF) (FSE: NE2) is pleased to announce that
following the COVID-19 pandemic closure of its lithium carbonate pilot plant
in Fiambalá (the "Plant"), work resumed in late Q4 2020, which has resulted in
battery grade lithium carbonate being produced using concentrated brine from
its wholly-owned Tres Quebradas lithium project ("3Q Project") in Catamarca
Province, Argentina.
The Plant produced lithium carbonate with a purity of 99.797%,
representing the highest purity level attained thus far while using the
improved process (see press release dated March 11, 2020 for more detailed
information). The improved process is expected to decrease operational and
capital costs while minimizing reagent, water and power consumption.
The composition of impurities in the lithium carbonate are as follows(x):
SO4        Cl       Mg        K       Ca        Si         Na          
Insoluble                Humidity

---


%
%
%
%
%
%
%
%
%

---


0.017         0.071     0.001     0.007     0.019      0.011       
0.033               0.038
<0.10

---
(x)Other elements undetected.
"We continue optimizing the process in terms of quality and reagent
consumption," stated Waldo Perez, President and CEO of Neo Lithium. "We are on
path to deliver a high-quality product and complete our DFS on time and on
budget with a new improved process"
The current lithium carbonate batch is the 13th batch since the Plant
started operation in May 2019. Due to the COVID-19 pandemic, the Company has
stored approximately 50 tonnes of concentrated brine ready to be processed at
the Plant. The Company will continue to test batches to optimize the process
for the Definitive Feasibility Study ("DFS") before turning the Plant into
continuous mode in Q2/Q3 2021. On continuous mode, the Plant can produce up to
40 tonnes a year.
The Process
Brine with average grade of 1000 mg/l was extracted from the production
wells located in the northern zone of the 3Q project and then evaporated at
the Company's 9 stage industrial pilot ponds. No chemical reagents were added
to the brine other than minor amounts of hydrochloric acid (HCl) for pH
control at the final stage of evaporation. Total evaporation time was about 1
year and the brine concentration was around 3% lithium. The concentrated brine
was then transported by truck to the pilot plant in Fiambalá, which is located
160 km from the 3Q Project. The concentrated brine was treated in the pilot
plant with a solvent extraction phase (SX-B) for Boron removal, as well as an
scrub and strip phase in order to regenerate the organic solution of SX-B
process. For magnesium removal was used liming addition which was produced in
situ from the calcium removal at alkaline pH and carbonation phase to calcium
polishing and any remaining Mg and heavy transition metals. The lithium
carbonate process is then completed with 3 stages of soda ash carbonation,
washing and drying.
Technical Information
The samples collected were delivered by Company personnel to Andesmar
Transport Company ("Andesmar") in La Rioja, in the province of Rioja. Andesmar
delivered the samples by truck to ASL, an ISO 9001-2008-certified laboratory
in Mendoza, Argentina. ASL used the following analytical methodologies:
ICP-OES (inductively-coupled plasma-optical (atomic) emission spectrometry) to
quantify boron, barium, calcium, lithium, magnesium, manganese, and potassium;
an argentometric method to assay for chloride; a gravimetric method to analyze
for sulfate; a volumetric analysis (acid/base titration) for the evaluation of
alkalinity (as CaCO3); a gravimetric method to determine density and total
dissolved solids; and, a laboratory pH meter to determine pH. All analytical
work is subject to a systematic and rigorous Quality Assurance-Quality
Control. A reference ("standard") sample was inserted into the sample stream
at a frequency of approximately 1 in 15 samples; a field blank was inserted at
a frequency of approximately 1 in 15 samples; and a field duplicate sample was
inserted at a frequency of approximately 1 in 15 samples.
Waldo Perez, Ph.D, P.Geo., the CEO and President of Neo Lithium Corp. is
the Qualified Person who approved the scientific and technical disclosure in
the news release.

About Neo Lithium Corp.
Neo Lithium Corp. has quickly become a prominent new name in lithium
brine development by virtue of its high quality 3Q Project and experienced
team. Neo Lithium is rapidly advancing its 100% owned 3Q Project - a unique
high-grade lithium brine lake and salar complex in Latin America's "Lithium
Triangle".
The 3Q Project is located in the Catamarca Province, the largest lithium
producing area in Argentina covering approximately 35,000 ha including a salar
complex of approximately 16,000 ha.
Additional information regarding Neo Lithium Corp. is available on SEDAR
at www.sedar.com under the Company's profile and at its website at
www.neolithium.ca, including various pictures of ongoing work at the project.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release. The TSX Venture
Exchange Inc. has in no way approved nor disapproved the contents of this
press release.
Cautionary Note Regarding Forward Looking Statements - Certain
information set forth in this news release may contain forward-looking
statements. Such statements include but are not limited to, statements as to
lithium brine grades at depth being consistent with surface results, the
potential for resource expansion at depth, the potential of the northern salar
sediments, and deeper sediments, for hosting brine, the ability to proceed to
scoping studies quickly, proceeding with continued work for additional
economic studies the potential for production expansion in the Company's
assessment of the economic potential of the 3Q Project, that test results are
indicative of future results, and the additional of additional independent
directors. Generally, forward-looking statements can be identified by the use
of words such as "plans", "expects" or "is expected", "scheduled", "estimates"
"intends", "anticipates", "believes", or variations of such words and phrases,
or statements that certain actions, events or results "can", "may", "could",
"would", "should", "might" or "will", occur or be achieved, or the negative
connotations thereof. These forward-looking statements are subject to numerous
risks and uncertainties, certain of which are beyond the control of the
Company, which could cause the actual results, performance or achievements of
the Company to be materially different from the future results, performance or
achievements expressed or implied by such statements. These risks include,
without limitation, risks related to failure to obtain adequate financing on a
timely basis and on acceptable terms, political and regulatory risks
associated with mining and exploration activities, including environmental
regulation, risks and uncertainties relating to the interpretation of drill
and sample results, risks related to the uncertainty of cost and time
estimation and the potential for unexpected delays, costs and expenses, risks
related to metal price fluctuations, the market for lithium products,
competition for experienced directors in the junior mineral exploration and
development sector, and other risks and uncertainties related to the Company's
prospects, properties and business detailed elsewhere in the Company's
disclosure record. Although the Company believes its expectations are based
upon reasonable assumptions and has attempted to identify important factors
that could cause actual actions, events or results to differ materially from
those described in forward-looking statements, there may be other factors that
cause actions, events or results not to be as anticipated, estimated or
intended and undue reliance should not be placed on forward-looking
statements.
SOURCE Neo Lithium Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/January2021/19/c0481.html

-0-                           01/19/2021
/For further information: Neo Lithium Corp., Carlos Vicens,
cvicens(at)neolithium.ca/
/Web Site: http://neolithium.ca/ /
(NTTHF NLC. NE2)

CO:  Neo Lithium Corp.
ST:  Ontario
IN:  OTC MIN MNG
SU:

-30-