Source	CANADA NEWSWIRE
Date	01/19/2021
Time	04:33:35 AM

Company	 Questex Gold & Copper Ltd.
Title	QuestEx Gold & Copper Announces Intention to Define Gold Resource for
the Inel Prospect on its 100% owned KSP Property





    CDNX Symbol: QEX











Press Release




" BC-QuestEx-InelProspect   01-19 1675
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.399752:
^QuestEx Gold & Copper Announces Intention to Define Gold Resource for
the Inel Prospect on its 100% owned KSP Property@

TSX-V: QEX
VANCOUVER, BC, Jan. 19, 2021 /CNW/ - QUESTEX GOLD & COPPER LTD. (TSXV:
QEX) ("QuestEx" or the "Company") is pleased to announce its intention to
publish a National Instrument ("NI") 43-101 compliant mineral resource
estimate for its Inel prospect prior to the end of 2021.
The Inel prospect is located on QuestEx's 100% owned, 312
square-kilometre ("km"), KSP property within the Bronson Corridor in British
Columbia's famed Golden Triangle (Figure 1). It is one of several structurally
controlled orogenic gold systems within the Bronson Corridor, which include
the past producing Johnny Mountain gold mine 7 km to the west and the Snip
gold mine 11 km to the northwest (Figure 1). Inel is one of the most advanced
exploration targets in British Columbia's Golden Triangle that does not
already have a 43-101 compliant mineral resource estimate ("Resource"). It is
primarily a gold ("Au") target with both high-grade Au mineralization (e.g.
1,670.51 grams per tonne ("g/t") Au over 1.4 metres ("m") in drill hole
INDDH17-081 from 35.60 m; Table 1 and Figure 2), and medium-grade high-tonnage
Au mineralization (e.g. 4.24 g/t Au over 52 m in INDDN16-029 from 44.00 m;
Table 1). Inel has been tested with more than 38,000 m of drilling in 305
drill holes and 1,240 m of underground development (Figure 3 and Figure 4).
Despite the significant amount of work completed at Inel, past attempts at
estimating mineral resources were challenged by poor quality topographic data,
limited understanding of complex deposit-scale geology and a focus on higher
grades. In the last five months, QuestEx has taken significant strides in
overcoming these challenges. Highlights include:
<<

--  GeoSim Services Inc. has been contracted to develop an independent, NI
43-101 compliant, mineral resource estimate for the Inel prospect;
o Initial evaluation/validation of the existing Inel drill hole database
indicates that it can support resource definition;
--  A LiDAR/Orthophoto survey that was completed in September 2020 and
covered the Inel area provides detailed topographic data (8 cm accuracy)
for resource and engineering related studies, as well as high-resolution
aerial photography to determine areas of new outcrop exposed by recent
glacial retreat;
--  A 2,000+ m drill program planned for Inel in 2021 will consist of infill
drilling, and testing of exploration targets, to better define and
expand the grade and tonnage of the anticipated resource;
--  QuestEx has compiled recent and historical geological data for Inel,
determining the key geological elements necessary to better constrain
the resource and exploration models; and
--  QuestEx has added Andrew Hilchey, P.Geo., who has 15 years of 3D
modelling and resource geology experience, to the growing technical team
and Mr. Hilchey's first priority will be to advance the 3D geological
model for Inel.
<>>
Joe Mullin, CEO of QuestEx comments: "I am excited that following a year
of compiling and evaluating data from QuestEx's large portfolio of properties,
Inel has emerged as a top priority target. Historical work at Inel
demonstrates near-surface, high-grade gold mineralization, as well as shallow
medium to low-grade gold mineralization that could be amenable to bulk-tonnage
mining methods. The technical team has made important strides in demonstrating
significant exploration-upside and advancing the prospect to the point where
we can anticipate a mineral resource estimate in late 2021."
Table 1 - Selection of Significant Results from Historical Drilling at
the Inel Prospect, KSP Property
Drill Hole         From (m)                       To (m)

Length (m)   Au (g/t)



High-Grade Drill Intersections (uncut)



INDDH17-081                      14.90                         
44.00                   29.10       82.53



Including                        35.60                         
37.00                    1.40     1670.51



IS130                            24.50                         
28.00                    3.50      423.81



IU171                            69.30                         
76.80                    7.50       41.04



IS148                            29.40                         
34.80                    5.40       38.08



IS116                            53.00                         
60.40                    7.40       20.93



IU040                            15.50                         
19.50                    4.00       30.28



INDDH17-055                     191.90                        
194.50                    2.60       31.59



IS119                            36.60                         
38.10                    1.50       42.72



IS098                            95.10                         
96.20                    1.10       41.21



Medium-Low-Grade Drill Intersections > 50 m (uncut)



INDDH16-029                      44.00                         
96.00                   52.00        4.24



INDDH16-025                      23.00                        
141.00                  118.00        1.82



INDDH16-049                      42.40                        
156.00                  113.60        1.34



INDDH16-046                      39.00                        
141.00                  102.00        1.36



INDDH18-125                     171.00                        
221.00                   50.00        1.94



INDDH16-009                      19.90                        
111.00                   91.10        1.18



INDDH16-004                      58.00                        
149.00                   91.00        1.02



INDDH16-018                       8.00                         
83.20                   75.20        1.23



INDDH16-042                     146.00                        
220.00                   74.00        1.02



INDDH16-006                      12.50                         
65.90                   53.40        1.36



INDDH17-061                       7.60                        
130.00                  122.40        0.69

---
About Inel
Inel was first discovered in 1965 by prospectors with Cominco Ltd..
Exploration in the early 70's was focused at the Camp Porphyry Cu-Au target
approximately 500 m west of Inel and at that time Inel was described as a
1,200 m by 700 m pyritic gossan with widespread porphyry-related gold and base
metal mineralization. However, between 1987 and 1991 the prospect saw
significant exploration focused on high-grade orogenic gold including 1,183 m
of underground development in two adits; one at the AK Zone and another at the
Discovery Zone. After 1991 little exploration was conducted until the prospect
was acquired by QuestEx (then Colorado Resources Ltd.) from SnipGold Corp. in
2013. Since 2014 QuestEx has completed numerous geochemical and geophysical
surveys and drilled 20,069 m in 113 holes at Inel.
Inel is located in the immediate footwall of the district-scale Big Rock
Deformation Zone ("BRDZ"), a structure that is spatially associated with gold
and zinc mineralization along its full > 6 km strike-length (Figure 3). In
2016 QuestEx drilled three targets associated with the BRDZ spanning 2.5 km
and made significant intersections of gold mineralization in each area.
Mineralization at Inel is concentrated in proximity to a faulted contact
between Triassic Stuhini Group mafic fragmental volcanic lithologies in the
hangingwall and bedded siltstone and feldspathic greywacke in the footwall
(Figure 3, Figure 4 and Figure 5). The contact, referred to as the Mafic
Fragmental Discontinuity, is a shallow dipping surface, interpreted to be a
thrust fault (Figure 4 and Figure 5). Gold mineralization at Inel is primarily
related to arrays of shallowly inclined shear-veins, and steeply inclined
extension veins. An early stage of often gold-enhanced zinc mineralization
comprises conformable or semi-conformable massive to semi-massive replacement
zones and associated veining. Multistage mineralization and post-mineral
deformation has posed challenges for resource definition. QuestEx's novel
approach in 2021 will be to target and model the overall, enclosing, deformed,
altered and mineralized envelope.
Exploration Potential
Exploration opportunities at Inel include:
<<

--  Infill drilling within areas where mineralized bodies are delineated,
but with insufficient drill density to support resource definition. This
opportunity includes the AK Zone where numerous high-grade historical
intercepts (e.g. drill holes IS148 and IS116 - Table 1) are associated
with mineralized breccias. At the AK Zone, and other historical areas
that were tested for high-grade mineralization, drill holes were not
sampled over their entire length and therefore are inadequate for
inclusion in a global resource estimate.
o In 2015 QuestEx collected 34 samples from historical drill core (both
previously sampled and unsampled intervals), with the best result from a
previously unsampled interval yielding 5 m of 1.12 g/t Au from 84 m depth in
drill hole IU099.
--  Stepout drilling from existing intersections that are open in one or
more directions to expand the known mineralized envelope and add to
potential resources. Examples include INDDH18-125 (1.88 g/t Au over 63 m
from 158 m) and INDDH17-055 (2.0 g/t Au over 147 m from 102 m) in the
Inel Ridge area, which is open in all directions.
--  Exploration targets immediately adjacent to Inel but with limited
drilling to date, such as the Camp Porphyry approximately 500 m to the
west of Inel, and ridge-crest targets along the Big Rock Deformation
Zone to the east.
<>>
Qualified Person
The Qualified Person responsible for the technical information in this
news release is David Fleming, P.Geo., QuestEx Gold & Copper's VP Exploration,
who has approved the technical information included herein.
About QuestEx
QuestEx Gold & Copper Ltd. is exploring for high-grade gold and copper
with a focus on the Golden Triangle and Toodoggone areas of British Columbia.
The property portfolio includes the Company's flagship Castle property, a
porphyry copper-gold project located in the Red Chris mining district of the
Golden Triangle neighbouring GT Gold's Tatogga property, and Newcrest Mining's
GJ property. Other properties include KSP, North ROK, Coyote, and Kingpin in
the Golden Triangle, Sofia in the Toodoggone district, and Heart Peaks and Hit
in other strategic districts within British Columbia. These assets are being
advanced by a newly assembled technical and management team with experience in
exploration, permitting and discovery.
ON BEHALF OF THE BOARD OF DIRECTORS OF QUESTEX GOLD & COPPER LTD."Joseph
Mullin"Joseph MullinChief Executive Officer and Director
Cautionary Note Regarding Forward-Looking Statements
All statements, trend analysis and other information contained in this
press release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but not
always, identified by the use of words such as "seek", "anticipate",
"believe", "plan", "estimate", "expect" and "intend" and statements that an
event or result "may", "will", "should", "could" or "might" occur or be
achieved and other similar expressions. All statements, other than statements
of historical fact, included herein, are forward-looking statements. Although
the Company believes that the expectations reflected in such forward-looking
statements and/or information are reasonable, undue reliance should not be
placed on forward-looking statements since the Company can give no assurance
that such expectations will prove to be correct. These statements involve
known and unknown risks, uncertainties and other factors that may cause actual
results or events to differ materially from those anticipated in such
forward-looking statements, including the risks, uncertainties and other
factors identified in the Company's periodic filings with Canadian securities
regulators as well as the risk that the ongoing COVID-19 pandemic may have on
the Company's business. Important factors could cause actual results to differ
materially from QuestEx expectations. Forward-looking statements are based on
estimates and opinions of management at the date the statements are made.
QuestEx does not undertake any obligation to update forward-looking statements
except as required by applicable securities laws. Investors should not place
undue reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE QuestEx Gold & Copper Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/January2021/19/c6326.html

-0-                           01/19/2021
/For further information: T: (250) 768-1511, TF: (855) 768-1511, W:
www.questex.ca/
/Web Site: www.questex.ca /
(QEX. CLASF)

CO:  QuestEx Gold & Copper Ltd.
ST:  British Columbia
IN:  MNG MIN OTC
SU:

-30-