Source	CANADA NEWSWIRE
Date	01/19/2021
Time	07:49:02 AM

Company	 Barsele Minerals Corp.
Title	Barsele regional hole BAS20007B at newly discovered Bastuträsk
intersects 0.70 metres grading 32.20 g/t gold, including 0.12% nickel,
0.08% copper, and 0.05% cobalt





    CDNX Symbol: BME











Press Release




" BC-BME-OpUpdateExplorati   01-19 2300
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.239444:
^Barsele regional hole BAS20007B at newly discovered Bastuträsk
intersects 0.70 metres grading 32.20 g/t gold, including 0.12% nickel,
0.08% copper, and 0.05% cobalt@

Regional "Orogenic Gold" hole RIS20003 between Skirasen and Risberget
intersects 1.0 metre grading 4.10 g/t gold
Regional "VMS" hole SKL20001 intersects 0.50 metre grading 3.25% zinc,
0.15% lead and 10.96 g/t silver
Bastuträsk regional hole BAS20002 intersects 1.65 metres grading 5.80 g/t
gold
Avan expansion hole AVA20008 intersects 1.0 metre grading 7.80 g/t gold
<<

--  Recent drilling at the Avan Zone has outlined some new potential lodes
that lie parallel and sub-parallel to the current resource.
--  Base of till testing (156 holes) followed by extensive MEFFA surface
till sampling (13,758 samples) combined with automated XRF scanning has
led to the outlining of geochemically anomalous areas at Bastuträsk and
Sundträsket.
--  Scout drilling at Bastuträsk to date has outlined a ~300 metre X ~300
metre area, roughly 4.8 kilometres east-northeast from the
Avan-Central-Skirasen zones requiring follow up drill testing.
--  Eighty-seven channel samples collected from the Central Zone trench,
plus drill core from the Avan and Skirasen zones will be submitted for
ongoing ore sorting studies.
--  A total of 741 Gravity stations had measurements taken in 2020.
--  A total of 765 kilometres of Magnetic surveying was completed during
2020 and additional surveying is ongoing.
--  Water sampling at 18 watercourses and three lakes, plus water flow
measurements in 5 creeks is ongoing.
--  Stringent COVID-19 protocols continue to be enforced, in order to keep
the workers and the people living in the surrounding community safe.
>>
VANCOUVER, BC, Jan. 19, 2021 /CNW/ - Barsele Minerals Corp. (TSXV: BME)
(the "Company" or "Barsele") is pleased to provide an operational update
regarding 2020 exploration activities within the Barsele Gold-VMS Project area
in Västerbottens Län, Northern Sweden (the "Barsele Project"). The exploration
program is being operated by joint venture partner Agnico Eagle Mines Limited
- (TSX, NYSE: AEM) ("Agnico Eagle"). Ownership in the Barsele Project is 55%
Agnico Eagle and 45% Barsele. Agnico Eagle can earn an additional 15% in the
Barsele Project through the completion of a pre-feasibility study. There is no
cash outlay requirement by Barsele until a pre-feasibility study is completed.
Between January 1st and December 31st, 2020, Agnico Eagle personnel and
contractors carried out office-related and field-specific exploration
activities at a number of exploration sites throughout the property. Work
included diamond drilling, gravity and magnetic surveys, base of till
drilling, ore-sorting test sampling, and water sampling, along with an
extensive surface till sampling campaign (MEFFA), utilizing multi-element fine
fraction analysis.
Within the Avan and Central gold zones, new mineralized structural trends
have emerged, and recent drilling has been encouraging. In addition, base of
till drilling and MEFFA sampling outlined a new area known as Bastuträsk,
located 4.8 kilometres east-northeast of the Barsele gold deposit. Nine short
drill holes have tested this area, with positive gold results and encouraging
base metal results.
Diamond drilling from July 14th into early November, within the
46,991-hectare property totaled 7,894 metres in 37 completed core holes. Since
late 2015, a total of 155,345 metres of overburden penetration and core
collection has been tabulated from a total of 404 drill holes. Analytical
results for the final 21 drill holes from the 2020 drilling program are
presented in this news release. The 2020 drilling campaign has tested the
northwest extension of the Avan-Central-Skirasen (CAS) "Orogenic Gold" system,
with infill and expansion drilling focused within and between the Central and
Avan zones. Volcanogenic massive sulphide ("VMS") targets have also been
tested, along with the most recent drill testing at newly discovered
Bastuträsk.
Following recent structural reinterpretations, drilling along the Avan
Zone has presented the technical team with new insights regarding high-grade
mineralized zones. Within a ~200 metre X ~200 metre X ~700 metre volume, there
are new high-grade (Bonanza-style) expansion drill intercepts adjacent to and
beneath the existing Avan mineral resource area. Here, possibly north-south to
northwest-southeast oriented cross structures carry high gold grades, along a
trend that lies outside 2019, NI 43-101 resource wireframes. Additionally, at
the Avan Zone, expansion hole AVA20008 cut three gold zones, including 16.0
metres core length (estimated 7.6 metres true thickness) grading 0.80 g/t
gold, at a midpoint depth of 75 metres below surface, plus 5.0 metres core
length (estimated 2.4 metres true thickness) grading 1.36 g/t gold, at a
midpoint depth of 235 metres below surface, plus 1.0 metre core length
(estimated 0.5 metre true thickness) grading 7.80 g/t gold, at midpoint depth
of 270 metres below surface.
At Bastuträsk, Regional hole BAS20001 (previously released) cut one gold
zone, with 6.0 metres core length (estimated 4.5 metres true thickness)
grading 0.89 g/t gold, including 1.0 metre core length (estimated 0.75 metre
true thickness) grading 2.78 g/t Au (not previously disclosed) at a midpoint
depth of 15.0 metres below surface.
Regional hole BAS20002 cut one gold zone, with 1.65 metres core length
(true thickness to be determined) grading 5.80 g/t gold, at a midpoint depth
of 25 metres below surface.
Regional hole BAS20003 cut two mineralized zones, including a gold zone
with 1.00 metre core length (true thickness to be determined) grading 1.43 g/t
gold, at a midpoint depth of 10 metres below surface, plus a base metal zone
of 12.0 metres core length (true thickness to be determined) grading 0.14%
nickel, 0.11% copper, and 0.04% cobalt at a midpoint depth of 60 metres below
surface.
Regional hole BAS20006B cut one gold zone, with 2.30 metres core length
(true thickness to be determined) grading 0.77 g/t gold, at a midpoint depth
of 20 metres below surface.
Regional hole BAS20007B cut one gold-base metal zone, with 0.70 metre
core length (true thickness to be determined) grading 32.20 g/t gold, 0.12%
nickel, 0.08% copper, and 0.05% cobalt at a midpoint depth of 85 metres below
surface.
Regional "VMS" hole NOR20004 intersected 3.00 metres core length (true
thickness to be determined) grading 0.48% zinc at a midpoint depth of 230
metres below surface.
Regional "VMS" hole SKL20001 intersected 0.50 metre core length (true
thickness to be determined) grading 3.25% zinc, 0.15% lead and 10.96 g/t
silver at a midpoint depth of 60 metres below surface.
Regional "Orogenic Gold" hole RIS20003, located 1.6 kilometres southeast
of the southeastern-most extension of the Avan-Central-Skirasen (CAS)
"Orogenic Gold" system intersected 1.0 metre core length of granodiorite host
rock grading 4.10 g/t gold at a depth of 140 metres below surface. More
sampling along 20 metres of this zone is planned. This intercept may reflect
continuity along the southeastward extension of the (CAS) mineralization.
Barsele's President, Gary Cope states; "We continue to be very pleased
with the ongoing drill results from the newly discovered Bastuträsk area,
which has drill demonstrated significant gold, as well as anomalous base metal
mineralization over a ~300 meter by ~300-meter area. The narrow good-grade
gold intercept in hole RIS20003 offers hope for continuity along the
southeastern trend of the CAS system. Also encouraging is hole SKL20001, in
relation to the ongoing hunt for a new volcanogenic massive sulphide deposit."


July through November Drilling Summary 2020

---

Hole ID

Easting

Northing                           Az                  
Dip                       DDH

From (m)

To

CL         TL         Au                 Top Cut
Length                                                                          
                                    (g/t)
(m)                  (m)        (m)      (g/t)

---                                                                             
                                                                                
                                                                                
                                              ---

AVA20007                                   617753.81                          
7215836.74                       221                   -56                     
248.10

---

Regional                    no anomalous gold/base
metals

---



AVA20008                                   617638.71                          
7215675.83                       239                   -52                     
477.80                         93.00               109.00                 
16.00      7.60          0.80

---



Expansion                                                                       
                                                                                
                    317.00               322.00                  5.00        
2.40        1.36

---

367.00               368.00                  1.00        0.50        7.80





BAS20002                                   623234.85                          
7216436.72                       272                   -50                      
71.20                         32.35                34.00                  
1.65       N/A         5.80

---



Regional

---



BAS20003                                   623176.87                          
7216637.82                       131                   -47                     
125.00                         15.00                16.00                  
1.00       N/A         1.43

---



Regional                                                                        
                                                                                
                     78.00                90.00                 12.00         
N/A

---


0.14%Ni
0.11%Cu
0.04%Co





BAS20004                                   623212.17                          
7216685.70                       125                   -47                      
70.50

---

Regional                    no anomalous gold/base
metals

---



BAS20005                                   623295.19                          
7216641.01                       125                   -47                      
72.90

---

Regional                    no anomalous gold/base
metals

---



BAS20006A                                  623335.61                          
7216601.07                        79                   -47                      
20.10

---

Regional                    no anomalous gold/base
metals

---



BAS20006B                                  623335.61                          
7216601.07                        79                   -47                      
99.80                         24.40                26.70                  
2.30       N/A         0.77

---



Regional

---



BAS20007A                                  623423.63                          
7216691.77                       270                   -50                      
14.00

---

Regional                    no anomalous gold/base
metals

---



BAS20007B                                  623423.63                          
7216691.77                       270                   -50                     
116.30                        109.00               109.70                  
0.70       N/A        32.20

---



Regional
0.12%Ni
0.08%Cu
0.05%Co

---



NOR20001                                   619183.45                          
7218479.87                        49                   -45                     
119.00

---

Regional                    no anomalous gold/base
metals

---



NOR20002                                   619234.29                          
7218306.85                       191                   -45                     
157.30

---

Regional                    no anomalous gold/base
metals

---


NOR20003                                   619600.35                          
7217793.38                        50                   -45                     
212.50

---

Regional                    no anomalous gold/base
metals

---



NOR20004                                   617611.79                          
7218046.05                        60                   -45                     
399.90                        349.00               352.00                  
3.00       N/A

---



Regional
0.48%Zn

---

NOR20005                                   618581.00                          
7219491.38                       209                   -45                     
139.70

---

Regional                    no anomalous gold/base
metals

---



NOR20006                                   617244.67                          
7216798.03                        40                   -50                     
100.10

---

Regional                    no anomalous gold/base
metals

---



NOR19004-ext                               616430.64                          
7218361.47                       305                   -60                     
506.30

---

Regional                    no anomalous gold/base
metals

---



SKL20001                                   620860.33                          
7216354.91                       135                   -52                     
104.40                         79.60                80.10                  
0.50       N/A

---



Regional
10.96g/t Ag
0.15%Pb
3.25%Zn

---



RIS20001                                   621465.73                          
7214433.59                       128                   -45                     
100.20

---

Regional                    no anomalous gold/base
metals

---



RIS20002                                   622010.37                          
7214436.66                       164                   -45                     
101.10

---

Regional                    no anomalous gold/base
metals

---



RIS20003                                   620656.13                          
7213584.78                        86                   -45                     
250.70                        205.00               206.00                  
1.00       N/A         4.10

---

Regional
assays pending

---




Az (equal sign) Compass Bearing    Dip (equal sign) Degrees Inclined       CL 
(equal sign) Core Length   TL (equal sign) Est. True Length       Top Cut 
varies 40-18 g/t Au (A-C-S)

---
The technical information in this news release was verified by way of the
last site visit in January of 2020 by the Qualified Person, wherein certain
data and protocols were discussed with the site management and the technical
staff and the database was reviewed and drill core and till sampling material
and handling procedures were examined. Since January 2020, updates have been
via detailed monthly reports and video conferencing between Barsele management
and Agnico Eagle management. Agnico Eagle maintains comprehensive quality
control/quality assurance protocols.
All samples referred to in this news release were tested at independent
MS Analytical Service, wherein core sawing and sample preparation is carried
out in Storuman, Sweden and the analyses of both Au and multi-element analysis
is completed in Canada. The as

" BC-BME-OpUpdateExplorati   01-19 2300
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.239444:
^Barsele regional hole BAS20007B at newly discovered Bastuträsk
intersects 0.70 metres grading 32.20 g/t gold, including 0.12% nickel,
0.08% copper, and 0.05% cobalt@

Regional "Orogenic Gold" hole RIS20003 between Skirasen and Risberget
intersects 1.0 metre grading 4.10 g/t gold
Regional "VMS" hole SKL20001 intersects 0.50 metre grading 3.25% zinc,
0.15% lead and 10.96 g/t silver
Bastuträsk regional hole BAS20002 intersects 1.65 metres grading 5.80 g/t
gold
Avan expansion hole AVA20008 intersects 1.0 metre grading 7.80 g/t gold
<<

--  Recent drilling at the Avan Zone has outlined some new potential lodes
that lie parallel and sub-parallel to the current resource.
--  Base of till testing (156 holes) followed by extensive MEFFA surface
till sampling (13,758 samples) combined with automated XRF scanning has
led to the outlining of geochemically anomalous areas at Bastuträsk and
Sundträsket.
--  Scout drilling at Bastuträsk to date has outlined a ~300 metre X ~300
metre area, roughly 4.8 kilometres east-northeast from the
Avan-Central-Skirasen zones requiring follow up drill testing.
--  Eighty-seven channel samples collected from the Central Zone trench,
plus drill core from the Avan and Skirasen zones will be submitted for
ongoing ore sorting studies.
--  A total of 741 Gravity stations had measurements taken in 2020.
--  A total of 765 kilometres of Magnetic surveying was completed during
2020 and additional surveying is ongoing.
--  Water sampling at 18 watercourses and three lakes, plus water flow
measurements in 5 creeks is ongoing.
--  Stringent COVID-19 protocols continue to be enforced, in order to keep
the workers and the people living in the surrounding community safe.
>>
VANCOUVER, BC, Jan. 19, 2021 /CNW/ - Barsele Minerals Corp. (TSXV: BME)
(the "Company" or "Barsele") is pleased to provide an operational update
regarding 2020 exploration activities within the Barsele Gold-VMS Project area
in Västerbottens Län, Northern Sweden (the "Barsele Project"). The exploration
program is being operated by joint venture partner Agnico Eagle Mines Limited
- (TSX, NYSE: AEM) ("Agnico Eagle"). Ownership in the Barsele Project is 55%
Agnico Eagle and 45% Barsele. Agnico Eagle can earn an additional 15% in the
Barsele Project through the completion of a pre-feasibility study. There is no
cash outlay requirement by Barsele until a pre-feasibility study is completed.
Between January 1st and December 31st, 2020, Agnico Eagle personnel and
contractors carried out office-related and field-specific exploration
activities at a number of exploration sites throughout the property. Work
included diamond drilling, gravity and magnetic surveys, base of till
drilling, ore-sorting test sampling, and water sampling, along with an
extensive surface till sampling campaign (MEFFA), utilizing multi-element fine
fraction analysis.
Within the Avan and Central gold zones, new mineralized structural trends
have emerged, and recent drilling has been encouraging. In addition, base of
till drilling and MEFFA sampling outlined a new area known as Bastuträsk,
located 4.8 kilometres east-northeast of the Barsele gold deposit. Nine short
drill holes have tested this area, with positive gold results and encouraging
base metal results.
Diamond drilling from July 14th into early November, within the
46,991-hectare property totaled 7,894 metres in 37 completed core holes. Since
late 2015, a total of 155,345 metres of overburden penetration and core
collection has been tabulated from a total of 404 drill holes. Analytical
results for the final 21 drill holes from the 2020 drilling program are
presented in this news release. The 2020 drilling campaign has tested the
northwest extension of the Avan-Central-Skirasen (CAS) "Orogenic Gold" system,
with infill and expansion drilling focused within and between the Central and
Avan zones. Volcanogenic massive sulphide ("VMS") targets have also been
tested, along with the most recent drill testing at newly discovered
Bastuträsk.
Following recent structural reinterpretations, drilling along the Avan
Zone has presented the technical team with new insights regarding high-grade
mineralized zones. Within a ~200 metre X ~200 metre X ~700 metre volume, there
are new high-grade (Bonanza-style) expansion drill intercepts adjacent to and
beneath the existing Avan mineral resource area. Here, possibly north-south to
northwest-southeast oriented cross structures carry high gold grades, along a
trend that lies outside 2019, NI 43-101 resource wireframes. Additionally, at
the Avan Zone, expansion hole AVA20008 cut three gold zones, including 16.0
metres core length (estimated 7.6 metres true thickness) grading 0.80 g/t
gold, at a midpoint depth of 75 metres below surface, plus 5.0 metres core
length (estimated 2.4 metres true thickness) grading 1.36 g/t gold, at a
midpoint depth of 235 metres below surface, plus 1.0 metre core length
(estimated 0.5 metre true thickness) grading 7.80 g/t gold, at midpoint depth
of 270 metres below surface.
At Bastuträsk, Regional hole BAS20001 (previously released) cut one gold
zone, with 6.0 metres core length (estimated 4.5 metres true thickness)
grading 0.89 g/t gold, including 1.0 metre core length (estimated 0.75 metre
true thickness) grading 2.78 g/t Au (not previously disclosed) at a midpoint
depth of 15.0 metres below surface.
Regional hole BAS20002 cut one gold zone, with 1.65 metres core length
(true thickness to be determined) grading 5.80 g/t gold, at a midpoint depth
of 25 metres below surface.
Regional hole BAS20003 cut two mineralized zones, including a gold zone
with 1.00 metre core length (true thickness to be determined) grading 1.43 g/t
gold, at a midpoint depth of 10 metres below surface, plus a base metal zone
of 12.0 metres core length (true thickness to be determined) grading 0.14%
nickel, 0.11% copper, and 0.04% cobalt at a midpoint depth of 60 metres below
surface.
Regional hole BAS20006B cut one gold zone, with 2.30 metres core length
(true thickness to be determined) grading 0.77 g/t gold, at a midpoint depth
of 20 metres below surface.
Regional hole BAS20007B cut one gold-base metal zone, with 0.70 metre
core length (true thickness to be determined) grading 32.20 g/t gold, 0.12%
nickel, 0.08% copper, and 0.05% cobalt at a midpoint depth of 85 metres below
surface.
Regional "VMS" hole NOR20004 intersected 3.00 metres core length (true
thickness to be determined) grading 0.48% zinc at a midpoint depth of 230
metres below surface.
Regional "VMS" hole SKL20001 intersected 0.50 metre core length (true
thickness to be determined) grading 3.25% zinc, 0.15% lead and 10.96 g/t
silver at a midpoint depth of 60 metres below surface.
Regional "Orogenic Gold" hole RIS20003, located 1.6 kilometres southeast
of the southeastern-most extension of the Avan-Central-Skirasen (CAS)
"Orogenic Gold" system intersected 1.0 metre core length of granodiorite host
rock grading 4.10 g/t gold at a depth of 140 metres below surface. More
sampling along 20 metres of this zone is planned. This intercept may reflect
continuity along the southeastward extension of the (CAS) mineralization.
Barsele's President, Gary Cope states; "We continue to be very pleased
with the ongoing drill results from the newly discovered Bastuträsk area,
which has drill demonstrated significant gold, as well as anomalous base metal
mineralization over a ~300 meter by ~300-meter area. The narrow good-grade
gold intercept in hole RIS20003 offers hope for continuity along the
southeastern trend of the CAS system. Also encouraging is hole SKL20001, in
relation to the ongoing hunt for a new volcanogenic massive sulphide deposit."


July through November Drilling Summary 2020

---

Hole ID

Easting

Northing                           Az                  
Dip                       DDH

From (m)

To

CL         TL         Au                 Top Cut
Length                                                                          
                                    (g/t)
(m)                  (m)        (m)      (g/t)

---                                                                             
                                                                                
                                                                                
                                              ---

AVA20007                                   617753.81                          
7215836.74                       221                   -56                     
248.10

---

Regional                    no anomalous gold/base
metals

---



AVA20008                                   617638.71                          
7215675.83                       239                   -52                     
477.80                         93.00               109.00                 
16.00      7.60          0.80

---



Expansion                                                                       
                                                                                
                    317.00               322.00                  5.00        
2.40        1.36

---

367.00               368.00                  1.00        0.50        7.80





BAS20002                                   623234.85                          
7216436.72                       272                   -50                      
71.20                         32.35                34.00                  
1.65       N/A         5.80

---



Regional

---



BAS20003                                   623176.87                          
7216637.82                       131                   -47                     
125.00                         15.00                16.00                  
1.00       N/A         1.43

---



Regional                                                                        
                                                                                
                     78.00                90.00                 12.00         
N/A

---


0.14%Ni
0.11%Cu
0.04%Co





BAS20004                                   623212.17                          
7216685.70                       125                   -47                      
70.50

---

Regional                    no anomalous gold/base
metals

---



BAS20005                                   623295.19                          
7216641.01                       125                   -47                      
72.90

---

Regional                    no anomalous gold/base
metals

---



BAS20006A                                  623335.61                          
7216601.07                        79                   -47                      
20.10

---

Regional                    no anomalous gold/base
metals

---



BAS20006B                                  623335.61                          
7216601.07                        79                   -47                      
99.80                         24.40                26.70                  
2.30       N/A         0.77

---



Regional

---



BAS20007A                                  623423.63                          
7216691.77                       270                   -50                      
14.00

---

Regional                    no anomalous gold/base
metals

---



BAS20007B                                  623423.63                          
7216691.77                       270                   -50                     
116.30                        109.00               109.70                  
0.70       N/A        32.20

---



Regional
0.12%Ni
0.08%Cu
0.05%Co

---



NOR20001                                   619183.45                          
7218479.87                        49                   -45                     
119.00

---

Regional                    no anomalous gold/base
metals

---



NOR20002                                   619234.29                          
7218306.85                       191                   -45                     
157.30

---

Regional                    no anomalous gold/base
metals

---


NOR20003                                   619600.35                          
7217793.38                        50                   -45                     
212.50

---

Regional                    no anomalous gold/base
metals

---



NOR20004                                   617611.79                          
7218046.05                        60                   -45                     
399.90                        349.00               352.00                  
3.00       N/A

---



Regional
0.48%Zn

---

NOR20005                                   618581.00                          
7219491.38                       209                   -45                     
139.70

---

Regional                    no anomalous gold/base
metals

---



NOR20006                                   617244.67                          
7216798.03                        40                   -50                     
100.10

---

Regional                    no anomalous gold/base
metals

---



NOR19004-ext                               616430.64                          
7218361.47                       305                   -60                     
506.30

---

Regional                    no anomalous gold/base
metals

---



SKL20001                                   620860.33                          
7216354.91                       135                   -52                     
104.40                         79.60                80.10                  
0.50       N/A

---



Regional
10.96g/t Ag
0.15%Pb
3.25%Zn

---



RIS20001                                   621465.73                          
7214433.59                       128                   -45                     
100.20

---

Regional                    no anomalous gold/base
metals

---



RIS20002                                   622010.37                          
7214436.66                       164                   -45                     
101.10

---

Regional                    no anomalous gold/base
metals

---



RIS20003                                   620656.13                          
7213584.78                        86                   -45                     
250.70                        205.00               206.00                  
1.00       N/A         4.10

---

Regional
assays pending

---




Az (equal sign) Compass Bearing    Dip (equal sign) Degrees Inclined       CL 
(equal sign) Core Length   TL (equal sign) Est. True Length       Top Cut 
varies 40-18 g/t Au (A-C-S)

---
The technical information in this news release was verified by way of the
last site visit in January of 2020 by the Qualified Person, wherein certain
data and protocols were discussed with the site management and the technical
staff and the database was reviewed and drill core and till sampling material
and handling procedures were examined. Since January 2020, updates have been
via detailed monthly reports and video conferencing between Barsele management
and Agnico Eagle management. Agnico Eagle maintains comprehensive quality
control/quality assurance protocols.
All samples referred to in this news release were tested at independent
MS Analytical Service, wherein core sawing and sample preparation is carried
out in Storuman, Sweden and the analyses of both Au and multi-element analysis
is completed in Canada. The assay method is SWED-Edh-6, which
comprises:-FAS-121, Au fire assay-AA on 50 gram-above 3 ppm Au fire
assay-gravimetric; FAS-425, Au by fire assay and gravimetric finish 50-gram
nominal sample weight; IMS-230, 48 element four-acid digestion ICP-MS;
ICF-6Xx, default over limit methods for ICF-6Ag, ICF-6As, ICF-6Cu, ICF-6Pb,
ICF-6Zn, SPM-210 (S); FAS-418, Ag by fire assay and gravimetric finish for Ag
above 1,000 ppm. For semi-massive to massive sulphide rock, ICP-130 aqua regia
is used for multi element analysis, instead of the four-acid digestion.
As project operator, Agnico Eagle has developed a community relations
program to engage the various stakeholders in the Barsele Project area. Basic
environmental assessment and surface water characterization, species studies
and hydrogeology studies are ongoing.
About the Barsele Gold Project
The Barsele Project is located on the western end of the Proterozoic
"Skellefte Trend", a prolific volcanogenic massive sulphide deposits belt,
that intersects with the "Gold Line" in Northern Sweden. Both polymetallic
"VMS" deposits and intrusive hosted "Orogenic Gold" deposits are present in
this region and on this property. Current and past producers in the region
include Boliden, Kristineberg, Bjorkdal, Svartliden and Storliden.
On February 21, 2019 (the effective date), Barsele released an
independently verified Mineral Resource Estimate that was completed by
Quebec-based InnovExplo Inc., for the purposes of the Company. This NI 43-101
Technical Report and Mineral Resource Estimate (Amended) for the Barsele
Property was modified and resubmitted effective December 16th, 2020. The
Amended Technical Report contains no material differences to the original
technical report filed on April 2, 2019.
The study concluded that drilling to the end of 2018 along the
Avan-Central-Skirasen gold zones at a 0.50 g/t gold cut-off for a pit
constrained extraction mining method, a 1.50 g/t gold cut-off for a bulk
underground extraction mining method, a 1.80 g/t cut-off for a selective
underground extraction mining method, has in combination, outlined an Inferred
Resource of 25,495,000 tonnes grading 2.54 g/t gold (2,086,000 ounces of
contained gold) and an Indicated Resource of 5,578,000 tonnes grading 1.81 g/t
gold (324,000 ounces of contained gold).
The main gold-bearing system remains open in all directions. The
structurally linked gold mineralized "lodes" occur mainly within a
granodiorite host and to a lesser extent, volcanic and sedimentary rocks.
Multiples of parallel to sub-parallel "lodes" that vary in width from 10
metres to 100 metres, combine for a maximum known thickness (including low
grade-waste islands) of 425 metres. The Avan-Central-Skirasen zones have a
strike length approaching 3.6 kilometres and that same northwest trending
structural corridor does contain localized bodies with gold mineralization
over an additional 4.4 kilometres. The drill tested depth of the mineralized
system approaches 1.0 kilometre and remains open. Gold is generally associated
with arsenopyrite and low base metal content and occurs often as native metal.
Since drilling commenced on July 14, 2020, "Orogenic Gold" targets were
initially prioritized, with "VMS" targets emphasized during the latter stages
of the program.
Art Freeze, P.Geo. is the Qualified Person as defined in NI 43-101 and
takes responsibility for the technical disclosure contained within this news
release.
About Barsele Minerals Corp.
Barsele is a Canadian-based junior exploration company managed by the
Belcarra Group, comprised of highly qualified mining professionals. Barsele's
main property is the Barsele Gold Project in Västerbottens Län, Sweden, a
joint venture with Agnico Eagle. An updated NI 43-101 Technical Report on the
Barsele Project with an effective date of February 21, 2019, was filed on
SEDAR on April 2, 2019.
ON BEHALF OF THE BOARD OF DIRECTORS
Gary CopePresident
This News Release may contain forward-looking statements including but
not limited to comments regarding the timing and content of upcoming work
programs, geological interpretations, receipt of property titles, potential
mineral recovery processes, etc. Forward-looking statements address future
events and conditions and therefore involve inherent risks and uncertainties.
Actual results may differ materially from those currently anticipated in such
statements and Barsele undertakes no obligation to update such statements,
except as required by law.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/barsele-regional-hole-bas20
007b-at-newly-discovered-bastutrask-intersects-0-70-metres-grading-32-20-gt-go
ld-including-0-12-nickel-0-08-copper-and-0-05-cobalt-301210973.html
SOURCE Barsele Minerals Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/January2021/19/c5768.html

-0-                           01/19/2021
/For further information: please contact Barsele Minerals Corp. at (604)
687-8566 x228, email info(at)barseleminerals.com or visit our website at
www.barseleminerals.com/
/Web Site: www.barseleminerals.com /
(BME.)

CO:  Barsele Minerals Corp.
ST:  British Columbia
IN:  MNG MIN
SU:

-30-