Source	CANADA NEWSWIRE
Date	01/26/2021
Time	04:46:40 AM

Company	 Pucara Gold Ltd.
Title	Pucara Gold Reports on its First Drill Campaign at Lourdes Gold Project
in Peru





    CDNX Symbol: TORO











Press Release




" BC-Pucara-Gold-successes   01-26 2405
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.577989:
^Pucara Gold Reports on its First Drill Campaign at Lourdes Gold Project
in Peru@

Highlights
<<

--  Drilling results confirmed presence of gold mineralization hosted within
silicified diatreme breccias within a 1.5km trend along the eastern
portion of the Lourdes project area
--  The drill hole intercepts to date suggest the eastern target areas of
Cascada, Paccha Huayco and Chucllani are one large contiguous system
favorable for gold mineralization
--  Lourdes Phase II drilling will focus on step-out drilling to locate the
Chucllani-Paccha Huayco structural feeder, test the Cascada Diatreme,
and follow up on targets identified from interpretation of Phase I drill
data
--  2021 Plans include Lourdes Phase II drillling, additional target
generation at Pacaska Gold-Copper Project while awaiting drill permits,
and advancing the Keyla Gold Project to drill ready status
--  Year-end 2020 treasury of of C$5.5M fully funds 2021 work programs
>>
VANCOUVER, BC, Jan. 26, 2021 /CNW/ - Pucara Gold Ltd. ("Pucara Gold",
"Pucara" or the "Company") (TSXV: TORO) announces that 25 holes totalling
3,955m of drilling (see figure 1 and appendix 1) were successfully completed
on budget and safely at the Lourdes Gold Project in Peru.
Drilling results confirmed the presence of gold mineralization hosted
within silicified diatreme breccias within a 1.5km trend along the eastern
portion of the Lourdes project area. Five of the nine target areas were tested
with follow up drilling planned during Phase II.
The most significant gold intercepts (see table 1) obtained from the
Chucllani area included 0.24 g/t gold over 18m in drill hole LOU011, 0.24 g/t
gold over 21m in nearby drill hole LOU013 (see figure 2) and 0.47g/t gold over
4.9m in drill hole LOU019. These mineralized intercepts appear stratiform and
are believed to represent the distal portion of the Paccha Huayco diatreme,
leaving a large portion of the inferred structural feeder to be tested in the
Phase II campaign.
Drill holes in the North Diatreme and the northern portion of the
Jellopata diatreme target areas encountered substantial thicknesses of
favorable silicic alteration and confirmed the target concept. Gold
mineralization was not encountered. Drill hole intercepts suggest remaining
potential to the south due to an inferred vector toward coarse diatreme
breccias indicative of the vent source, the increased presence of massive to
vuggy silica with depth, limonite contents, and anomalous gold in surface
sampling.
Ken Balleweg, VP Exploration, "Our initial drill program at Lourdes was
testing an area of approximately six square kilometers and will require
additional holes to test the full potential of the targets. This first
subsurface data has allowed us to focus in on the most promising area of the
greater Paccha Huayco complex. The Chucllani intercepts provide an encouraging
vector toward the structural feeder that has the highest probability of
hosting an economic gold deposit."
Steve Zuker, CEO." We are encouraged by the results of the first ever
drill program at Lourdes. Our drill program gave us critical information in
the third dimension, assisting us to target the best host rocks, alteration,
and structural setting for gold deposition. We will use this new information
to target drilling for Phase II and to prioritize numerous attractive, but
previously less understood, target areas. We are well financed to continue
with Phase II drilling at Lourdes and initiate the first ever drill campaign
at our Pacaska Gold-Copper Project."
Discussion of Phase I Results
Chucllani Zone
Seven holes were drilled into the target area totalling 856m. The most
significant gold intercepts include 0.24 g/t gold over 18m in drill hole
LOU011 and 0.24 g/t gold over 21m in drill hole LOU013.
Chucllani has strong similarities of mineralization and alteration to the
Apumayo gold deposits being mined 14km to the south. The primary drill target
consisted of a more than 200m long northeast-trending zone of granular silica
alteration with outcropping gold mineralization up to 0.64 g/t Au. Drilling
indicates that the gold zone is stratiform, occurring in the basal portion of
a zone of granular to massive silica extending laterally outward from the
Paccha Huayco diatreme and outcropping 150m south of the drill collars. While
low-grade, the zone is comparable to granular-silica hosted ore-grade
mineralization at the Apumayo Mine.
The Chucillani intercepts are most likely the distal portion of a
structurally controlled gold zone located to the northwest toward the Paccha
Huayco diatreme and warrants additional step-out drilling to be included in
Phase II.
Drilling indicates that the Chucllani zone exhibits moderate to strong
multi-element geochemistry with elevated pathfinder elements: arsenic,
bismuth, barium, and mercury.
Paccha Huayco Complex
Core hole (LOU012) into the Paccha Huayco target confirmed the diatreme
concept, transecting 230m of strongly silicified multi-stage diatreme
breccias.
Multiple stages of cross-cutting hydrothermal breccias are present, as
well as late-stage cross-cutting silica veinlets similar to those carrying
gold at the Apumayo Mine. Anomalous gold concentrations were encountered at
depth and appear to be correlative with Chucllani intercepts. The hole ended
in strongly altered andesite host rock, indicating that the hole is not
located in the central diatreme vent area and the target therefore requires
additional exploration drilling.
Jellopata Diatreme Target
Eight holes were drilled into the northern 600m of the 1.2km long
Jellopata diatreme resistivity anomaly and targeted the inferred central
diatreme feeder. Thick 100m to 229m plus intercepts of highly oxidized
granular to massive silica alteration were encountered that are anomalous in
molybdenum but lack anomalous gold concentrations.
One Jellopata drill hole (LOU003) appears to have penetrated close to the
inferred diatreme feeder, with the others transecting altered lateral and
distal stratiform diatreme fill sediments. Drill hole LOU003 had the thickest
silica interval encountered of 229m, and the hole was lost in favorable
silicic alteration in a fault zone at 246m. The hole showed transition to more
favorable vuggy and massive silica with higher limonite content at depth.
The character of the drill hole lithologies suggest remaining potential
to the south due to the presence of coarser diatreme fill breccias, increased
massive to vuggy silica with depth, higher limonite contents and more gold in
surface sampling.
Ayani Vent Target
Four holes were drilled into the Ayani target, a structurally controlled
zone located at the extreme northeastern portion of the Lourdes system. Drill
holes encountered the strongest trace element geochemical signature of the
program and weakly anomalous gold. Alteration indicative of the upper barren
portion of the hydrothermal system was encountered; follow-up drilling will
test the deeper portions of the zone.
North Diatreme Zone
Two holes were drilled into the North Zone, located at the extreme
northern end of the project area with outcropping northeast-trending
silicified hydrothermal breccias, granular silica breccias, and silicified
limonitic matrix breccias highly anomalous in pathfinder elements. Both holes
encountered strongly anomalous molybdenum and weakly anomalous gold
concentrations.
Cascada Diatreme Target
The Cascada target, containing some of the most continuous outcropping
gold mineralization, was not tested during the Phase I program due to
difficult access. Plans are to test the target at the start of the Phase II
program.
Drill hole intercepts to date suggest that the Cascada-Paccha
Huayco-Chucllani area is a larger continuous system and the most favorable for
gold mineralization.
Table 1. Summary of assay results and significant gold intercepts.
Drill
Hole                         Target                       Drill 
Method(1)                       Azimuth°                       
Dip°                       Total                       From                  
To           Interval           Gold
Depth (m)                      (m)                       (m)           1 
(m)              (g/t)


Area


LOU008
Chucllani
RC                                        320                         
-45                          126                         0.0                    
3                  3            0.18

---                                                                             
                                                                                
                                                                                
  ---

LOU009
Chucllani
RC                                        320                         
-55                          159                        79.5                 
85.5                  6            0.17

---                                                                             
                                                                                
                                                                                
  ---

LOU011
Chucllani
RC                                        270                         
-50                          192                          84                  
102                 18            0.24
Paccha Huayco

---                                                                             
                                                                                
                                                                                
      ---

LOU012
Paccha Huayco
CORE                                       270                         
-70                        265.7                       180.6                
183.6                  3            0.12
191.2                                     9.8            0.11
201

---                                                                             
                                                                                
                                                                                
      ---

LOU013
Chucllani
RC                                        170                         
-50                          114                          42                   
63                 21            0.24

---                                                                             
                                                                                
                                                                                
  ---

LOU019
Chucllani
CORE                                       270                         
-75                        133.2                        78.7                 
84.6                4.9            0.47
Paccha Huayco

---                                                                             
                                                                                
                                                                                
      ---

(1) Intersections presented herein may not necessarily represent true width of 
mineralization, are interpreted to be approximately representative due to the 
stratiform nature of the zone, indicated
dip angle from geophysics, and hole inclination.
Phase II Plans
The Phase II drilling program is planned to recommence after the end of
the rainy season in April. Evaluation of the drilling data will continue over
the next months and will be integrated with into the existing exploration data
to improve targeting for follow-up drilling. Phase II drilling will focus on
step-out drilling to locate the Chucllani-Paccha Huayco structural feeder,
testing the Cascada Diatreme, and following up on other targets identified
from the Phase I drill campaign.
Quality Assurance
Pucara has a Quality Assurance and Quality Control ("QA/QC") program for
all of its exploration projects which conforms to industry best practices.
Samples are sent to ALS PERU SA, an ISO/IEC 17025:2017 accredited laboratory,
in Lima, Peru for analysis. Analytical method is a 30-gram fire assay with
atomic adsorption finish. Strict sampling and QA/QC protocol are followed,
including the insertion of standards, blanks, and duplicates on a routine
basis. Results of these QC samples are tracked and failures are re-analyzed.
Sample intervals are usually 1.5m. All exploration diamond drill cores are
split in half by core sawing and sampled at appropriate intervals for assay.
The remaining core, coarse reject and pulps are stored on-site in a secure
location. Composites presented in the assay results table include intervals at
greater than 0.1 g/t Au over a 1.5m minimum width.
About Lourdes Gold Project
The wholly-owned Lourdes Gold Project is a fully-permitted, high
sulfidation epithermal precious metal project, which lies at the intersection
of two regional mineralized trends with neighboring high sulfidation prospects
and a producing mine. Pucara has identified a complex of nested diatremes,
vent breccias, and breccia bodies at Lourdes that are similar in size (km2)
and associated alteration to the high sulfidation epithermal gold deposits at
Yanacocha and Pierina in northern Peru, and the Mulatos district of Mexico.
The 2,576 hectare-property is approximately 400 kilometres southeast of Lima
and is easily accessible by a paved, single-lane road originating in the town
of Puquio, 155 kilometres east of the Pan American Highway.
About Pacaska Gold -- Copper ProjectThe Pacaska Gold-Copper Project consists of 
a highly prospective and
contiguous area of 7,650 hectares over nine concessions, wholly owned by
Pucara Gold. Pacaska is a high sulfidation epithermal precious metals project
with a possible copper porphyry system at depth. The alteration system
contains anomalous, outcropping concentrations of gold with values in rock of
up to 17 g/t and anomalous copper in rock of up to 11%. Pacaska is easily
accessible by a paved, single lane road originating at the Pan American
Highway in the town of Palpa 90 kilometres southwest of Pacaska.
The Company is currently permitting the Pacaska project for drill
testing, after completion of a large IP survey, which identified resistivity
anomalies extending to depth correlative with the gold-bearing breccias, as
well as a large broad chargeability anomaly suggestive of a porphyry copper
system. Multiple drill targets have been selected. The Company expects to
inform the market about its 2021 work program at Pacaska in a forthcoming
corporate update.
About Pucara Gold
Pucara Gold is a well-financed junior exploration company focused on the
discovery and advancement of economic precious metals deposits in
resource-rich Peru. Pucara has a portfolio approach to project acquisition and
controls nine precious and base metal projects, located in Peru. Pucara is
advancing six projects while the remaining three are under option agreements
with strategic partners. Pucara plans to grow through discoveries, strategic
relationships, and grassroots exploration. For more information, please visit
Pucara Gold's YouTube channel.
Qualified Person
The Lourdes exploration programs are conducted under the supervision of
Ken Balleweg, B.Sc. Geological Engineering, M.Sc. Geology, Registered
Professional Geologist, Vice President of Exploration, a Qualified Person as
defined by National Instrument 43-101 of the Canadian Securities
Administrators.
Cautionary Statements
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of th

" BC-Pucara-Gold-successes   01-26 2405
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.577989:
^Pucara Gold Reports on its First Drill Campaign at Lourdes Gold Project
in Peru@

Highlights
<<

--  Drilling results confirmed presence of gold mineralization hosted within
silicified diatreme breccias within a 1.5km trend along the eastern
portion of the Lourdes project area
--  The drill hole intercepts to date suggest the eastern target areas of
Cascada, Paccha Huayco and Chucllani are one large contiguous system
favorable for gold mineralization
--  Lourdes Phase II drilling will focus on step-out drilling to locate the
Chucllani-Paccha Huayco structural feeder, test the Cascada Diatreme,
and follow up on targets identified from interpretation of Phase I drill
data
--  2021 Plans include Lourdes Phase II drillling, additional target
generation at Pacaska Gold-Copper Project while awaiting drill permits,
and advancing the Keyla Gold Project to drill ready status
--  Year-end 2020 treasury of of C$5.5M fully funds 2021 work programs
>>
VANCOUVER, BC, Jan. 26, 2021 /CNW/ - Pucara Gold Ltd. ("Pucara Gold",
"Pucara" or the "Company") (TSXV: TORO) announces that 25 holes totalling
3,955m of drilling (see figure 1 and appendix 1) were successfully completed
on budget and safely at the Lourdes Gold Project in Peru.
Drilling results confirmed the presence of gold mineralization hosted
within silicified diatreme breccias within a 1.5km trend along the eastern
portion of the Lourdes project area. Five of the nine target areas were tested
with follow up drilling planned during Phase II.
The most significant gold intercepts (see table 1) obtained from the
Chucllani area included 0.24 g/t gold over 18m in drill hole LOU011, 0.24 g/t
gold over 21m in nearby drill hole LOU013 (see figure 2) and 0.47g/t gold over
4.9m in drill hole LOU019. These mineralized intercepts appear stratiform and
are believed to represent the distal portion of the Paccha Huayco diatreme,
leaving a large portion of the inferred structural feeder to be tested in the
Phase II campaign.
Drill holes in the North Diatreme and the northern portion of the
Jellopata diatreme target areas encountered substantial thicknesses of
favorable silicic alteration and confirmed the target concept. Gold
mineralization was not encountered. Drill hole intercepts suggest remaining
potential to the south due to an inferred vector toward coarse diatreme
breccias indicative of the vent source, the increased presence of massive to
vuggy silica with depth, limonite contents, and anomalous gold in surface
sampling.
Ken Balleweg, VP Exploration, "Our initial drill program at Lourdes was
testing an area of approximately six square kilometers and will require
additional holes to test the full potential of the targets. This first
subsurface data has allowed us to focus in on the most promising area of the
greater Paccha Huayco complex. The Chucllani intercepts provide an encouraging
vector toward the structural feeder that has the highest probability of
hosting an economic gold deposit."
Steve Zuker, CEO." We are encouraged by the results of the first ever
drill program at Lourdes. Our drill program gave us critical information in
the third dimension, assisting us to target the best host rocks, alteration,
and structural setting for gold deposition. We will use this new information
to target drilling for Phase II and to prioritize numerous attractive, but
previously less understood, target areas. We are well financed to continue
with Phase II drilling at Lourdes and initiate the first ever drill campaign
at our Pacaska Gold-Copper Project."
Discussion of Phase I Results
Chucllani Zone
Seven holes were drilled into the target area totalling 856m. The most
significant gold intercepts include 0.24 g/t gold over 18m in drill hole
LOU011 and 0.24 g/t gold over 21m in drill hole LOU013.
Chucllani has strong similarities of mineralization and alteration to the
Apumayo gold deposits being mined 14km to the south. The primary drill target
consisted of a more than 200m long northeast-trending zone of granular silica
alteration with outcropping gold mineralization up to 0.64 g/t Au. Drilling
indicates that the gold zone is stratiform, occurring in the basal portion of
a zone of granular to massive silica extending laterally outward from the
Paccha Huayco diatreme and outcropping 150m south of the drill collars. While
low-grade, the zone is comparable to granular-silica hosted ore-grade
mineralization at the Apumayo Mine.
The Chucillani intercepts are most likely the distal portion of a
structurally controlled gold zone located to the northwest toward the Paccha
Huayco diatreme and warrants additional step-out drilling to be included in
Phase II.
Drilling indicates that the Chucllani zone exhibits moderate to strong
multi-element geochemistry with elevated pathfinder elements: arsenic,
bismuth, barium, and mercury.
Paccha Huayco Complex
Core hole (LOU012) into the Paccha Huayco target confirmed the diatreme
concept, transecting 230m of strongly silicified multi-stage diatreme
breccias.
Multiple stages of cross-cutting hydrothermal breccias are present, as
well as late-stage cross-cutting silica veinlets similar to those carrying
gold at the Apumayo Mine. Anomalous gold concentrations were encountered at
depth and appear to be correlative with Chucllani intercepts. The hole ended
in strongly altered andesite host rock, indicating that the hole is not
located in the central diatreme vent area and the target therefore requires
additional exploration drilling.
Jellopata Diatreme Target
Eight holes were drilled into the northern 600m of the 1.2km long
Jellopata diatreme resistivity anomaly and targeted the inferred central
diatreme feeder. Thick 100m to 229m plus intercepts of highly oxidized
granular to massive silica alteration were encountered that are anomalous in
molybdenum but lack anomalous gold concentrations.
One Jellopata drill hole (LOU003) appears to have penetrated close to the
inferred diatreme feeder, with the others transecting altered lateral and
distal stratiform diatreme fill sediments. Drill hole LOU003 had the thickest
silica interval encountered of 229m, and the hole was lost in favorable
silicic alteration in a fault zone at 246m. The hole showed transition to more
favorable vuggy and massive silica with higher limonite content at depth.
The character of the drill hole lithologies suggest remaining potential
to the south due to the presence of coarser diatreme fill breccias, increased
massive to vuggy silica with depth, higher limonite contents and more gold in
surface sampling.
Ayani Vent Target
Four holes were drilled into the Ayani target, a structurally controlled
zone located at the extreme northeastern portion of the Lourdes system. Drill
holes encountered the strongest trace element geochemical signature of the
program and weakly anomalous gold. Alteration indicative of the upper barren
portion of the hydrothermal system was encountered; follow-up drilling will
test the deeper portions of the zone.
North Diatreme Zone
Two holes were drilled into the North Zone, located at the extreme
northern end of the project area with outcropping northeast-trending
silicified hydrothermal breccias, granular silica breccias, and silicified
limonitic matrix breccias highly anomalous in pathfinder elements. Both holes
encountered strongly anomalous molybdenum and weakly anomalous gold
concentrations.
Cascada Diatreme Target
The Cascada target, containing some of the most continuous outcropping
gold mineralization, was not tested during the Phase I program due to
difficult access. Plans are to test the target at the start of the Phase II
program.
Drill hole intercepts to date suggest that the Cascada-Paccha
Huayco-Chucllani area is a larger continuous system and the most favorable for
gold mineralization.
Table 1. Summary of assay results and significant gold intercepts.
Drill
Hole                         Target                       Drill 
Method(1)                       Azimuth°                       
Dip°                       Total                       From                  
To           Interval           Gold
Depth (m)                      (m)                       (m)           1 
(m)              (g/t)


Area


LOU008
Chucllani
RC                                        320                         
-45                          126                         0.0                    
3                  3            0.18

---                                                                             
                                                                                
                                                                                
  ---

LOU009
Chucllani
RC                                        320                         
-55                          159                        79.5                 
85.5                  6            0.17

---                                                                             
                                                                                
                                                                                
  ---

LOU011
Chucllani
RC                                        270                         
-50                          192                          84                  
102                 18            0.24
Paccha Huayco

---                                                                             
                                                                                
                                                                                
      ---

LOU012
Paccha Huayco
CORE                                       270                         
-70                        265.7                       180.6                
183.6                  3            0.12
191.2                                     9.8            0.11
201

---                                                                             
                                                                                
                                                                                
      ---

LOU013
Chucllani
RC                                        170                         
-50                          114                          42                   
63                 21            0.24

---                                                                             
                                                                                
                                                                                
  ---

LOU019
Chucllani
CORE                                       270                         
-75                        133.2                        78.7                 
84.6                4.9            0.47
Paccha Huayco

---                                                                             
                                                                                
                                                                                
      ---

(1) Intersections presented herein may not necessarily represent true width of 
mineralization, are interpreted to be approximately representative due to the 
stratiform nature of the zone, indicated
dip angle from geophysics, and hole inclination.
Phase II Plans
The Phase II drilling program is planned to recommence after the end of
the rainy season in April. Evaluation of the drilling data will continue over
the next months and will be integrated with into the existing exploration data
to improve targeting for follow-up drilling. Phase II drilling will focus on
step-out drilling to locate the Chucllani-Paccha Huayco structural feeder,
testing the Cascada Diatreme, and following up on other targets identified
from the Phase I drill campaign.
Quality Assurance
Pucara has a Quality Assurance and Quality Control ("QA/QC") program for
all of its exploration projects which conforms to industry best practices.
Samples are sent to ALS PERU SA, an ISO/IEC 17025:2017 accredited laboratory,
in Lima, Peru for analysis. Analytical method is a 30-gram fire assay with
atomic adsorption finish. Strict sampling and QA/QC protocol are followed,
including the insertion of standards, blanks, and duplicates on a routine
basis. Results of these QC samples are tracked and failures are re-analyzed.
Sample intervals are usually 1.5m. All exploration diamond drill cores are
split in half by core sawing and sampled at appropriate intervals for assay.
The remaining core, coarse reject and pulps are stored on-site in a secure
location. Composites presented in the assay results table include intervals at
greater than 0.1 g/t Au over a 1.5m minimum width.
About Lourdes Gold Project
The wholly-owned Lourdes Gold Project is a fully-permitted, high
sulfidation epithermal precious metal project, which lies at the intersection
of two regional mineralized trends with neighboring high sulfidation prospects
and a producing mine. Pucara has identified a complex of nested diatremes,
vent breccias, and breccia bodies at Lourdes that are similar in size (km2)
and associated alteration to the high sulfidation epithermal gold deposits at
Yanacocha and Pierina in northern Peru, and the Mulatos district of Mexico.
The 2,576 hectare-property is approximately 400 kilometres southeast of Lima
and is easily accessible by a paved, single-lane road originating in the town
of Puquio, 155 kilometres east of the Pan American Highway.
About Pacaska Gold -- Copper ProjectThe Pacaska Gold-Copper Project consists of 
a highly prospective and
contiguous area of 7,650 hectares over nine concessions, wholly owned by
Pucara Gold. Pacaska is a high sulfidation epithermal precious metals project
with a possible copper porphyry system at depth. The alteration system
contains anomalous, outcropping concentrations of gold with values in rock of
up to 17 g/t and anomalous copper in rock of up to 11%. Pacaska is easily
accessible by a paved, single lane road originating at the Pan American
Highway in the town of Palpa 90 kilometres southwest of Pacaska.
The Company is currently permitting the Pacaska project for drill
testing, after completion of a large IP survey, which identified resistivity
anomalies extending to depth correlative with the gold-bearing breccias, as
well as a large broad chargeability anomaly suggestive of a porphyry copper
system. Multiple drill targets have been selected. The Company expects to
inform the market about its 2021 work program at Pacaska in a forthcoming
corporate update.
About Pucara Gold
Pucara Gold is a well-financed junior exploration company focused on the
discovery and advancement of economic precious metals deposits in
resource-rich Peru. Pucara has a portfolio approach to project acquisition and
controls nine precious and base metal projects, located in Peru. Pucara is
advancing six projects while the remaining three are under option agreements
with strategic partners. Pucara plans to grow through discoveries, strategic
relationships, and grassroots exploration. For more information, please visit
Pucara Gold's YouTube channel.
Qualified Person
The Lourdes exploration programs are conducted under the supervision of
Ken Balleweg, B.Sc. Geological Engineering, M.Sc. Geology, Registered
Professional Geologist, Vice President of Exploration, a Qualified Person as
defined by National Instrument 43-101 of the Canadian Securities
Administrators.
Cautionary Statements
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release. This news release
includes forward-looking statements that are subject to risks and
uncertainties. All statements within, other than statements of historical
fact, are to be considered forward looking. Although the Company believes the
expectations expressed in such forward-looking statements are based on
reasonable assumptions, such statements are not guarantees of future
performance and actual results or developments may differ materially from
those in forward-looking statements. Factors that could cause actual results
to differ materially from those in forward-looking statements include market
prices, exploitation and exploration successes, the impact of the COVID-19
pandemic on the worldwide economy, continued availability of capital and
financing, and general economic, market or business conditions and regulatory
and administrative approvals, processes and filing requirements. There can be
no assurances that such statements will prove accurate and, therefore, readers
are advised to rely on their own evaluation of such uncertainties. We do not
assume any obligation to update any forward-looking statements.
Appendix 1: Phase I Drill Collars
Drill                    Target                 Drill          UTM

UTM  Azimuth°   Dip°              Total          Note (2)
Hole                                           Method            East           
North                              Depth (m)
Area (1)


LOU001
Jellopata
RC             617,740         8,364,300        270     -65                 252
NS

---

LOU002
Jellopata
RC             617,750         8,364,100        270     -65                 201
NS

---

LOU003
Jellopata
RC             617,750         8,364,100        090     -65                 246
NS

---

LOU004
Jellopata
RC             617,700         8,363,900        270     -75                 180
NS

---

LOU005
Jellopata
RC             617,750         8,363,700        270     -70                 216
NS

---

LOU006
Jellopata
RC             617,550         8,364,300          0     -90                 210
NS

---

LOU007
Jellopata
CORE            617,700         8,363,900        090     -65                 170
NS

---

LOU008
Chucllani
RC             619,310         8,363,725        320     -45                 
126   See Table 1

---

LOU009
Chucllani
RC             619,250         8,363,900        320     -55                 
159   See Table 1

---

LOU010
Jellopata
CORE            617,750         8,363,700        090     -70               148.2
NS

---

LOU011
Chucllani
RC             619,250         8,363,900        270     -50                 
192   See Table 1


Paccha Huayco

---

LOU012
Paccha Huayco
CORE            619,095         8,364,115        270     -70               
265.7   See Table 1

---

LOU013
Chucllani
RC             619,250         8,363,900        170     -50                 
114   See Table 1

---

LOU014
Ayani
RC             619,775         8,364,500        300     -45                  63
NS

---

LOU015
Ayani
RC             619,470         8,364,500        300     -55                  75
NS

---

LOU016
Ayani
RC             619,850         8,364,570        300     -50                 114
NS

---

LOU017
Chucllani
RC             619,625         8,364,000        270     -53                  60
NS

---

LOU018
Chucllani
RC             619,625         8,364,000        220     -55                  72
NS

---

LOU019
Chucllani
CORE            619,185         8,364,100        270     -75               
133.2   See Table 1


Paccha Huayco

---

LOU020
Ayani
RC             619,635         8,364,510        325     -55                 126
NS

---

LOU021              Paccha Huayco East
RC             618,870         8,364,100        270     -70               154.5
NS

---

LOU022              Paccha Huayco East
RC             618,870         8,364,100        140     -60                 177
NS

---

LOU023
North
CORE            617,500         8,365,660        350     -50               144.7
NS

---

LOU024
North SE Ext
CORE            617,640         8,365,500          0     -90               151.8
NS

---

LOU025              Paccha Huayco East
RC             618,750         8,363,900        270     -85                 204
NS

---
(1) See figure 1 for location of
Target areas.
2 NS - No significant
mineralization.

SOURCE Pucara Gold Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/January2021/26/c1984.html

-0-                           01/26/2021
/For further information: Steve Zuker CEO, Director, info(at)pucaragold.com,
+1 604 687 9931/
(TORO.)

CO:  Pucara Gold Ltd.
ST:  British Columbia, Peru
IN:  MNG PRM
SU:

-30-