Source	CANADA NEWSWIRE
Date	02/05/2021
Time	10:25:54 AM

Company	 Minsud Resources Corp.
Title	Minsud announces results of Phase 2 drilling program at Chita Valley
Project, San Juan, Argentina





    CDNX Symbol: MSR











Press Release




" BC-Minsud-Phase2-Results   02-05 1738
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.166670:
^Minsud announces results of Phase 2 drilling program at Chita Valley
Project, San Juan, Argentina@

TSX-V: MSR
TORONTO, Feb. 5, 2021 /CNW/ - Minsud Resources Corp. (TSX-V: MSR)
("Minsud" or the "Company"), is pleased to announce the completion of Phase 2
diamond drilling program, comprised of 12 holes, 5,818 meters, with variable
depths between 350-650 meters, completed at the Chita and Chinchillones
porphyry targets, part of the Chita Valley Project. Together with Phase 1, the
Company completed a total of 9,377 meters during 2020, as shown in Map 1.
The program tested targets identified during the systematic
multidisciplinary exploration program conducted in the sector during Phase 1
drilling program completed during first half of 2020, and the results from the
pole-dipole geophysical survey covering 68 kilometers over 13 Induced
Polarization (IP) lines completed on July 2020.
Target Chinchillones: Scouting drill holes CHDH20-04 and CHDH20-05 (Phase
1) together with drill hole CHDH20-17 (Phase 2) confirm the presence of a deep
porphyry system and linked shallow polymetallic Cu-Au-Pb-Zn mineralizations
hosted in breccias and veins at the North West edge of the Chita Valley. Early
Chalcopyrite-molybdenum veins crosscut by hydrothermal late veins suggests a
telescoping hydrothermal event overimpossed to the porphyry system, potassium
alteration (Magnetite-Biotite) appears as a relict in the widespread
Quartz-sericite alteration. At the southern edge of the Chinchillones area,
the porphyry system appears to be intruded by a late phreato magmatic breccia
(Diatreme) and a Dacite Dome. Intermediate sulphidation (IS) Pb-Zn-Mn-Au-Ag
mineralization types, appear to be related with these magmatic hydrothermal
breccias aligned in the North North East direction. Anomalous values of
Cu-Au-Ag-Pb-Zn detected in drillhole CHDH20-08 are a typical dome-related
mineralization.
The Cu-Mo and Pb-Zn +/- Au Ag mineralization identified at the
Chinchillones area confirms that this area constitutes a high priority target
with significant potential of exploration.


Phase 2: Chinchillones area - Summary of Analytical Results

---

Hole ID                          From                           To             
Length                       Au                       Ag     Cu       Mo      
Pb         Zn

---

(mt)                            (mt)                       (mts) 
((x))           g/t                         g/t                      %      
ppm      ppm     ppm

---

CHDH20-07                                 66                               
82               16                       0.07                    13.63     
0.46      81        728     2,276


including                                 66                               
68                2                       0.11                    25.30     
2.68      99      1,950     8,610


120                              186               66                       
0.11                    14.35     0.14      65      1,321     3,061


264                              393              129                       
0.02                     9.69     0.05      99      1,047     4,926



CHDH20-08                                 42                               
68               26                       0.12                     4.80     
0.07       2        756     1,629


114.5                            115.3              0.8                       
0.99                   307.00     7.45       7      3,000    18,850


303                              309                6                       
0.34                    54.22     0.27      32        498     3,579


354                              450               96                       
0.07                    15.16     0.03       3      2,140     5,467



CHDH20-09                                       
122                              128                6                       
0.19                    24.26     0.11       6        737     1,553


450                              456                6                       
0.07                    76.64     0.17       5      1,728     4,973



CHDH20-10                                 12                               
22               10                       0.36                    75.79     
2.66       4     22,489     7,079


including                                 16                             
18.3              2.3                       0.60                   163.78     
8.43       6     49,170    23,052


65                               69                4                       
0.10                    14.40     0.10      47        541     3,763


132                              136                4                       
0.11                    10.65     0.03       2      5,493    20,810


235                              241                6                       
0.13                    35.87     0.19       2      2,153    16,743


CHDH20-17                                100                              
178               78                       0.16                     6.47     
0.21      87        144     3,531


240                              347              107                       
0.20                    24.07     0.11      16      2,046     5,942


464                              524               60                       
0.02                     1.49     0.24     137         59       740



CHDH20-18                                104                              
238              134                       0.07                     3.38     
0.19      76         68       190


including                                107                              
108                1                       0.32                   102.00     
3.52      15        430     2,850


285                              292                7                       
0.35                     5.00     0.28      39         60       167


388                              398               10                       
0.06                    11.71     0.25      57         76       408





((x)) Intervals reported in the above table are not true thicknesses
Target Chita North porphyry (PNO): This target was tested through drill
holes CHDH20-11, CHDH20-12, CHDH20-14, CHDH20-15 and CHDH20-16. The main rock
type intercepted corresponds to an Andesite porphyry. The dominant
hydrothermal alteration corresponds to a marginal propylitic Py halo (3%-5%).
Drill hole CHDH20-12, approximately at 412 meters deep, intercepted a porphyry
with Potassium alteration type, conformed by Biotite-Magnetite +/- Potassium
Feldspar. The mineralization is scarce, associated to North North East
structures with Chalcopyrite-Sphalerite (intermediate sulphidation system) and
relict of primary Molybdenite mineralization. The continuity to the north of
the potassium alteration detected at the southern margin of the Chita Valley
is still not clear and should be confirmed through future geological mapping
and drillings.
Target Chita South porphyry (PSU): It was only tested through drill hole
CHDH20-13. Mineralization of 0.3% to 0.4% Cu, up to 100 - 120 meters. The best
grades are associated with Chalcocite (product of a secondary enrichment
process) coating on Pyrite and Chalcopyrite, together with copper oxide
fillings (mix Cu Ox -Sulphur zone).


Phase 2: Chita PSU and PNO - Summary of Analytical Results

---

Hole ID                             From                               
To         Length                           Au                           Ag     
Cu       Mo      Pb      Zn

---

(mt)                              (mt)                           (mts) 
((x))        g/t                            g/t                          %      
ppm      ppm     ppm

---

CHDH20-11                                   
424                                  480           56                           
0.02                         0.64     0.09     271       7       29

---

CHDH20-12                                    
32                                   48           16                           
0.08                         4.74     0.39      40     155      492


including                                  
39.5                                   40          
0.5                           0.88                        64.20     3.47     
351     118      780


332                                  342           10                           
0.05                         2.76     0.17      35      72      263



CHDH20-13                                    
24                                  126          102                           
0.08                         2.06     0.33     253      39      104


152                                  192           40                           
0.04                         0.87     0.11     189      18      181



CHDH20-14                                         
120                                  124            4                           
0.06                         2.37     0.06      22      96    5,765


174                                  182            8                           
0.08                         2.81     0.04       6     610    3,303



CHDH20-15                                   
288                                  292            4                           
0.21                         9.30     0.16       5     110      300

---

CHDH20-16
Intercepts hydrothermal pyrite halo

---                                 ---



((x)) Intervals reported in the above table are not true thicknesses
The results of this Phase 2 scout drilling exploration program confirm
very interesting intercepts that support effectively the presence at shallow
and at down depth level of a Zn-Pb-Cu-(Ag-Au) polymetallic epithermal system
and deeper parental porphyry Cu-Mo-Au open to the North North East at
Chinchillones area.
The geological team is currently working on detailed re-logging of the
Phase 2 drill core and mapping, together with the review of all the available
structural and geochemical data in order to assist on targeting for the next
Phase 3 drill program that is being designed and scheduled to commence during
the first half of 2021.
Conceptual Geological Model
Different magmatic-hydrothermal breccias observed at Chita and
Chinchillones reflect a complex sequence of multiple events that can be linked
to explosive events developing in the upper parts of the porphyry system
during their emplacement, uplift and unroofing. In fact, at Chita and
Chinchillones, a large part of the evolution of this porphyry system would
have developed in a tectonic framework characterized by the occurrence of high
rates of regional tectonic uplift and erosion, which would have favored the
generation of telescoping processes related to mineralization process and the
formation of the diatreme complex.
Quality Assurance/Quality Control
All core samples were submitted to the ALS Laboratories in Mendoza,
Argentina for preparation and analysis. All samples were analyzed for Au by
fire assay/ AA finish 50g, plus a 48-element ultra-trace four acid digest with
ICP-MS and ICP-AES finish. Minsud followed industry standard procedures for
the work with a quality assurance/quality control (QA/QC) program. Field
duplicates, standards and blanks were included with all sample shipments to
the principal laboratory. Minsud detected no significant QA/QC issues during
review of the data.
Mr. Mario Alfaro, Professional Geoscientist, VP-Exploration of the
Company, is a qualified person as defined by Canadian National Instrument
43-101. Mr. Alfaro visited the property and has read and approved the contents
of this release.
About the Chita Valley Project, San Juan Province: The Chita Valley
Project is a large exploration stage porphyry system with classic alteration
features, widespread porphyry style Cu-Mo-Ag-Au mineralization and associated
gold and silver-bearing polymetallic veins of intermediate sulfide composition
that conformed an outcropping porphyry system at Chita and a lithocap of a
porphyry system at Chinchillones. San Juan Province of Argentina has a robust
mining sector and recognizes the important economic benefits of responsible
development of its substantial Mineral Resource endowment.
About Minsud Resources Corp. Minsud is a mineral exploration company
focused on exploring its flagship Chita Valley Cu-Mo- Au-Ag Project, in the
Province of San Juan, Argentina. The Company also holds a 100% owned portfolio
of selected early stage prospects, including 6,000 ha in Santa Cruz Province,
Argentina.
CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION:
This news release includes certain information that may constitute
forward-looking information under applicable Canadian securities laws.
Forward-looking information includes, but is not limited to, statements about
strategic plans, spending commitments, future operations, results of
exploration, anticipated financial results, future work programs, capital
expenditures and objectives. Forward-looking information is necessarily 
basedupon a number of estimates and assumptions that, while considered 
reasonable,
are subject to known and unknown risks, uncertainties, and other factors which
may cause the actual results and future events to differ materially from those
expressed or implied by such forward-looking information including, but not
limited to: fluctuations in the currency markets (such as the Canadian dollar,
Argentina peso, and the U.S. dollar); changes in national and local
government, legislation, taxation, controls, regulations and political or
economic developments in Canada and Argentina or other countries in which the
Corporation may carry on business in the future; operating or technical
difficulties in connection with exploration and development activities; risks
and hazards associated with the business of mineral exploration and
development (including environmental hazards or industrial accidents); risks
relating to the credit worthiness or financial condition of suppliers and
other parties with whom the Company does business; presence of laws and
regulations that may impose restrictions on mining, including those currently
enacted in Argentina; employee relations; relationships with and claims by
local communities; availability and increasing costs associated with
operational inputs and labour; the speculative nature of mineral exploration
and development, including the risks of obtaining necessary licenses, permits
and approvals from government authorities; business opportunities that may be
presented to, or pursued by, the Company; challenges to, or difficulty in
maintaining, the Company's title to properties; risks relating to the
Company's ability to raise funds; and the factors identified under "Risk
Factors" in the Company's Filing Statement dated April 27, 2011. There can be
no assurance that such information will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such information. Accordingly, readers should not place undue reliance on
forward-looking information. All forward-looking-information contained in this
news release is given as of the date hereof and is based upon the opinions and
estimates of management and information available to management as at the date
hereof. The Company disclaims any intention or obligation to update or revise
any forward-looking information, whether as a result of new information,
futu

" BC-Minsud-Phase2-Results   02-05 1738
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.166670:
^Minsud announces results of Phase 2 drilling program at Chita Valley
Project, San Juan, Argentina@

TSX-V: MSR
TORONTO, Feb. 5, 2021 /CNW/ - Minsud Resources Corp. (TSX-V: MSR)
("Minsud" or the "Company"), is pleased to announce the completion of Phase 2
diamond drilling program, comprised of 12 holes, 5,818 meters, with variable
depths between 350-650 meters, completed at the Chita and Chinchillones
porphyry targets, part of the Chita Valley Project. Together with Phase 1, the
Company completed a total of 9,377 meters during 2020, as shown in Map 1.
The program tested targets identified during the systematic
multidisciplinary exploration program conducted in the sector during Phase 1
drilling program completed during first half of 2020, and the results from the
pole-dipole geophysical survey covering 68 kilometers over 13 Induced
Polarization (IP) lines completed on July 2020.
Target Chinchillones: Scouting drill holes CHDH20-04 and CHDH20-05 (Phase
1) together with drill hole CHDH20-17 (Phase 2) confirm the presence of a deep
porphyry system and linked shallow polymetallic Cu-Au-Pb-Zn mineralizations
hosted in breccias and veins at the North West edge of the Chita Valley. Early
Chalcopyrite-molybdenum veins crosscut by hydrothermal late veins suggests a
telescoping hydrothermal event overimpossed to the porphyry system, potassium
alteration (Magnetite-Biotite) appears as a relict in the widespread
Quartz-sericite alteration. At the southern edge of the Chinchillones area,
the porphyry system appears to be intruded by a late phreato magmatic breccia
(Diatreme) and a Dacite Dome. Intermediate sulphidation (IS) Pb-Zn-Mn-Au-Ag
mineralization types, appear to be related with these magmatic hydrothermal
breccias aligned in the North North East direction. Anomalous values of
Cu-Au-Ag-Pb-Zn detected in drillhole CHDH20-08 are a typical dome-related
mineralization.
The Cu-Mo and Pb-Zn +/- Au Ag mineralization identified at the
Chinchillones area confirms that this area constitutes a high priority target
with significant potential of exploration.


Phase 2: Chinchillones area - Summary of Analytical Results

---

Hole ID                          From                           To             
Length                       Au                       Ag     Cu       Mo      
Pb         Zn

---

(mt)                            (mt)                       (mts) 
((x))           g/t                         g/t                      %      
ppm      ppm     ppm

---

CHDH20-07                                 66                               
82               16                       0.07                    13.63     
0.46      81        728     2,276


including                                 66                               
68                2                       0.11                    25.30     
2.68      99      1,950     8,610


120                              186               66                       
0.11                    14.35     0.14      65      1,321     3,061


264                              393              129                       
0.02                     9.69     0.05      99      1,047     4,926



CHDH20-08                                 42                               
68               26                       0.12                     4.80     
0.07       2        756     1,629


114.5                            115.3              0.8                       
0.99                   307.00     7.45       7      3,000    18,850


303                              309                6                       
0.34                    54.22     0.27      32        498     3,579


354                              450               96                       
0.07                    15.16     0.03       3      2,140     5,467



CHDH20-09                                       
122                              128                6                       
0.19                    24.26     0.11       6        737     1,553


450                              456                6                       
0.07                    76.64     0.17       5      1,728     4,973



CHDH20-10                                 12                               
22               10                       0.36                    75.79     
2.66       4     22,489     7,079


including                                 16                             
18.3              2.3                       0.60                   163.78     
8.43       6     49,170    23,052


65                               69                4                       
0.10                    14.40     0.10      47        541     3,763


132                              136                4                       
0.11                    10.65     0.03       2      5,493    20,810


235                              241                6                       
0.13                    35.87     0.19       2      2,153    16,743


CHDH20-17                                100                              
178               78                       0.16                     6.47     
0.21      87        144     3,531


240                              347              107                       
0.20                    24.07     0.11      16      2,046     5,942


464                              524               60                       
0.02                     1.49     0.24     137         59       740



CHDH20-18                                104                              
238              134                       0.07                     3.38     
0.19      76         68       190


including                                107                              
108                1                       0.32                   102.00     
3.52      15        430     2,850


285                              292                7                       
0.35                     5.00     0.28      39         60       167


388                              398               10                       
0.06                    11.71     0.25      57         76       408





((x)) Intervals reported in the above table are not true thicknesses
Target Chita North porphyry (PNO): This target was tested through drill
holes CHDH20-11, CHDH20-12, CHDH20-14, CHDH20-15 and CHDH20-16. The main rock
type intercepted corresponds to an Andesite porphyry. The dominant
hydrothermal alteration corresponds to a marginal propylitic Py halo (3%-5%).
Drill hole CHDH20-12, approximately at 412 meters deep, intercepted a porphyry
with Potassium alteration type, conformed by Biotite-Magnetite +/- Potassium
Feldspar. The mineralization is scarce, associated to North North East
structures with Chalcopyrite-Sphalerite (intermediate sulphidation system) and
relict of primary Molybdenite mineralization. The continuity to the north of
the potassium alteration detected at the southern margin of the Chita Valley
is still not clear and should be confirmed through future geological mapping
and drillings.
Target Chita South porphyry (PSU): It was only tested through drill hole
CHDH20-13. Mineralization of 0.3% to 0.4% Cu, up to 100 - 120 meters. The best
grades are associated with Chalcocite (product of a secondary enrichment
process) coating on Pyrite and Chalcopyrite, together with copper oxide
fillings (mix Cu Ox -Sulphur zone).


Phase 2: Chita PSU and PNO - Summary of Analytical Results

---

Hole ID                             From                               
To         Length                           Au                           Ag     
Cu       Mo      Pb      Zn

---

(mt)                              (mt)                           (mts) 
((x))        g/t                            g/t                          %      
ppm      ppm     ppm

---

CHDH20-11                                   
424                                  480           56                           
0.02                         0.64     0.09     271       7       29

---

CHDH20-12                                    
32                                   48           16                           
0.08                         4.74     0.39      40     155      492


including                                  
39.5                                   40          
0.5                           0.88                        64.20     3.47     
351     118      780


332                                  342           10                           
0.05                         2.76     0.17      35      72      263



CHDH20-13                                    
24                                  126          102                           
0.08                         2.06     0.33     253      39      104


152                                  192           40                           
0.04                         0.87     0.11     189      18      181



CHDH20-14                                         
120                                  124            4                           
0.06                         2.37     0.06      22      96    5,765


174                                  182            8                           
0.08                         2.81     0.04       6     610    3,303



CHDH20-15                                   
288                                  292            4                           
0.21                         9.30     0.16       5     110      300

---

CHDH20-16
Intercepts hydrothermal pyrite halo

---                                 ---



((x)) Intervals reported in the above table are not true thicknesses
The results of this Phase 2 scout drilling exploration program confirm
very interesting intercepts that support effectively the presence at shallow
and at down depth level of a Zn-Pb-Cu-(Ag-Au) polymetallic epithermal system
and deeper parental porphyry Cu-Mo-Au open to the North North East at
Chinchillones area.
The geological team is currently working on detailed re-logging of the
Phase 2 drill core and mapping, together with the review of all the available
structural and geochemical data in order to assist on targeting for the next
Phase 3 drill program that is being designed and scheduled to commence during
the first half of 2021.
Conceptual Geological Model
Different magmatic-hydrothermal breccias observed at Chita and
Chinchillones reflect a complex sequence of multiple events that can be linked
to explosive events developing in the upper parts of the porphyry system
during their emplacement, uplift and unroofing. In fact, at Chita and
Chinchillones, a large part of the evolution of this porphyry system would
have developed in a tectonic framework characterized by the occurrence of high
rates of regional tectonic uplift and erosion, which would have favored the
generation of telescoping processes related to mineralization process and the
formation of the diatreme complex.
Quality Assurance/Quality Control
All core samples were submitted to the ALS Laboratories in Mendoza,
Argentina for preparation and analysis. All samples were analyzed for Au by
fire assay/ AA finish 50g, plus a 48-element ultra-trace four acid digest with
ICP-MS and ICP-AES finish. Minsud followed industry standard procedures for
the work with a quality assurance/quality control (QA/QC) program. Field
duplicates, standards and blanks were included with all sample shipments to
the principal laboratory. Minsud detected no significant QA/QC issues during
review of the data.
Mr. Mario Alfaro, Professional Geoscientist, VP-Exploration of the
Company, is a qualified person as defined by Canadian National Instrument
43-101. Mr. Alfaro visited the property and has read and approved the contents
of this release.
About the Chita Valley Project, San Juan Province: The Chita Valley
Project is a large exploration stage porphyry system with classic alteration
features, widespread porphyry style Cu-Mo-Ag-Au mineralization and associated
gold and silver-bearing polymetallic veins of intermediate sulfide composition
that conformed an outcropping porphyry system at Chita and a lithocap of a
porphyry system at Chinchillones. San Juan Province of Argentina has a robust
mining sector and recognizes the important economic benefits of responsible
development of its substantial Mineral Resource endowment.
About Minsud Resources Corp. Minsud is a mineral exploration company
focused on exploring its flagship Chita Valley Cu-Mo- Au-Ag Project, in the
Province of San Juan, Argentina. The Company also holds a 100% owned portfolio
of selected early stage prospects, including 6,000 ha in Santa Cruz Province,
Argentina.
CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION:
This news release includes certain information that may constitute
forward-looking information under applicable Canadian securities laws.
Forward-looking information includes, but is not limited to, statements about
strategic plans, spending commitments, future operations, results of
exploration, anticipated financial results, future work programs, capital
expenditures and objectives. Forward-looking information is necessarily 
basedupon a number of estimates and assumptions that, while considered 
reasonable,
are subject to known and unknown risks, uncertainties, and other factors which
may cause the actual results and future events to differ materially from those
expressed or implied by such forward-looking information including, but not
limited to: fluctuations in the currency markets (such as the Canadian dollar,
Argentina peso, and the U.S. dollar); changes in national and local
government, legislation, taxation, controls, regulations and political or
economic developments in Canada and Argentina or other countries in which the
Corporation may carry on business in the future; operating or technical
difficulties in connection with exploration and development activities; risks
and hazards associated with the business of mineral exploration and
development (including environmental hazards or industrial accidents); risks
relating to the credit worthiness or financial condition of suppliers and
other parties with whom the Company does business; presence of laws and
regulations that may impose restrictions on mining, including those currently
enacted in Argentina; employee relations; relationships with and claims by
local communities; availability and increasing costs associated with
operational inputs and labour; the speculative nature of mineral exploration
and development, including the risks of obtaining necessary licenses, permits
and approvals from government authorities; business opportunities that may be
presented to, or pursued by, the Company; challenges to, or difficulty in
maintaining, the Company's title to properties; risks relating to the
Company's ability to raise funds; and the factors identified under "Risk
Factors" in the Company's Filing Statement dated April 27, 2011. There can be
no assurance that such information will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such information. Accordingly, readers should not place undue reliance on
forward-looking information. All forward-looking-information contained in this
news release is given as of the date hereof and is based upon the opinions and
estimates of management and information available to management as at the date
hereof. The Company disclaims any intention or obligation to update or revise
any forward-looking information, whether as a result of new information,
future events or otherwise, except as required by law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Minsud Resources Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/February2021/05/c4166.html

-0-                           02/05/2021
/For further information: Ramiro Massa, President and Chief Executive
Officer, info(at)minsud.com, +1 416-479-4466/
/Web Site: www.minsud.com/ /
(MSR.)

CO:  Minsud Resources Corp.
ST:  Ontario
IN:  MNG MIN
SU:

-30-