Source	CANADA NEWSWIRE
Date	03/17/2021
Time	04:04:00 AM

Company	 Skyharbour Resources Ltd.
Title	Skyharbour Commences Exploration and Mobilizes for Upcoming Drill
Program at its High Grade Moore Uranium Project, Saskatchewan





    CDNX Symbol: SYH











Press Release




" BC-SKYHARBOUR-Drill-Prog   03-17 1983
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.586192:
^Skyharbour Commences Exploration and Mobilizes for Upcoming Drill
Program at its High Grade Moore Uranium Project, Saskatchewan@

VANCOUVER, BC, March 17, 2021 /CNW/ - Skyharbour Resources Ltd.
(TSX-V:SYH) (OTCQB:SYHBF) (Frankfurt:SC1P) (the "Company") is pleased to
announce that mobilization has begun for its 2021 geophysical and diamond
drilling programs at its flagship 35,705 hectare Moore Uranium Project,
located approximately 15 kilometres east of Denison Mine's Wheeler River
project and near regional infrastructure on the southeast side of the
Athabasca Basin, Saskatchewan. The Company has planned a 9 km Small Moving
Loop EM (SML-EM) geophysical program to refine additional drill targets and
has begun mobilization of drilling equipment for a subsequent 3,000 metre
diamond drilling program consisting of 10 to 12 drill holes. These fully
funded and permitted programs will focus on following-up on existing
unconformity and basement-hosted targets along the high grade Maverick
structural corridor as well as identifying new targets at the Grid Nineteen
area.
Moore Uranium Project Claims
Map:https://skyharbourltd.com/_resources/maps/MooreLakeRegionalTenure-v1.jpg
Jordan Trimble, President and CEO of Skyharbour Resources, states: "We
have been very pleased with the results to date at the Maverick East Zone, and
we will continue to focus on the expansion of this high grade mineralized
zone. The uranium mineralization identified during previous drill programs
illustrates the strong discovery potential at Moore and recent geophysical
programs and new geological modeling have encouraged the Company to develop
new regional drill targets in areas such as Grid Nineteen. Outside of our
Moore Project, Skyharbour's partner companies have been advancing some of our
other projects. Azincourt is currently conducting a minimum 2,000 metre
diamond drilling program at the East Preston Project and at our Hook Lake
Project (previously called North Falcon Point), Valor Resources has begun
planning for their upcoming exploration programs including airborne geophysics
and ground-based exploration in the summer. The uranium market has shown
notable signs of recovery with increasing equity valuations and improving
sentiment, and this recovery appears to be accelerating."
Winter 2021 Geophysical and Diamond Drilling Programs at the Moore
Uranium Project:
Skyharbour will continue to systematically explore and drill test the
Moore Lake property this year. As part of this work, a 9 line-km SML-EM survey
has been planned for a previously untested area called Grid Nineteen located
between the Rarotonga and East Venice conductors. The focus of this work will
be to better define the historic airborne EM conductors in this area and
develop drill targets on these conductor systems.
Moore Uranium Project Regional Drill Targets Map:
http://skyharbourltd.com/_resources/maps/Moore-Lake-Property-Wide.jpg
Mobilization for a planned 3,000 metre diamond drilling program,
consisting of 10 to 12 holes, will take place concurrently with the
geophysical program. The drilling will focus on both unconformity and
basement-hosted targets along the Maverick structural corridor and new targets
identified in the Grid Nineteen area. The Company specifically plans to expand
the high grade mineralization discovered recently at the Maverick East Zone,
along strike, down-plunge and at depth with a focus on basement-hosted
mineralization. Other targets along the 4.7 km long Maverick structural
corridor will be investigated, including the Esker Target, again with a focus
on basement-hosted mineralization.
Maverick East Target:
The high grade Maverick East Zone has been identified over a minimum of
170 metres strike length. It is currently a minimum of 10 metres wide, it is
open down dip and it is up to 17.9 metres thick with grades of up to 9.12%
U3O8 with a minimum grade of 0.1% U3O8. The mineralization is accompanied by
intense clay alteration, geochemical enrichment of pathfinder elements such as
B, Ni and Cu, with the localized high grade uranium mineralization extending
from the unconformity into the basement rocks. The mineralized zone appears to
plunge moderately to the northeast. In the eastern extent of the Maverick East
Zone, copper values of up to 2.3% Cu were obtained from graphitic, clay-rich
fractures within a broader zone of uranium-enriched and clay-altered granitic
pegmatite and granite nearly 100 metres below the unconformity. This may be an
important vector for additional basement-hosted mineralization. Some of the
better drill hole intersections in the Maverick East Zone include ML-202,
which returned 1.79% U3O8 over 11.5 metres, including 4.17% U3O8 over 4.5
metres and 9.12% U3O8 over 1.4 metres, as well as recently announced hole
ML20-09, which returned 0.72% U3O8 over 17.5 metres from 271.5 metres to 289.0
metres, including 1.00% U3O8 over a 10.0 metre interval in the basement
portion of the interval (279.0 metres to 289.0 metres). The focus for future
drilling in this area will be on the down-dip, along strike and down-plunge
extensions of the Maverick East target.
Moore Uranium Project Main and East Maverick Zones Drilling
Map:https://www.skyharbourltd.com/_resources/maps/Fall-2020-Maverick-East-deta
il.pdf
Maverick Structural Corridor - Northeast Extension and Esker Targets:
Drilling to the northeast of the Main Maverick and Maverick East
mineralized zones will be within the remaining 2.2 km of the Maverick
Structural Corridor. A large portion of this trend has been tested by a series
of broadly spaced drill holes and fences with significant untested gaps.
Virtually all the holes exhibited extensive sandstone and basement alteration
as well as geochemical enrichment similar to that found within the Main
Maverick and Maverick East Zones. Narrow intercepts of uranium mineralization
have been identified in numerous locations along this portion of the Maverick
corridor. Many of these mineralized intercepts occur at the unconformity, but
in a few key areas significant strongly altered basement structures within
prospective graphitic and metasedimentary units are the host for this
mineralization with only limited drilling of the basement rocks at depth.
The Esker Target lies at the northeastern limits of the Maverick
Structural Corridor. Of note from historic drilling in this area is the
anomalous uranium in drill hole MT-04 which returned up to 170 ppm U in the
basal 3.0 metres of sandstone and up to 343 ppm U in the top 5.5 metres of the
basement rock. The uranium is accompanied by anomalous amounts of pathfinder
elements including Ni, Co, Cu, Pb, and Zn. Follow-up of the anomalous uranium
mineralization has been limited with the next closest hole MT-10 (also with
anomalous U in the sandstone) located 120 metres to the south. Further south
in the Esker area, weak uranium mineralization was intersected in historical
hole ML-165 (1.0 metre of 0.307% U3O8 from 291.85 metres to 292.85 metres),
hole ML-169 (1.5 metres of 0.070% U3O8 at 287.25 metres to 288.75 metres), and
hole ML-171 (0.5 metres of 0.160% U3O8 from 296.2 to 296.7 metres). Drilling
will follow-up on the anomalous uranium encountered in historical holes MT-04
and MT-10 where there has been very limited investigation and follow-up work
along trend.
Grid Nineteen Geophysical Program:
A review of historical airborne EM has identified several conductive
features in an area located between the East Venice and Rarotonga conductor
systems that warrant follow-up groundwork. The airborne conductors lie in a
structurally complex area that bridges a break in the east trending Venice
East conductive system and the north trending Rarotonga conductors. A total of
9 line km of survey is planned to utilize 200 metre loops in a moving array.
The program was designed and will be interpreted by Bingham Geoscience of
Saskatoon. The survey is being conducted by Patterson Mining Geophysics of La
Ronge. Both Bingham and Patterson have been active in uranium exploration of
the Athabasca Basin for over 35 years and have a wealth of experience in the
district.
Winter 2021 Geophysical Program at Moore:
https://www.skyharbourltd.com/_resources/maps/Moore2021-Geophysics.jpg
Moore Uranium Project Overview:
In June 2016, Skyharbour secured an option to acquire Denison Mine's
Moore Uranium Project on the southeastern side of the Athabasca Basin, in
northern Saskatchewan. The project consists of 12 contiguous claims totaling
35,705 hectares located 42 kilometres northeast of the Key Lake mill,
approximately 15 kilometres east of Denison's Wheeler River project, and 39
kilometres south of Cameco's McArthur River uranium mine. Unconformity style
uranium mineralization was discovered on the Moore Project at the Maverick
Zone in May 2000. Historical drill results include 4.03% eU3O8 over 10.0
metres including 20% eU3O8 over 1.4 metres. In 2017, Skyharbour announced
drill results of 6.0% U3O8 over 5.9 metres including 20.8% U3O8 over 1.5
metres at a vertical depth of 265.0 metres at the Maverick Zone. In addition
to the Maverick Zone, the project hosts other mineralized targets with strong
discovery potential which the Company plans to test with future drill
programs. The project is easily accessible by air and in winter via ice roads
which simplifies logistics and lowers costs.
Moore Lake Uranium Project Geophysics
Map:http://skyharbourltd.com/_resources/maps/MooreLake-Basic-geo-revamp.jpg
Qualified Person:
The technical information in this news release has been prepared in
accordance with the Canadian regulatory requirements set out in National
Instrument 43-101 and reviewed and approved by Richard Kusmirski, P.Geo.,
M.Sc., Skyharbour's Head Technical Advisor and a Director, as well as a
Qualified Person.
About Skyharbour Resources Ltd.:
Skyharbour holds an extensive portfolio of uranium exploration projects
in Canada's Athabasca Basin and is well positioned to benefit from improving
uranium market fundamentals with six drill-ready projects covering over
240,000 hectares of land. Skyharbour has acquired from Denison Mines, a large
strategic shareholder of the Company, a 100% interest in the Moore Uranium
Project which is located 15 kilometres east of Denison's Wheeler River project
and 39 kilometres south of Cameco's McArthur River uranium mine. Moore is an
advanced stage uranium exploration property with high grade uranium
mineralization at the Maverick Zone that returned drill results of up to 6.0%
U3O8 over 5.9 metres including 20.8% U3O8 over 1.5 metres at a vertical depth
of 265 metres. The Company has plans for upcoming drill programs at the
project.
Skyharbour has an option agreement with Orano Canada Inc. and a joint
venture partnership with Azincourt Energy. Orano can earn-in up to 70% of the
Preston Project and Azincourt recently earned-in 70% of the East Preston
Project through exploration expenditures, cash payments and Azincourt share
issuance. Preston and East Preston are large, geologically prospective
properties proximal to Fission Uranium's Triple R deposit as well as NexGen
Energy's Arrow deposit.
The Company owns a 100% interest in the South Falcon Uranium Project on
the eastern perimeter of the Basin which contains a NI 43-101 inferred
resource totaling 7.0 million pounds of U3O8 at 0.03% and 5.3 million pounds
of ThO2 at 0.023%. Furthermore, Skyharbour has recently signed a Definitive
Agreement with ASX-listed Valor Resources on the Hooke Lake (previously North
Falcon Point) Uranium Project whereby Valor can earn-in 80% of the project
through $3,500,000 in total exploration expenditures, $475,000 in total cash
payments over three years and an initial share issuance.
Skyharbour's goal is to maximize shareholder value through new mineral
discoveries, committed long-term partnerships, and the advancement of
exploration projects in geopolitically favourable jurisdictions.
Skyharbour's Uranium Project Map in the Athabasca
Basin:http://skyharbourltd.com/_resources/maps/SYH-Athabasca-Map.jpg
To find out more about Skyharbour Resources Ltd. (TSX-V: SYH) visit the
Company's website at www.skyharbourltd.com.
SKYHARBOUR RESOURCES LTD.
"Jordan Trimble" Jordan TrimblePresident and CEO
For further information contact myself or:Spencer CoulterCorporate
Development and CommunicationsSkyharbour Resources Ltd. Telephone:
604-687-3376Toll Free: 800-567-8181Facsimile: 604-687-3119Email:
info(at)skyharbourltd.com
NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER
ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THE CONTENT OF THIS
NEWS RELEASE.
This release includes certain statements that may be deemed to be
"forward-looking statements". All statements in this release, other than
statements of historical facts, that address events or developments that
management of the Company expects, are forward-looking statements. Although
management believes the expectations expressed in such forward-looking
statements are based on reasonable assumptions, such statements are not
guarantees of future performance, and actual results or developments may
differ materially from those in the forward-looking statements. The Company
undertakes no obligation to update these forward-looking statements if
management's beliefs, estimates or opinions, or other factors, should change.
Factors that could cause actual results to differ materially from those in
forward-looking statements, include market prices, exploration and development
successes, continued availability of capital and financing, and general
economic, market or business conditions. Please see the public filings of the
Company at www.sedar.com for further information.
SOURCE Skyharbour Resources Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/March2021/17/c4135.html

-0-                           03/17/2021
/For further information:/
(SC1P SYHBF SYH.)

CO:  Skyharbour Resources Ltd.
ST:  British Columbia
IN:  OTC MNG
SU:  CXP

-30-