Source	CANADA NEWSWIRE
Date	03/29/2021
Time	04:33:22 AM

Company	 Great Bear Resources Ltd.
Title	Great Bear Doubles Vertical Extent of LP Fault, Intersects High-Grade
Gold at 942.20 m Downhole: 15.57 g/t Gold Over 3.05 m





    CDNX Symbol: GBR











Press Release




" BC-Great-Bear-report   03-29 1982
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.398740:
^Great Bear Doubles Vertical Extent of LP Fault, Intersects High-Grade
Gold at 942.20 m Downhole: 15.57 g/t Gold Over 3.05 m@

TSX-V: GBR
VANCOUVER, BC, March 29, 2021 /CNW/ - Great Bear Resources Ltd. (the
"Company" or "Great Bear", (TSXV: GBR) (OTCQX: GTBAF) today reported results
from its ongoing fully funded $45 million 2021 exploration program at its 100%
owned flagship Dixie Project in the Red Lake district of Ontario.
Expansion of the LP Fault
<<

--  Deep drilling has doubled the drill-confirmed vertical extent of the LP
Fault gold zone, which begins at bedrock surface, to approximately 800
vertical metres. The area of ongoing grid drilling extends along 4
kilometres of strike length. Figure 1 and Figure 2.
--  Three new 400 - 450 metre step-down holes drilled along 500 metres of
strike length all successfully intersected the continuation of the LP
Fault host rocks and gold mineralization at depths of 700 - 820 vertical
metres.
--  Gold grades and mineralized zone thickness were better at depth on two
of three tested drill sections.
--  Initial deep drilling tested below the most weakly mineralized segment
of the LP Fault, formerly referred to as the "Gap" zone (February 13,
2020).
--  Large scale step-out drilling at depth, including below areas of
high-grade gold mineralization, will continue throughout 2021.
<>>
High-Grade Gold in the First Deep LP Fault Drill Holes
<<

--  High-grade gold was intersected at depth in two of the three deep drill
holes, with better grades and thickness than previously observed in the
near surface. All three deep drill holes contained multiple intervals of
gold mineralization. Table 1 and Table 2.
--  BR-260 is the deepest LP Fault drill hole to date. It assayed 15.57 g/t
gold over 3.05 metres from 942.20 to 945.25 metres, within a broader
interval of 1.08 g/t gold over 70.25 metres from 906.15 to 976.40
metres. Figure 3 and Figure 4.
--  While high-grade intervals are the primary drill targets at these
depths, the dual high-grade and bulk-tonnage character of the LP Fault
gold zone remains strongly developed at depth.
--  Oriented core data collected from these initial deep holes will assist
with determining controls to higher grade panels within the broad
envelope of gold mineralization.
<>>
Great Bear has now published results from 270 LP Fault drill holes and
anticipates at least 130 additional LP Fault drill holes will be completed by
the end of 2021, for a total of at least 400 drill holes.
Chris Taylor, President and CEO of Great Bear said, "We drilled below the
most weakly mineralized segment of the LP Fault with our first deep holes, and
discovered better gold mineralization at depth. After 270 drill holes we have
yet to find the limits of the LP Fault's gold mineralization. Mesothermal gold
systems of this type, particularly in the Red Lake area, can extend vertically
over kilometres. We are currently working with in-house and external modelers
to finalize 2021 drill plans, and will provide guidance over the coming weeks
on expected timing of delivery of initial estimates of mineral resources."
Figure 1 (Top): Long section of the LP Fault zone showing the locations
and depths of the new deep drill holes (labeled). Figure 2 (Bottom) : Map of
current drill results showing the location of the new deep drill holes.
Table 1: Drill holes released to date on section 21450 showing increased
gold mineralization grades and widths with increasing depth in the former
"Gap" zone. See news releases of April 9, 2020 and May 4, 2020 for previously
reported drill holes. New results from BR-260 in italics.
Drill
Hole                       From (m) To (m)  Width(x) (m)   Gold 
(g/t)              Vertical
Depth (m)

---

BR-
078                               176.00  212.90        36.90          
0.42                    150

---

BR-
097                               255.00  259.00         4.00          
1.39                    220



and             391.70  393.50         1.80          3.49                    335



BR-
098                               419.70  448.50        28.80          
0.65                    365



and             493.25  495.05         1.80          9.90                    425



BR-
260                   906.15  976.40        70.25          
1.08                    760


(new)       including   942.20  945.25         3.05         
15.57                    790

---
(x) Widths are drill indicated
core length, as insufficient
drilling has been undertaken
to determine true widths at
this time.  Average grades
are calculated with un-
capped gold assays, as
insufficient drilling has
been completed to determine
capping levels for higher
grade gold intercepts.
Interval widths are
calculated using a 0.10 g/t
gold cut-off grade with up
to 3 m of internal dilution
of zero grade.
Table 2: New drill results from the first three deep holes into the LP
Fault system along 500 metres of strike length in the "Gap" area.
Drill
Hole                            From (m) To (m)  Width(x) (m)   Gold (g/t)    
Section

---

BR-
260                                   906.15  976.40        70.25          
1.08       21450




including     929.30  948.00        18.70          3.33


and including   929.30  929.80         0.50         16.50


and including   942.20  945.25         3.05         15.57


and including   942.20  942.80         0.60         73.10



BR-
261                                   624.85  638.50        13.65          
0.57       21200


747.15  761.00        13.85          0.44


811.60  823.25        11.65          0.96




including     822.00  823.25         1.25          5.62



and               835.00  839.50         4.50          1.17



BR-
262                                   871.00  876.50         5.50          
1.19       21700




and        933.50  950.50        17.00          1.04




including     946.50  948.50         2.00          7.27


and including   946.50  947.50         1.00         12.30
(x) Widths are drill indicated
core length, as insufficient
drilling has been undertaken
to determine true widths at
this time.  Average grades
are calculated with un-
capped gold assays, as
insufficient drilling has
been completed to determine
capping levels for higher
grade gold intercepts.
Interval widths are
calculated using a 0.10 g/t
gold cut-off grade with up
to 3 m of internal dilution
of zero grade.

<br /><p>Figure 3: Section 21450 showing BR-260, the deepest drill hole in the 
LP Fault to date.  This section is located in what was formerly referred to as 
the "Gap" zone.</p>
<p>Figure 4:  The deepest drill hole in the LP Fault to date.  73.10 g/t gold 
over 0.60 metres at 942.20 metres down hole in BR-260 (790 metres vertical 
depth).  The shear-zone hosted disseminated high-grade gold with sparse 
accessory sulphides within a felsic volcanic host matches mineralization at 
shallower depths within the LP Fault.  Image is of a selected interval and is 
not representative of all gold mineralization on the property.</p>
<p></p>
<p>Great Bear's progress can be followed using the Company's plan maps, long 
sections and cross sections, and through the VRIFY model posted at the 
Company's web site at www.greatbearresources.ca, which will next be updated in 
Q2 2021.  All LP Fault drill hole highlighted assays, plus drill collar 
locations and orientations can also be downloaded at the Company's web site.</p>
<p>Drill collar location, azimuth and dip for drill holes included in this 
release are provided in the table below (UTM zone 15N, NAD 83):</p>
<pre>
Hole ID Easting Northing  Elevation   Length    Dip     Azimuth

---

BR-260        456566   5635016         372      1200     -64         225

---

BR-261        456714   5634887         364      1284     -63         220

---

BR-262        456384   5635181         378      1110     -63         224

---
</pre><p>About the Dixie Project</p>
<p>The Dixie Project is 100% owned, comprised of 9,140 hectares of contiguous 
claims that extend over 22 kilometres, and is located approximately 25 
kilometres southeast of the town of Red Lake, Ontario. The project is 
accessible year-round via a 15 minute drive on a paved highway which runs the 
length of the northern claim boundary and a network of well-maintained logging 
roads. </p>
<p>The Dixie Project hosts two principal styles of gold mineralization:</p>
<ul type(equal sign)"disc"><li>High-grade gold in quartz veins and 
silica-sulphide replacement zones (Dixie Limb, Hinge and Arrow zones). Hosted 
by mafic volcanic rocks and localized near regional-scale D2 fold axes.  These 
mineralization styles are also typical of the significant mined deposits of the 
Red Lake district. </li><li>High-grade disseminated gold with broad moderate to 
lower grade envelopes (LP Fault).  The LP Fault is a significant gold-hosting 
structure which has been seismically imaged to extend to 14 kilometres depth 
(Zeng and Calvert, 2006), and has been interpreted by Great Bear to have up to 
18 kilometres of strike length on the Dixie property.  High-grade gold 
mineralization is controlled by structural and geological contacts, and 
moderate to lower-grade disseminated gold surrounds and flanks the high-grade 
intervals.  The dominant gold-hosting stratigraphy consists of felsic sediments 
and volcanic units.</li></ul><p>About Great Bear</p>
<p>Great Bear Resources Ltd. is a well-financed gold exploration company 
managed by a team with a track record of success in mineral exploration.  Great 
Bear is focused in the prolific Red Lake gold district in northwest Ontario, 
where the company controls over 330 km2 of highly prospective tenure across 5 
projects: the flagship Dixie Project (100% owned), the Pakwash Property 
(earning a 100% interest), the Dedee Property (earning a 100% interest), the 
Sobel Property (earning a 100% interest), and the Red Lake North Property 
(earning a 100% interest) all of which are accessible year-round through 
existing roads.</p>
<p>QA/QC and Core Sampling Protocols</p>
<p>Drill core is logged and sampled in a secure core storage facility located 
in Red Lake Ontario.  Core samples from the program are cut in half, using a 
diamond cutting saw, and are sent to Activation Laboratories in Ontario, an 
accredited mineral analysis laboratory, for analysis. All samples are analysed 
for gold using standard Fire Assay-AA techniques. Samples returning over 10.0 
g/t gold are analysed utilizing standard Fire Assay-Gravimetric methods.  Pulps 
from approximately 5% of the gold mineralized samples are submitted for check 
analysis to a second lab.  Selected samples are also chosen for duplicate assay 
from the coarse reject of the original sample.  Selected samples with visible 
gold are also analyzed with a standard 1 kg metallic screen fire assay.  
Certified gold reference standards, blanks and field duplicates are routinely 
inserted into the sample stream, as part of Great Bear's quality 
control/quality assurance program (QAQC).  No QAQC issues were noted with the
results reported herein.  </p>
<p>Qualified Person and NI 43-101 Disclosure</p>
<p>Mr. R. Bob Singh, P.Geo, VP Exploration, and Ms. Andrea Diakow P.Geo, 
Exploration Manager for Great Bear are the Qualified Persons as defined by 
National Instrument 43-101 responsible for the accuracy of technical 
information contained in this news release.</p>
<p>ON BEHALF OF THE BOARD</p>
<p>"Chris Taylor"                                   </p>
<p>Chris Taylor, President and CEO</p>
<p>Cautionary note regarding forward-looking statements</p>
<p>This release contains certain "forward looking statements" and certain 
"forward-looking information" as defined under applicable Canadian and U.S. 
securities laws. Forward-looking statements and information can generally be 
identified by the use of forward-looking terminology such as "may", "will", 
"should", "expect", "intend", "estimate", "anticipate", "believe", "continue", 
"plans" or similar terminology. The forward-looking information contained 
herein is provided for the purpose of assisting readers in understanding 
management's current expectations and plans relating to the future. Readers are 
cautioned that such information may not be appropriate for other purposes.</p>
<p>Forward-looking information are based on management of the parties' 
reasonable assumptions, estimates, expectations, analyses and opinions, which 
are based on such management's experience and perception of trends, current 
conditions and expected developments, and other factors that management 
believes are relevant and reasonable in the circumstances, but which may prove 
to be incorrect.</p><p>Such factors, among other things, include: impacts 
arising from the global 
disruption caused by the Covid-19 coronavirus outbreak, business integration 
risks; fluctuations in general macroeconomic conditions; fluctuations in 
securities markets; fluctuations in spot and forward prices of gold or certain 
other commodities; change in national and local government, legislation, 
taxation, controls, regulations and political or economic developments; risks 
and hazards associated with the business of mineral exploration, development 
and mining (including environmental hazards, industrial accidents, unusual or 
unexpected formations pressures, cave-ins and flooding); discrepancies between 
actual and estimated metallurgical recoveries; inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); and 
title to properties. </p>
<p>Great Bear undertakes no obligation to update forward-looking information 
except as required by applicable law. Such forward-looking information 
represents management's best judgment based on information currently available. 
No forward-looking statement can be guaranteed and actual future results may 
vary materially. Accordingly, readers are advised not to place undue reliance 
on forward-looking statements or information.</p>
<p id(equal sign)"PURL">View original content to download 
multimedia:http://www.prnewswire.com/news-releases/great-bear-doubles-vertical-e
xtent-of-lp-fault-intersects-high-grade-gold-at-942-20-m-downhole-15-57-gt-gold-
over-3-05-m-301257347.html</p>

<p>SOURCE  Great Bear Resources Ltd.</p>



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/March2021/29/c7151.html

-0-                           03/29/2021
/For further information: Investor Inquiries: Mr. Knox Henderson, Tel:
604-646-8354, Direct: 604-551-2360, info(at)greatbearresources.ca,
www.greatbearresources.ca/
/Web Site: https://greatbearresources.ca/ /
(GTBAF GBR.)

CO:  Great Bear Resources Ltd.
ST:  British Columbia
IN:  MNG OTC
SU:

-30-