Source	CANADA NEWSWIRE
Date	03/31/2021
Time	05:04:32 AM

Company	 District Metals Corp.
Title	District Reports on Significant Gravity High Anomalies at the Tomtebo
Property





    CDNX Symbol: DMX











Press Release




" BC-District-Metals-repor   03-31 1590
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.564126:
^District Reports on Significant Gravity High Anomalies at the Tomtebo
Property@

VANCOUVER, BC, March 31, 2021 /CNW/ - District Metals Corp. (TSXV: DMX)
(FSE: DFPP); ("District" or the "Company") is pleased to announce the results
of a ground gravity survey at the high grade polymetallic Tomtebo Property
located in the Bergslagen Mining District in south-central Sweden. This
gravity survey was carried out in December 2020, and focused on the Tomtebo
Mine Trend (Figure 1) that is centered on the historic Tomtebo Mine, and is
delineated by numerous conductive and magnetic high anomalies identified from
the July 2020 SkyTEM survey.
Gravity Survey Highlights:
<<

--  Numerous gravity high anomalies have been identified at the historic
Tomtebo Mine (Figure 2). These gravity high anomalies are within and
well outside of the known mineralized domains, which provides
confirmation and immense expansion potential.

--  The gravity high anomalies at the historic Tomtebo Mine show an
exploration target of over 72.0 Mt at a density of 3.45 g/cm3 from near
surface down to a depth of 650 m. The gravity survey established a
background density of 2.72 g/cm3 for the host felsic volcanic rocks, and
the modeled gravity high anomalies could correspond with polymetallic
and/or iron sulphide mineralization, or a mafic unit.

--  A very significant blind gravity high anomaly has been identified 1.0 km
northeast along trend from the historic Tomtebo Mine (Figure 2). This
gravity high anomaly remains open to the northeast and at depth where an
exploration target of 34.0 Mt at a density of 3.45 g/cm3 has been
modeled at shallow depths (40 to 320 m).

--  A significant gravity high anomaly has been identified 600 m southwest
from the historic Tomtebo Mine (Figure 2). This gravity high anomaly is
associated with historic iron sulphide occurrences, which are known to
sometimes coalesce with polymetallic sulphide mineralization in the
Bergslagen District. This exploration target remains open to the
southwest and at depth where 28.7 Mt at a density of 3.50 g/cm3 has been
modeled at shallow depths (near surface to 420 m).
<>>
The potential quantity and density of the exploration targets described
above are conceptual in nature, and it is not possible to make assumptions on
metal grades from a gravity survey. There has been insufficient or no drilling
to define a mineral resource or to determine if polymetallic sulphide
mineralization is present, respectively. It is uncertain if further drilling
will result in these exploration targets being delineated as a mineral
resource or resulting in the discovery of polymetallic sulphide
mineralization.
Garrett Ainsworth, CEO of District, commented: "Our ground gravity survey
covering the Tomtebo Mine Trend has worked extraordinarily well.
Interpretation of the gravity data has successfully confirmed proof of concept
and identified compelling expansion potential at the historic Tomtebo Mine.
This survey has also revealed two high priority gravity targets with
coincident magnetic and/or conductive anomalies located 0.6 to 1.0 km along
trend from the Tomtebo Mine. We are especially excited about the gravity high
anomaly located one kilometer to the northeast of the Tomtebo Mine, which
represents a potential grassroots discovery opportunity with a modeled tonnage
that compares with the historic production tonnage from the historic Falun
Mine."
The December 2020 ground gravity survey covered a 2 km by 3 km portion of
the Tomtebo Mine Trend with 200 m line spacings and stations 50 m along the
lines, which totaled approximately 400 gravity stations. The large density
differential between the surrounding host felsic volcanic rocks, and targeted
polymetallic sulphide mineralization on the Tomtebo Mine Trend has generated
an important data layer that in combination with magnetic, electromagnetic,
and geochemical data has revealed priority drill targets.
Gravity Survey Background
Gravity surveys measure differences in the Earth's gravity field in
milligals (mGal), which is sensitive to variations in rock density, and can be
used to detect excess mass, which may indicate a potential massive sulphide
deposit at depth, and to estimate the size of the excess mass. The sulphide
minerals found in massive sulphide (VMS or SedEx) deposits have relatively
high density values in marked contrast to lower density values measured in
their volcanic and sedimentary host rocks. In its purest form, massive
sulphide mineral density ranges from 4.0 to 7.5 g/cm3 while the felsic
volcanic host rock ranges from 2.6 to 2.8 g/cm3. Gravity high anomalies of 3.2
g/cm3 or greater are typical VMS and SedEx signatures that center over these
types of deposits.
Volcanic Massive Sulphide (VMS) and SedEx deposits can often be
identified by gravity survey data. Metal content zonation within VMS systems
in particular is typical from proximal feeder copper-gold zones being strongly
conductive and weakly to strongly magnetic with the more distal SedEx
silver-zinc-lead zones being weakly- to non-conductive and weakly to strongly
magnetic, which can be greatly complemented by gravity data. Where targets are
blind, exploration drilling should be prioritized in areas that exhibit at
least two coincident anomalies of conductivity, magnetics, or gravimetry.
Figure 1: Ground Gravity Survey Station Plan
Figure 2: Terrain Corrected Gravity on Tomtebo Mine Trend
Technical Information
All scientific and technical information in this news release has been
prepared by, or approved by Garrett Ainsworth, PGeo, President and CEO of the
Company. Mr. Ainsworth is a qualified person for the purposes of National
Instrument 43-101 - Standards of Disclosure for Mineral Projects.
Mr. Ainsworth has not verified any of the information regarding any of
the properties or projects referred to herein other than the Tomtebo Property.
Mineralization on any other properties referred to herein is not necessarily
indicative of mineralization on the Tomtebo Property.
About District Metals Corp.
District Metals Corp. is led by industry professionals with a track
record of success in the mining industry. The Company's mandate is to seek
out, explore, and develop prospective mineral properties through a disciplined
science-based approach to create shareholder value and benefit other
stakeholders.
The advanced exploration stage Tomtebo Property is located in the
Bergslagen Mining District of south-central Sweden is the Company's main
focus. Tomtebo comprises 5,144 ha, and is situated between the historic Falun
Mine and Boliden's Garpenberg Mine that are located 25 km to the northwest and
southeast, respectively. Two historic polymetallic mines and numerous
polymetallic showings are located on the Tomtebo Property along an approximate
17 km trend that exhibits similar geology, structure, alteration and VMS/SedEx
style mineralization as other significant mines within the district.
Mineralization that is open at depth and along strike at the historic mines on
the Tomtebo Property has not been followed up on, and modern systematic
exploration has never been conducted on the Property.
On Behalf of the Board of Directors"Garrett Ainsworth"President and Chief
Executive Officer
(604) 288-4430
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement Regarding "Forward-Looking" Information.
This news release contains certain statements that may be considered
"forward-looking statements" within the meaning of applicable securities laws.
In some cases, but not necessarily in all cases, forward-looking information
can be identified by the use of forward-looking terminology such as "plans",
"targets", "expects" or "does not expect", "is expected", "an opportunity
exists", "is positioned", "estimates", "intends", "assumes", "anticipates" or
"does not anticipate" or "believes", or variations of such words and phrases
or state that certain actions, events or results "may", "could", "would",
"might", "will" or "will be taken", "occur" or "be achieved" and other similar
expressions. In addition, statements in this news release that not historical
facts are forward looking statements including anticipated results of future
exploration and the results of additional compilation work.
These statements and other forward-looking information are based on
assumptions and estimates that the Company believes are appropriate and
reasonable in the circumstances, including, without limitation, assumptions
about the reliability of historical data and the accuracy of publicly reported
information regarding past and historic mines in the Bergslagen District the
Company's ability to raise sufficient capital to fund planned exploration
activities, maintain corporate capacity and satisfy the exploration
expenditure requirements required by the definitive purchase agreement between
the Company and the vendor of the Tomtebo property (the "Definitive Purchase
Agreement") by the times specified therein (failing which the Tomtebo Property
will be forfeited without any repayment to the Company); and stability in
financial and capital markets.
There can be no assurance that such statements will prove to be accurate
and actual results, and future events could differ materially from those
anticipated in such statements. Important factors that could cause actual
results to differ materially from the Company's expectations include; the risk
that historic data regarding the Tomtebo property is unreliable; the risk that
information concerning production and mineralization at current and historic
mines within the Bergslagen District proves to be inaccurate; the risk that
the Company will be unable to raise sufficient capital to finance planned
exploration (including incurring prescribed exploration expenditures required
by the Definitive Purchase Agreement, failing which the Tomtebo Property will
be forfeited without any repayment of the purchase price); future metal
prices, general economic, market or business conditions, and other exploration
or other risks detailed herein and from time to time in the filings made by
the Company with securities regulators, including those described under the
heading "Risks and Uncertainties" in the Company's MD&A for the financial year
ended June 30, 2020. The Company does not undertake to update or revise any
forward-looking statements, except in accordance with applicable law. Readers
are cautioned not to put undue reliance on these forward-looking statements.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/district-reports-on-signifi
cant-gravity-high-anomalies-at-the-tomtebo-property-301259118.html
SOURCE District Metals Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/March2021/31/c5740.html

-0-                           03/31/2021
/For further information: Garrett Ainsworth, President and Chief
Executive Officer, (604) 288-4430/
(DMX. DFPP)

CO:  District Metals Corp.
ST:  British Columbia
IN:  MNG
SU:  ECO

-30-