Source	CANADA NEWSWIRE
Date	05/06/2021
Time	05:32:15 AM

Company	 Tarku Resources Ltd.
Title	Tarku Provides Update on its Silver Strike Project, Arizona Drilling
intercepts 213.5 g/t Ag over 3 meters





    CDNX Symbol: TKU











Press Release




" BC-Tarku-Drill-Update   05-06 1965
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.305153:
^Tarku Provides Update on its Silver Strike Project, Arizona Drilling
intercepts 213.5 g/t Ag over 3 meters@

MONTREAL, May 6, 2021 /CNW/ - Tarku Resources Ltd (TSXV: TKU) (FRA: 7TK)
(the "Company" or "Tarku") is pleased to announce initial results from its
2021 drilling program on the high-grade Silver Strike Project, Tombstone
District, Arizona (the "Project"). Significant results include 213.5 g/t Ag
and 3.9% Mn over 3.0 m in hole SS21-004 targeting north-south structure
located in the historic East Side mine area.
The first phase of 10 drill holes, completed on April 15th and totaling
3,701 feet, targeted the Silver vein system located in the historical mine
areas known as the Lucky Cuss, Luck Sure, East Side and the Bunker Hill
historic mines areas. The second phase of the planned 10,000-foot RC drill
program, recommenced on May 5th, will put emphases on the Ground Hog, Sunset,
Ace-in-the-Hole, and the Solstice historic mine areas. These holes will target
a regional structure known to carry silver, manganese, copper, lead and zinc
mineralisation. They will be located between 2-5 km away from the Tombstone
historic mines center (see Image 1).
Julien Davy, President and CEO of Tarku, stated: "213 g/t Ag over 3
meters is a great start for a first systematic exploration program on the
project since 1930! Although we did not hit all expected mine structures in
those first 5 holes, we are very encouraged by the results obtained to date
and what maybe found in the next 17 drill holes. It is a learning process for
Tarku, and we still have 3/4 of our drilling results to come. We are learning
about the complexity of the mineralized vein structures found at the Project,
as they are not planar structures as historically reported. The presence of
wide near-surface manganese and lead-zinc halos are strong indicators of a
manganese-oxide silver replacement horizon. We are now looking forward to
building further the knowledge of the Project as drilling continues."
The results received to date include the first 5 holes (SS21-001 to
SS21-005) targeting the north-south structures in the Lucky Cuss area.
Sampling methodology includes taking of 5 ft long samples and all results
represent an average grade over 5 ft. With holes SS21-001 and SS21-002, we
learned that the targeted Lucky Cuss veining structure is located further
westward than expected because the collars entered directly into wide
low-grade Ag and Mn halos. In hole SS21-003, we intersected another
north-south sub-parallel structure returning 37.5 g/t Ag and 1.0% Mn over 1.5
m. Holes SS21-004 and SS21-005 targeted the East Side area, located 250 m
south of the previous holes, and that is now interpretated to be along the
same Lucky Cuss structure. Hole SS21-004 intersected an interesting 10.7 m
grading 79.8 g/t Ag and 1.8% Mn, including 213.5 g/t Ag and 3.9% Mn over 3.0
m, showing the high-grade potential of the Lucky Cuss veining system.
Bernard Lapointe, Chairman of Tarku, stated: "This new and impressive
land package may have contained some 167 historic mining sites, but very
little modern and documented exploration work has been carried out on the
Property. These initial and encouraging results announced today warrant us to
continuing our work to assess the full potential of the Tombstone area, which
experiencing a recent exploration resurgence by Tarku and other juniors."
As shown in Table 1, those holes allow us to identify wide mineralized
zones with lower grade material. These results appear to be adjacent to the
historical high-grade silver veins, potentially defining a larger epithermal
system.
Based on the results to date, the Company intends to complete the
remaining 1,600 m of RC drilling (6,600 ft) at Silver Strike by June 2021,
covering the Ground Hog, Sunset, Ace-in-the-Hole, and the Solstice areas. With
all results in hand, Tarku will be a in good position to plan the future
exploration programs that will encompass soil geochemistry, geophysics
surveys, and further major drill programs.
IMPORTANTLY, the above projected exploration activities are subject to
COVID-19 restrictions in Arizona. While the Company's recent work programs
have been relatively unimpeded, there is a risk that tighter restrictions may
impact the Company's ability to conduct fieldwork.
Table 1: Drill Hole Assay Results - News Release May 6, 2021
Hole (number sign)

Target        From  To            Drilled              Ag (g/t)    Mn (g/t)     
Pb (%)     Zn (%)
width (m)

---


SS21-001
Lucky Cuss            3.0 18.3                15.2                    
5.5        2,684
na
na

---

42.7 51.8                 9.1                    4.3        1,630
na
na




SS21-002
Lucky Cuss            0.0 42.7                42.7                    
4.4        5,053
na
na

---


incl.   0.0  3.0                 3.0                   12.4        2,550        
0.5         0.3




SS21-003
Luck Sure            47.2 48.8                 1.5                   37.5       
10,200        0.1         0.2

---


SS21-004
East Side            62.5 73.2                10.7                   79.8       
17,970        0.1
na

---

incl.  70.1 73.2                 3.0                  213.5       38,700        
0.1          na




SS21-004                                80.8 86.9                 
6.1                   21.2        7,560        0.1
na

---



incl.  82.3 86.9                 4.6                   28.4        8,347        
0.2          na




SS21-005
East Side           123.4  125                 1.5                   
35.7        7,450        0.2
na

---


SS21-006
Lucky Cuss                                         Assays Pending

---


SS21-007
Lucky Cuss                                         Assays Pending

---


SS21-008
Bunker Hill                                         Assays Pending

---


SS21-009
Bunker Hill                                         Assays Pending

---


SS21-010
Bunker Hill                                         Assays Pending

---
Table 2: Drill Hole Locations - News Release May 5, 2021
Hole ID            Target Azimuth  Dip                Length               
Length    Coord_X (utmZ12N)     Coord_Y (utmZ12N)
drilled (ft)          drilled (m)

---


SS21-001
Lucky Cuss         135     50                   400                 
121.9             587,663.0            3,507,702.0

---


SS21-002
Lucky Cuss          95     50                   439                 
133.8             587,663.0            3,507,702.0

---


SS21-003
Luck Sure           95     50                   525                 
160.0             587,516.0            3,507,262.0

---


SS21-004
East Side           95     50                   292                  
89.0             587,614.0            3,507,537.0

---


SS21-005
East Side           95     56                   435                 
132.6             587,614.0            3,507,537.0

---


SS21-006
Lucky Cuss          95     55                   220                  
67.1             587,663.0            3,507,702.0

---


SS21-007
Lucky Cuss          95     90                   325                  
99.1             587,663.0            3,507,702.0

---


SS21-008         Bunker Hill         325     50                   
440                 134.1             588,756.6            3,506,613.4

---


SS21-009         Bunker Hill         325     50                   
225                  68.6             588,670.2            3,506,564.6

---


SS21-010         Bunker Hill         325     60                   
400                 121.9             588,670.2            3,506,564.6

---

TOTAL                3,701               1,128.1
Drilling Sample Method and Quality Assurance / Quality Control
The first phase (3,701 ft) was conducted by Major Drilling of Salt Lake
City, Utah. Drill samples were collected by reverse circulation drilling using
a face sampling, centre return, downhole hammer that collects rock samples
directly from the drill face, thereby reducing downhole contamination. Each
sample was collected using a binary splitter that directs half the sample into
a sample bag which is sent for analysis, while the other half is bagged and
kept in storage as a field duplicate. Samples collected varied in weight from
15-20 kilograms.
Shipping of samples, to the ALS Minerals prep lab facility in Tucson, AZ,
involved a direct chain of custody (CoC) from the drill site to the ALS
minerals transport truck and then directly to the prep lab. CoC forms are
maintained at each change of custody - in this case from the locked storage
area at site direct to the lab's transport truck.
At the prep lab, each sample is then crushed to greater than 70% passing
-2mm (10 mesh), and then a Boyd rotary split of 1 kilogram is pulverized to
greater than 85% passing 75 microns (200 mesh). The sample is then treated
with aqua regia and analyzed by ICP-MS for 51 elements including Silver (Ag),
Copper (Cu), Lead (Pb), Zinc (Zn) and Gold (Au). Note that the Gold analysis
by this method is semi-quantitative due to the small sample size used.
Overlimit samples for gold and silver are analyzed by 30g Fire assay with
a gravimetric finish. Overlimit samples for copper, lead, manganese and zinc
are treated with aqua regia and analyzed by ICP-OES (Inductively Coupled
Plasma Optical Emission Spectroscopy).
Quality Assurance / Quality Control (QA/QC) samples included the use of
field duplicates, blank material samples, and certified reference materials
(CRM) for Au, Ag, and Cu. QA/QC samples were controlled by Tarku field staff
at all-times. Field duplicates were collected as the second sample from the
drill cyclone and made up 5% of the sample stream. Blank material included
pure marble chips from a commercial source and made up 2.5% of the sample
stream. CRMs made up 2.5% of the sample stream and were obtained from
Shea-Clark Smith of Reno, NV. QA/QC additions to the sample stream total an
additional 10% of the samples for analysis.
Analysis of the QA/QC materials are conducted as soon as analytical
results are received. Statistically identified failures will be brought to the
attention of ALS Minerals for re-testing.
Qualified persons
Julien Davy, P.Geo., M.Sc, MBA, President and Chief Executive Officer of
Tarku, the qualified person under National Instrument 43-101 Standards of
Disclosure for Mineral Projects, prepared, supervised and approved the
technical information in this news release.
Update on the Silver Strike Transaction
On October 12, 2020, Tarku signed the final option agreement with arm's
length parties (the "Vendors") under which Tarku can earn up to 75% interest
over 3 years in 1,250 hectares of unpatented mineral claims (the "Unpatented
Claims Agreement") in the Tombstone mining District, Arizona. Pursuant to the
agreement, to earn the 75% interest in the Property, the Company shall issue
3,000,000 common shares (issued), pay US$ 175,000 (of which a minimum of
US$50,000 will be a cash payment and US$125,000 will be paid either in shares
or in cash at the Company's discretion), and incur up to US$3 million in
project expenditures to earn the interest, as follows:
<<

--  Tarku will acquire 25% of the Property after spending US$ 1,000,000 in
exploration expenses within the first year of earn-in period (in
progress),
--  Tarku will acquire an additional 26% (total of 51%) of the Property
after spending an additional US$ 1,000,000 in exploration expenses and
the production of a 43-101 report on the Property within the first 2
years of earn-in period,
--  Tarku will acquire an additional 24% (total of 75%) of the Property
after spending an additional US$ 1,000,000 for a cumulative US$
3,000,000 in exploration expenses within the first 3 years of earn-in
period.
<>>
At the end of this Earn-in Period, the Vendors and Tarku will become JV
partners on the Property, 75% Tarku, 25% the Vendors. Should the Vendors elect
to dispose of their remaining interest, Tarku will keep a Right of First
Refusal.
In addition, the signing of this agreement, also allows Tarku to acquire
additional 33 patented claims in the historical area of Tombstone under
agreement between third parties and the Vendors, namely the Rohe, Corkran, and
Turner Options (The "Options"). These agreements are separate and independent
from the Unpatented Claims Agreement. These Options require various cash
payments with a total cost of US$ 700,000. The payments are spread out until
July 2025 for the Rohe Option, until October 2021 for the Corkran Option, and
July 2023 for the Turner Option. Tarku will also issue 50,000 shares for the
Corkran Option. At the end of each Option acquisition, the patented claims
will be added to the above Unpatented Claim Agreement to form the 75% Tarku,
25% Vendor JV Partnership.
About Tarku Resources Ltd. (TSX.V: TKU - FRA: 7TK)
Tarku is an exploration company focused on making new discoveries in
favourable mining jurisdictions as Quebec and Arizona. In Quebec, Tarku owns
100% on the "Three A's" exploration projects, (Apollo, Admiral and Atlas
Projects), in the Matagami greenstone belt, which has been interpreted by
management as the eastern extension of the Detour Belt, and which has seen
recent exploration successes by Midland Exploration Inc., Wallbridge 
MiningCompany Ltd., Probe Metals Inc. In Arizona, in the Tombstone district, 
Tarku
owns the option to acquire 75% on 20km2 in the Silver Strike Project.
Please follow (at)TarkuResources on LinkedIn, Facebook, Twitter and
Instagram.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This press release may contain forward-looking statements that are
subject to known and unknown risks and uncertainties that could cause actual
results and activities to vary materially from targeted results and planning.
Such risks and uncertainties include those described in Tarku's periodic
reports including the annual report or in the filings made by Tarku from time
to time with securities regulatory authorities.
SOURCE Tarku Resources Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/06/c4961.html

-0-                           05/06/2021
/For further information: Email: investors(at)tarkuresources.com, Website:
www.tarkuresources.com/
(TKU. 7TK)

CO:  Tarku Resources Ltd.
ST:  Quebec, Arizona
IN:  MIN MNG PRM
SU:

-30-