Source	CANADA NEWSWIRE
Date	04/13/2021
Time	04:05:43 AM

Company	 1911 Gold Corporation
Title	1911 Gold Drills High-Grade Gold Zones at Tinney





    CDNX Symbol: AUMB











Press Release




" BC-1911-GoldDrillsTinney   04-13 1725
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.355563:
^1911 Gold Drills High-Grade Gold Zones at Tinney@

Step-out drilling returns intercepts up to 32.8 g/t gold over 1.1 metres
TORONTO, April 13, 2021 /CNW/ - 1911 Gold Corporation ("1911 Gold" or the
"Company") (TSXV: AUMB) (OTCQX: AUMBF) is pleased to report results from eight
additional exploration drillholes within its 100% owned Rice Lake exploration
properties in Manitoba, highlighted by multiple intercepts of high-grade gold
mineralization at the Tinney project (Figure 1). Step-out drilling on the
contiguous Edna-Otter-Cougar targets at Tinney has intersected gold-bearing
structures over 550 metres of strike (Figure 2) and to vertical depths greater
than 300 metres, and has demonstrated continuity of the principal host unit,
the Gunnar porphyry, providing significant scope for further exploration
drilling.
Highlights:
<<

--  Drillhole EO-21-014 intersected four zones of gold mineralization over a
drillcore length of 120 metres, including 5.6 g/t gold over 1.4 metres,
3.3 g/t gold over 1.8 metres, 32.8 g/t gold over 1.1 metres, and 3.4 g/t
gold over 2.2 metres

--  Quartz-sulphide veins containing visible gold within these zones
returned localized high-grade values up to 59.8 g/t gold over 0.6 metres


--  Drilling along strike from drillhole EO-21-014 yielded several
additional high-grade intercepts, including 7.1 g/t gold over 2.5 metres
in drillhole EO-21-016 (includes 19.5 g/t gold over 0.9 metres), 20.2
g/t gold over 0.9 metres in drillhole EO-21-020, and 42 g/t gold over
0.6 metres in drillhole CG-21-004

--  Results are pending from four drillholes completed to test these
high-grade zones for possible plunge extensions toward the northwest and
northeast along strike
<>>
Dr. Scott Anderson, Vice President Exploration, commented: "Drilling to
date confirms the Gunnar porphyry as a compelling exploration target, with its
continuity now established both along strike and to depth, demonstrating
significant scale potential. Initial drilling at Tinney confirmed the presence
of favourable structures at relatively shallow (<150 metres) depth both
internal and external to the porphyry, and follow-up drilling has now tested
these structures to depths up to 400 metres vertical. Importantly, as
exemplified by drillhole EO-21-014, this drilling has intersected multiple
gold-bearing structures (Figure 3), analogous to the near-surface portion of
the True North gold deposit at Bissett. In the coming weeks, we will release
the remaining eighteen drillholes from the recently completed winter drilling
program and will continue detailed planning to follow-up on these exciting
results".
Tinney Project
The principal exploration targets in the Tinney Project area are arranged
along the Gunnar porphyry - a large synvolcanic intrusion that has been traced
along strike on surface for 2.4 kilometres and hosts, at its southern extent,
the historical high-grade Gunnar deposit (1936-1941; 100,000 ounces produced
at 11.9 g/t Au). Drilling to date at Tinney has focused on the northern
portion of the porphyry, targeting structures within the porphyry and its host
rocks, as well as structural intersections at the contacts of the porphyry.
Previously-reported drillhole EO-21-005, collared 240 metres southwest of
EO-21-014, returned intercepts of 8.1 g/t gold over 5.7 metres (includes 29.9
g/t gold over 1.5 metres) from the porphyry and 11.3 g/t gold over 1.6 metres
(includes 31.2 g/t gold over 0.5 metres) from its host rocks (refer to news
release dated March 24, 2021), demonstrating potential for both to host
significant gold mineralization.
Intensely fractured, veined and altered porphyry with anomalous gold
values has been intersected over thick, continuous intervals in several
drillholes, with localized high-grade gold associated with quartz-sulphide
veins in the porphyry and at its contacts (e.g., EO-21-014; Figure 4),
indicating that it was a significant conduit for gold-bearing fluids. Numerous
targets remain to be tested along this kilometre scale gold system, which has
seen no modern systematic exploration and remains open in all directions.
Table 1: Selected gold intercepts from drillholes at the Tinney project.
Project,               Hole ID
(1)            Easting     Northing           Length            Az.        
Incl.         From           To       Length
(2)        Gold
(3)


Target                                (NAD83, UTMZ15N)
(m)
(deg.)
(deg.)
(m)
(m)
(m)
(g/t)

---

Tinney,
EO-21-012                 340783       5638867               401             
220           -70        304.05        305.00                 0.95              
0.97


Edna-Otter
EO-21-013                 340680       5638903               326             
200           -50         61.50         62.00                 0.50             
10.10


117.10        118.80                 1.70              0.49


136.00        137.75                 1.75              0.31


157.05        158.05                 1.00              5.69


192.48        192.78                 0.30             10.50


196.00        196.80                 0.80              2.96


198.50        199.50                 1.00              0.60



EO-21-014                            340694       5638952               
353             200           -60        208.50        209.90                 
1.40              5.56


inc.       208.50        209.00                 0.50             15.30


259.90        261.70                 1.80              3.33


inc.       260.75        261.70                 0.95              5.22


323.50        324.60                 1.10             32.79


inc.       323.50        324.10                 0.60             59.80


328.30        330.50                 2.20              3.38


inc.       329.30        330.00                 0.70             10.10



EO-21-016                            340581       5638928               
299             200           -62         38.50         39.40                 
0.90              0.91


134.00        135.50                 1.50              0.52


143.40        145.90                 2.50              7.12


inc.       143.90        144.75                 0.85             19.50


151.40        154.55                 3.15              0.41


177.65        178.65                 1.00              0.81


185.60        186.60                 1.00              3.34


190.50        193.50                 3.00              0.29


201.00        202.50                 1.50              4.71


217.60        218.60                 1.00              2.57



EO-21-017                            340628       5639036               
380             200           -56        324.30        327.00                 
2.70              0.59



EO-21-019                            340473       5638973               
266             195           -60        146.90        149.80                 
2.90              0.67


164.20        167.80                 3.60              0.33



EO-21-020                            340669       5638998               
443             195           -67        289.55        292.30                 
2.75              0.21


301.70        303.50                 1.80              0.96


337.40        339.30                 1.90              1.00



inc.       338.70        339.30                 0.60              2.55


350.35        351.20                 0.85             20.20


Tinney,
CG-21-004                            340788       5638644               
252             265           -58         70.10         74.00                 
3.90              0.67


Cougar
inc.        72.93         74.00                 1.07              1.86


101.60        103.00                 1.40              1.10


107.43        108.07                 0.64             42.00


210.52        213.77                 3.25              0.48


(1)
Numbering reflects order in which drillholes were planned, rather than sequence 
of drilling




(2)
Represents drillcore length; true widths are presently unknown




(3)
Intervals are weighted averages, cut-off at 0.2 g/t Au and at 0.5 grade x width 
multiple; NSV, no significant values
QA-QC Protocols
Sample handling, preparation and analysis are monitored through the
implementation of formal chain-of-custody procedures and quality
assurance-quality control (QA-QC) programs designed to follow industry best
practices. Drillcore is logged and sampled in a secure facility located in
Bissett, Manitoba. Drillcore samples for gold assay are cut in half using a
diamond saw and are submitted to Activation Laboratories Ltd. (Actlabs) in
Ancastor, Ontario, for preparation by crushing to 80% passing 2.0 millimetres,
riffle splitting to obtain 250-gram aliquots, and pulverizing to 95% passing
106 microns; the pulverizer bowl is cleaned with sand after each sample. Pulps
are analyzed by a 30-gram fire assay and AAS finish. For assays above 5 g/t
Au, a cut of the original pulp was re-assayed with a gravimetric finish.
Samples with visible gold are analyzed by metallic screen assay, with the
weighted average of gold for the entire sample reported, based on fire assays
of the screen oversize and undersize fractions. In addition to Actlabs'
in-house QA-QC protocols, 1911 Gold inserts certified standards, non-certified
blanks and field duplicates into the sample stream at regular intervals, such
that QA-QC accounts for 10% of the total samples submitted. Blanks are also
inserted after heavily mineralized or visible-gold-bearing samples. Results
are routinely evaluated for accuracy, precision and contamination.
Qualified Person Statement
Technical information in this news release has been reviewed and approved
by Dr. Scott Anderson, Ph.D., P.Geo., the Company's Vice President,
Exploration, and Qualified Person as defined by Canadian National Instrument
43-101 - Standards of Disclosure for Mineral Projects.
About 1911 Gold Corporation
1911 Gold is a junior explorer that holds a highly prospective,
consolidated land package totalling 55,500 hectares within and adjacent to the
Archean Rice Lake greenstone belt in Manitoba, and also owns the True North
mine and mill complex at Bissett, Manitoba, where it is reprocessing historic
tailings on a seasonal basis. 1911 Gold believes its land package is a prime
exploration opportunity, with potential to develop a mining district centredon 
the True North complex. The Company also owns the Tully and Denton-Keefer
projects near Timmins, Ontario, and intends to focus on both organic growth
opportunities and accretive acquisition opportunities in North America.
1911 Gold's True North complex and exploration land package are located
within the traditional territory of the Hollow Water First Nation, signatory
to Treaty No. 5 (1875-76). 1911 Gold looks forward to maintaining open,
co-operative and respectful communication with the Hollow Water First Nation
in order to build mutually beneficial working relationships.
ON BEHALF OF THE BOARD OF DIRECTORS
Ron ClaytonPresident and CEO
CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION
This news release may contain forward-looking statements. Often, but not
always, forward-looking statements can be identified by the use of words such
as "plans", "expects" or "does not expect", "is expected", "budget",
"scheduled", "estimates", "forecasts", "intends", "anticipates" or "does not
anticipate", or "believes", or describes a "goal", or variation of such words
and phrases or state that certain actions, events or results "may", "could",
"would", "might" or "will" be taken, occur or be achieved.
All forward-looking statements reflect the Company's beliefs and
assumptions based on information available at the time the statements were
made. Actual results or events may differ from those predicted in these
forward-looking statements. All of the Company's forward-looking statements
are qualified by the assumptions that are stated or inherent in such
forward-looking statements, including the assumptions listed below. Although
the Company believes that these assumptions are reasonable, this list is not
exhaustive of factors that may affect any of the forward-looking statements.
Forward-looking statements involve known and unknown risks, future
events, conditions, uncertainties and other factors which may cause the actual
results, performance or achievements to be materially different from any
future results, prediction, projection, forecast, performance or achievements
expressed or implied by the forward-looking statements. All statements that
address expectations or projections about the future, including, but not
limited to, statements about exploration plans and the timing and results
thereof, are forward-looking statements. Although 1911 Gold has attempted to
identify important factors that could cause actual actions, events or results
to differ materially from those described in forward-looking statements, there
may be other factors that cause actions, events or results not to be as
anticipated, estimated or intended. There can be no assurance that
forward-looking statements will prove to be accurate, as actual results and
future events could differ materially from those anticipated in such
statements. Accordingly, readers should not place undue reliance on
forward-looking statements.
All forward-looking statements contained in this news release are given
as of the date hereof. The Company disclaims any intention or obligation to
update or revise any forward-looking statements whether as a result of new
information, future events or otherwise, except in accordance with applicable
securities laws.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE: 1911 Gold Corporation
SOURCE 1911 Gold Corporation



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/13/c0334.html

-0-                           04/13/2021
/For further information: Shaun Heinrichs, Chief Financial Officer, (604)
674-1293, sheinrichs(at)1911gold.com/
/Web Site: https://www.1911gold.com/ /
(AUMB. AUMBF)

CO:  1911 Gold Corporation
ST:  Ontario
IN:  MIN MNG PRM OTC
SU:

-30-