Source	Business Wire
Date	04/07/2021
Time	04:59:37 AM

Company	 LOMIKO METALS INC.
Title	[EXTERNAL] Lomiko La Loutre Metallurgical Testing Produces Concentrate 
Grading...





    CDNX Symbol: LMR











Press Release




April 7, 2021 11:58 UTC

Lomiko La Loutre Metallurgical Testing Produces Concentrate Grading 97.8% 
Carbon and 93.5% Graphite Recovery 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Lomiko Metals Inc. 

TSX VENTURE SYMBOL: LMR 

MONTREAL--(BUSINESS WIRE)-- Lomiko Metals Inc. (TSX-V: LMR, OTC: LMRMF, FSE: 
DH8C) (Lomiko or the “Company”) is pleased to provide an update on its La 
Loutre graphite project (“La Loutre”), located in Quebec, Canada. La Loutre 
comprises the Graphene-Battery (GB) zone and the Electric Vehicle (EV) Zone. 
The names of the zones are not reflective of the products each will produce but 
generally indicate applications of products. The recent testwork program 
confirmed that each zone will produce similar products. 

Highlights 

A metallurgical flowsheet development program was carried out on two composite 
samples of La Loutre graphite project. One composite was generated from 
mineralized samples from the EV zone yielding 9.70% graphitic carbon, and the 
second composite from drill core of the GB zone yielding 4.80% graphitic 
carbon. 

The process development was carried out on both composites and resulted in a 
flowsheet and conditions that are suitable to treat both zones of La Loutre 
mineralization in the same processing plant. 

The program culminated in a locked cycle test (“LCT”) that generated a combined 
concentrate grading 97.8% total carbon at 93.5% graphite recovery. 

Although the two mineralized zones produced noticeably different flake size 
distributions, they responded equally well to the same flowsheet and conditions 
with combined concentrate grades of over 97% total carbon. 

“These very encouraging results of initial testing suggest that La Loutre 
graphite may be suitable for high-end industrial use,” stated A. Paul Gill, 
CEO. “Our next step is to complete a Preliminary Economic Assessment.” 

Technical Discussion 

Process Development

In January 2021, a metallurgical process development program was initiated at 
SGS Minerals in Lakefield, Ontario. The objective of the program was to develop 
the flowsheet and conditions suitable to upgrade La Loutre mineralization to at 
least 95% total carbon. 

Metallurgical development work was carried out on two composites representing 
the two zones. The process development program produced a flowsheet and 
conditions that generated concentrates of over 97% total carbon for both 
mineralized zones. The equipment and reagents selected for the process are well 
established in the mineral processing field and are consistent with other 
graphite projects. The flowsheet, which is depicted in Figure 1, comprises 
rougher/scavenger flotation stage, followed by a primary and secondary cleaning 
circuit. 

The GB composite produced a final concentrate with a significantly higher mass 
recovery into the +80 mesh size fraction of approximately 50% compared to 
25-30% for the EV composite. However, both composites responded equally well to 
the same flowsheet and conditions, producing combined concentrate grades that 
are consistently at least 97% C(t). 

The program culminated in a locked cycle test (LCT) using a 50:50 blend of the 
two mineralized zones. The overall mass balance is presented in Table 1. The 
mill feed grading 7.60% carbon was upgraded to a combined concentrate grading 
98.5% carbon at an overall graphite recovery of 93.5%. 

Table 1: Mass Balance of Locked Cycle Test LCT-1 

Sample ID		 	
			Weight 
				
				Assays (%) 
					
					% Distribution 
					
		 	
			% 
				
				C(t) 
					
					C(t) 
					
Combined Concentrate	 	 	
			7.2 
				
				98.5 
					
					93.5 
					
+80 Mesh 2nd Clnr Conc	 	 	
			2.9 
				
				99.0 
					
					37.1 
					
+80 mesh 1st Clnr Tails	 	 	
			0.1 
				
				34.9 
					
					0.3 
					
-80 mesh 3rd Clnr Conc	 	 	
			4.4 
				
				98.1 
					
					56.4 
					
-80 mesh 1st Clnr Conc	 	 	
			0.4 
				
				9.64 
					
					0.5 
					
		1st Clnr Tails	
			22.3 
				
				1.26 
					
					3.7 
					
		Scav Tails	
			69.9 
				
				0.21 
					
					1.9 
					
		Head (calc)	
			100.0 
				
				7.63 
					
					100.0 
					

  

The final concentrates of the three cycles that were used to develop the 
overall mass balance were submitted for a size fraction analysis (SFA), and the 
average results of the three SFAs are presented in Table 2. The combined 
concentrate grade of 97.8% total carbon is slightly lower compared to the 
direct concentrate analysis of the LCT mass balance, which is related to 
measurement uncertainties associated with assay methods. 

A total of 32.4% of the concentrate mass reported to the +80 mesh size 
fractions at a combined grade of 97.8% total carbon. Another 10.8% of the mass 
was recovered into the -80/+100 mesh product at a grade of 98.2% and the 
balance of 56.8% reported to the -100 mesh size fractions at a combined grade 
97.7% total carbon. 

One of the primary applications for the -100 mesh size fraction is the 
value-add process to produce spherical graphite for batteries. The ability to 
upgrade the fines size fraction to almost 98% total carbon by flotation only 
might have a positive impact on downstream purification costs since 
concentrations of impurities are often proportional to purification cost. 

Table 2: Average Size Fraction Analysis Results of LCT-1 

		
		Size 
			
			Mass 
				
				Grade 
					
					Distribution 
					
	
	Mesh  
		
		Microns
			
			% 
				
				%Ct 
					
					%Ct 
					
	
	   
		
		  
			
			  
				
				  
					
					  
					
	
	32 
		
		500 
			
			1.0 
				
				97.6 
					
					1.0 
					
	
	48 
		
		300 
			
			9.8 
				
				97.4 
					
					9.7 
					
	
	80 
		
		180 
			
			21.6 
				
				98.0 
					
					21.7 
					
	
	100 
		
		150 
			
			10.8 
				
				98.2 
					
					10.9 
					
	
	150 
		
		106 
			
			17.5 
				
				98.1 
					
					17.5 
					
	
	200 
		
		75 
			
			13.0 
				
				98.3 
					
					13.1 
					
	
	325 
		
		45 
			
			13.5 
				
				98.1 
					
					13.6 
					
	
	Pan 
		
		-45 
			
			12.8 
				
				96.0 
					
					12.5 
					
	
	  
		
		  
			
			  
				
				  
					
					  
					
	
	Total 
		
		  
			
			100.0 
				
				97.8 
					
					100.0 
					

  

Preliminary comminution tests produced Bond ball mill work indices of 6.9 kWh/t 
for the EV zone and 11.2 kWh/t for the GB zone, which places La Loutre 
mineralization into the very soft to soft category, which is favourable for 
minimizing grinding energy costs. 

Next Steps

Variability flotation testing on four composites that made up the two 
development composites will be performed to complete the scoping level 
metallurgical study. 

The combined concentrate of the LCT will be subjected to chemical and 
mineralogical characterization, which will determine the type and association 
of the remaining impurities in the graphite concentrate. This information will 
be used to commence marketing initiatives for La Loutre graphite concentrate. 

The current process development program will be completed within the next 
couple of weeks, and the company commenced work on a preliminary economic 
assessment (PEA) study. 

During the next phase of metallurgical testing, conditions of the existing 
flowsheet will be optimized to minimize flake degradation and maximize graphite 
recovery. Further, the optimization will evaluate potential capital and 
operating cost savings. 

The robustness of the optimized flowsheet and conditions will be verified with 
a larger number of variability samples, and a more comprehensive comminution 
program will be completed. 

Qualified Persons 

Mr. Oliver Peters, a Principal Metallurgist with Metpro Management Inc., is a 
Qualified Person within the meaning of NI 43-101. Mr. Peters is satisfied that 
the analytical and testing procedures used are standard industry operating 
procedures and methodologies, and he has reviewed, approved and verified the 
technical information disclosed in this news release, including sampling, 
analytical and test data underlying the technical information. 

Quebec’s Role in The New Green Economy 

In 2020, The Quebec Government released the Quebec Plan for Development of 
Critical and Strategic Minerals (“The Quebec Plan”) which indicates graphite 
demand would likely increase 300-500% in the coming decades as more is used in 
the production of spherical graphite for anode portion of Electric Vehicle 
Lithium-ion batteries. Quebec has an opportunity to play a vital role in 
reducing carbon emissions and become a key provider of critical battery 
materials to the North American economy. 

For more information on Lomiko Metals, review the website at www.lomiko.com, 
contact A. Paul Gill at 604-729-5312 or email: info@lomiko.com. 

On Behalf of the Board, 

“A. Paul Gill” Chief Executive Officer 

We Seek Safe Harbour. Neither TSX Venture Exchange nor its Regulation Services 
Provider (as that term is defined in the policies of the TSX Venture Exchange) 
accepts responsibility for the adequacy or accuracy of this release. 

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20210407005393/en/

Contacts

A. Paul Gill 604-729-5312 info@lomiko.com 

Source: Lomiko Metals Inc.