Source	CANADA NEWSWIRE
Date	04/15/2021
Time	05:03:14 AM

Company	 Desert Gold Ventures Inc.
Title	Desert Gold Highlights New Exploration Targets; 20,000 Metres of
Drilling in Progress - SMSZ Project, West Mali





    CDNX Symbol: DAU











Press Release




" BC-DAU-NewExplorTargets   04-15 1760
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.149832:
^Desert Gold Highlights New Exploration Targets; 20,000 Metres of
Drilling in Progress - SMSZ Project, West Mali@

TSX.V: DAU Frankfurt: QXR2 OTC: DAUGF
SURREY, BC, April 15, 2021 /CNW/ - Desert Gold Ventures Inc. (the
"Company") (TSXV: DAU) (FF: QXR2) (OTC: DAUGF) is pleased to present a series
of new, high priority, gold-in-auger exploration targets on its SMSZ Project.
These untested anomalies lie under shallow laterite cover proximal to the
regional scale Senegal Mali Shear zone.
Exploration is well advanced on the Company's largest exploration program
to date at its flagship Senegal Mali Shear Zone project in Western Mali (the
"SMSZ Project"). The 410 km2 SMSZ Project is both named after and overlies a
38 km section of the prolific Senegal Mali Shear Zone (the "SMSZ"). The SMSZ
is related to 5 large mines located both to the north and south, along strike
of the Company's SMSZ Project, including B2 Gold's Fekola Mine, Barrick's
Gounkoto and Loulo Mines and Allied Gold's Sadiola and Yatela Mines1. To the
Company's knowledge, the SMSZ Project is the largest, contiguous, non-producer
land package over this highly prospective structural feature (see Figure 1).
Field work recommenced at the SMSZ Project in early December, 2020. The
goal of the exploration program is to develop/discover a stand-alone Tier 1
gold deposit(s). Exploration comprises drilling to advance known gold zones
and soil, auger and IP surveys to identify new targets, with real-time
follow-up of drill testing of newly developed targets. The SMSZ exploration
program is fully underway with one multipurpose drill, two auger drills, a
geological mapping team and a couple of soil sampling teams.
Highlights - (see Figures 2 and 3)
<<

--  Gold-in auger results to 1,452 ppb gold in 2021 with values to 5,060 ppb
gold from 2020 surveys
--  15, 2021 samples contain >200 ppb gold. 36 samples >100 ppb gold. 84
samples >50 ppb gold
<>>
<<

--  Gold-in auger results define 10 untested target areas, five of which are
2+ km long (see Figure 2)
o 3 of the 10 target areas related to known gold-bearing trends.

o New target area at north end of 2 km long granodiorite intrusion - pressure
shadow target.

o Geophysical data shows clockwise rotation of geological units, coincident
with gold-in auger anomalies (see Figure 3). These areas are interpreted to
represent dilatant zones which are some of the best targets for the
discovery of gold mineralization

o Additional auger target areas likely - results pending
<>>


(1) Mineralization hosted on adjacent
and/or nearby properties is not
necessarily representative of
mineralization hosted on the
Company's SMSZ Property.
Jared Scharf, President and CEO Desert Gold Ventures commented "The new
auger results are extremely encouraging. Based on our previous work, we know
that testing of laterite-covered gold-in-auger anomalies, can lead to the
discovery of new gold zones. Regionally, several major gold deposits,
including Siou in Burkina Faso, Fekola in western Mali and Gounkoto, also in
western Mali, were discoveries under shall laterite cover. It is also
important to point out, is that all of the new anomalies are proximal to the
east side of the Senegal Mali Shear Zone, where regionally, 5, large gold
mines have been discovered1. We are pleased with the scenario and plan to
drill-test the bulk of these anomalies during the current exploration
program."
Technical data - Gold-in-auger and geophysical survey results
Summary results from 761 auger holes and approximately 85-line km of
gradient IP surveys are presented in this release.
Five IP geophysical survey grids were completed in late 2020 and the
first part of 2021. Data from four of the new grids was merged with data from
4 previous geophysical survey grids with data covering a 12 km by
approximately 11 km area. New IP grid lines were oriented at 270 degrees
azimuth and spaced 200 metres apart with data stations every 25 metres. The
merged IP data was interpreted with map products including chargeability,
resistivity, conductivity, residual chargeability, residual resistivity,
residual conductivity, structural pattern maps for each and anomaly
interpretation maps including interpreted structures.
The auger drilling was carried out on lines 400 metres apart with
stations every 25 metres. This release, presents the results of 1,522 assay
samples from 761 auger holes. Auger holes ranged up to 25 metres deep with an
average depth of 8.86 metres. Two samples were collected in each hole with one
sample of the basal laterite and one sample of the uppermost metre of
saprolite (near surface altered rock). Samples from the auger program were
subject to 24-hour bottle roll cyanide leach.
The IP geophysical data provides insight into potential areas of pyrite
enrichment (chargeability highs), silicification (resistivity highs),
geological trends, potential shear zones and areas of clockwise structural
rotation (see Figure 3). This data, combined with geological mapping, drilling
and auger data, provides a coherent framework for interpretation of the
gold-in-auger data, and, in this case, the delineation of at least 10
potential gold bearing trends. Three of the gold trends, line along strike of
previously defined trends. Seven of the gold trends are new target areas. It
is interesting to note that there are only a few anomalous outliers and that
the gold-in-auger anomalies generally line up well along north-northwest and
north-northeast trends. In summary, 15 samples contain >200 ppb gold, 36
samples >100 ppb gold and 84 samples >50 ppb gold.
Zones of structural rotation, as inferred from the IP geophysical data,
are expected to represent dilatant zones, which would be supportive for the
formation of a gold deposit. High priority targets occur where these
structural rotation zones are combined with anomalous gold-in-auger values, IP
chargeability highs suggesting increased pyrite content and IP resistivity
highs suggesting silicification.
Exploration Progress to April 11, 2021
<<

--  Drilling - 32% complete. Drilling pace has picked up after a series of
breakdowns with 521 metres drilled on April 11 and 5,714 metres drilled
to date.

--  Auger Drilling - 92 % complete
o 18,121 metres drilling in 2,262 holes
o Two rigs active
--  IP Geophysical Surveys - 100% complete
o 90.8 line kilometres completed
o Historic and new IP data have been merged.
--  Soil Sampling - 97 % complete

--  Mapping and prospecting ongoing

--  Community Support Program in progress
o Medical and school supplies to be donated to 9 communities in the SMSZ
Project region
<>>
2021 Exploration Program
<<

--  Fully Funded 20,000 metres of drilling- Drilling started January 2021
o Follow-up on Gourbassi West, Gourbassi East and Barani East Zones
o Continue to trace gold mineralization from Barani East northeast to Soa and
south to Keniegoulou
o Follow up drill testing at Gourbassi NE, Goubassi SE, Berola, Frikidi, KE,
Komana and Manakoto zones
o Test gold-in-auger targets
o Contingency metres will follow-up drill success
--  Approximately 19,000 metres of auger drilling
o Auger drilling will commence in mid-December to follow up on 2020 auger
anomalies
o Testing for gold mineralization along thinly-covered laterite, and/or, not
yet evaluated, regional scale structures
--  90-line km of induced polarization gradient geophysical surveys
o Five grid areas, with four covering structural targets related to the SMSZ
and one covering a felsic intrusion that hosts gold mineralization
o Survey to start mid-December
--  7,000 soil samples
o Test 3 areas comprising ~100 km2, that have not been soil sampled, mapped or
drilled
--  Geological mapping and prospecting
o Approximately 55% of the property still requires mapping and prospecting
--  Complete a 43-101 compliant report in Q4, 2021
<>>
Next Steps
Eighty-five additional air core drill holes, totaling 4,250 metres have
been planned to test most of the new auger anomalies. Drilling to test these
targets will be carried out in due course as part of the current 20,000 metre
drill program.
Review drill results as they are received and plan follow-up holes as
required.
QAQC
All auger samples are delivered to SGS in Bamako, Mali where they are
prepped. The prepped samples, were then shipped by truck to SGS's facility in
Ouagadougou, Burkina Faso for Au determination by 24 hours CN bottle roll
leach. Standards, assay blanks and sample duplicates, are inserted into the
assay stream every 25, 23 and 22 samples, respectively equaling one control
sample for every 8 assay samples. All assay batches are reviewed for quality
with re-assays requested for standards that assay more than 2 to 3 SD from an
excepted value and for blanks that contain more than 10 ppb gold.
This press release contains certain scientific and technical information.
The Company is solely responsible for the contents and accuracy of any
scientific and technical information related to it. Don Dudek, P.Geo. a
director of Desert Gold and a Qualified Person under National Instrument
43-101, has reviewed and approved the scientific and technical information
contained in this press release.
On Behalf of the Board
"Jared Scharf"
___________________________Jared Scharf President & CEO
About Desert Gold
Desert Gold Ventures Inc. is a gold exploration and development company
which holds 2 gold exploration permits in Western Mali (SMSZ Project and
Djimbala), its Anumso project in Ghana's Ashanti Belt and its Rutare gold
project in central Rwanda. For further information please visit www.SEDAR.com
under the company's profile. Website: www.desertgold.ca
This news release contains forward-looking statements. These
forward-looking statements entail various risks and uncertainties that could
cause actual results to differ materially from those reflected in these
forward-looking statements. Such statements are based on current expectations,
are subject to a number of uncertainties and risks, and actual results may
differ materially from those contained in such statements. These uncertainties
and risks include, but are not limited to, the strength of the capital
markets, the price of gold; operational, funding, liquidity risks, the degree
to which mineral resource estimates are reflective of actual mineral
resources, the degree to which factors which would make a mineral deposit
commercially viable, and the risks and hazards associated with mining
operations. Risks and uncertainties about the Company's business are more
fully discussed in the company's disclosure materials filed with the
securities regulatory authorities in Canada and available at www.sedar.com and
readers are urged to read these materials. The Company assumes no obligation
to update any forward-looking statement or to update the reasons why actual
results could differ from such statements unless required by law. Neither the
TSX Venture Exchange nor its regulation services provider (as that term is
defined in the policies of the TSX Venture Exchange) accepts responsibility
for the adequacy or accuracy of this release. This news release does not
constitute an offer to sell or a solicitation of an offer to buy the
securities described herein in the United States. The securities described
herein have not been and will not be registered under the united states
securities act of 1933, as amended, and may not be offered or sold in the
United States or to the account or benefit of a U.S. person absent an
exemption from the registration requirements of such act.
SOURCE Desert Gold Ventures Inc.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/15/c2735.html

-0-                           04/15/2021
/For further information: Jared Scharf, President and CEO, Email:
jared.scharf(at)desertgold.ca, Tel. No.: +1 (858) 247-8195/
/Web Site: http://www.desertgold.ca/ /
(DAUGF DAU. QXR2)

CO:  Desert Gold Ventures Inc.
ST:  British Columbia
IN:  MNG OTC PRM
SU:

-30-