Source	CANADA NEWSWIRE
Date	04/15/2021
Time	02:04:13 AM

Company	 Firefox Gold Corp.
Title	FireFox Gold Reports Visible Gold in First Hole of New Drill Program at
Mustajärvi Gold Project, Finland





    CDNX Symbol: FFOX











Press Release




" BC-FireFox-reports-gold   04-15 2278
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.365516:
^FireFox Gold Reports Visible Gold in First Hole of New Drill Program at
Mustajärvi Gold Project, Finland@

SODANKYLÄ, Finland, April 15, 2021 /CNW/ - FireFox Gold Corp. (TSXV:
FFOX) ("FireFox" or the "Company") is pleased to report that it has
encountered coarse visible gold (VG) in the first drill hole of a newly
commenced phase 4 diamond drilling program at its 100%-owned Mustajärvi Gold
Project in the Central Lapland Greenstone Belt of northern Finland. The
visible gold occurs as six discrete flakes (up to 1.0mm across) in a
quartz-carbonate-tourmaline vein (QCT vein) within a 32-metre-wide zone of
variably veined and altered metasedimentary rocks. The drill core is being
logged and prepared for sampling, so no assays are available yet to confirm
the quantity or extent of gold in the drill hole.
FireFox has reported numerous drill intercepts of relatively narrow
high-grade gold mineralization (as shown in Table 1) at the Mustajärvi Project
since its first drill program in 2018, but this is the first visible gold
reported by FireFox geologists at the project. Drill hole 21MJ001 is a
significant step-out (150 metres) to the northeast from a recently reported
high-grade intersection in drill hole 20MJ009 (2.0m at 33.25 g/t gold, see
Company news release dated January 27, 2021) (see Figure 1:
https://bit.ly/3uQyuYF ).
Highlights:
<<

--  Hole 21MJ001 intercepted visible gold (at least six discrete flakes up
to 1.0mm across) at a depth of approximately 185.5m downhole (see Figure
2: https://bit.ly/32guK6w)
--  The VG occurs in a 1.4 metre (m) section of QCT-veins from 184.2 to
185.6m depth
--  QCT veins also host the high-grade gold mineralization previously
reported in drill holes 20MJ009, 19MJ006, and others in the Central Zone
--  There are several QCT veins of variable thickness within altered
metamorphosed sedimentary and volcaniclastic rocks from 165.6m to the
end of this hole at 199.4m downhole (see Figure 3:
https://bit.ly/3adj2Of)
--  This hole is a step-out of approximately 150m from drill hole 20MJ009
along the northeast trending Mustajärvi Shear Zone
--  Drill hole 21MJ001 was completed in the early hours of April 11, 2021,
so assays have not yet been completed to confirm the quantity or extent
of gold in the drill core
<>>
"We are very excited to report the first visible gold from drilling at
the Mustajärvi Project. The new drilling has encountered significant zones of
intense alteration and veining along trend but beyond the extents of previous
drilling," commented Carl Löfberg, President and CEO of FireFox. "In light of
this favorable geology, we shall move quickly to secure assays on these
samples and to carefully consider our plans for the current drill program."
Preliminary Geologic Details of Drill Hole
The Mustajärvi Project lies along the highway between the cities of
Kittilä and Sodankylä, approximately 17 kilometers east of Kittilä. The
project remains in the early stages of exploration, having only seen
approximately 4,170m of drilling by FireFox since 2018. The property straddles
the Mustajärvi Shear Zone (MSZ), a major right-lateral shear zone that has
associated second and third-order structures which further dissect the project
into separate structural zones. FireFox has developed a structural model that
has identified dilatant zones along the major structure where higher grade
gold is concentrated. Company geologists believe that the most prospective
gold targets are in the Sodankylä Group metasedimentary rocks, which are to
the north of the shear zone in the footwall. In this area, the Sodankylä Group
includes metamorphosed sedimentary and volcaniclastic rocks. At Mustajärvi,
the most quartz-rich portions of these rocks have become brittle due to
pre-gold pervasive alteration with silica and albite, and host higher-grade
gold where they have been shattered, brecciated, and veined.
The 2021 drill program is targeting the brittle rocks in these
interpreted dilatant zones at the Northeast Target, the Central Zone with its
historic surface workings, and possibly at new targets farther to the
northeast and southwest. These high-grade gold (>5 g/t) pods are known to
occur along a distance of more than 1.5 kilometres of the hydrothermally
altered shear zone from the southwest to northeast on the project. The
sparsely drilled Northeast Target is one of these pods, and the area returned
the best intercepts in both the 2019 and 2020 drill programs (see Table 1).
The current Phase 4 drilling program was planned to include approximately
1,400 metres of diamond core drilling, but the program may be expanded. The
first hole, 21MJ001, is in the Northeast Target area, approximately 150m
northeast from drill hole 20MJ009, and nearly 750m from the Central Zone of
gold mineralization.
Table 1: Highlights of Previous Mustajärvi High-Grade Drill Intercepts
Drill                        Easting                       
Northing                       Azimuth                       
Plunge                       Depth             From         To            
Interval(x)         Gold



Hole

(°)                           (°)                         (m)              
(m)          (m)

(m)            (g/t)

---                                                                             
                                                                                
                                                               ---



Central Zone

---

18MJ002                             427702                         
7500228                            340                            
45                         82.1             34.35        34.75                
0.35          11.63

---

18MJ010                             422728                         
7500162                            340                            
45                        154.8             125.5        127.5                
2.00          45.05

---

20MJ008                             427716                         
7500191                            340                            
45                          200              97.5         98.0                 
0.5          11.20

---



Northeast Zone

---

19MJ006                             427709                         
7500244                            340                            
45                          179            125.75        127.9
1.95(x)(x)               12.0

---

including                          126.25             127.1         
0.85                 24.7



20MJ009                             428335                         
7500581                            340                            
45                        178.5              65.0         67.0                 
2.0          33.25

---

146.5        147.0                  0.5           9.36






(x)

- Drilling is believed to be perpendicular to the dip of the mineralization, 
however true widths are not yet known and will be
confirmed with additional drilling and geological modeling.



(x)(x) - Including 0.2m of core loss



Please see the original news releases for additional details:  Holes 18MJ002 
and 18MJ010 reported January 21, 2019; 19MJ006,
reported January 15, 2020; and 20MJ008 & 20MJ009 reported January 27th, 2021.

---
In drill hole 21MJ001, the targeted volcano-sedimentary series was
encountered at approximately 104m down hole and continued to the termination
of the hole at 199.4m. This section of rocks is pervasively altered with
moderate to very abundant amounts of silica, albite, sericite, and pyrite. The
altered rock sequence is cut throughout its width by QCT veins, quartz
tourmaline, and quartz veins that contain abundant to semi-massive and massive
zones of pyrite (see Figure 3). There are additional sulfide, or possibly
telluride and bismuth-bearing minerals (not yet confirmed), that are common in
the most intensely altered and veined rocks. Intense sericitic alteration with
disseminated pyrite and narrow quartz tourmaline veins (up to 1cm) can be
observed at the bottom of the drill hole.
It may be significant that the most intense mineralization occurs at
depths below previous drilling at the Northeast Target. Six individual zones
of very well-developed tourmaline and pyrite alteration can be distinguished
within the albite-sericite altered tuffs and sediments from 172.8-184.2m. Near
the top of this zone there is an occurrence of bladed calcite textures in a
vein (see Figure 4: https://bit.ly/3uLMbrC). This is often an indication of
separation of liquid and vapor phases during vein formation, which may occur
in the epizonal portion of orogenic gold deposits.
Visible gold appears as six individual flakes, up to 1.0mm in size,
observed on the core surface. These are hosted in a milky-colored
carbonate-rich portion of a QCT vein. The vein is 1.4m-thick (184.2 - 185.6m)
in total, with an approximately 5cm-wide zone of milky carbonate hosting the
VG occurrence. Pyrite is abundant throughout the vein, increasing to
semi-massive in places. The VG at 185.5 metres downhole occurs in close
proximity to semi-massive pyrite and unconfirmed silver-colored minerals
within a QCT vein.
The previous holes in the Northeast Target also hosted high-grade
mineralization in quartz tourmaline and QCT veins. However, the altered and
veined volcano-sedimentary package encountered in 21MJ001 is interpreted to be
stratigraphically below the mineralization encountered in 19MJ006 and 20MJ009.
Previous drilling reported brecciated zones in altered metasediments with
abundant quartz tourmaline veins and pyrite. FireFox geologists have confirmed
that the alteration and veining in the vicinity of the VG occurrence is
geologically similar to the previously reported mineralization along the
Mustajärvi Shear Zone and at the Northeast Target.
The drill rig has moved to drill hole location 21MJ002 (See Figure 1),
which is approximately midway between drill hole 20MJ009 and 21MJ001. Company
geologists are working diligently to complete the drill logging and sampling
process for 21MJ001 so that samples will be delivered to the lab promptly.
FireFox cautions the reader that the samples from this new core hole have
not yet been assayed. Hence, descriptions of mineralization and comparisons to
previously reported mineralized intervals cannot be relied upon. However, the
reported visible gold has been visually confirmed by experienced Company
geologists, including FireFox's Exploration Manager and General Manager of
Exploration. The team further collaborated closely through a photographic
review with senior technical advisors (Dr. Richard Goldfarb and Dr. Quinton
Hennigh) and senior geologists on the board of directors (Timo Maki and
Patrick Highsmith) who all confirmed the presence of coarse visible gold in
the drill core.
Quality Assurance
The core was transported from the rig to the Company´s core storage
facility in Sodankylä, where FireFox's exploration team conducted geological
and geotechnical logging and photographed the core. Company geologists will
select and mark sample intervals prior to sawing of drill core and sampling
for analysis. After insertion of quality controls samples into the shipment,
the samples will be promptly delivered to an accredited laboratory for gold
and multielement analyses.
Patrick Highsmith, Certified Professional Geologist (AIPG CPG (number sign) 
11702)
and director of the Company, is a qualified person as defined by National
Instrument 43-101. Mr. Highsmith has reviewed and approved all of the
geological data and observations disclosed in this news release. The review
process included a rigorous analysis of photographs, telephone discussions
with geologists on site, and consultation with senior technical advisors to
the Company. Mr. Highsmith has visited the Mustajärvi Project and reviewed
drill core in person from earlier drill programs. Mr. Highsmith is not
independent of the Company, as he owns shares and is a member of the board of
directors.
About the Mustajärvi Gold Project
The Mustajärvi Gold Project (the "Project") consists of an exploration
permit and exploration permit application totaling 2.68 km2. The project area
is flat, glacial till-covered terrain in the Lapland region of northern
Finland, 17km east of the town of Kittilä, with road and power on the
property. The Project is situated in the Central Lapland Greenstone Belt,
which hosts several recent gold discoveries. The Project occupies more than
two kilometres strike length of the Mustajärvi Shear Zone, which is believed
to be a splay of the Venejoki Thrust Zone and related to the Sirkka Thrust
Zone, an important host to gold mineralization in the belt. The observed gold
mineralization, structural setting and work to date support the potential for
a high-grade orogenic gold deposit on the Mustajärvi property.
For additional details on the Project, please visit the Company's website
www.firefoxgold.com.
About FireFox Gold Corp.
FireFox Gold Corp is listed on the TSX Venture stock exchange under the
ticker symbol FFOX. The Company has been exploring for gold in Finland since
2017 where it holds a project portfolio that includes over 80,000 hectares of
prospective ground.
Finland is one of the top mining investment jurisdictions in the world 
asindicated by its multiple top-10 rankings in recent Fraser Institute Surveys
of Mining Companies. Having a strong mining law and long mining tradition,
Finland remains underexplored for gold. Recent exploration results in the
country have highlighted its prospectivity, and FireFox is proud to have a
Finland based CEO and technical team.
For more information, please refer to the Company's website and profile
on the SEDAR website at www.sedar.com.
On behalf of the Board of Directors,
"Carl Löfberg"Chief Executive Officer
Forward Looking Statements
The information herein contains forward looking statements that are
subject to a number of known and unknown risks, uncertainties and other
factors that may cause actual results to differ materially from those
anticipated in our forward-looking statements. Factors that could cause such
differences include: the receipt of the assay results, changes in world
commodity markets, equity markets, the extent of work stoppage and economic
impacts that may result from the COVID 19 virus, costs and supply of materials
relevant to the mining industry, change in government and changes to
regulations affecting the mining industry.
Forward-looking statements in this release may include statements
regarding: the intent to move quickly to complete the drill logging and
sampling process so that samples will be delivered to the lab promptly so that
the Company can secure assays on the samples; plans to review the current
drill program in light of the results disclosed herein; the belief as to the
location of the most prospective gold targets; the location of possible new
targets for the 2021 drill program; the current and future work program,
including the extent and nature of exploration to be conducted in 2021; and
the potential expansion of the same and the significance of the most intense
mineralization occurring at depths below previous drilling at the Northeast
Target. Although we believe the expectations reflected in our forward-looking
statements are reasonable, results may vary.
FireFox cautions the reader that the samples from this new core hole are
currently being logged and prepared for sampling, so no assays are available
yet to confirm the quantity or extent of gold in the drill hole. Hence,
descriptions of minera

" BC-FireFox-reports-gold   04-15 2278
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.365516:
^FireFox Gold Reports Visible Gold in First Hole of New Drill Program at
Mustajärvi Gold Project, Finland@

SODANKYLÄ, Finland, April 15, 2021 /CNW/ - FireFox Gold Corp. (TSXV:
FFOX) ("FireFox" or the "Company") is pleased to report that it has
encountered coarse visible gold (VG) in the first drill hole of a newly
commenced phase 4 diamond drilling program at its 100%-owned Mustajärvi Gold
Project in the Central Lapland Greenstone Belt of northern Finland. The
visible gold occurs as six discrete flakes (up to 1.0mm across) in a
quartz-carbonate-tourmaline vein (QCT vein) within a 32-metre-wide zone of
variably veined and altered metasedimentary rocks. The drill core is being
logged and prepared for sampling, so no assays are available yet to confirm
the quantity or extent of gold in the drill hole.
FireFox has reported numerous drill intercepts of relatively narrow
high-grade gold mineralization (as shown in Table 1) at the Mustajärvi Project
since its first drill program in 2018, but this is the first visible gold
reported by FireFox geologists at the project. Drill hole 21MJ001 is a
significant step-out (150 metres) to the northeast from a recently reported
high-grade intersection in drill hole 20MJ009 (2.0m at 33.25 g/t gold, see
Company news release dated January 27, 2021) (see Figure 1:
https://bit.ly/3uQyuYF ).
Highlights:
<<

--  Hole 21MJ001 intercepted visible gold (at least six discrete flakes up
to 1.0mm across) at a depth of approximately 185.5m downhole (see Figure
2: https://bit.ly/32guK6w)
--  The VG occurs in a 1.4 metre (m) section of QCT-veins from 184.2 to
185.6m depth
--  QCT veins also host the high-grade gold mineralization previously
reported in drill holes 20MJ009, 19MJ006, and others in the Central Zone
--  There are several QCT veins of variable thickness within altered
metamorphosed sedimentary and volcaniclastic rocks from 165.6m to the
end of this hole at 199.4m downhole (see Figure 3:
https://bit.ly/3adj2Of)
--  This hole is a step-out of approximately 150m from drill hole 20MJ009
along the northeast trending Mustajärvi Shear Zone
--  Drill hole 21MJ001 was completed in the early hours of April 11, 2021,
so assays have not yet been completed to confirm the quantity or extent
of gold in the drill core
<>>
"We are very excited to report the first visible gold from drilling at
the Mustajärvi Project. The new drilling has encountered significant zones of
intense alteration and veining along trend but beyond the extents of previous
drilling," commented Carl Löfberg, President and CEO of FireFox. "In light of
this favorable geology, we shall move quickly to secure assays on these
samples and to carefully consider our plans for the current drill program."
Preliminary Geologic Details of Drill Hole
The Mustajärvi Project lies along the highway between the cities of
Kittilä and Sodankylä, approximately 17 kilometers east of Kittilä. The
project remains in the early stages of exploration, having only seen
approximately 4,170m of drilling by FireFox since 2018. The property straddles
the Mustajärvi Shear Zone (MSZ), a major right-lateral shear zone that has
associated second and third-order structures which further dissect the project
into separate structural zones. FireFox has developed a structural model that
has identified dilatant zones along the major structure where higher grade
gold is concentrated. Company geologists believe that the most prospective
gold targets are in the Sodankylä Group metasedimentary rocks, which are to
the north of the shear zone in the footwall. In this area, the Sodankylä Group
includes metamorphosed sedimentary and volcaniclastic rocks. At Mustajärvi,
the most quartz-rich portions of these rocks have become brittle due to
pre-gold pervasive alteration with silica and albite, and host higher-grade
gold where they have been shattered, brecciated, and veined.
The 2021 drill program is targeting the brittle rocks in these
interpreted dilatant zones at the Northeast Target, the Central Zone with its
historic surface workings, and possibly at new targets farther to the
northeast and southwest. These high-grade gold (>5 g/t) pods are known to
occur along a distance of more than 1.5 kilometres of the hydrothermally
altered shear zone from the southwest to northeast on the project. The
sparsely drilled Northeast Target is one of these pods, and the area returned
the best intercepts in both the 2019 and 2020 drill programs (see Table 1).
The current Phase 4 drilling program was planned to include approximately
1,400 metres of diamond core drilling, but the program may be expanded. The
first hole, 21MJ001, is in the Northeast Target area, approximately 150m
northeast from drill hole 20MJ009, and nearly 750m from the Central Zone of
gold mineralization.
Table 1: Highlights of Previous Mustajärvi High-Grade Drill Intercepts
Drill                        Easting                       
Northing                       Azimuth                       
Plunge                       Depth             From         To            
Interval(x)         Gold



Hole

(°)                           (°)                         (m)              
(m)          (m)

(m)            (g/t)

---                                                                             
                                                                                
                                                               ---



Central Zone

---

18MJ002                             427702                         
7500228                            340                            
45                         82.1             34.35        34.75                
0.35          11.63

---

18MJ010                             422728                         
7500162                            340                            
45                        154.8             125.5        127.5                
2.00          45.05

---

20MJ008                             427716                         
7500191                            340                            
45                          200              97.5         98.0                 
0.5          11.20

---



Northeast Zone

---

19MJ006                             427709                         
7500244                            340                            
45                          179            125.75        127.9
1.95(x)(x)               12.0

---

including                          126.25             127.1         
0.85                 24.7



20MJ009                             428335                         
7500581                            340                            
45                        178.5              65.0         67.0                 
2.0          33.25

---

146.5        147.0                  0.5           9.36






(x)

- Drilling is believed to be perpendicular to the dip of the mineralization, 
however true widths are not yet known and will be
confirmed with additional drilling and geological modeling.



(x)(x) - Including 0.2m of core loss



Please see the original news releases for additional details:  Holes 18MJ002 
and 18MJ010 reported January 21, 2019; 19MJ006,
reported January 15, 2020; and 20MJ008 & 20MJ009 reported January 27th, 2021.

---
In drill hole 21MJ001, the targeted volcano-sedimentary series was
encountered at approximately 104m down hole and continued to the termination
of the hole at 199.4m. This section of rocks is pervasively altered with
moderate to very abundant amounts of silica, albite, sericite, and pyrite. The
altered rock sequence is cut throughout its width by QCT veins, quartz
tourmaline, and quartz veins that contain abundant to semi-massive and massive
zones of pyrite (see Figure 3). There are additional sulfide, or possibly
telluride and bismuth-bearing minerals (not yet confirmed), that are common in
the most intensely altered and veined rocks. Intense sericitic alteration with
disseminated pyrite and narrow quartz tourmaline veins (up to 1cm) can be
observed at the bottom of the drill hole.
It may be significant that the most intense mineralization occurs at
depths below previous drilling at the Northeast Target. Six individual zones
of very well-developed tourmaline and pyrite alteration can be distinguished
within the albite-sericite altered tuffs and sediments from 172.8-184.2m. Near
the top of this zone there is an occurrence of bladed calcite textures in a
vein (see Figure 4: https://bit.ly/3uLMbrC). This is often an indication of
separation of liquid and vapor phases during vein formation, which may occur
in the epizonal portion of orogenic gold deposits.
Visible gold appears as six individual flakes, up to 1.0mm in size,
observed on the core surface. These are hosted in a milky-colored
carbonate-rich portion of a QCT vein. The vein is 1.4m-thick (184.2 - 185.6m)
in total, with an approximately 5cm-wide zone of milky carbonate hosting the
VG occurrence. Pyrite is abundant throughout the vein, increasing to
semi-massive in places. The VG at 185.5 metres downhole occurs in close
proximity to semi-massive pyrite and unconfirmed silver-colored minerals
within a QCT vein.
The previous holes in the Northeast Target also hosted high-grade
mineralization in quartz tourmaline and QCT veins. However, the altered and
veined volcano-sedimentary package encountered in 21MJ001 is interpreted to be
stratigraphically below the mineralization encountered in 19MJ006 and 20MJ009.
Previous drilling reported brecciated zones in altered metasediments with
abundant quartz tourmaline veins and pyrite. FireFox geologists have confirmed
that the alteration and veining in the vicinity of the VG occurrence is
geologically similar to the previously reported mineralization along the
Mustajärvi Shear Zone and at the Northeast Target.
The drill rig has moved to drill hole location 21MJ002 (See Figure 1),
which is approximately midway between drill hole 20MJ009 and 21MJ001. Company
geologists are working diligently to complete the drill logging and sampling
process for 21MJ001 so that samples will be delivered to the lab promptly.
FireFox cautions the reader that the samples from this new core hole have
not yet been assayed. Hence, descriptions of mineralization and comparisons to
previously reported mineralized intervals cannot be relied upon. However, the
reported visible gold has been visually confirmed by experienced Company
geologists, including FireFox's Exploration Manager and General Manager of
Exploration. The team further collaborated closely through a photographic
review with senior technical advisors (Dr. Richard Goldfarb and Dr. Quinton
Hennigh) and senior geologists on the board of directors (Timo Maki and
Patrick Highsmith) who all confirmed the presence of coarse visible gold in
the drill core.
Quality Assurance
The core was transported from the rig to the Company´s core storage
facility in Sodankylä, where FireFox's exploration team conducted geological
and geotechnical logging and photographed the core. Company geologists will
select and mark sample intervals prior to sawing of drill core and sampling
for analysis. After insertion of quality controls samples into the shipment,
the samples will be promptly delivered to an accredited laboratory for gold
and multielement analyses.
Patrick Highsmith, Certified Professional Geologist (AIPG CPG (number sign) 
11702)
and director of the Company, is a qualified person as defined by National
Instrument 43-101. Mr. Highsmith has reviewed and approved all of the
geological data and observations disclosed in this news release. The review
process included a rigorous analysis of photographs, telephone discussions
with geologists on site, and consultation with senior technical advisors to
the Company. Mr. Highsmith has visited the Mustajärvi Project and reviewed
drill core in person from earlier drill programs. Mr. Highsmith is not
independent of the Company, as he owns shares and is a member of the board of
directors.
About the Mustajärvi Gold Project
The Mustajärvi Gold Project (the "Project") consists of an exploration
permit and exploration permit application totaling 2.68 km2. The project area
is flat, glacial till-covered terrain in the Lapland region of northern
Finland, 17km east of the town of Kittilä, with road and power on the
property. The Project is situated in the Central Lapland Greenstone Belt,
which hosts several recent gold discoveries. The Project occupies more than
two kilometres strike length of the Mustajärvi Shear Zone, which is believed
to be a splay of the Venejoki Thrust Zone and related to the Sirkka Thrust
Zone, an important host to gold mineralization in the belt. The observed gold
mineralization, structural setting and work to date support the potential for
a high-grade orogenic gold deposit on the Mustajärvi property.
For additional details on the Project, please visit the Company's website
www.firefoxgold.com.
About FireFox Gold Corp.
FireFox Gold Corp is listed on the TSX Venture stock exchange under the
ticker symbol FFOX. The Company has been exploring for gold in Finland since
2017 where it holds a project portfolio that includes over 80,000 hectares of
prospective ground.
Finland is one of the top mining investment jurisdictions in the world 
asindicated by its multiple top-10 rankings in recent Fraser Institute Surveys
of Mining Companies. Having a strong mining law and long mining tradition,
Finland remains underexplored for gold. Recent exploration results in the
country have highlighted its prospectivity, and FireFox is proud to have a
Finland based CEO and technical team.
For more information, please refer to the Company's website and profile
on the SEDAR website at www.sedar.com.
On behalf of the Board of Directors,
"Carl Löfberg"Chief Executive Officer
Forward Looking Statements
The information herein contains forward looking statements that are
subject to a number of known and unknown risks, uncertainties and other
factors that may cause actual results to differ materially from those
anticipated in our forward-looking statements. Factors that could cause such
differences include: the receipt of the assay results, changes in world
commodity markets, equity markets, the extent of work stoppage and economic
impacts that may result from the COVID 19 virus, costs and supply of materials
relevant to the mining industry, change in government and changes to
regulations affecting the mining industry.
Forward-looking statements in this release may include statements
regarding: the intent to move quickly to complete the drill logging and
sampling process so that samples will be delivered to the lab promptly so that
the Company can secure assays on the samples; plans to review the current
drill program in light of the results disclosed herein; the belief as to the
location of the most prospective gold targets; the location of possible new
targets for the 2021 drill program; the current and future work program,
including the extent and nature of exploration to be conducted in 2021; and
the potential expansion of the same and the significance of the most intense
mineralization occurring at depths below previous drilling at the Northeast
Target. Although we believe the expectations reflected in our forward-looking
statements are reasonable, results may vary.
FireFox cautions the reader that the samples from this new core hole are
currently being logged and prepared for sampling, so no assays are available
yet to confirm the quantity or extent of gold in the drill hole. Hence,
descriptions of mineralization and comparisons to previously reported
mineralized intervals cannot be relied upon.
Further, although drilling is believed to be perpendicular to the dip of
the mineralization, true widths are not yet known and will be confirmed with
additional drilling and geological modeling.
The forward-looking statements contained herein represent the
expectations of FireFox as of the date of dissemination and, accordingly, are
subject to change after such date. Readers should not place undue importance
on forward-looking statements and should not rely upon this information as of
any other date. FireFox does not undertake to update this information at any
particular time except as required in accordance with applicable laws.
SOURCE FireFox Gold Corp.



View original content:
http://www.newswire.ca/en/releases/archive/April2021/15/c6993.html

-0-                           04/15/2021
/For further information: FireFox Gold Corp., Email:
info(at)firefoxgold.com, Telephone: +1-778-244-8439/
/Web Site: www.firefoxgold.com /
(FFOX.)

CO:  FireFox Gold Corp.
ST:  British Columbia, Finland
IN:  MIN MNG PRM
SU:

-30-