Source	CANADA NEWSWIRE
Date	04/20/2021
Time	04:04:14 AM

Company	 Northern Vertex Mining Corp.
Title	Northern Vertex Identifies 45 New Targets for Exploration at Hercules
Gold Project, Nevada





    CDNX Symbol: NEE











Press Release




" BC-NorthernVertexProject   04-20 1810
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.313199:
^Northern Vertex Identifies 45 New Targets for Exploration at Hercules
Gold Project, Nevada@

VANCOUVER, B.C., April 20, 2021 /CNW/ - Northern Vertex Mining Corp.
(TSXV: NEE) (OTC Nasdaq Intl.: NHVCF) (the "Company" or "Northern Vertex") a
U.S.-focused gold producer with district-scale exploration projects in the
Walker Lane Trend is pleased to report highlights of a recent airborne
geophysical survey at its Hercules Gold Project in Lyon County, Nevada.
Survey Highlights
<<

--  Identified at least 45 new targets for follow-up exploration.
--  Highlighted the structural framework of the Hercules property, providing
support for the Company's district-scale geological model.
--  Indicated the presence of an extensive and open-ended thirteen
kilometers long by six kilometers wide alteration zone trending
northwest-southeast across the property that is coincident with known
mineralization.
--  Data to-date suggests that mineralization is controlled by the
intersection of generally northerly trending structures and the broad
alteration zone.
<>>
Michael G. Allen, President commented, "From the first time we set foot
on the property we knew there was significant potential, and after expanding
the property to more than 100 square kilometers we see that investment
validated and with very strong support of our premise that there were multiple
potential discoveries to be made at Hercules. After a detailed review of this
new geophysical data, along with other recently acquired data sets, we see
confirmation of many previous assumptions underpinning our understanding of
the structures bearing gold and silver mineralization."
Dr. Warwick S. Board, Vice President of Exploration Northern Vertex,
commented, "The exposed, known mineralization target areas at the Hercules
Gold Project correlated strongly with all of the geophysical techniques and
are centered in a broad alteration zone on the flank of a large volcanic
center. With at least 45 new targets identified to be advanced, we have ample
opportunity to make additional discoveries. Having the structural framework
gives us a predictive geological model for efficient future drilling at the
Hercules Gold Project."
Recent drilling by the Company highlighted the potential of the Hercules
Gold Property with 30.48 meters grading 1.63 g/t gold and 18.27 g/t silver as
well as 39.62 meters grading 1.12 g/t gold and 5.38 g/t silver. For further
details on the Hercules Gold Project drilling, please see the Company's March
22, 2021 news release or the Company's website.
Airborne Geophysical Survey of Hercules Project
A combined magnetic, electromagnetic (Geotech's proprietary Versatile
Time Domain Electromagnetic; VTEMTM), and gamma-ray spectrometry (radiometric
potassium, thorium, and uranium) airborne geophysical survey was completed
over the Hercules Project between July and September 2020 by Geotech Ltd.
(Geotech) out of Aurora, ON. A total of 2,260 line-kilometers of geophysical
data were collected along 50-meter spaced west-east oriented traverse lines
and 500-meter spaced north-south tie lines across the property. Data
processing and first-pass interpretation was provided by Geotech and J L
Wright Geophysics, of Spring Creek, NV.
The objective of the combined airborne geophysical survey was to
delineate structures, lithologies, and alteration using the resistivity (from
the VTEMTM survey), magnetic, and radiometric geophysical parameters.
The results of the airborne geophysical survey highlight the presence of
an extensive, volcanic center-related hydrothermal system on the Hercules
property. The geophysical survey data support our geological model of a
collapsed caldera in which curviplanar concentric structures are considered to
have controlled epithermal mineralization. The recognition of an apparent
deep-seated radial structure that may have controlled hydrothermal fluids in
the volcanic center is a key finding for additional exploration on the
property. Resistivity and radiometric potassium anomalies along concentric
structures to the south of this feature attest to the district-scale
exploration potential at Hercules.
Geophysical Areas of Interest
A low sulphidation epithermal gold-silver system has been identified on
the Hercules Gold Project. At Hercules, and at other similar deposits, such as
the Company's Moss Mine, epithermal gold-silver mineralization is both
structurally and lithologically controlled, being hosted in veins, vein
stockwork, and zones of elevated silica alteration in faults and fractures,
and where available, permeable volcaniclastic host rocks. Variably extensive
clay mineral alteration footprints are associated with the silica-rich zones.
Zones of elevated silica alteration are generally associated with
elevated resistivity, whereas zones of intense clay mineral alteration are
associated with lower resistivity. Both have been found to be associated with
elevated potassium signatures and subdued airborne magnetic survey responses
due to magnetic mineral destruction by hydrothermal alteration. Variations in
magnetic responses across geological structures form the basis for
interpreting the structural framework of the Hercules property. Results from
each geophysical dataset were used to check and augment individual dataset
interpretations.
Controls on Mineralization
The structural, lithological, and alteration picture revealed by the
geophysical survey is consistent with the Company's interpretation that the
Hercules property covers part of a larger collapsed Messinian-aged volcanic
caldera centered to the southeast (Figure 1. Regional Geological Map).
An open-ended approximately six kilometers wide zone of elevated
radiometric potassium trends approximately thirteen kilometers
northwest-southeast across the northern parts of the property (Figure 2.
Shaded Radiometric Potassium Map). The zone is associated with areas of
anomalous resistivity and a generally subdued magnetic response, features
suggestive of an extensive hydrothermal system (Figure 3. Shaded VTEMTM
Resistivity Map at 50 m depth, Figure 4. Shaded Total Magnetic Intensity Map).
The zone contains the Hercules mine as well as the mapped veins and alteration
of the Hercules, Cliffs, Loaves, Northeast, Rattlesnakes, Lucky Rusty, Sprite,
Sirens, and part of the Pony Meadows exploration target areas. Within the
zone, mapped veins and alteration in the various exploration target areas
follow north-northeast trending structures that appear to be concentric about
the volcanic center to the east.
The zone is interpreted as having been created by deep-seated volcanic
center-related radial structures controlling potassic, silica, and clay
mineral alteration. Intersection of the deep feeder zone with concentric
structures is interpreted as being an important control on mineralization on
the Hercules property.
Geophysical Target Generation
Mapped mineralized epithermal veins and associated alteration correlate
well with elevated radiometric potassium signatures. First-pass interpretation
of the geophysical data using this relationship has identified 29 new separate
radiometric potassium targets (Figure 2. Shaded Radiometric Potassium Map,
Figure 5. New Geophysical Target Summary Map).
Additionally, most of the known epithermal veins are associated with
resistivity highs surrounded by concentric rings of lower resistivity. This
high-low resistivity pattern is interpreted to reflect silica alteration in
the center surrounded by broader areas of clay mineral alteration. An initial
total of 16 new separate resistivity anomaly targets have been identified
based on this relationship (Figure 3. Shaded VTEMTM Resistivity Map at 50 m
depth, Figure 5. New Geophysical Target Summary Map).
Additional potentially anomalous resistivity target areas, with
associated structures, lithological contacts, and anomalous radiometric
potassium signatures are identified in the southern parts of the Hercules
property based on a similar resistivity signature to that beneath the main
target areas in the main northwest-southeast trending radiometric potassium
band.
Parallel concentric north-south to northeast-southwest trending
structures with subdued to no resistivity and/or radiometric potassium
responses and along which basaltic andesite lava has been interpreted, remain
of interest but are considered secondary targets (Figure 4. Shaded Total
Magnetic Intensity Map, Figure 5. New Geophysical Target Summary Map).
Follow-up Work
The Company is reviewing the geophysical targets in conjunction with its
recent surface mapping, surface sampling, and drilling data towards target
prioritization and future drill programs on the Hercules property.
Qualified Person
Dr. Warwick Board, P.Geo., Vice President Exploration of Northern Vertex,
is the QP as defined by NI 43-101 responsible for the regional exploration of
the Hercules Project and has reviewed and approved the scientific and
technical information in this news release related thereto.
About Northern Vertex Mining Corp.
Northern Vertex offers investors a rare combination of cash flow,
production, top-tier management, and exceptional exploration potential within
two projects on the Walker Lane Gold Trend of western Nevada and Arizona.
Management is executing a clear strategy that expands production and resources
at the Moss Mine in Arizona while aggressively exploring the Hercules Project
in Nevada.
ON BEHALF OF THE BOARD OF NORTHERN VERTEX
"Michael G. Allen"President
TSXV: NEE | Nasdaq Intl: NHVCF | Frankfurt: 54N | ISIN: CA6660061012 |
WKN: A1JUA0
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement Regarding Forward-Looking Information
All statements, trend analysis and other information contained in this
press release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but not
always, identified by the use of words such as "seek", "anticipate",
"believe", "plan", "estimate", "expect" and "intend" and statements that an
event or result "may", "will", "should", "could" or "might" occur or be
achieved and other similar expressions. All statements, other than statements
of historical fact, included herein, are forward-looking statements. Although
Northern Vertex believes that the expectations reflected in such
forward-looking statements and/or information are reasonable, undue reliance
should not be placed on forward-looking statements since Northern Vertex can
give no assurance that such expectations will prove to be correct. These
statements involve known and unknown risks, uncertainties and other factors
that may cause actual results or events to differ materially from those
anticipated in such forward-looking statements, including the risks,
uncertainties and other factors identified in Northern Vertex's periodic
filings with Canadian securities regulators. Forward-looking statements are
subject to business and economic risks and uncertainties and other factors
that could cause actual results of operations to differ materially from those
contained in the forward-looking statements. Important factors that could
cause actual results to differ materially from Northern Vertex's expectations
include risks associated with the business of Northern Vertex; risks related
to reliance on technical information provided by Northern Vertex; risks
related to exploration and potential development of Northern Vertex's
projects; business and economic conditions in the mining industry generally;
fluctuations in commodity prices and currency exchange rates; uncertainties
relating to interpretation of drill results and the geology, continuity and
grade of mineral deposits; the need for cooperation of government agencies in
the exploration and development of properties and the issuance of required
permits; the need to obtain additional financing to develop properties and
uncertainty as to the availability and terms of future financing; the
possibility of delay in exploration or development programs and uncertainty of
meeting anticipated program milestones; uncertainty as to timely availability
of permits and other governmental approvals; and other risk factors as
detailed from time to time and additional risks identified in Northern
Vertex's filings with Canadian securities regulators on SEDAR (available at
www.sedar.com). Forward-looking statements are based on estimates and opinions
of management at the date the statements are made. Northern Vertex does not
undertake any obligation to update forward-looking statements except as
required by applicable securities laws. Investors should not place undue
reliance on forward-looking statements.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/northern-vertex-identifies-
45-new-targets-for-exploration-at-hercules-gold-project-nevada-301272246.html
SOURCE Northern Vertex Mining Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/20/c4925.html

-0-                           04/20/2021
/For further information: CORPORATE INQUIRIES: Michael G. Allen,
President, Company Website: www.northernvertex.com, +1 (855) 633-8798 Toll
Free, +1 (604) 601-3656 Office, Email: mike(at)northernvertex.com/
/Web Site: www.northernvertex.com /
(NHVCF NEE.)

CO:  Northern Vertex Mining Corp.
ST:  British Columbia
IN:  MNG OTC PRM
SU:

-30-