Source	CANADA NEWSWIRE
Date	04/20/2021
Time	03:34:15 AM

Company	 Soma Gold Corp.
Title	Soma Gold Updates Exploration Results





    CDNX Symbol: SOMA











Press Release




" BC-SomaGold-Exploration   04-20 1647
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.570927:
^Soma Gold Updates Exploration Results@

VANCOUVER, BC, April 20, 2021 /CNW/ - Soma Gold Corp. (TSXV: SOMA) (WKN:
A2P4DU) (OTC: SMAGF) (the "Company" or "Soma") is pleased to announce new
drilling and channel sampling results for the on-going exploration program at
the Company's Zara property in Antioquia, Colombia.
Highlights
<<

--  The drilling and sampling indicates that the Estrella-Diamantina
mineralized trend extends for over 4km in strike from Estrella in the
north to Diamantina in the south with an exploration target of +500k
ounces of Au down to 250m in depth.
--  Multiple +10g/t channel samples from existing small miner workings (up
to 64 g/t).
--  Drill hole ADDDH_21_02 intercepted 13.85g/t gold over 0.75m.
<>>
Soma has built a new 3D model integrating channel samples, mapping and
mining data for this under-explored mineralized trend on its Zara project.
This work has identified three new zones for follow-up exploration and
drilling with the potential for high gold grades (see map (number sign)1). The 
first phase
of drilling in the Alacran-Diamantina zone and extensive vein channel sampling
at the Diamantina mine have confirmed the presence of high gold grades to
depth.
Alacran-Diamantina Zone
This zone is located 2 km to the south west of the Company's past
producing, high-grade Limon mine and is at the southern end of the larger 7-km
Estrella-Diamantina mineralized trend. The presence of historic small miners
provided access to underground workings that allowed the company to confirm
reported high grades. Soma is planning 3,500m of drilling to test the down-dip
continuity of the main mineralized zone that was mined in the past by local
miners (see cross-section (number sign)1). The current drilling program 
commenced in early
February 2021. The first three drill holes, totaling 847m, the results of
which are reported in this press release, represent approximately 25% of the
planned program and were completed by the end of March. The remaining drilling
will be completed by the end of June 2021.
Highlights include:
<<

--  Drill hole ADDDH_21_02 intersected 0.75 meters, from 105.20 to 105.95m,
of milky quartz-carbonates vein with veining of sulphides, mainly pyrite
and sphalerite, grading 13.85 g/t Au.
--  Drill hole ADDDH_21_03 intersected 1.30 meters, from 100.3 to 101.6m, of
milky quartz-carbonates vein with scarce pyrite and sphalerite, grading
1.96g/t Au.
o The above includes 0.60 meters of fine-grained sphalerite and pyrite grading
3.1g/t Au, starting at 101.0 meters.
<>>
Location

Hole ID       From   To    From     To      Length      Length       Au

---

(m)                 (m)         (ft)  (ft)   (m)     (ft)     (g/t)

---

Alacran-
Diamantina

ADDDH_21_01    48.30  49.00  158.47   160.77        0.70         2.30     5.43

---

ADDDH_21_02                 105.20 105.95 345.16  347.62     0.75        
2.46        13.85

---

ADDDH_21_03                 100.30 101.60 329.08  333.35     1.30        
4.27         1.96

---


Including                       100.30 101.00 329.08  331.38     0.70        
2.30         0.98

---


Including                       101.00 101.60 331.38  333.35     0.60        
1.97          3.1

---
(x) Widths reported are drilled core lengths. Drill holes were oriented to
be perpendicular to the dip of the veins, and management believes the reported
intersections approximate their true widths.

Map (number sign)1. Plan view of drilling targets defined at Zara´s north
concessions.
In addition to the drilling, channel sampling at the Diamantina mine was
completed in level one and in three incline raises (see table (number sign) 1). 
Forty two
(42) channel samples were collected by hand, using hammer and chisel,
perpendicular to the exposed mineralized quartz-carbonate vein to best
represent true width. The channel samples results corroborate the presence of
the high grades previously reported. The high grades and vein continuity
remain open along strike and down-dip.
Table (number sign)1. Channel sample assays
Location          Channel From   To    From     To      Length      
Length       Au

---

(m)               (m)   (ft)  (ft)   (m)     (ft)     (g/t)

---

Alacran-
Diamantina
Y51202        0.00   0.80    0.00     2.62        0.80         2.62     0.5

---

Y51203                     0.00  0.40   0.00    1.31     0.40        
1.31         23.1

---

Y51205                     0.00  0.40   0.00    1.31     0.40        
1.31          0.7

---

Y51214                     0.00  0.15   0.00    0.49     0.15        
0.49         0.01

---

Y51218                     0.00  0.15   0.00    0.49     0.15        
0.49          5.0

---

Y51220                     0.00  0.50   0.00    1.64     0.50        
1.64          2.1

---

Y51222                     0.00  0.50   0.00    1.64     0.50        
1.64         12.6

---

Y51224                     0.00  0.30   0.00    0.98     0.30        
0.98          0.4

---

Y51226                     0.00  0.20   0.00    0.66     0.20        
0.66          0.2

---

Y51243                     0.00  0.25   0.00    0.82     0.25        
0.82         0.01

---

Y51246                     0.00  0.30   0.00    0.98     0.30        
0.98          3.5

---

Y51248                     0.00  0.20   0.00    0.66     0.20        
0.66         12.9

---

Y51250                     0.00  0.20   0.00    0.66     0.20        
0.66         13.1

---

Y51253                     0.00  0.30   0.00    0.98     0.30        
0.98          5.2

---

Y51255                     0.00  0.30   0.00    0.98     0.30        
0.98          5.0

---

Y51256                     0.00  0.30   0.00    0.98     0.30        
0.98         12.7

---

Y51259                     0.00  0.30   0.00    0.98     0.30        
0.98          0.7

---

Y51262                     0.00  0.20   0.00    0.66     0.20        
0.66          3.5

---

Y51264                     0.00  0.20   0.00    0.66     0.20        
0.66         64.2

---

Y51267                     0.00  0.15   0.00    0.49     0.15        
0.49          0.3

---

Y51268                     0.00  0.20   0.00    0.66     0.20        
0.66          0.2

---

Y51270                     0.00  0.35   0.00    1.15     0.35        
1.15          0.3

---

Y51272                     0.00  0.40   0.00    1.31     0.40        
1.31         39.2

---

Y51274                     0.00  0.20   0.00    0.66     0.20        
0.66          0.0

---

A3101                     0.00  0.50   0.00    1.64     0.50        
1.64         39.4

---

A3119                     0.00  0.80   0.00    2.62     0.80        
2.62          0.7

---

A3120                     0.00  0.75   0.00    2.46     0.75        
2.46          1.8

---

A3121                     0.00  0.95   0.00    3.12     0.95        
3.12          8.5

---

A3123                     0.00  0.30   0.00    0.98     0.30        
0.98          4.6

---

A3124                     0.00  0.25   0.00    0.82     0.25        
0.82         0.01

---

A3125                     0.00  0.30   0.00    0.98     0.30        
0.98          0.3

---

A3127                     0.00  0.35   0.00    1.15     0.35        
1.15         12.5

---

A3128                     0.00  0.40   0.00    1.31     0.40        
1.31          1.1

---

A3129                     0.00  0.35   0.00    1.15     0.35        
1.15          2.6

---

A3131                     0.00  0.30   0.00    0.98     0.30        
0.98         12.3

---

A3133                     0.00  0.35   0.00    1.15     0.35        
1.15         10.7

---

A3135                     0.00  0.65   0.00    2.13     0.65        
2.13         11.9

---

A3136                     0.00  0.40   0.00    1.31     0.40        
1.31         19.7

---

A3137                     0.00  0.35   0.00    1.15     0.35        
1.15          4.1

---

A3138                     0.00  0.30   0.00    0.98     0.30        
0.98          6.0

---

A3140                     0.00  0.20   0.00    0.66     0.20        
0.66          8.1

---

A3141                     0.00  0.35   0.00    1.15     0.35        
1.15         19.3

---
(x) Lengths are sampled intervals lengths and not necessarily true widths.
Samples were taken in a manner to reflect, as closely as possible, true width.
North to South cross-section (number sign)1 showing the under explored
Alacran-Diamantina mineralized trend and vein interception of drill holes
ADDDH_21_01 to ADDDH_21_03. Planned drill holes are expected to be completed
by the end of Q2.
Drill core from hole ADDDH-21-02 at Diamentina with visible gold
Javier Cordova, Soma's CEO, states, "The results of the current program
supports the Company's assumptions on the continuity of the mineralized trend
and bodes well for the establishment of a larger resource as the exploration
program moves south. The Company's existing mines are located at the northern
end of the claims blocks. The current program is leveraging the work, at the
surface and near the surface, completed by small miners in the region to map
the mineralized veins and pinpoint the locations of the highest grade
material. This mapping and sampling will focus on the planned four-year,
100,000-meter DDH drilling program. We have only begun to understand the
extent, grade and depth of the mineralized zone on the northern section of the
Otu Valley. Mapping of the veins exposed by the small miners indicates that
the mineralized trend continues south for 13 km on Soma's property."
QA/QC CONTROLS
For exploration core drilling, the company applied its standard protocols
for sampling and assay. NQ core is sawn or split with one-half shipped to a
sample preparation laboratory in Medellin run by ALS Colombia Limited ("ALS").
Channel samples were collected by hand using hammer and chisel perpendicularly
across exposed mineralized quartz-carbonate vein to best represent the true
width. Channel sample locations were surveyed using total station. Each sample
location has been photographed with channel traces painted to indicate the
location and orientation of each sample. Samples are then shipped for analysis
to an ALS-certified assay laboratory in Toronto, Canada and Lima, Perú. The
samples were analyzed for gold using standard fire-assay on a 50-gram sample
with an AA finish. Multi-element geochemistry was determined by ICP-MS using
either aqua regia (ME-MS41) or four acid (ME-MS61) digestions. Blanks,
duplicates and certified reference standards are inserted into the sample
stream to monitor laboratory performance. Comparison to control samples and
their standard deviations indicates acceptable accuracy of the assays and no
detectible contamination. The remainder of the core is stored in a secured
storage facility for future assay verification.
Mr. Edwin Naranjo Sierra, FAusIMM, MSc, Senior geologist, Director of
Exploration for Soma Gold Corp is the Qualified Person, within the meaning of
NI 43-101. Mr. Naranjo is satisfied that the analytical procedures and best
practices used are standard industry methodologies, and he has reviewed and
approved the technical information disclosed in this news release.
ABOUT SOMA GOLD
Soma Gold Corp. (TSXV: SOMA) is a mining company focused on gold
production and exploration. The Company owns two adjacent mining properties in
Antioquia, Colombia with a combined milling capacity of 675 tpd. (permitted
for 1,400 tpd). The El Bagre Mill is currently operating and producing.
Internally generated funds are being used to finance a regional exploration
program.
The Company also owns an exploration and development property near
Tucuma, Para State, Brazil.
On behalf of the Board of Directors
"Javier Cordova Unda"Chief Executive Officer and President
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
All statements, analysis and other information contained in this press
release about anticipated future events or results constitute forward-looking
statements. Forward-looking statements are often, but not always, identified
by the use of words such as "seek", "anticipate", "believe", "plan",
"estimate", "expect" and "intend" and statements that an event or result
"may", "will", "should", "could" or "might" occur or be achieved and other
similar expressions. Forward-looking statements are subject to business and
economic risks and uncertainties and other factors that could cause actual
results of operations to differ materially from those contained in the
forward-looking statements. Forward-looking statements are based on estimates
and opinions of management at the date the statements are made. The Company
does not undertake any obligation to update forward-looking statements even if
circumstances or management's estimates or opinions should change except as
required by applicable laws. Investors should not place undue reliance on
forward-looking statements.
SOURCE Soma Gold Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/20/c2514.html

-0-                           04/20/2021
/For further information: please contact Andrea Laird, telephone:
+1-604-259-0302/
(SMAGF SOMA. 8PR1)

CO:  Soma Gold Corp.
ST:  British Columbia, Colombia
IN:  OTC MNG PRM
SU:

-30-