Source	Business Wire
Date	04/20/2021
Time	04:04:17 AM

Company	 RUPERT RESOURCES LTD.
Title	[EXTERNAL] Rupert Resources Drills 4.4g/t Gold Over 188m From 64m 
Including 8....





    CDNX Symbol: RUP











Press Release




April 20, 2021 11:03 UTC

Rupert Resources Drills 4.4g/t Gold Over 188m From 64m Including 8.9g/t Au Over 
23m and 3.8g/t Over 141m From 30m Including 8.2g/t Au Over 49m at Ikkari  

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Rupert Resources Ltd 

TSX VENTURE SYMBOL: RUP 

TORONTO--(BUSINESS WIRE)-- Rupert Resources Ltd (“Rupert” or “the Company”) 
reports new drill results from its Ikkari prospect, the focus of its ongoing 
60,000m exploration programme at the 100% owned Pahtavaara Project in the 
Central Lapland Greenstone Belt, Finland (figure 1). The mineralised strike 
length at Ikkari is at least 650m in total (figure 2) with mineralisation on 
all sections intersected to a depth of at least 300 to 500m. 

Highlights* 

Hole 121021 intersected 3.3g/t gold (“Au”) over 37m from 517m- 400m vertical 
depth a 100m vertical increase on that section
Hole 121023 intersected 3.0g/t Au over 42m from 331m, including 10.7g/t Au over 
9m 
Hole 121024 intersected 2.6g/t Au over 72m, from 86m 
Hole 121025 intersected 3.8g/t Au over 141m from 30m, including 8.2g/t Au over 
49m
Hole 121026 intersected 4.4g/t Au over 188m from 64m, including 8.9g/t Au over 
23m* with a further intercept of 1.5g/t Au over 66m from 365m 
Hole 121027 intersected 3.0g/t Au over 29mfrom 286m and 3.0g/t Au over 137mfrom 
327m  
Ikkari remains open at depth and along strike in both directions

* Highlight intercepts only, see tables 3 and 4 for full breakdown 

James Withall, CEO of Rupert Resources commented “Drill hole 121026 is the best 
intercept reported at Ikkari to date and together with the other headline drill 
holes released today further confirms the exceptional continuity and grade of 
the discovery over significant drill intercept lengths. Ikkari is emerging as 
one of the best new discoveries of this gold cycle with a near surface, high 
grade component allied with non-refractory metallurgy in a top tier 
jurisdiction in close proximity to infrastructure. Drilling continues at 
priority targets on our wholly owned 451km2 licence package in the Central 
Lapland Greenstone Belt.” 

Summary of new drill results 

The seven holes released today are from the central part of Ikkari from the 
ongoing infill and extension drill program. Results from hole 121026 represent 
the best intercept drilled at Ikkari to date, with consistent mineralisation 
across 188m downhole, and includes 19 individual meter samples over 10g/t Au 
(full assay log of this intercept in table 4). Mineralisation occurs at a 
structurally disrupted intersection of lithologies, with narrow interfingering 
of brittle sedimentary units and mineralised breccias within altered ultramafic 
rocks (figure 3). This intercept is overlain by robust mineralisation towards 
surface demonstrated by infill holes 121024 and 121025 (table 3). Results are 
pending for additional down-dip infill holes on this section. 

Results from holes 121023 and 121027 are from deeper holes on the previously 
reported infill section that included holes 121016 and 121019 (figure 4). The 
new holes demonstrate good continuity of the mineralised zone to 380m vertical 
depth on this section. These results also confirm the extent of the mineralised 
envelope on adjacent sections, including a high-grade component (table 3). 

Results from hole 121021 reported here, records the deepest intercept to date 
in the main part of the Ikkari mineralised system. At 425m vertical depth, the 
intercept of 3.3g/t Au over 37m includes a higher-grade component of 7.2g/t Au 
over 6m, as well as multiple other mineralised intercepts downhole (figure 3c) 
and demonstrates that the mineralising system remains open. 

Results from hole 121022 record mineralisation associated with altered 
ultramafic rocks in the western part of the deposit indicating that the Ikkari 
system persists along strike, although an interpreted key structure has not yet 
been intersected along this section. Recent base of till sampling completed in 
this area has indicated further high-grade anomalism to the west of drill hole 
121022 (figure 2) which will be drill tested along with a number of new 
anomalies in south west of the Heinä South target. 

Table 1. Headline assay results from Ikkari (20 April 2021) 


Hole ID  
	
	From (m) 
		
		To (m) 
			
			Interval (m) 
				
				Grade Au g/t 
				

121027 
	
	286.0 
		
		315.0 
			
			29.0 
				
				3.7 
				

121027 
	
	327.0 
		
		464.0 
			
			137.0 
				
				3.0 
				

121026 
	
	64.0 
		
		252.0 
			
			188.0 
				
				4.4 
				

121025 
	
	30.0 
		
		171.0 
			
			141.0 
				
				3.8 
				

121024 
	
	86.0 
		
		159.1* 
			
			73.1 
				
				2.6 
				

121023 
	
	331.0 
		
		373.0 
			
			42.0 
				
				3.7 
				

121021 
	
	517.0 
		
		554.0 
			
			37.0 
				
				3.3 
				

Notes to table: No upper cut-off grade and a 0.4g/t Au lower cut-off applied. 
Unless specified, true widths cannot be accurately determined from the 
information available. Full breakdown of new holes with “includings” in Table 
3. Refer to this link for spreadsheet of previously released drilling 
intercepts. *hole collapsed and ended in mineralisation 

Drilling continues with further infill sections being completed across the 
deposit, as well as selected deeper holes, that will contribute to a resource 
estimation later in the year. To date, 29,000 metres have been drilled at 
Ikkari in 83 holes, with results reported for 67 holes. Drilling is also 
ongoing at other Area 1 prospects as part of the continuing new target 
generation programme. 

Table 2. Collar locations of new drill holes 


Hole ID
	
	Prospect 
		
		Easting
			
			Northing 
				
				Elevation 
					
					Azimuth
						
						Dip 
							
							EOH (m)
							

121027 
	
	Ikkari 
		
		454171.8 
			
			7496692.2 
				
				226.4 
					
					330.7 
						
						-57.2 
							
							556.0 
							

121026 
	
	Ikkari 
		
		454061.1 
			
			7496739.8 
				
				224.7 
					
					331.9 
						
						-51.3 
							
							484.3 
							

121025 
	
	Ikkari 
		
		454036.0 
			
			7496794.0 
				
				224.5 
					
					333.5 
						
						-52.2 
							
							364.1 
							

121024 
	
	Ikkari 
		
		454022.9 
			
			7496821.6 
				
				224.3 
					
					338.1 
						
						-50.1 
							
							159.1 
							

121023 
	
	Ikkari 
		
		454159.1 
			
			7496718.9 
				
				225.9 
					
					336.0 
						
						-53.8 
							
							461.3 
							

121022 
	
	Ikkari 
		
		453689.6 
			
			7496839.2 
				
				226 
					
					152.7 
						
						-48.2 
							
							275.3 
							

121021 
	
	Ikkari 
		
		454256.2 
			
			7496606.8 
				
				230.9 
					
					334.1 
						
						-52.3 
							
							649.8 
							

Notes to table: The coordinates are in ETRS89 Z35 and all holes are surveyed at 
3m intervals downhole and all core is orientated. 

Geological description of the Ikkari Discovery 

Mineralisation at Ikkari is characterised by intense alteration and 
deformation. Gold is associated with fine-grained disseminated pyrite within 
planar quartz-carbonate veins and / or disseminated in the host rocks, commonly 
as fine-grained visible gold. Mineralisation is hosted by sedimentary rocks 
overprinted by albite-sericite alteration, and strongly foliated 
chlorite-altered mafic-ultramafic rocks. A broader, variably mineralised 
alteration zone comprising magnetite ± hematite ± tourmaline ± K-feldspar ± 
fuchsite is also present. Holes demonstrate strong foliation, shearing, and 
veining that is predominantly parallel to the dominant structural fabric and 
gold appears to be concentrated in sedimentary intercalations associated with 
zones of structural disruption at lithological boundaries, represented by 
irregular, cross-cutting vein associations and brittle fracture in 
albite-altered rocks. The regional structural data collected so far suggest a 
subvertical, broad and linear structure, within which cross-cutting fractures 
and variably dipping lithologies, as well as possibly folded bedding, appear to 
have controlled the introduction of gold-bearing fluids and associated 
alteration zones. In general, alteration and structure appear to be 
sub-vertical, with lithologies generally dipping ~70 degrees north. 

Review by Qualified Person, Quality Control and Reports  

Dr Charlotte Seabrook, MAIG, RPGeo. Exploration Manager is the Qualified Person 
as defined by National Instrument 43-101 responsible for the accuracy of 
scientific and technical information in this news release. 

Samples are prepared by ALS Finland in Sodankylä and assayed in ALS 
laboratories in Ireland, Romania or Sweden. All samples are under watch from 
the drill site to the storage facility. Samples are assayed using fire assay 
method with aqua regia digest and analysis by AAS for gold. Over limit analysis 
for >10 ppm Au is conducted using fire assay and gravimetric finish for assays 
over >100ppm Au. For hole 120071 all mineralised samples were submitted for 
screen fire assays with gravimetric finish. For multi-element assays Ultra 
Trace Level Method by HF-HNO3-HClO4 acid digestion, HCl leach and a combination 
of ICP-MS and ICP-AES is used. The Company’s QA/QC program includes the regular 
insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. Standards, blanks and duplicates are inserted at 
appropriate intervals. Approximately five percent (5%) of the pulps and rejects 
are sent for check assaying at a second lab. 

Base of till samples are prepared in ALS Sodankylä by dry-sieving method 
prep-41, and assayed by fire assay with ICP-AES finish for gold. Multi-elements 
are assayed in ALS laboratories in either of Ireland, Romania or Sweden by aqua 
regia with ICP-MS finish. Rupert maintains a strict chain of custody procedure 
to manage the handling of all samples. The Company’s QA/QC program includes the 
regular insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. 

About Rupert 

Rupert is a Canadian based gold exploration and development company that is 
listed on the TSX Venture Exchange under the symbol “RUP”. The Company owns the 
Pahtavaara gold mine, mill, and exploration permits and concessions located in 
the Central Lapland Greenstone Belt in Northern Finland (“Pahtavaara”). 
Pahtavaara previously produced over 420koz of gold and 474koz remains in an 
Inferred mineral resource (4.6 Mt at a grade of 3.2 g/t Au at a 1.5 g/t Au 
cut-off grade, see the technical report entitled “NI 43-101 Technical Report: 
Pahtavaara Project, Finland” with an effective date of April 16, 2018, prepared 
by Brian Wolfe, Principal Consultant, International Resource Solutions Pty 
Ltd., an independent qualified person under National Instrument 43-101 – 
Standards of Disclosure for Mineral Projects). The Company also holds a 100% 
interest in the Surf Inlet Property in British Columbia, a 100% interest in 
properties in Central Finland and a 20% carried participating interest in the 
Gold Centre property located adjacent to the Red Lake mine in Ontario. 

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release. 

Cautionary Note Regarding Forward Looking Statements  

This press release contains statements which, other than statements of 
historical fact constitute “forward-looking statements” within the meaning of 
applicable securities laws, including statements with respect to: results of 
exploration activities, mineral resources. The words “may”, “would”, “could”, 
“will”, “intend”, “plan”, “anticipate”, “believe”, “estimate”, “expect” and 
similar expressions, as they relate to the Company, are intended to identify 
such forward-looking statements. Investors are cautioned that forward-looking 
statements are based on the opinions, assumptions and estimates of management 
considered reasonable at the date the statements are made, and are inherently 
subject to a variety of risks and uncertainties and other known and unknown 
factors that could cause actual events or results to differ materially from 
those projected in the forward-looking statements. These factors include the 
general risks of the mining industry, as well as those risk factors discussed 
or referred to in the Company's annual Management's Discussion and Analysis for 
the year ended February 29, 2020 available at www.sedar.com. Should one or more 
of these risks or uncertainties materialize, or should assumptions underlying 
the forward-looking statements prove incorrect, actual results may vary 
materially from those described herein as intended, planned, anticipated, 
believed, estimated or expected. Although the Company has attempted to identify 
important factors that could cause actual actions, events or results to differ 
materially from those described in forward-looking information, there may be 
other factors that cause actions, events or results not to be as anticipated, 
estimated or intended. There can be no assurance that such information will 
prove to be accurate as actual results and future events could differ 
materially from those anticipated in such statements. The Company does not 
intend, and does not assume any obligation, to update these forward-looking 
statements except as otherwise required by applicable law.  

  

										
										
 APPENDIX  
										
										
										
Table 3. New Intercepts at Ikkari 
										

Hole ID  
	 	
		  
			 	
				From (m) 
					 	
						To (m) 
							 	
								Interval (m) 
									
 	
										
Grade Au g/t 
										

121027 
	
	  
		
		  
			
			  
				
				263.0 
					
					  
						
						264.0 
							
							  
								
								1.0 
									
									  
										
										
2.7 
										

  
	
	  
		
		  
			
			  
				
				286.0 
					
					  
						
						315.0 
							
							  
								
								29.0 
									
									  
										
										
3.7 
										

  
	
	  
		
		including 
			
			  
				
				294.0 
					
					  
						
						295.0 
							
							  
								
								1.0 


April 20, 2021 11:03 UTC

Rupert Resources Drills 4.4g/t Gold Over 188m From 64m Including 8.9g/t Au Over 
23m and 3.8g/t Over 141m From 30m Including 8.2g/t Au Over 49m at Ikkari  

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Rupert Resources Ltd 

TSX VENTURE SYMBOL: RUP 

TORONTO--(BUSINESS WIRE)-- Rupert Resources Ltd (“Rupert” or “the Company”) 
reports new drill results from its Ikkari prospect, the focus of its ongoing 
60,000m exploration programme at the 100% owned Pahtavaara Project in the 
Central Lapland Greenstone Belt, Finland (figure 1). The mineralised strike 
length at Ikkari is at least 650m in total (figure 2) with mineralisation on 
all sections intersected to a depth of at least 300 to 500m. 

Highlights* 

Hole 121021 intersected 3.3g/t gold (“Au”) over 37m from 517m- 400m vertical 
depth a 100m vertical increase on that section
Hole 121023 intersected 3.0g/t Au over 42m from 331m, including 10.7g/t Au over 
9m 
Hole 121024 intersected 2.6g/t Au over 72m, from 86m 
Hole 121025 intersected 3.8g/t Au over 141m from 30m, including 8.2g/t Au over 
49m
Hole 121026 intersected 4.4g/t Au over 188m from 64m, including 8.9g/t Au over 
23m* with a further intercept of 1.5g/t Au over 66m from 365m 
Hole 121027 intersected 3.0g/t Au over 29mfrom 286m and 3.0g/t Au over 137mfrom 
327m  
Ikkari remains open at depth and along strike in both directions

* Highlight intercepts only, see tables 3 and 4 for full breakdown 

James Withall, CEO of Rupert Resources commented “Drill hole 121026 is the best 
intercept reported at Ikkari to date and together with the other headline drill 
holes released today further confirms the exceptional continuity and grade of 
the discovery over significant drill intercept lengths. Ikkari is emerging as 
one of the best new discoveries of this gold cycle with a near surface, high 
grade component allied with non-refractory metallurgy in a top tier 
jurisdiction in close proximity to infrastructure. Drilling continues at 
priority targets on our wholly owned 451km2 licence package in the Central 
Lapland Greenstone Belt.” 

Summary of new drill results 

The seven holes released today are from the central part of Ikkari from the 
ongoing infill and extension drill program. Results from hole 121026 represent 
the best intercept drilled at Ikkari to date, with consistent mineralisation 
across 188m downhole, and includes 19 individual meter samples over 10g/t Au 
(full assay log of this intercept in table 4). Mineralisation occurs at a 
structurally disrupted intersection of lithologies, with narrow interfingering 
of brittle sedimentary units and mineralised breccias within altered ultramafic 
rocks (figure 3). This intercept is overlain by robust mineralisation towards 
surface demonstrated by infill holes 121024 and 121025 (table 3). Results are 
pending for additional down-dip infill holes on this section. 

Results from holes 121023 and 121027 are from deeper holes on the previously 
reported infill section that included holes 121016 and 121019 (figure 4). The 
new holes demonstrate good continuity of the mineralised zone to 380m vertical 
depth on this section. These results also confirm the extent of the mineralised 
envelope on adjacent sections, including a high-grade component (table 3). 

Results from hole 121021 reported here, records the deepest intercept to date 
in the main part of the Ikkari mineralised system. At 425m vertical depth, the 
intercept of 3.3g/t Au over 37m includes a higher-grade component of 7.2g/t Au 
over 6m, as well as multiple other mineralised intercepts downhole (figure 3c) 
and demonstrates that the mineralising system remains open. 

Results from hole 121022 record mineralisation associated with altered 
ultramafic rocks in the western part of the deposit indicating that the Ikkari 
system persists along strike, although an interpreted key structure has not yet 
been intersected along this section. Recent base of till sampling completed in 
this area has indicated further high-grade anomalism to the west of drill hole 
121022 (figure 2) which will be drill tested along with a number of new 
anomalies in south west of the Heinä South target. 

Table 1. Headline assay results from Ikkari (20 April 2021) 


Hole ID  

	From (m) 
	
		To (m) 
		
			Interval (m) 
			
				Grade Au g/t 
				

121027 

	286.0 
	
		315.0 
		
			29.0 
			
				3.7 
				

121027 

	327.0 
	
		464.0 
		
			137.0 
			
				3.0 
				

121026 

	64.0 
	
		252.0 
		
			188.0 
			
				4.4 
				

121025 

	30.0 
	
		171.0 
		
			141.0 
			
				3.8 
				

121024 

	86.0 
	
		159.1* 
		
			73.1 
			
				2.6 
				

121023 

	331.0 
	
		373.0 
		
			42.0 
			
				3.7 
				

121021 

	517.0 
	
		554.0 
		
			37.0 
			
				3.3 
				

Notes to table: No upper cut-off grade and a 0.4g/t Au lower cut-off applied. 
Unless specified, true widths cannot be accurately determined from the 
information available. Full breakdown of new holes with “includings” in Table 
3. Refer to this link for spreadsheet of previously released drilling 
intercepts. *hole collapsed and ended in mineralisation 

Drilling continues with further infill sections being completed across the 
deposit, as well as selected deeper holes, that will contribute to a resource 
estimation later in the year. To date, 29,000 metres have been drilled at 
Ikkari in 83 holes, with results reported for 67 holes. Drilling is also 
ongoing at other Area 1 prospects as part of the continuing new target 
generation programme. 

Table 2. Collar locations of new drill holes 


Hole ID

	Prospect 
	
		Easting
		
			Northing 
			
				Elevation 
				
					Azimuth
					
						Dip 
						
							EOH (m)
							

121027 

	Ikkari 
	
		454171.8 
		
			7496692.2 
			
				226.4 
				
					330.7 
					
						-57.2 
						
							556.0 
							

121026 

	Ikkari 
	
		454061.1 
		
			7496739.8 
			
				224.7 
				
					331.9 
					
						-51.3 
						
							484.3 
							

121025 

	Ikkari 
	
		454036.0 
		
			7496794.0 
			
				224.5 
				
					333.5 
					
						-52.2 
						
							364.1 
							

121024 

	Ikkari 
	
		454022.9 
		
			7496821.6 
			
				224.3 
				
					338.1 
					
						-50.1 
						
							159.1 
							

121023 

	Ikkari 
	
		454159.1 
		
			7496718.9 
			
				225.9 
				
					336.0 
					
						-53.8 
						
							461.3 
							

121022 

	Ikkari 
	
		453689.6 
		
			7496839.2 
			
				226 
				
					152.7 
					
						-48.2 
						
							275.3 
							

121021 

	Ikkari 
	
		454256.2 
		
			7496606.8 
			
				230.9 
				
					334.1 
					
						-52.3 
						
							649.8 
							

Notes to table: The coordinates are in ETRS89 Z35 and all holes are surveyed at 
3m intervals downhole and all core is orientated. 

Geological description of the Ikkari Discovery 

Mineralisation at Ikkari is characterised by intense alteration and 
deformation. Gold is associated with fine-grained disseminated pyrite within 
planar quartz-carbonate veins and / or disseminated in the host rocks, commonly 
as fine-grained visible gold. Mineralisation is hosted by sedimentary rocks 
overprinted by albite-sericite alteration, and strongly foliated 
chlorite-altered mafic-ultramafic rocks. A broader, variably mineralised 
alteration zone comprising magnetite ± hematite ± tourmaline ± K-feldspar ± 
fuchsite is also present. Holes demonstrate strong foliation, shearing, and 
veining that is predominantly parallel to the dominant structural fabric and 
gold appears to be concentrated in sedimentary intercalations associated with 
zones of structural disruption at lithological boundaries, represented by 
irregular, cross-cutting vein associations and brittle fracture in 
albite-altered rocks. The regional structural data collected so far suggest a 
subvertical, broad and linear structure, within which cross-cutting fractures 
and variably dipping lithologies, as well as possibly folded bedding, appear to 
have controlled the introduction of gold-bearing fluids and associated 
alteration zones. In general, alteration and structure appear to be 
sub-vertical, with lithologies generally dipping ~70 degrees north. 

Review by Qualified Person, Quality Control and Reports  

Dr Charlotte Seabrook, MAIG, RPGeo. Exploration Manager is the Qualified Person 
as defined by National Instrument 43-101 responsible for the accuracy of 
scientific and technical information in this news release. 

Samples are prepared by ALS Finland in Sodankylä and assayed in ALS 
laboratories in Ireland, Romania or Sweden. All samples are under watch from 
the drill site to the storage facility. Samples are assayed using fire assay 
method with aqua regia digest and analysis by AAS for gold. Over limit analysis 
for >10 ppm Au is conducted using fire assay and gravimetric finish for assays 
over >100ppm Au. For hole 120071 all mineralised samples were submitted for 
screen fire assays with gravimetric finish. For multi-element assays Ultra 
Trace Level Method by HF-HNO3-HClO4 acid digestion, HCl leach and a combination 
of ICP-MS and ICP-AES is used. The Company’s QA/QC program includes the regular 
insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. Standards, blanks and duplicates are inserted at 
appropriate intervals. Approximately five percent (5%) of the pulps and rejects 
are sent for check assaying at a second lab. 

Base of till samples are prepared in ALS Sodankylä by dry-sieving method 
prep-41, and assayed by fire assay with ICP-AES finish for gold. Multi-elements 
are assayed in ALS laboratories in either of Ireland, Romania or Sweden by aqua 
regia with ICP-MS finish. Rupert maintains a strict chain of custody procedure 
to manage the handling of all samples. The Company’s QA/QC program includes the 
regular insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. 

About Rupert 

Rupert is a Canadian based gold exploration and development company that is 
listed on the TSX Venture Exchange under the symbol “RUP”. The Company owns the 
Pahtavaara gold mine, mill, and exploration permits and concessions located in 
the Central Lapland Greenstone Belt in Northern Finland (“Pahtavaara”). 
Pahtavaara previously produced over 420koz of gold and 474koz remains in an 
Inferred mineral resource (4.6 Mt at a grade of 3.2 g/t Au at a 1.5 g/t Au 
cut-off grade, see the technical report entitled “NI 43-101 Technical Report: 
Pahtavaara Project, Finland” with an effective date of April 16, 2018, prepared 
by Brian Wolfe, Principal Consultant, International Resource Solutions Pty 
Ltd., an independent qualified person under National Instrument 43-101 – 
Standards of Disclosure for Mineral Projects). The Company also holds a 100% 
interest in the Surf Inlet Property in British Columbia, a 100% interest in 
properties in Central Finland and a 20% carried participating interest in the 
Gold Centre property located adjacent to the Red Lake mine in Ontario. 

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release. 

Cautionary Note Regarding Forward Looking Statements  

This press release contains statements which, other than statements of 
historical fact constitute “forward-looking statements” within the meaning of 
applicable securities laws, including statements with respect to: results of 
exploration activities, mineral resources. The words “may”, “would”, “could”, 
“will”, “intend”, “plan”, “anticipate”, “believe”, “estimate”, “expect” and 
similar expressions, as they relate to the Company, are intended to identify 
such forward-looking statements. Investors are cautioned that forward-looking 
statements are based on the opinions, assumptions and estimates of management 
considered reasonable at the date the statements are made, and are inherently 
subject to a variety of risks and uncertainties and other known and unknown 
factors that could cause actual events or results to differ materially from 
those projected in the forward-looking statements. These factors include the 
general risks of the mining industry, as well as those risk factors discussed 
or referred to in the Company's annual Management's Discussion and Analysis for 
the year ended February 29, 2020 available at www.sedar.com. Should one or more 
of these risks or uncertainties materialize, or should assumptions underlying 
the forward-looking statements prove incorrect, actual results may vary 
materially from those described herein as intended, planned, anticipated, 
believed, estimated or expected. Although the Company has attempted to identify 
important factors that could cause actual actions, events or results to differ 
materially from those described in forward-looking information, there may be 
other factors that cause actions, events or results not to be as anticipated, 
estimated or intended. There can be no assurance that such information will 
prove to be accurate as actual results and future events could differ 
materially from those anticipated in such statements. The Company does not 
intend, and does not assume any obligation, to update these forward-looking 
statements except as otherwise required by applicable law.  

  

									
 APPENDIX  

									
Table 3. New Intercepts at Ikkari 


Hole ID  
	 
		  
			 
				From (m) 
					 
						To (m) 
							 
								Interval (m) 
									 
										Grade Au g/t 
										

121027 

	  
	
		  
		
			  
			
				263.0 
				
					  
					
						264.0 
						
							  
							
								1.0 
								
									  
									
										2.7 
										

  

	  
	
		  
		
			  
			
				286.0 
				
					  
					
						315.0 
						
							  
							
								29.0 
								
									  
									
										3.7 
										

  

	  
	
		including 
		
			  
			
				294.0 
				
					  
					
						295.0 
						
							  
							
								1.0 
								
									  
									
										17.4 
										

  

	  
	
		including 
		
			  
			
				299.0 
				
					  
					
						300.0 
						
							  
							
								1.0 
								
									  
									
										11.0 
										

  

	  
	
		  
		
			  
			
				327.0 
				
					  
					
						464.0 
						
							  
							
								137.0 
								
									  
									
										3.0 
										

  

	  
	
		including 
		
			  
			
				331.0 
				
					  
					
						332.0 
						
							  
							
								1.0 
								
									  
									
										7.1 
										

  

	  
	
		including 
		
			  
			
				335.0 
				
					  
					
						336.0 
						
							  
							
								1.0 
								
									  
									
										8.9 
										

  

	  
	
		including 
		
			  
			
				350.0 
				
					  
					
						351.0 
						
							  
							
								1.0 
								
									  
									
										10.6 
										

  

	  
	
		including 
		
			  
			
				380.0 
				
					  
					
						387.0 
						
							  
							
								7.0 
								
									  
									
										8.4 
										

  

	  
	
		and including 
		
			  
			
				385.0 
				
					  
					
						387.0 
						
							  
							
								2.0 
								
									  
									
										20.3 
										

  

	  
	
		including 
		
			  
			
				410.0 
				
					  
					
						411.0 
						
							  
							
								1.0 
								
									  
									
										6.7 
										

  

	  
	
		including 
		
			  
			
				430.0 
				
					  
					
						431.0 
						
							  
							
								1.0 
								
									  
									
										21.8 
										

  

	  
	
		including 
		
			  
			
				442.0 
				
					  
					
						444.0 
						
							  
							
								2.0 
								
									  
									
										12.4 
										

  

	  
	
		Including 
		
			  
			
				456.0 
				
					  
					
						457.0 
						
							  
							
								1.0 
								
									  
									
										17.9 
										

  

	  
	
		  
		
			  
			
				480.0 
				
					  
					
						482.0 
						
							  
							
								2.0 
								
									  
									
										1.7 
										

  

	  
	
		  
		
			  
			
				509.0 
				
					  
					
						510.0 
						
							  
							
								1.0 
								
									  
									
										2.8 
										

121026 

	  
	
		  
		
			  
			
				64.0 
				
					  
					
						252.0 
						
							  
							
								188.0 
								
									  
									
										4.4 
										

  

	  
	
		including 
		
			  
			
				82.0 
				
					  
					
						84.0 
						
							  
							
								2.0 
								
									  
									
										11.1 
										

  

	  
	
		including 
		
			  
			
				119.0 
				
					  
					
						129.0 
						
							  
							
								10.0 
								
									  
									
										8.6 
										

  

	  
	
		and including 
		
			  
			
				128.0 
				
					  
					
						129.0 
						
							  
							
								1.0 
								
									  
									
										18.2 
										

  

	  
	
		including 
		
			  
			
				138.7 
				
					  
					
						140.0 
						
							  
							
								1.3 
								
									  
									
										14.6 
										

  

	  
	
		including 
		
			  
			
				151.0 
				
					  
					
						174.0 
						
							  
							
								23.0 
								
									  
									
										8.9 
										

  

	  
	
		and including 
		
			  
			
				157.0 
				
					  
					
						158.0 
						
							  
							
								1.0 
								
									  
									
										19.6 
										

  

	  
	
		and including 
		
			  
			
				167.0 
				
					  
					
						168.0 
						
							  
							
								1.0 
								
									  
									
										25.7 
										

  

	  
	
		and including 
		
			  
			
				173.0 
				
					  
					
						174.0 
						
							  
							
								1.0 
								
									  
									
										25.2 
										

  

	  
	
		including 
		
			  
			
				191.0 
				
					  
					
						192.0 
						
							  
							
								1.0 
								
									  
									
										10.7 
										

  

	  
	
		including 
		
			  
			
				206.0 
				
					  
					
						208.0 
						
							  
							
								2.0 
								
									  
									
										17.5 
										

  

	  
	
		including 
		
			  
			
				246.0 
				
					  
					
						247.0 
						
							  
							
								1.0 
								
									  
									
										24.4 
										

  

	  
	
		  
		
			  
			
				303.0 
				
					  
					
						317.0 
						
							  
							
								14.0 
								
									  
									
										1.8 
										

  

	  
	
		including 
		
			  
			
				303.0 
				
					  
					
						304.0 
						
							  
							
								1.0 
								
									  
									
										5.9 
										

  

	  
	
		  
		
			  
			
				322.0 
				
					  
					
						323.0 
						
							  
							
								1.0 
								
									  
									
										3.6 
										

  

	  
	
		  
		
			  
			
				340.0 
				
					  
					
						341.0 
						
							  
							
								1.0 
								
									  
									
										3.3 
										

  

	  
	
		  
		
			  
			
				349.0 
				
					  
					
						350.0 
						
							  
							
								1.0 
								
									  
									
										3.4 
										

  

	  
	
		  
		
			  
			
				359.0 
				
					  
					
						361.0 
						
							  
							
								2.0 
								
									  
									
										1.1 
										

  

	  
	
		  
		
			  
			
				365.0 
				
					  
					
						431.0 
						
							  
							
								66.0 
								
									  
									
										1.5 
										

  

	  
	
		including 
		
			  
			
				368.0 
				
					  
					
						390.0 
						
							  
							
								22.0 
								
									  
									
										3.3 
										

  

	  
	
		and including 
		
			  
			
				369.0 
				
					  
					
						371.0 
						
							  
							
								2.0 
								
									  
									
										19.7 
										

  

	  
	
		  
		
			  
			
				477.0 
				
					  
					
						479.0 
						
							  
							
								2.0 
								
									  
									
										1.3 
										

121025 

	  
	
		  
		
			  
			
				30.0 
				
					  
					
						171.0 
						
							  
							
								141.0 
								
									  
									
										3.8 
										

  

	  
	
		including 
		
			  
			
				42.0 
				
					  
					
						91.0 
						
							  
							
								49.0 
								
									  
									
										7.5 
										

  

	  
	
		and including 
		
			  
			
				42.0 
				
					  
					
						46.6 
						
							  
							
								4.6 
								
									  
									
										15.6 
										

  

	  
	
		and including 
		
			  
			
				52.0 
				
					  
					
						61.0 
						
							  
							
								9.0 
								
									  
									
										13.5 
										

  

	  
	
		and including 
		
			  
			
				68.0 
				
					  
					
						69.0 
						
							  
							
								1.0 
								
									  
									
										17.5 
										

  

	  
	
		and including 
		
			  
			
				80.0 
				
					  
					
						81.0 
						
							  
							
								1.0 
								
									  
									
										19.2 
										

  

	  
	
		including 
		
			  
			
				134.0 
				
					  
					
						135.0 
						
							  
							
								1.0 
								
									  
									
										20.6 
										

  

	  
	
		including 
		
			  
			
				157.0 
				
					  

						158.0 
						
							  
							
								1.0 
								
									  
									
										12.1 
										

  

	  
	
		including 
		
			  
			
				168.0 
				
					  
					
						169.0 
						
							  
							
								1.0 
								
									  
									
										15.0 
										

  

	  
	
		  
		
			  
			
				202.0 
				
					  
					
						351.0 
						
							  
							
								149.0 
								
									  
									
										1.2 
										

  

	  
	
		including 
		
			  
			
				251.0 
				
					  
					
						252.0 
						
							  
							
								1.0 
								
									  
									
										5.6 
										

  

	  
	
		including 
		
			  
			
				259.0 
				
					  
					
						263.0 
						
							  
							
								4.0 
								
									  
									
										4.1 
										

  

	  
	
		including 
		
			  
			
				280.0 
				
					  
					
						281.0 
						
							  
							
								1.0 
								
									  
									
										4.2 
										

  

	  
	
		including 
		
			  
			
				298.0 
				
					  
					
						299.0 
						
							  
							
								1.0 
								
									  
									
										4.1 
										

121024 

	  
	
		  
		
			  
			
				28.9 
				
					  
					
						32.0 
						
							  
							
								3.1 
								
									  
									
										0.7 
										

  

	  
	
		  
		
			  
			
				38.0 
				
					  
					
						62.0 
						
							  
							
								24.0 
								
									  
									
										2.4 
										

  

	  
	
		including 
		
			  
			
				43.0 
				
					  
					
						45.0 
						
							  
							
								2.0 
								
									  
									
										8.9 
										

  

	  
	
		including 
		
			  
			
				61.0 
				
					  
					
						62.0 
						
							  
							
								1.0 
								
									  
									
										21.3 
										

  

	  
	
		  
		
			  
			
				72.0 
				
					  
					
						76.0 
						
							  
							
								4.0 
								
									  
									
										0.6 
										

  

	  
	
		  
		
			  
			
				86.0 
				
					  
					
						159.1* 
						
							  
							
								73.1 
								
									  
									
										2.6 
										

  

	  
	
		including 
		
			  
			
				101.0 
				
					  
					
						103.0 
						
							  
							
								2.0 
								
									  
									
										15.5 
										

  

	  
	
		including 
		
			  
			
				110.0 
				
					  
					
						111.0 
						
							  
							
								1.0 
								
									  
									
										10.1 
										

  

	  
	
		including 
		
			  
			
				116.0 
				
					  
					
						117.0 
						
							  
							
								1.0 
								
									  
									
										8.7 
										

  

	  
	
		including 
		
			  
			
				135.0 
				
					  
					
						136.0 
						
							  
							
								1.0 
								
									  
									
										9.0 
										

  

	  
	
		including 
		
			  
			
				151.0 
				
					  
					
						152.0 
						
							  
							
								1.0 
								
									  
									
										9.0 
										

121023 

	  
	
		  
		
			  
			
				18.2 
				
					  
					
						52.0 
						
							  
							
								33.8 
								
									  
									
										1.2 
										

  

	  
	
		including 
		
			  
			
				19.0 
				
					  
					
						21.8 
						
							  
							
								2.8 
								
									  
									
										6.4 
										

  

	  
	
		including 
		
			  
			
				32.0 
				
					  
					
						33.0 
						
							  
							
								1.0 
								
									  
									
										5.6 
										

  

	  
	
		including 
		
			  
			
				51.0 
				
					  
					
						52.0 
						
							  
							
								1.0 
								
									  
									
										14.1 
										

  

	  
	
		  
		
			  
			
				220.0 
				
					  
					
						224.0 
						
							  
							
								4.0 
								
									  
									
										2.5 
										

  

	  
	
		  
		
			  
			
				253.0 
				
					  
					
						256.0 
						
							  
							
								3.0 
								
									  
									
										0.7 
										

  

	  
	
		  
		
			  
			
				238.0 
				
					  
					
						289.0 
						
							  
							
								1.0 
								
									  
									
										2.5 
										

  

	  
	
		  
		
			  
			
				294.0 
				
					  
					
						320.0 
						
							  
							
								26.0 
								
									  
									
										3.5 
										

  

	  
	
		including 
		
			  
			
				308.0 
				
					  
					
						309.0 
						
							  
							
								1.0 
								
									  
									
										19.4 
										

  

	  
	
		including 
		
			  
			
				318.0 
				
					  
					
						319.0 
						
							  
							
								1.0 
								
									  
									
										28.3 
										

  

	  
	
		  
		
			  
			
				331.0 
				
					  
					
						373.0 
						
							  
							
								42.0 
								
									  
									
										3.7 
										

  

	  
	
		including 
		
			  
			
				335.0 
				
					  
					
						344.0 
						
							  
							
								9.0 
								
									  
									
										10.7 
										

  

	  
	
		and including 
		
			  
			
				335.0 
				
					  
					
						336.0 
						
							  
							
								1.0 
								
									  
									
										24.1 
										

  

	  
	
		  
		
			  
			
				421.0 
				
					  
					
						422.0 
						
							  
							
								1.0 
								
									  
									
										1.7 
										

121022 

	  
	
		  
		
			  
			
				27.0 
				
					  
					
						28.0 
						
							  
							
								1.0 
								
									  
									
										1.2 
										

  

	  
	
		  
		
			  
			
				86.0 
				
					  
					
						87.0 
						
							  
							
								1.0 
								
									  
									
										1.3 
										

  

	  
	
		  
		
			  
			
				243.0 
				
					  
					
						245.0 
						
							  
							
								2.0 
								
									  
									
										0.6 
										

121021 

	  
	
		  
		
			  
			
				279.0 
				
					  
					
						281.0 
						
							  
							
								2.0 
								
									  
									
										5.8 
										

  

	  
	
		  
		
			  
			
				294.0 
				
					  
					
						297.0 
						
							  
							
								3.0 
								
									  
									
										9.7 
										

  

	  
	
		including 
		
			  
			
				295.0 
				
					  
					
						296.0 
						
							  
							
								1.0 
								
									  
									
										27.6 
										

  

	  
	
		  
		
			  
			
				313.0 
				
					  
					
						371.0 
						
							  
							
								58.0 
								
									  
									
										0.8 
										

  

	  
	
		including 
		
			  
			
				315.0 
				
					  
					
						318.0 
						
							  
							
								3.0 
								
									  
									
										6.7 
										

  

	  
	
		and including 
		
			  
			
				317.0 
				
					  
					
						318.0 
						
							  
							
								1.0 
								
									  
									
										15.2 
										

  

	  
	
		including 
		
			  
			
				346.0 
				
					  
					
						350.0 
						
							  
							
								4.0 
								
									  
									
										2.1 
										

  

	  
	
		including 
		
			  
			
				360.0 
				
					  
					
						362.0 
						
							  
							
								2.0 
								
									  
									
										2.2 
										

  

	  
	
		  
		
			  
			
				408.0 
				
					  
					
						482.0 
						
							  
							
								74.0 
								
									  
									
										1.4 
										

  

	  
	
		including 
		
			  
			
				426.0 
				
					  
					
						427.0 
						
							  
							
								1.0 
								
									  
									
										6.6 
										

  

	  
	
		including 
		
			  
			
				433.0 
				
					  
					
						447.0 
						
							  
							
								14.0 
								
									  
									
										2.9 
										

  

	  
	
		and including 
		
			  
			
				433.0 
				
					  
					
						434.0 
						
							  
							
								1.0 
								
									  
									
										12.7 
										

  

	  
	
		including 
		
			  
			
				467.0 
				
					  
					
						475.0 
						
							  
							
								8.0 
								
									  
									
										2.9 
										

  

	  
	
		and including 
		
			  
			
				472.0 
				
					  
					
						473.0 
						
							  
							
								1.0 
								
									  
									
										9.3 
										

  

	  
	
		  
		
			  
			
				517.0 
				
					  
					
						554.0 
						
							  
							
								37.0 
								
									  
									
										3.3 
										

  

	  
	
		including 
		
			  
			
				525.0 
				
					  
					
						532.0 
						
							  
							
								6.0 
								
									  
									
										7.2 
										

  

	  
	
		including 
		
			  
			
				537.0 
				
					  
					
						538.0 
						
							  
							
								1.0 
								
									  
									
										9.2 
										

  

	  
	
		including 
		
			  
			
				553.0 
				
					  
					
						554.0 
						
							  
							
								1.0 
								
									  
									
										15.0 
										

No upper cut-off grade and a 0.4g/t Au lower cut-off applied. Unless specified, 
true widths cannot be accurately determined from the information available. 
Bold intervals referred to in text of release. Refer to this spreadsheet for 
details of previously released drilling intercepts. Eoh – End of Hole. * hole 
collapsed and ended in mineralisation 

Table 4. Uncut mineralised intercept of 4.4g/t Au over 188m in drill hole 121026


From (m)  
	 
		To (m) 
			 
				Int (m)  
					 
						Au (g/t)  
						

64.0 
	 
		65.0 
			 
				1.0 
					 
						1.5 
						

65.0 
	 
		66.0 
			 
				1.0 
					 
						0.4 
						

66.0 
	 
		67.0 
			 
				1.0 
					 
						0.9 
						

67.0 
	 
		68.0 
			 
				1.0 
					 
						2.6 
						

68.0 
																																																																																																																																																																																																																																																											 
		69.0 
			 
				1.0 
					 
						3.9 
						

69.0 
	 
		70.0 
			 
				1.0 
					 
						0.3 
						

70.0 
	 
		71.0 
			 
				1.0 
					 
						1.2 
						

71.0 
	 
		72.0 
			 
				1.0 
					 
						0.5 
						

72.0 
	 
		73.0 
			 
				1.0 
					 
						0.4 
						

73.0 
	 
		74.0 
			 
				1.0 
					 
						0.5 
						

74.0 
	 
		75.0 
			 
				1.0 
					 
						0.7 
						

75.0 
	 
		76.0 
			 
				1.0 
					 
						0.4 
						

76.0 
	 
		77.0 
			 
				1.0 
					 
						1.3 
						

77.0 
	 
		78.0 
			 
				1.0 
					 
						3.4 
						

78.0 
	 
		79.0 
			 
				1.0 
					 
						3.7 
						

79.0 
	 
		80.0 
			 
				1.0 
					 
						1.6 
						

80.0 
	 
		81.0 
			 
				1.0 
					 
						1.0 
						

81.0 
	 
		82.0 
			 
				1.0 
					 
						4.6 
						

82.0 
	 
		83.0 
			 
				1.0 
					 
						8.6 
						

83.0 
	 
		84.0 
			 
				1.0 
					 
						13.6 
						

84.0 
	 
		85.0 
			 
				1.0 
					 
						4.0 
						

85.0 
	 
		86.0 
			 
				1.0 
					 
						0.4 
						

86.0 
	 
		87.0 
			 
				1.0 
					 
						1.0 
						

87.0 
	 
		88.0 
			 
				1.0 
					 
						0.8 
						

88.0 
	 
		89.0 
			 
				1.0 
					 
						0.2 
						

89.0 
	 
		90.0 
			 
				1.0 
					 
						0.1 
						

90.0 
	 
		91.0 
			 
				1.0 
					 
						1.4 
						

91.0 
	 
		92.0 
			 
				1.0 
					 
						0.4 
						

92.0 
	 
		93.0 
			 
				1.0 
					 
						3.9 
						

93.0 
	 
		94.0 
			 
				1.0 
					 
						0.1 
						

94.0 
	 
		95.0 
			 
				1.0 
					 
						0.4 
						

95.0 
	 
		96.0 
			 
				1.0 
					 
						0.8 
						

96.0 
	 
		97.0 
			 
				1.0 
					 
						2.9 
						

97.0 
	 
		98.0 
			 
				1.0 
					 
						1.5 
						

98.0 
	 
		99.0 
			 
				1.0 
					 
						1.7 
						

99.0 
	 
		100.0 
			 
				1.0 
					 
						1.7 
						

100.0 
	 
		101.0 
			 
				1.0 
					 
						9.8 
						

101.0 
	 
		102.0 
			 
				1.0 
					 
						2.2 
						

102.0 
	 
		103.0 
			 
				1.0 
					 
						1.7 
						

103.0 
	 
		104.0 
			 
				1.0 
					 
						0.3 
						

104.0 
	 
		105.0 
			 
				1.0 
					 
						2.8 
						

105.0 
	 
		106.0 
			 
				1.0 
					 
						0.3 
						

106.0 
	 
		107.0 
			 
				1.0 
					 
						2.5 
						

107.0 
	 
		108.0 
			 
				1.0 
					 
						0.7 
						

108.0 
	 
		109.0 
			 
				1.0 
					 
						1.7 
						

109.0 
	 
		110.0 
			 
				1.0 
					 
						7.1 
						

110.0 
	 
		111.0 
			 
				1.0 
					 
						2.3 
						

111.0 
	 
		112.0 
			 
				1.0 
					 
						5.2 
						

112.0 
	 
		112.6 
			 
				0.6 
					 
						2.2 
						

112.6 
	 
		112.7 
			 
				0.1 
					 
						  
						

112.7 
	 
		113.0 
			 
				0.3 
					 
						0.4 
						

113.0 
	 
		114.0 
			 
				1.0 
					 
						3.6 
						

114.0 
	 
		115.0 
			 
				1.0 
					 
						5.5 
						

115.0 
	 
		116.0 
			 
				1.0 
					 
						2.7 
						

116.0 
	 
		117.0 
			 
				1.0 
					 
						7.4 
						

117.0 
	 
		118.0 
			 
				1.0 
					 
						7.2 
						

118.0 
	 
		119.0 
			 
				1.0 
					 
						6.5 
						

119.0 
	 
		120.0 
			 
				1.0 
					 
						9.9 
						

120.0 
	 
		121.0 
			 
				1.0 
					 
						6.2 
						

121.0 
	 
		122.0 
			 
				1.0 
					 
						6.2 
						

122.0 
	 
		123.0 
			 
				1.0 
					 
						10.9 
						

123.0 
	 
		124.0 
			 
				1.0 
					 
						1.4 
						

124.0 
	 
		125.0 
			 
				1.0 
					 
						4.5 
						

125.0 
	 
		126.0 
			 
				1.0 
					 
						11.4 
						

126.0 
	 
		127.0 
			 
				1.0 
					 
						4.0 
						

127.0 
	 
		128.0 
			 
				1.0 
					 
						10.0 
						

128.0 
	 
		129.0 
			 
				1.0 
					 
						16.1 
						

129.0 
	 
		130.0 
			 
				1.0 
					 
						7.9 
						

130.0 
	 
		131.0 
			 
				1.0 
					 
						2.2 
						

131.0 
	 
		132.0 
			 
				1.0 
					 
						3.2 
						

132.0 
	 
		133.0 
			 
				1.0 
					 
						2.1 
						

133.0 
	 
		134.0 
			 
				1.0 
					 
						0.1 
						

134.0 
	 
		135.0 
			 
				1.0 
					 
						2.2 
						

135.0 
	 
		136.0 
			 
				1.0 
					 
						2.7 
						

136.0 
	 
		136.5 
			 
				0.5 
					 
						2.7 
						

136.5 
	 
		137.0 
			 
				0.5 
					 
						3.4 
						

137.0 
	 
		138.0 
			 
				1.0 
					 
						3.3 
						

138.0 
	 
		138.7 
			 
				0.7 
					 
						5.7 
						

138.7 
	 
		139.0 
			 
				0.3 
					 
						10.0 
						

139.0 
	 
		140.0 
			 
				1.0 
					 
						14.6 
						

140.0 
	 
		141.0 
			 
				1.0 
					 
						6.2 
						

141.0 
	 
		142.0 
			 
				1.0 
					 
						3.1 
						

142.0 
	 
		143.0 
			 
				1.0 
					 
						0.8 
						

143.0 
	 
		144.0 
			 
				1.0 
					 
						0.6 
						

144.0 
	 
		145.0 
			 
				1.0 
					 
						2.9 
						

145.0 
	 
		146.0 
			 
				1.0 
					 
						0.1 
						

146.0 
	 
		147.0 
			 
				1.0 
					 
						0.1 
						

147.0 
	 
		148.0 
			 
				1.0 
					 
						0.0 
						

148.0 
	 
		149.0 
			 
				1.0 
					 
						0.1 
						

149.0 
	 
		150.0 
			 
				1.0 
					 
						0.4 
						

150.0 
	 
		151.0 
			 
				1.0 
					 
						9.4 
						

151.0 
	 
		152.0 
			 
				1.0 
					 
						9.7 
						

152.0 
	 
		153.0 
			 
				1.0 
					 
						7.4 
						

153.0 
	 
		154.0 
			 
				1.0 
					 
						8.1 
						

154.0 
	 
		155.0 
			 
				1.0 
					 
						8.1 
						

155.0 
	 
		156.0 
			 
				1.0 
					 
						11.7 
						

156.0 
	 
		157.0 
			 
				1.0 
					 
						8.7 
						

157.0 
	 
		158.0 
			 
				1.0 
					 
						19.2 
						

158.0 
	 
		159.0 
			 
				1.0 
					 
						2.4 
						

159.0 
	 
		160.0 
			 
				1.0 
					 
						2.6 
						

160.0 
	 
		161.0 
			 
				1.0 
					 
						6.7 
						

161.0 
	 
		162.0 
			 
				1.0 
					 
						2.3 
						

162.0 
	 
		163.0 
			 
				1.0 
					 
						5.8 
						

163.0 
	 
		164.0 
			 
				1.0 
					 
						8.2 
						

164.0 
	 
		165.0 
			 
				1.0 
					 
						4.1 
						

165.0 
	 
		166.0 
			 
				1.0 
					 
						1.1 
						

166.0 
	 
		167.0 
			 
				1.0 
					 
						4.8 
						

167.0 
																																																																																																																																																																																																																																																											 
		168.0 
			 
				1.0 
					 
						26.6 
						

168.0 
	 
		169.0 
			 
				1.0 
					 
						6.3 
						

169.0 
	 
		170.0 
			 
				1.0 
					 
						2.9 
						

170.0 
	 
		171.0 
			 
				1.0 
					 
						4.5 
						

171.0 
	 
		172.0 
			 
				1.0 
					 
						15.0 
						

172.0 
	 
		173.0 
			 
				1.0 
					 
						8.6 
						

173.0 
	 
		174.0 
			 
				1.0 
					 
						24.2 
						

174.0 
	 
		175.0 
			 
				1.0 
					 
						2.6 
						

175.0 
	 
		176.0 
			 
				1.0 
					 
						9.3 
						

176.0 
	 
		177.0 
			 
				1.0 
					 
						7.1 
						

177.0 
	 
		178.0 
			 
				1.0 
					 
						0.0 
						

178.0 
	 
		179.0 
			 
				1.0 
					 
						3.4 
						

179.0 
	 
		180.0 
			 
				1.0 
					 
						1.5 
						

180.0 
	 
		181.0 
			 
				1.0 
					 
						7.9 
						

181.0 
	 
		182.0 
			 
				1.0 
					 
						4.6 
						

182.0 
	 
		183.0 
			 
				1.0 
					 
						3.3 
						

183.0 
	 
		184.0 
			 
				1.0 
					 
						2.1 
						

184.0 
	 
		185.0 
			 
				1.0 
					 
						5.2 
						

185.0 
	 
		186.0 
			 
				1.0 
					 
						4.5 
						

186.0 
	 
		187.0 
			 
				1.0 
					 
						1.8 
						

187.0 
	 
		188.0 
			 
				1.0 
					 
						5.3 
						

188.0 
	 
		189.0 
			 
				1.0 
					 
						5.9 
						

189.0 
	 
		190.0 
			 
				1.0 
					 
						0.7 
						

190.0 
	 
		191.0 
			 
				1.0 
					 
						0.4 
						

191.0 
	 
		192.0 
			 
				1.0 
					 
						7.6 
						

192.0 
	 
		193.0 
			 
				1.0 
					 
						1.1 
						

193.0 
	 
		194.0 
			 
				1.0 
					 
						6.4 
						

194.0 
	 
		195.0 
			 
				1.0 
					 
						5.5 
						

195.0 
	 
		196.0 
			 
				1.0 
					 
						1.5 
						

196.0 
	 
		197.0 
			 
				1.0 
					 
						2.8 
						

197.0 
	 
		198.0 
			 
				1.0 
					 
						5.8 
						

198.0 
	 
		199.0 
			 
				1.0 
					 
						2.7 
						

199.0 
	 
		200.0 
			 
				1.0 
					 
						1.5 
						

200.0 
	 
		201.0 
			 
				1.0 
					 
						0.9 
						

201.0 
	 
		201.6 
			 
				0.6 
					 
						1.7 
						

201.6 
	 
		202.0 
			 
				0.4 
					 
						0.4 
						

202.0 
	 
		203.0 
			 
				1.0 
					 
						0.4 
						

203.0 
	 
		204.2 
			 
				1.2 
					 
						0.3 
						

204.2 
	 
		205.0 
			 
				0.8 
					 
						5.2 
						

205.0 
	 
		206.0 
			 
				1.0 
					 
						7.1 
						

206.0 
	 
		207.0 
			 
				1.0 
					 
						22.6 
						

207.0 
	 
		208.0 
			 
				1.0 
					 
						11.0 
						

208.0 
	 
		209.0 
			 
				1.0 
					 
						5.3 
						

209.0 
	 
		210.0 
			 
				1.0 
					 
						1.2 
						

210.0 
	 
		211.0 
			 
				1.0 
					 
						0.9 
						

211.0 
	 
		212.0 
			 
				1.0 
					 
						2.4 
						

212.0 
	 
		213.0 
			 
				1.0 
					 
						2.7 
						

213.0 
	 
		214.0 
			 
				1.0 
					 
						2.4 
						

214.0 
	 
		215.0 
			 
				1.0 
					 
						0.3 
						

215.0 
	 
		216.0 
			 
				1.0 
					 
						0.2 
						

216.0 
	 
		217.0 
			 
				1.0 
					 
						2.1 
						

217.0 
	 
		218.0 
			 
				1.0 
					 
						4.1 
						

218.0 
	 
		219.0 
			 
				1.0 
					 
						1.1 
						

219.0 
	 
		220.0 
			 
				1.0 
					 
						3.0 
						

220.0 
	 
		221.0 
			 
				1.0 
					 
						3.5 
						

221.0 
	 
		222.0 
			 
				1.0 
					 
						1.6 
						

222.0 
	 
		223.0 
			 
				1.0 
					 
						6.6 
						

223.0 
	 
		224.0 
			 
				1.0 
					 
						5.2 
						

224.0 
	 
		225.0 
			 
				1.0 
					 
						5.3 
						

225.0 
	 
		226.0 
			 
				1.0 
					 
						1.1 
						

226.0 
	 
		227.0 
			 
				1.0 
					 
						0.0 
						

227.0 
	 
		228.0 
			 
				1.0 
					 
						6.7 
						

228.0 
	 
		229.0 
			 
				1.0 
					 
						7.0 
						

229.0 
	 
		230.0 
			 
				1.0 
					 
						0.4 
						

230.0 
	 
		231.0 
			 
				1.0 
					 
						0.1 
						

231.0 
	 
		232.0 
			 
				1.0 
					 
						8.3 
						

232.0 
	 
		233.0 
			 
				1.0 
					 
						3.4 
						

233.0 
	 
		234.0 
			 
				1.0 
					 
						12.3 
						

234.0 
	 
		235.0 
			 
				1.0 
					 
						6.1 
						

235.0 
	 
		236.0 
			 
				1.0 
					 
						2.3 
						

236.0 
	 
		237.0 
			 
				1.0 
					 
						0.1 
						

237.0 
	 
		238.0 
			 
				1.0 
					 
						0.4 
						

238.0 
	 
		239.0 
			 
				1.0 
					 
						3.1 
						

239.0 
	 
		240.0 
			 
				1.0 
					 
						0.1 
						

240.0 
	 
		241.0 
			 
				1.0 
					 
						2.5 
						

241.0 
	 
		242.0 
			 
				1.0 
					 
						1.4 
						

242.0 
	 
		243.0 
			 
				1.0 
					 
						0.4 
						

243.0 
	 
		244.0 
			 
				1.0 
					 
						1.3 
						

244.0 
	 
		245.0 
			 
				1.0 
					 
						3.9 
						

245.0 
	 
		246.0 
			 
				1.0 
					 
						2.6 
						

246.0 
	 
		247.0 
			 
				1.0 
					 
						24.4 
						

247.0 
	 
		248.0 
			 
				1.0 
					 
						0.4 
						

248.0 
	 
		249.0 
			 
				1.0 
					 
						0.1 
						

249.0 
	 
		250.0 
			 
				1.0 
					 
						0.6 
						

250.0 
	 
		251.0 
			 
				1.0 
					 
						0.4 
						

251.0 
	 
		252.0 
			 
				1.0 
					 
						1.9  
						

  

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20210420005633/en/

Contacts

James Withall  Chief Executive Officer jwithall@rupertresources.com  Thomas 
Credland Head of Corporate Development  tcredland@rupertresources.com  Rupert 
Resources Ltd  82 Richmond Street East, Suite 203, Toronto, Ontario M5C 1P1 
Tel: +1 416-304-9004 Web: http://rupertresources.com/ 

Source: Rupert Resources Ltd
Powered by Business Wire