Source	CANADA NEWSWIRE
Date	04/29/2021
Time	06:34:14 AM

Company	 Golden Arrow Resources Corporation
Title	Golden Arrow Provides Exploration Update and Reports Trench Results from
Flecha de Oro Project, Argentina





    CDNX Symbol: GRG











Press Release




" BC-GRG-ExplorationUpdate   04-29 1704
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.290083:
^Golden Arrow Provides Exploration Update and Reports Trench Results from
Flecha de Oro Project, Argentina@

TSX Venture Exchange (TSX-V): GRG Frankfurt Stock Exchange (FSE): G6A
OTCQB Venture Market (OTCQB): GARWF
VANCOUVER, BC, April 29, 2021 /CNW/ - Golden Arrow Resources Corporation
(TSXV: GRG) (FSE: G6A) (OTCQB: GARWF), ("Golden Arrow" or the "Company") is
pleased to provide an update on exploration activities at its three most
active projects, including the first results from the on-going trenching
program at the Esperanza property of the Flecha de Oro gold project,
Argentina.
Phase I of the trenching program at Esperanza is focused on a nine square
kilometre area where numerous gold-bearing quartz-veins have been identified
at surface. Of particular note are results from a single vein, mapped over 540
metres of strike extent, that returned significant gold intervals in two
separate trenches located approximately 160 metres apart, including:
<<

--  five metres averaging 2.98 g/t gold, including two metres averaging 6.21
g/t gold, in trench TE-10, and;
--  one metre interval averaging 5.52 g/t gold in trench TE-6, located 160
metres east, in the same vein (see Figure 1: https://bit.ly/3udLQOw).
<>>
Golden Arrow VP Exploration and Development Brian McEwen commented, "We
have seen from our previous surface sampling that there is widespread gold in
the system at Esperanza, so we are encouraged to find some broader intervals
in the near-surface that will help us vector into the heart of the system."
Additional details from the trenching program, as well as other work in
progress, are included below. In addition to its exploration programs, Golden
Arrow is continuing with its project acquisition efforts by constantly
reviewing new opportunities to add to its exploration pipeline.
Flecha de Oro Gold Project, Rio Negro Argentina The Flecha de Oro Project
includes the La Esperanza, Puzzle and Maquinchao exploration properties,
consisting of 9,968, 1,952 and 2,000 hectares respectively, in central Rio
Negro Province. The Project lies within the Somuncara Massif, where low and
high sulphidation gold systems have been explored for since the first
discovery of gold in the area in 1995. Examples of similar projects in the
area include the Calcatreu low sulphidation gold-silver project located 165
kilometres to the southwest, hosting 746,000 oz of Indicated gold equivalent
resources and a further 390,000 oz of Inferred AuEq resourcesi.
At the La Esperanza property, Golden Arrow has identified similarities in
size and geologic style to the Cerro Vanguardia district to the south in Santa
Cruz province that has produced 4.5 million ounces of goldii, which is now
being used as an exploration model.
[Readers are cautioned that results from other companies, including on
properties proximal to those controlled by the Company, are not indicative of
expected Golden Arrow results, as there has been insufficient exploration on
these properties. These facts are simply used to aid in the exploration of
these properties.]
Golden Arrow commenced the trenching program at Flecha de Oro in December
2020, with the initial work undertaken at the Puzzle property. Results from
the first 10 trenches at Puzzle identified gold in multiple samples over
significant widths in several trenches (see Figure 2: https://bit.ly/2R7PpqU),
but at grades below the threshold targeted by the Company. As a result, the
Esperanza property has been prioritized for on-going exploration. Esperanza
hosts multiple vein corridors defined by outcropping quartz veins, boulders
and quartz float. The areas sampled by the trenches reported in this news
release returned high-grade gold samples in earlier surface sampling programs
(see Figure 1, and Company news releases dated March 2, 2020, December 3, 2019
and September 25, 2019).
Since the commencement of trenching at Esperanza on March 1st, 2021,
Golden Arrow has completed 20 trenches totaling 1,693 metres across surface
quartz veins and sheeted veinlets that range from a few centimeters to two
metres in width. Assays have been received for 10 of these trenches. An
additional fifteen trenches are underway, and the Phase I program is expected
to continue through most of May. A summary of the results from the first ten
trenches is presented in Table 1.
Table 1. Summary of Intervals >1g/t Au from Trenches 1 - 10, Esperanza
target, Flecha de Oro Project.
Trench                    Width (m) Au g/t  Ag g/t

---


T-1                                            1.4    2.58      1.2

---


0.3                                1.03     0.9

---


T-2                                            1.2    0.39      1.7

---


T-3                                            1.8    3.19     16.3

---


0.5                                0.96    18.5

---


T-4                                            0.9    1.10

---


T-5                           no significant
mineralization

---


T-6                                            1.0    5.52

---


T-7                           no significant
mineralization

---


T-8                           no significant
mineralization

---


T-9                           no significant
mineralization

---


T-10                                           5.0    2.98

---

Incl. 2.0                 6.21

---
Rosales Copper Project, Chile Golden Arrow has awarded Quantec Geoscience
Chile Ltda the contract for completing a new Transient Electromagnetic (TEM)
surface geophysical survey at the Rosales Copper Project in May. The goal of
the program is to detect and delineate prospective electromagnetic conductor
responses, consistent with near-surface copper stockwork mineralization,
potentially related to Manto-type mineralized copper systems at depth. The
program will be executed in two phases:
<<

--  An initial test over approximately 300 hectares that includes known
copper sulphide mineralization will be conducted and the results
assessed to determine if the TEM technique successfully detects the
mineralization.
--  If successful, a second survey covering approximately 800 hectares will
be completed.
<>>
Tierra Dorada Gold Project, Paraguay The planned follow-up drill program
at the Alvaro target has been delayed until permits are received that will
allow deeper drilling. While it is possible to continue with the shallow
(<20m) drill hole program allowed by the existing permit, after further review
of the initial shallow drilling results and the new targets identified by the
IP geophysical survey (see News Release of January 9, 2021) it was concluded
that there was greater benefit to waiting to be able to drill the deeper
holes. Granting of permits has been delayed by outbreaks of COVID-19 within
several government agencies and elsewhere in Paraguay. In the interim, the
Golden Arrow exploration team has commenced a detailed soil sampling program
over the new geophysical targets that have no surface outcrop to refine drill
targets in those areas. In addition, mapping, trenching and surface sampling
programs at the Alvaro target, and regionally throughout the project, are
ongoing.
For additional details on the Company's main projects, please visit the
website www.goldenarrowresources.com.
Methodology and QA/QC At the Flecha de Oro project, trenches were opened
across the vein width and continued into the host rock on either side. Channel
samples were cut along the trench walls with an electric saw and sampled in
one-metre intervals. Samples were shipped for preparation and analysis at ALS
Laboratories, an internationally recognized assay service provider. Samples
were prepared at their facility in Mendoza, Argentina and assayed for gold by
Fire Assay/Atomic Absorption finish and analyzed for a multi-element package
by ICP-OES following a four-acid digestion at their laboratory in Lima, Peru.
The Company follows industry standard procedures for the work carried out on
the Flecha de Oro Project, with a quality assurance/quality control (QA/QC)
program. Blank, duplicate and standard samples were inserted in each batch of
samples sent to the laboratory for analysis. Golden Arrow detected no
significant QA/QC issues during review of the data.
Qualified Persons
The results of the Company's exploration program have been reviewed,
verified (including sampling, analytical and test data) and compiled by the
Company's geological staff under the supervision of Brian McEwen, P.Geol., VP
Exploration and Development to the Company. Mr. McEwen is a Qualified Person
as defined in National Instrument 43-101, and has reviewed and approved the
contents of the news release.
About Golden Arrow:
Golden Arrow Resources Corporation is a mining exploration company with a
successful track record of creating value by making precious and base metal
discoveries and advancing them into exceptional deposits. The Company is well
leveraged to the price of gold, having monetized its Chinchillas silver
discovery into a significant holding in precious metals producer SSR Mining
Inc.
Golden Arrow is actively exploring a portfolio that includes a new
epithermal gold project in Argentina, a district-scale frontier gold
opportunity in Paraguay, a base-metal project in the heart of a leading mining
district in Chile and more than 180,000 hectares of properties in Argentina.
The Company is a member of the Grosso Group, a resource management group
that has pioneered exploration in Argentina since 1993.
ON BEHALF OF THE BOARD
"Joseph Grosso"
_______________________________ Mr. Joseph Grosso, Executive Chairman,
President and CEO
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release may contain forward-looking statements. Forward-looking
statements address future events and conditions and therefore involve inherent
risks and uncertainties. All statements, other than statements of historical
fact, that address activities, events or developments the Company believes,
expects or anticipates will or may occur in the future, including, without
limitation, statements about the Company's plans for its mineral properties;
the Company's business strategy, plans and outlooks; the future financial or
operating performance of the Company; and future exploration and operating
plans are forward-looking statements.
Forward-looking statements are subject to a number of risks and
uncertainties that may cause the actual results of the Company to differ
materially from those discussed in the forward-looking statements and, even if
such actual results are realized or substantially realized, there can be no
assurance that they will have the expected consequences to, or effects on, the
Company. Factors that could cause actual results or events to differ
materially from current expectations include, among other things: the impact
of COVID-19; risks and uncertainties related to the ability to obtain, amend,
or maintain licenses, permits, or surface rights; risks associated with
technical difficulties in connection with mining activities; and the
possibility that future exploration, development or mining results will not be
consistent with the Company's expectations. Actual results may differ
materially from those currently anticipated in such statements. Readers are
encouraged to refer to the Company's public disclosure documents for a more
detailed discussion of factors that may impact expected future results. The
Company undertakes no obligation to publicly update or revise any
forward-looking statements, unless required pursuant to applicable laws.


i Patagonia Gold Corp, NI 43-101 report with effective date
of 31 of December 2018, filed on SEDAR.com


ii http://panorama-minero.com/noticias/cerro-
vanguardia-ha-sido-y-sigue-siendo-escuela/ (112119)

View original content to download
multimedia:http://www.prnewswire.com/news-releases/golden-arrow-provides-explo
ration-update-and-reports-trench-results-from-flecha-de-oro-project-argentina-
301280332.html
SOURCE Golden Arrow Resources Corporation



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2021/29/c5260.html

-0-                           04/29/2021
/For further information: Corporate Communications, Tel: 1-604-687-1828,
Toll-Free: 1-800-901-0058, Email: info(at)goldenarrowresources.com/
(GARWF GRG. G6A)

CO:  Golden Arrow Resources Corporation
ST:  British Columbia
IN:  MIN MNG OTC
SU:

-30-