Source	CANADA NEWSWIRE
Date	05/03/2021
Time	05:03:15 AM

Company	 Freeport Resources Inc.
Title	Freeport Resources Announces Star Mountains AI Evaluation and K-means
Analysis Results Produced by Minerva Intelligence





    CDNX Symbol: FRI











Press Release




" BC-FreeportMinervaResult   05-03 1711
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.105565:
^Freeport Resources Announces Star Mountains AI Evaluation and K-means
Analysis Results Produced by Minerva Intelligence@

VANCOUVER, BC, May 3, 2021 /CNW/ - Freeport Resources Inc. (TSX-V: FRI)
(FSE: 4XH) (OTCQB: FEERF) ("Freeport", or the "Company") is pleased to share
results from an evaluation of the Star Mountains data conducted by Minerva
Intelligence Inc. (TSX-V: MVAI) ("Minerva"), an artificial intelligence
company focused on knowledge engineering. Previously announced on November 23,
2020, Minerva utilized DRIVER, its cutting-edge AI software, to perform an
evaluation of multi-element drilling data. In addition, Minerva reinterpreted
existing geophysical information on the project and completed traditional
K-Means Cluster analysis on the multi-element data.
Freeport engaged Minerva to apply its cognitive AI-powered DRIVER
technology to sub-surface geochemical data available for the Star Mountains
project to enhance its next phases of surface and sub-surface evaluation of
the extensive property, located 25 kilometres from the Ok Tedi mine in Papua
New Guinea.
DRIVER and K-Means Cluster analyses were focused in the Olgal deposit
area, utilizing geochemical analyses from 23 drillholes, for which a current
inferred resource was previously determined. Evaluation identified multiple
mineralized subgroups of dioritic rocks and skarn as potentially significant
for copper, as well as a significant overlap of copper and gold-bearing
volumes. These sub-groups are located at the core of the deposit area and well
distributed from near surface to the basal thrust fault at depth. Two
mineralized dioritic sub-groups for gold were identified.
DRIVER EvaluationDRIVER delivers valuable insights from multi-element
geochemical data through comprehensive evaluation of all elements present
within a given database, not simply elements of direct economic interest.
Comparable evaluation of such data has typically been prohibitively
time-consuming and too complex for geologists to attempt.
Many of the DRIVER volumes examined at the Olgal deposit exhibit a
prominent central pipe-like feature having a strong spatial association with
Quartz Diorite and "Early Diorite". This pipe-like feature is interpreted to
represent a composite volume resulting from gold - copper intercepts hosted
within quartz diorite and/or "Diorite 4'' in drillholes 001OLG10, 002OLG10 and
014OLG12. As such, study results confirm previous interpretation of at least
two dioritic intrusive phases (Quartz Diorite and "Early Diorite"). A separate
and distinct molybdenum volume southeast of the core of the deposit area is
interpreted to indicate a third diorite intrusion. The Olgal Deposit is
interpreted to result from multi-phase intrusion of diorite at the contact
between Derai Limestone and Leru Sediments. Study results also support
interpretation of a mineralized copper and gold trend extending
north-northwest from the Olgal Deposit. These results and interpretations
independently validate similar interpretations by Freeport personnel.
K-Means Cluster AnalysisK-Means Cluster analysis was focused in the Olgal
deposit area, utilizing geochemical analyses from 23 drillholes, for which a
current inferred resource was previously determined (see below). Evaluation
identified multiple mineralized subgroups of dioritic rocks and skarn as
potentially significant for copper. These sub-groups are located at the core
of the deposit area and well distributed from near surface to the basal thrust
fault at depth. Two mineralized dioritic sub-groups for gold were identified.
Widespread presence of Derai Limestone in the project area, within which
numerous occurrences of diorite intrusions have been documented, supports
interpreted potential for Cu ± Au skarn-style mineralization.
Subsequent application of K-Means Cluster analysis to geochemical results
from limited drill holes around the broader area of the Olgal Deposit are
interpreted to indicate that Futik, Ratatat and Kum Kom have multiple
intercepts corresponding to the mineralized sub-groups described above.
Therefore, they are interpreted to represent targets for future evaluation.
Geophysics ReinterpretationAvailable geophysics, dominated by various
generations of magnetic data, with subordinate electromagnetic data, were also
evaluated. Spatial association of strong magnetic anomalies with surface
geochemical results are interpreted to indicate the Star Mountains project
area has multiple targets having a signature similar to the Olgal Deposit and
are, therefore, worthy of further evaluation.
Magnetic Inversion modeling identified a large volume underlying the
Olgal Deposit, with the majority of the volume extending northwest, toward
Futik and beyond. As such, geophysical results are interpreted to support
potential for identification of additional sub-surface mineralization,
extending northwest from Olgal, through Futik and beyond.
In addition, magnetic inversion results also document subsurface volumes
spatially associated with Ratatat and Tuk. There are comparatively small
sub-surface inversion volumes (relative to the Olgal - Futik anomaly) evident
at Ratatat and Tuk, however, there are only limited drill hole results with
which to evaluate sub-surface potential. Note: the detailed survey did not
extend far enough north to cover Kum Kom and, therefore, there are no magnetic
data available to assess potential at that locality. Results of magnetic
inversion support results of K-Means Cluster analysis, interpreted to support
further evaluation of these areas.
Finally, results of magnetic inversion are interpreted to indicate the
Olgal Deposit is a decapitated porphyry, again, consistent with previous
interpretation. However, the Olgal Deposit is interpreted to have been tilted
to the north-northeast in the hanging wall of the thrust fault and transported
to the northeast. Therefore, the root of the Olgal porphyry system is
interpreted to be located to the west-southwest of the current surface
exposure.
Significant Conclusions
<<

1. Based on K-Means Cluster, DRIVER and 3D inversion results, potential to
expand both grade and volume of copper ± gold porphyry-style mineralization
is interpreted to exist at the core of the Olgal Deposit area, extending to
the northwest. Infill drilling is recommended.
2. Extending drill holes 003OLG10 and 004OLG10 below the basal thrust fault is
expected to return mineralized intercepts associated with an anomaly
identified through 3D inversion of magnetic data, based on magnetic
susceptibility results.
3. Mapped exposures of epidote alteration, marble, skarn and diorite,
supported by trends interpreted from the results of both K-Means Cluster
and DRIVER analysis and a large sub-surface volume delineated by magnetic
inversion, are interpreted to indicate strong potential for identification
of additional porphyry-style mineralization extending from the Olgal
Deposit northwest to Futik and beyond.
4. Limited drilling at Futik, Ratatat, Pad 48 and Tuk is interpreted to have
tested the margins of their respective target anomalies, particularly those
defined by 3D inversion of magnetic data, with holes either collared too
far laterally and/or not drilled deep enough. Further evaluation is
strongly recommended.
<>>
"We found Minerva's analysis and the DRIVER system to be very useful to
our understanding of the project," said Gord Friesen, CEO of Freeport. "DRIVER
validated our geologists' interpretation of the deposit zonation and gave
indication of mineral potential beyond known resources on our properties and
confirmed it in a fraction of the time. The synthesis of independent
methodologies was a valuable contribution to the project and gave us
confidence about the results."
A summary report prepared by Minerva can be found on the Freeport website
at www.freeportresources.com.
Dr. Nathan Chutas, PhD, CPG, Senior Vice-President of Operations for
Freeport, is a qualified person for the purposes of National Instrument
43-101. Dr. Chutas has reviewed and approved the technical content in this
news release.
About Freeport Resources Inc.Freeport is a Canadian junior exploration
company. Freeport recently acquired Quidum Resources and, through its wholly
owned subsidiary Highlands Pacific Resources Ltd., controls the Star Mountains
project in Papua New Guinea. Please visit www.freeportresources.com or contact
the email address below for more information.
About the Star Mountains PropertyStar Mountains is a large copper and
gold porphyry project in mining-friendly Papua New Guinea, comprising 4
tenements located 25 kilometres northeast of the giant Ok Tedi mine. H&S
Consultants Pty. Ltd. completed a maiden mineral resource estimate, in
accordance with National Instrument 43-101, for the Olgal deposit situated on
the EL 1312 tenement. The current inferred resource, using a 0.3% copper
cut-off grade, is 210 million tonnes grading 0.4% copper and 0.4 g/t gold, for
2.9 million ounces of contained gold and 1.9 billion pounds (840,000 tonnes)
of contained copper. Using current prices for gold and copper, this is
equivalent to approximately 7.4 million ounces of gold or 3.1 billion pounds
(1,380,000 tonnes) of copper.
About Papua New GuineaPapua New Guinea (PNG) is a country that occupies
the eastern half of the island of New Guinea in the southwestern Pacific
Ocean. PNG is richly endowed with mineral resources, and the geological arc
spanning the island is home to some of the world's largest gold and copper
mines/projects including Grasberg, Porgera, Frieda River, Ok Tedi, Ramu and
Lihir. PNG is considered a stable and mining-friendly jurisdiction and
presents tremendous exploration potential.
About Minerva Intelligence Inc.Minerva Intelligence Inc. is a knowledge
engineering company based in Vancouver, Canada, with a subsidiary office in
Darmstadt, Germany. Their proprietary evidence-based, decision-making software
applies the benefits of artificial intelligence technology to industries
dependent on reasoning with complex technical and scientific data.Currently,
Minerva's AI applications focus on earth science-related domains, including,
but not limited to, natural hazards and mineral exploration; their technology
has applications in diverse industries and domains.
Minerva's common shares are currently listed on the TSX Venture Exchange
(symbol MVAI). For further details, please refer to their website
www.minervaintelligence.com or follow Minerva on Twitter or LinkedIn.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release may contain certain "Forward-Looking Statements" within
the meaning of the United States Private Securities Litigation Reform Act of
1995 and applicable Canadian securities laws. When or if used in this news
release, the words "anticipate", "believe", "estimate", "expect", "target,
"plan", "forecast", "may", "schedule", "intends" and similar words or
expressions identify forward-looking statements or information. Such
statements represent the Company's current views with respect to future events
and are necessarily based upon a number of assumptions and estimates that,
while considered reasonable by the Company, are inherently subject to
significant business, economic, competitive, political and social risks,
contingencies and uncertainties. Many factors, both known and unknown, could
cause results, performance or achievements to be materially different from the
results, performance or achievements that are or may be expressed or implied
by such forward-looking statements. The Company does not intend, and does not
assume any obligation, to update these forward-looking statements or
information to reflect changes in assumptions or changes in circumstances or
any other events affecting such statements and information other than as
required by applicable laws, rules and regulations.
SOURCE Freeport Resources Inc.



View original content:
http://www.newswire.ca/en/releases/archive/May2021/03/c1898.html

-0-                           05/03/2021
/For further information: Freeport Resources Inc., Gord Friesen, Chief
Executive Officer, (236) 334-1660 or gord(at)freeportresources.com; Minerva
Intelligence Inc., Dan Vroon, Business Development Manager, (604) 620-1051 or
dvroon(at)minervaintelligence.com/
/Web Site: www.freeportresources.com /
(4XH FEERF FRI.)

CO:  Freeport Resources Inc.
ST:  British Columbia
IN:  MNG OTC
SU:

-30-